Doc# SEC-2014-0380R01-TS-0003_CR_generalizing_purpose_of_MEF_bootstrap_scenario

| CHANGE REQUEST |
| --- |
| Group Name:* | SEC 12 |
| Source:* | Francois Ennesser, Gemalto (ETSI) |
| Format:* | Face-to-Face |
| Date:* | 2014-07-20 |
| Contact:* | francois.ennesser@gemalto.com; mireille.pauliac@gemalto.com |
| Reason for Change/s:* | The scenario MEF-based bootstrap framework described in clause 8.3.2.1 of TS-0003, could be advantageously used with a direct security association framework using symmetric keys and should therefore not be bound to be used with a MAF based Security Association Framework. This CR proposes to generalize this scenario accordingly. |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0003 v0.6.0 Note 1: This baseline does not incorporate SEC-2014-0335R01, which modifies some text in the clauses that are displaced by the present contribution Note2: This contribution can be applied independently of our other contribution moving the affected scenario from the “direct” to the “centralized framework” clause |
| Clauses/Sub Clauses* | 8.3.1.2, 8.3.2.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

As described, the MEF based symmetric key security Bootstrap framework is tied to be used with a centralized (MAF based) security association establishment framework, while there would be value in using such a scenario in conjunction with a direct security association establishment framework based on symmetric key. We therefore propose to generalize the description of MEF based bootstrap to enable provisioning pairs of entities with a common key, without requiring one of the entities to be a MAF.

### -----------------------Start of change 1-------------------------------------------

### 8.2.2	Direct Security Association Establishment Frameworks

#### 8.2.2.1	Provisioned Symmetric Key Security Association Establishment Frameworks

This clause describes the Provisioned Secure Connection Key Security Association Establishment Framework.  This framework enables mutual authentication of two entities corresponding to either two CSEs or a CSE and an AE. The Credential for this framework is a long-term symmetric key that has been provisioned into the entities to be authenticated. This key is called a Provisioned Secure Connection Key and is denoted Kpsa. The provisioning of Kpsa could be a pre-provisioning or a remote provisioning thanks to Security Bootstrap Frameworks, as described in clause 8.3.The entities authenticate each other by verifying message authentication codes in the Security Handshake which were generated using the Provisioned Secure Connection Key.

NOTE:	Long term Provisioned Secure Connection Keys can pose a security risk if not adequately secured, and for this reason long term Provisioned Secure Connection Keys are recommended to be stored in Secure Environments.

Figure 8.2.2.1-1 illustrates the sequence of events when using the Provisioned Secure Connection Key Security Association Establishment Framework. In this description, "Entity A" and "Entity B" correspond to either two CSEs or a CSE and an AE or an AE and a CSE (respectively).

NOTE:	The following font colours differentiate the general topic that the text relates to:
Blue italic text highlights details specific to this particular Security Association Establishment Framework.

Purple italic text highlights technical actions that may include steps not specified by oneM2M.

Red italic text highlights security-related properties.

Figure 8.2.2.1-1: The sequence of events when using the Pre-Provisioned Secure Connection Key
Security Association Establishment Framework

Credential Configuration: The Provisioned Secure Connection Key (Kpsa) and the corresponding Provisioned Secure Connection Key Identifier, denoted KpsaId, are provisioned to both entities either with pre-provisioning or remote provisioning

NOTE 1:	The pre-provisioning (by definition) uses mechanisms not specified by oneM2M. The remote provisioning is performed thanks to Security Bootstrap Frameworks described in clause 8.3

Association Configuration: Each entity is configured with the information needed for mutual authentication and identification:

Entity A is commanded to initiate Security Context Establishment, and includes the following arguments:

The Provisioned Secure Connection Key Identifier KpsaId.

Entity A identity (IdA). Entity A is to assume this identity when interacting with Entity B.

Entity B identity (IdB). Entity A is to use this identity for Entity B authenticating using the above arguments. This identity is also used to route the (D)TLS exchange.

The mechanisms for achieving this are discussed in clause 8.4.1.2 (for the cases where Entity A is in the Field Domain) and Clause 8.4.2 (for the cases where Entity A is in the Infrastructure Domain).

NOTE 2:	Entity A will associate Entity B's identity with messages secured within Security Contexts established using the Provisioned Secure Connection Key Kpsa associated with the Provisioned Secure Connection Key Identifier KpsaId.

Entity B is configured with the following arguments describing Entity A authorized to perform Security Context Establishment with the Registrar:

The Provisioned Secure Connection Key Identifier KpsaId.

Entity A identity (IdA). Entity B is to use this identity for Entity A authenticating using the above arguments..

Entity B Identity (IdB), if not already configured to Entity B. Entity B is to assume this identity when interacting with Entity A.

The mechanisms for achieving this are discussed in clause 8.4.1.2 (for the cases where Entity B is in the Field Domain) and Clause 8.4.2 (for the cases where Entity B is in the Infrastructure Domain).

NOTE 3:	Entity B will associate the configured Entity A identity with messages secured within Security Contexts established using the Provisioned Secure Connection Key Kpsa associated with the Provisioned Secure Connection Key Identifier KpsaId.

NOTE 4:	In many scenarios, the entity identities will be configured when the Provisioned Secure Connection Key Kpsa is established, so a separate configuration is not required in those scenarios.

Association Security Handshake: The entities perform a (D)TLS-PSK handshake [15] to establish a secure session.

Centralized Key Distribution Server Handshake: There is no Centralized Key Distribution Server Handshake applied in the Provisioned Secure Connection Key Security Association Establishment Framework.

The "psk_identity" parameter [15] is set to the value of the Provisioned Secure Connection Key Identifier KpsaId.

The "psk" parameter [15] is set to the value of the Provisioned Secure Connection Key Kpsa.

Mandatory and optional (D)TLS cipher suites for this phase are specified in clause 9.2.

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## 8.3	Security Bootstrap Frameworks

### 8.3.1	Overview on Security Bootstrap Frameworks

#### 8.3.1.1	Purpose of Security Bootstrap Frameworks

Security Bootstrap Frameworks enable the provisioning of a symmetric key shared between two entities. Those two entities can be either a CSE/AE and a M2M Authentication Function (MAF) or two CSEs/AEs.

The provisioned symmetric key can be used for Provisioned Symmetric Key Security Association Establishment Framework or MAF-based Symmetric Key Security Association Establishment Frameworks.

Provisioned Symmetric Key Security Association Establishment

Provisioned Symmetric Key Association Establishment uses a symmetric key Kpsa and corresponding KpsaId, shared between two entities (Entity A and Entity B), to establish security associations between those two entities (CSE/AEs), as described in clause 8.2.2.1. This symmetric key Kpsa and corresponding KpsaId shall be either pre-provisioned or remotely provisioned to the two CSE/AEs thanks to Security Bootstrap Frameworks.

MAF-based Symmetric Key Security Association Establishment

The MAF-based Security Association Establishment Framework uses a Master Credential (Km) and corresponding Master Credential Identifier (KmId), shared by a CSE/AE and an M2M Authentication Function, to establish security associations between the CSE/AE and other CSEs and/or AEs as described in clause 8.2.3.

The Master Credential (Km) and corresponding Master Credential Identifier (KmId) shall either be pre-provisioned or remotely provisioned to the CSE/AE and M2M Authentication Function.

General

The details for pre-provisioning are not described in this specification.

Clause 8.3 describes the set of remotely provisioning mechanisms; called Security Bootstrap Frameworks. An M2M Enrolment Function facilitates the remote provisioning.

#### 8.3.1.2	Overview on Security Bootstrap Frameworks

An AE or CSE that requires remote provisioning of a Master Credential and Master Credential Identifier or a Provisioned Secure Connection Key (Kpsa) and Provisioned Secure Connection Key Identifier (KpsaId) is called an Enrolee.The AE or CSE with whom the enrolee is to establish a security association is called Enrolee B. The oneM2M system supports the following Security Bootstrap Frameworks:

Direct Security Bootstrap Frameworks

Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework: A symmetric key is pre-provisioned to the Enrolee and M2M Enrolment Function for the mutually authentication of those entities. For more details, see clause 8.3.2.1.

Certificate-Based Security Bootstrap Framework: The Enrolee and M2M Enrolment Function are each issued with

a Private Signing Key that is known only to that entity,

a Certificate containing the corresponding Public Verification Key, and

(Optionally) a Certificate Chain from the entity's Certificate to a Root Certificate.

The Enrolee and M2M Enrolment Function shall validate each other's Certificate before trusting the Public Verification Keys in the Certificate. Within the Security Handshake, the M2M Enrolment Function creates a digital signature of the session parameters using its private signing key and the Enrolee verifies the digital signature using the M2M Enrolment Function's public verification key. Then the roles are reversed: the Enrolee creates a digital signature and the M2M Enrolment Function verifies it. For more details see clause 8.3.2.2.

Centralized Security Bootstrap Frameworks

GBA-based Security Bootstrap Framework. In this case, the M2M Enrolment Function includes the functionality of a GBA Bootstrap Server Function. This framework uses 3GPP or 3GPP2 symmetric keys to authenticate the Enrolee and the M2M Enrolment Function (which is also a GBA BSF). The details are specified by 3GPP [13] and 3GPP2 [14]. For more details see clause 8.3.3.1.

For a more detailed description of the above Security Bootstrap Frameworks, it is useful to compare the following aspects of the Security Bootstrap Frameworks.

Bootstrap Credential Configuration: The Enrolee and M2M Enrolment Function are pre-provisioned with the Bootstrap Credential that the entity will use to authenticate itself to the other entity. The mechanisms for this pre-provisioning are not described in this specification.

Bootstrap Instruction Configuration: The Enrolee and M2M Enrolment Function are provided with

Either the M2M Authentication Function Identifier (MAF-ID) identifying the M2M Authentication Function for which the Enrolee is to be remotely provisioned when used in conjunction with a MAF-based security association establishment framework; or the identifier of Enrolee B (Enrolee B-ID), when used in conjunction with a Provisioned Symmetric Key Security Association Establishment.

NOTE 1:	The identity of the M2M Authentication Function or the Enrolee B is assumed to have been configured prior to the Bootstrap Instruction Configuration phase.

The CSE-ID or AE-ID that the M2M Authentication Function or Enrolee B is to associate with the Enrolee.

Additionally, in the case of Certificate-Based Security Bootstrap Framework:

The Enrolee is configured with the M2M Enrolment Function URI (for the purpose of routing the (D)TLS messages to the M2M Enrolment Function), M2M Enrolment Function Certificate Name and M2M Enrolment Function Root of Trust that the Enrolee will use to verify the M2M Enrolment Function.

The M2M Enrolment Function is configured with the Enrolee Certificate Name and Enrolee Root of Trust that the M2M Enrolment Function will use to verify the Enrolee.

Bootstrap Enrolment Handshake: Identification, authentication and security context establishment between the Enrolee and M2M Enrolment Function.

Enrolment Key Generation: generating a symmetric Enrolment Key,(Ke) and corresponding Enrolment Key Identifier (KeId) shared by the Enrolee and M2M Enrolment Function, which is used for subsequent generation of the Master Credential (Km).

Usage in Centralized Key Distribution Server Handshake:

For MAF-based symmetric Key Security Association, the following steps occur during the Centralized Key Distribution Server Handshake of the MAF-Based Security Association Establishment.The Enrolee derives the Master Credential (Km) from the Enrolment Key (Ke) and M2M Authentication Function Identifier (MAF-ID). Details of the derivation are provided in clause 9.4.

The Enrolee generates the Master Credential Identifier (KmId) from Master Credential (Km) as described in clause 9.1, and stores Km and KmId.

The Enrolee passes the Enrolment Key Identifier (KeId)  to the M2M Authentication Function (see "Centralized Key Distribution Server Handshake" in clause 8.2.3.1)

NOTE 2:	When the Enrolee first communicates with the M2M Authentication Function, then the M2M Authentication Function has not yet retrieved the Km from the M2M Enrolment Function. Consequently, the Enrolee provides the KeId to the M2M Authentication function, which is then passed to the M2M Enrolment Function to identify the Enrolment Key. The M2M Enrolment Function then returns the Km from which the M2M Authentication Function can derive the KmId. In subsequent Security Establishments, the Enrolee may provide the KmId or the KeId, and the M2M Authentication Function will know that both identifiers indicate the retrieved Km. For more details, see "Centralized Key Distribution Server Handshake" in clause 8.2.3.1.

Upon receipt of the KeId, the M2M Authentication Function determines if it already has the corresponding Km and CSE-ID or AE-ID of the Enrolee

If the M2M Authentication Function already has the corresponding Km and CSE-ID or AE-ID of the Enrolee, then the Km is used for mutual authentication (see "Centralized Key Distribution Server Handshake" in clause 8.2.3.1)

If the M2M Authentication Function does not have the corresponding Master Credential (Km) and CSE-ID or AE-ID of the Enrolee, then the following steps are followed.

-	The M2M Authentication Function (securely) passes the KeId to the M2M Enrolment Function, along with the M2M Authentication Function's URI.

-	The M2M Enrolment Function derives the Km from the Ke and MAF-ID. Details of the derivation are provided in clause 9.4.

-	The M2M Enrolment Function returns the Km to the M2M Authentication Function. The M2M Enrolment Function also passes the USS, including the CSE-ID or AE-ID of the Enrolee. More details are provided in clause 8.6.

-	The M2M Authentication Function generates the Master Credential Identifier (KmId) from Master Credential (Km) as described in clause 9.1, and stores Km and KmId.

-	The Master Credential (Km) is used for mutual authentication (see "Centralized Key Distribution Server Handshake" in clause 8.2.3.1).

For Provisioned Symmetric Key Security Association Establishment, similar procedure applies where Enrolee B plays the role of M2M Authentication Function, Kpsa plays the role of Km, KpsaId is generated instead of KmId.

Figure 8.3.1.2-1 provides a summary of the above defined Security Bootstrap Frameworks.

Figure 8.3.1.2-1: Overview of the Security Bootstrap Frameworks supported by oneM2M

Editor's note: In the above figure and other similar ones, more parameters may need to be transferred from MAF to MEF in the "Usage in Centralized Key Distribution Server Handshake". This is FFS. (ACTION Qualcomm)

### -----------------------End of change 2-------------------------------------------