| CHANGE REQUEST |
| --- |
| Group Name:* | SEC#12 |
| Source:* | Qualcomm Inc. (TIA) |
| Format:* | Plenary |
| Date:* | 2014-07-23 |
| Contact:* | Philip Hawkes, Qualcomm, phawkes@qti.qualcomm.com, Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | Informative Annex describing use of Security Association Establishment and Security Bootstrap Frameworks |
| CR against: | TS-0003v0.6.0 |
| Clauses/Sub Clauses Affected* | New Annex A.x |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include proposed text into a new Annex of TS-0003 (or, alternatively, merge with contribution SEC-2014-0371_Clause_6_cleanup_CR as update of clause 6) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

At the SEC#10.4 Adhoc meeting in Paris, participating people agreed that it would be useful to have some pictorial representation of the various security frameworks specified in chapter 8 of TS-0008 and to insert it into an informative Annex to TS-0003. Such picture and description should help the reader to better understand the selection of security frameworks and organization of chapter 8. It could be similar to the presentation on slide 4 of SEC-2014-0253R01.

This contribution proposes a respective informative Annex for TS-0003. However, we may alternatively consider to include the proposed text into clause 6 of TS-0003. In this case the text proposed in this contribution could be merged with our contribution SEC-2014-0371_Clause_6_cleanup_CR.

### -----------------------Start of change 1-------------------------------------------

Annex X (informative):
Overview on oneM2M Security Frameworks

## X.1	Introduction

In this specification, the term Security Frameworks refers to the set of procedures needed to establish a security association between M2M entities (i.e. AEs and CSEs) that intend to establish secure communication connectivity with each other.

The main purpose of M2M Security Association Establishment is to provide a secure mechanism allowing the communicating entities to mutually authenticate their identities and establish a secure communication session for exchange of oneM2M request/response messages.

In this specification, it is differentiated between two groups of Security Association Establishment Frameworks:

Direct Security Frameworks, where the entities authenticate each other directly, and

Centralized Security Frameworks, where the entities authenticate each other with the assistance of a Central Server (denoted in this specification generically as Central Key Distribution Server).

It is not always possible to pre-provision an M2M entity with all parameters needed to start a Security Association Establishment procedure. In this case it is necessary to first enter into a Security Bootstrap procedure, where the M2M entity first contacts a bootstrap server (denoted M2M Enrolment Function (MEF), see Annex X.3) to obtain the parameters needed for Security Association Establishment with the target M2M entity.

The set of Security Frameworks specified in Section 8 of this document includes both, the Security Association Establishment Frameworks and Security Bootstrap Frameworks.

## X.2	Security Association Establishment Frameworks

Figure X.2-1 illustrates the different use cases and entities involved in the various Security Association Establishment Frameworks (SAEF) considered in this specification.

Figure X.2-1:  Entities involved in Security Association Establishment

Direct SAEF is applied between two M2M entities A and B. There are two Direct Security Frameworks specified in this document, Pre-Provisioned Symmetric Key SAEF and Certificate-Based SAEF.

Pre-Provisioned Symmetric Key SAEF requires that both M2M entities A and B are pre-provisioned with a shared key (Kpsa) and an associated key identifier (KpsaId) (cf. subsection 8.2.2.1).

Certificate-Based SAEF requires that both M2M entities A and B are pre-provisioned with their certificates (CertA, Cert B) and (optionally) their certificate chains (allowing certificate verification), and their private keys associated with the certificates (cf. subsection 8.2.2.2).

Two Centralized Security Frameworks are specified in this document, GBA-based SAEF and MAF-Based SAEF. Both frameworks require a centralized key distribution server. The difference between these two centralized frameworks is the domain where the key distribution server is located and the communication interfaces used between the involved nodes.

For MAF-based SAEF, the centralized key distribution server is an M2M Authentication Function (MAF) hosted either by a 3rd party service provider which has a service relationship with the M2M Service Provider (M2M-SP), or hosted by the M2M-SP itself.   Interfaces between entity A and MAF and between entities A and B are described in this document (cf. subsection 8.2.3.1).  The interface between MAF and Entity B is not specified in this document.

For GBA-based SAEF, the centralized key distribution server is a Bootstrap Server Function (BSF) of the 3GPP Generic Bootstrap Architecture (GBA) hosted by the Underlying Network Service Provider (UN-SP). The 3GPP-defined communication protocols as specified in [28 - 30] are employed (cf. subsection 8.2.3.2).

## X.3	Security Bootstrap Frameworks

A security bootstrap procedure is needed when the M2M SP requires the Field Domain entity A to use the MAF-Based SAEF, and Entity A is not pre-provisioned with security credentials for that MAF.

Such scenario e.g. is applicable when a customer has acquired an M2M device (host of M2M entity A) which is not branded for a specific application and M2M-SP at manufacture stage. Such entity could still have security credentials pre-provisioned that allows it to contact securely an M2M Enrolment Function (MEF), even automatically when powered-on without any user interaction.

For security bootstrapping, the same authentication mechanisms as used for the SAEF frameworks in Annex X.2 (pre-provisioned key, certificate-based, GBA-based) may be employed for mutual authentication between an M2M entity A and the MEF in the first phase of the bootstrap process, and to establish the keys that are used for subsequent generation of the master credential to be shared with the MAF.

Section 8 of this document specifies accordingly three different Security Bootstrap Frameworks:

- Pre-Provisioned Symmetric Enrolee Key (PPESK) SBF (see subsection 8.3.2.1)

- Certificate-Based SBF (see subsection 8.3.2.2)

- GBA-Based SBF (see subsection 8.3.3.1)

By means of the bootstrap procedure, the M2M entity is enroled to the M2M-SP subscriber base. Therefore the enroling M2M entity is denoted as Enrolee in this context. The result of a SBF is the assignment of a Master Credential (Km) and Master Credential Identifier (KmId) to the Enrolee by the MAF.

Figure X.3-1 illustrates the different Security Bootstrap Frameworks. Note there is no communication between M2M Entities A and B in the bootstrap procedure. After successful completion of the bootstrap procedure, the MAF-Based Security Association Establishment procedure outlined in Annex X.2 is applied.

Figure X.3-1:  Entities involved in Security Bootstrap

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Does this change request avoid conflict with the content of an already approved text, by modification, deletion or the addition of an editor’s note?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change  include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Text boxes

M2M

Entity

A

M2M

Entity

B

UN-SP Domain

Field Domain

3rd Party Domain

or M2M-SP Domain

M2M-SP Domain

GBA

BSF

MAF

Direct SAEF

MAF

GBA and MAS based SAEF

MAF

M2M

Entity

A

M2M

Entity

B

UN-SP Domain

Field Domain

3rd Party Domain

or M2M-SP Domain

M2M-SP Domain

GBA

BSF

(=MEF)

MAF

MEF