| CHANGE REQUEST |
| --- |
| Group Name:* | SEC 12 |
| Source:* | Francois Ennesser, Gemalto (ETSI) |
| Format:* | Face-to-Face |
| Date:* | 2014-07-25 |
| Contact:* | francois.ennesser@gemalto.com |
| Reason for Change/s:* | Cleanup of clause 6.1.7 of TS-0003 |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0003 v0.6.0 |
| Clauses/Sub Clauses* | 6.1.7 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR provides editorial cleanup of section 6.1.7.

### -----------------------Start of change 1-------------------------------------------

### 6.1.7	Trust Enabler security functions

OneM2M Trust Enabling Architecture requires the presence of two security functionalities within the Infrastructure Domain: the M2M Authentication Function (MAF) and the M2M Enrolment Function (MEF). They can be either under M2M Service Provider control or delegated to a M2M Trust Enabler.

M2M Enrolment Function (MEF)

The MEF supports the security bootstrap procedure enabling the provisioning of the Master Credentials to be used to mutually authenticate entities accessing the infrastructure of an M2M Service Provider. The MEF relies on an initial credential pre-provisioned in the M2M node (e.g. during manufacturing). In case of MAF-based M2M Remote Security Provisioning procedure, the MEF provides the M2M Master Credential both to the MAF and the ASN/MN-CSE.

M2M Authentication Function (MAF)

M2M Master Credentials, used to mutually authenticate CSEs/AEs before granting them access to M2M services, shall be securely stored in a specific infrastructure functionality named M2M Authentication Function (MAF).

The MAF securely contains the set of M2M Master Credentials that are used for authenticating CSEs/AEs that have been enrolled for M2M services. The MAF stores the M2M Master Credentials and possibly the identifiers of the associated CSE/AE. The MAF is identified by  its MAF-ID.

When M2M Remote Security Provisioning procedure takes place to share a M2M Master Credential between an ASN/MN CSE and the M2M Authentication Function, the M2M Enrolment Function (MEF) communicates with the MAF through an appropriate secure interface, if not co-located.

The MAF is also in charge of all security operations involving the usage of the M2M Master Credentials.

### -----------------------End of change 1---------------------------------------------