| CHANGE REQUEST |
| --- |
| Group Name:* | SEC 12 |
| Source:* | Francois Ennesser, Gemalto (ETSI) |
| Format:* | Face-to-Face |
| Date:* | 2014-07-20 |
| Contact:* | francois.ennesser@gemalto.com |
| Reason for Change/s:* | Though a clause explaining the positioning of security procedures in the M2M sequence of events was contributed to TS_0001 (WG2), TS-0003 still lacks information on the topic. It is confusing for readers if the Security TS lacks information on how security procedures integrate with what is specified in other oneM2M TSs. |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0003 v0.6.0 |
| Clauses/Sub Clauses* | 6 and sub-clauses |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR provides information on the positioning of security procedures in the oneM2M sequence of events and other useful information to understand the security frameworks, as a new section 6.2.

### -----------------------Start of change 1-------------------------------------------

# 6	Security Services and Interactions

# 6.1 	Security Integration in oneM2M flow of events

This clause specifies the integration of security process and procedures during deplotyment and operation of a oneM2M solution.

### 6.1.1 	Interactions between layers

Before any M2M Common Services layer procedure can take place, connectivity has to be established in the underlying Network Services Layer, which may involve independent provisioning and service registration procedures specified by the underlying network.

The Service Layer Security provisioning (security pre-provisioning or security bootstrapping) and Security Association Establishment procedures specified in the present document can take place independently (and generally consecutively) from any required Network Service Layer connectivity establishment procedures.

Finally, the security provisioning and security association establishment requirements imposed by M2M Application Service Providers have to be accounted for.

### 6.1.2 	High level sequence of events

### 6.1.2.1 	Enrolment phase

### M2M equipments typically require provisioning and configuration phases before being put in actual operation. This may be performed by a pre-provisioning that can be integrated in the manufacturing or product deployment phase, or by means of a security bootstrapping procedure (i.e. remote security provisioning) that takes place before the equipment starts actual operation.

At the service layer level, such provisioning and configuration requires  selection of the stakeholder that will provide services through the equipment, especially the M2M Service Provider. This Enrolment phase requires contractual agreements between the stakeholders.

### Enrolment phase may occur several times during the lifecycle of an M2M equipment, but is only repeated when a change in the Service Provider affects the provisioning or configuration of the equipment.

The security provisioning phase for the different layers can be combined using a common method of  security pre-provisioning.

Remote Security Provisioning frameworks provide post-provisioning of the essential information to establish a security association between a Field Domain entity and the M2M Authentication Function of a chosen M2M Service Provider. The essential security information includes the security credentials and identifiers. Remote Security Provisioning procedures rely on an M2M Enrolment Function which can be external to the M2M Service Provider to establish appropriate credentials.

- Provisioned Symmetric Enrolee Key Security Bootstrap Framework: A symmetric key is pre-provisioned to the Enrolee and M2M Enrolment Function for the mutual authentication of those entities. For more details, see clause 8.3.2.1.

- Certificate-Based Security Bootstrap Framework: The Enrolee and M2M Enrolment Function are each issued and authenticate themselves with private signing keys and Certificates containing the corresponding Public Verification Key. For more details see clause 8.3.2.2.

- GBA-based Security Bootstrap Framework. In this case, the M2M Enrolment Function includes the functionality of a GBA Bootstrap Server Function. This framework uses 3GPP or 3GPP2 symmetric keys to authenticate the Enrolee and the M2M Enrolment Function (which is also a GBA BSF). The details are specified by 3GPP TS 33.220 [13] and 3GPP2 S.S0109-A [14]. For more details see clause 8.3.3.1.

Figure X.2.3-1 illustrates the different Security Bootstrap Frameworks. Note there is no communication between M2M Entities A and B in the bootstrap procedure. After successful completion of the bootstrap procedure, the MAF-Based Security Association Establishment procedure is applied.

Figure X.2.3-1:  Entities involved in Security Bootstrap

### 6.1.2.2 	Operational phase

#### 6.1.2.2.1	M2M Service Access

AEs and CSEs seeking access to M2M services need to be mutually identified and authenticated with the M2M Service Infrastructure, in order to provide protection from unauthorized access and Denial of Service attacks. This mutual authentication enables to additionally provide encryption and integrity protection for the exchange of messages across a single Mca, Mcc or Mcc’ reference point.

This is the purpose of the Security Association Establishment procedure, which shall take place before execution of the service related procedures specified in TS-0001 [1] for the corresponding reference point.

On the Mca and Mcc reference points, security association establishment between a field domain AE or CSE, respectively,  and an IN-CSE is mandatory.

On the Mcc’ reference point, security association establishment between IN-CSE and IN-CSE is mandatory.

On the Mca reference point, security association establishment between AE and the CSE in the field domain is strongly recommended.

The security association establishment phase of the M2M Service Layer and M2M Application Layer are generally independent from similar procedures that may be required by the Network Layer, though they may rely on the security services provided by the Network Layer.

The oneM2M system supports the following authentication mechanisms for Security Association Establishment, described in more detail in clause 8.2.1 “Overview on Security Association Establishment Frameworks”:

Provisioned M2M Secure Connection Key Security Association Establishment Framework: A symmetric key is pre-provisioned to the Security Association end-points. For more details see clause 8.2.2.1.

Certificate-Based Security Association Establishment Framework: Security Association end-points authenticate themselves using private signing keys and Certificates containing the corresponding Public Verification Key. For more details see clause 8.2.2.2.

M2M Authentication Function (MAF) Security Association Establishment Framework. For MAF-based SAEF, the centralized key distribution server is a MAF hosted either by a 3rd party service provider which has a service relationship with the M2M Service Provider (M2M-SP), or hosted by the M2M-SP itself. The MAF authenticates a Field Domain entitiy on behalf of an IN-CSE using a symmetric key. For more details see clause 8.2.3.1.

GBA-Based Security Association Establishment Framework, where the centralized key distribution server is a Bootstrap Server Function (BSF) of the 3GPP Generic Bootstrap Architecture (GBA) hosted by the Underlying Network Service Provider. 3GPP or 3GPP2 symmetric keys are used to authenticate Field Domain entities. The 3GPP-defined communication protocols as specified in 3GPP TS 33.222 [28], 3GPP TS 24.109 [29] and 3GPP TS 29.109 [30] are employed. The details are specified by 3GPP TS 33.220 [13] and 3GPP2 S.S0109-A [14], see clause 8.2.3.2.

Figure X.2.2-1 illustrates the different use cases and entities involved in the various Security Association Establishment Frameworks (SAEF) considered in this specification.

Figure X.2.2-1:  Entities involved in Security Association Establishment

#### 6.1.2.2.2	Authorization to access M2M resources

### Once an AE or CSE has been granted access to M2M services, the Access Control procedure specified in Clause 7 of the present document shall be executed before accessing an M2M resource, as specified in oneM2M TS-0001 [1].

## 6.2	Security Service Layer

### […]-----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

# 3	Definitions and abbreviations

## 3.1	Definitions

[…]

enrolment phase: The step in the lifecycle of an M2M equipment where it becomes provisioned for operation with a specific M2M Service Provider.

operational phase: The period in the lifecycle of an M2M equipment where it is actually used for providing M2M services.

[…]

## 3.3	Abbreviations

SAEF			Security Association Establishment Framework

SBF			Security Bootstrap Framework

### -----------------------End of change2---------------------------------------------

# Text boxes

GBA and MAS based SAEF

MAF

Direct SAEF

MAF

MAF

GBA

BSF

M2M-SP Domain

3rd Party Domain

or M2M-SP Domain

Field Domain

UN-SP Domain

M2M

Entity

B

M2M

Entity

A

MEF

MAF

GBA

BSF

(=MEF)

M2M-SP Domain

3rd Party Domain

or M2M-SP Domain

Field Domain

UN-SP Domain

M2M

Entity

B

M2M

Entity

A