| CHANGE REQUEST |
| --- |
| Group Name:* | SEC#12 |
| Source:* | Qualcomm Inc. (TIA) |
| Format:* | Plenary |
| Date:* | 2014-07-31 |
| Contact:* | Philip Hawkes, Qualcomm, phawkes@qti.qualcomm.com, Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | Updates clause 9.1 |
| CR against: | TS-0003 and 0.6.0 |
| Clauses/Sub Clauses Affected* | 9.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include the proposed changes in TS-0003 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Do not conflict with the content of an already approved text, by modification, deletion or the addition of an editor’s note.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Note that the following indicates a row/columns of tables that should be deleted by making the row/column background red, and striking through the text in the row/column, as shown below.

This cell should be deleted

### -----------------------Start of change 1-------------------------------------------

# 9 	Security Framework Procedures and Parameters

This clause specifies procedures and parameters of the phases of Security Association Establishment Frameworks (clause 8.2) and Remote Security Provisioning Frameworks (clause 8.3).

## 9.1 	Security Association Establishment Framework Procedures and Parameters

### 9.1.1 	Credential Configuration Parameters

The following Credential Configuration procedures are described in the present clause:

- Credential Configuration of Entity A and Entity B, see Clause 9.1.1.1,

- Credential Configuration of M2M Authentication Functions, see Clause 9.1.1.2,

The following Credential Configuration procedures are specified by other organizations:

- Credential Configuration of Underlying Network Service Provider authentication server (e.g. HLR, HSS or AAA) for the GBA-Based Security Association Establishment Framework. These details are specified by 3GPP, 3GPP2 and ETSI specifications.

- Credential Configuration of Entity A in the Field-Domain for the GBA-Based Security Association Establishment Framework. These details are specified by 3GPP, 3GPP2 and ETSI specifications.

#### 9.1.1.1	 Credential Configuration of Entity A and Entity B

Table 9.1.1.1-1 lists the parameters configured to a Field-Domain Security Association End-Points in the Credential Configuration phase.

Table 9.1.1.1-1	 Parameters configured to a Field Domain Security Association end-point during the Credential Configuration phase.

| Security Association Establishment Framework | Parameter | Mandatory /Optional for this Security Association Establishment Framework |
| --- | --- | --- |
| Pre-Provisioned M2M Secure Connection Key | Kpsa | Mandatory |
|  | KpsaId | Mandatory |
| Certificate Based | thisEntityPrivateKey | Mandatory |
|  | thisEntityCertificate | Mandatory |
|  | thisEntityCertificateChain | Optional |
| Certificate Based | Entity authenticates itself using a Raw Public Key Certificate | Entity’s Private Key | Mandatory |
|  |  | Entity’s Raw Public Key Certificate | Mandatory |
|  | Entity authenticates itself using a Device Certificate | Entity’s Private Key | Mandatory |
|  |  | Entity’s Certificate and Chain | Mandatory |
|  | Entity authenticates itself using a CSE-ID Certificate | Entity’s CSE-ID | Mandatory |
|  |  | Entity’s Private Key | Mandatory |
|  |  | Entity’s Certificate and Chain | Mandatory |
|  | Entity authenticates itself using an AE-ID Certificate | Entity’s AE-ID | Mandatory |
|  |  | Entity’s Private Key | Mandatory |
|  |  | Entity’s Certificate and Chain | Mandatory |
| MAF-Based | Entity A | MAF Identifier (MAF-ID) | Mandatory |
|  |  | thisEntityIdentifier | Mandatory |
|  |  | Master Credential (Km Id) | Mandatory |
|  |  | Master Credential Identifier (KmId) | Mandatory |
|  |  | masterCredentialExpiry | Optional |
|  | Entity B | Entity B and MAF shall be able to establish mutually-authenticated secure communication. The details are not specified in the present document | Mandatory |
| GBA-Based | Entity B plays role of NAF. Details specified in 3GPP 33.220 [13]. Where this description differs from [13], [13] takes precedence | NAF Private Key | See 3GPP 33.220 [13]. |
|  |  | NAF Certificate and Chain | See 3GPP 33.220 [13]. |
|  |  | CertificateChain | See 3GPP 33.220 [13]. |
|  |  | BSF trust anchor certificate | See 3GPP 33.220 [13]. |

The Credential Configuration of Entity A, Entity B and the MAF for the Pre-Provisioned M2M Secure Connection Key Security Association Establishment Framework, or the MAF-Based Security Association Establishment Framework is achieved through either:

- Pre-provisioning via out of band mechanisms which are not specified in the present document.

- Remote provisioning via one of the Remote Security Provisioning Frameworks in Clause 8.3.

The Credential Configuration of Entity A and Entity B for the Certificate Security Association Establishment Frameworks is performed by pre-provisioning via out of band mechanisms which are not specified in the present document .

#### 9.1.1.2	Credential Configuration of M2M Authentication Functions

Table 9.1.1.3-1 lists the parameters configured to M2M Authentication Functions in the Credential Configuration phase. The M2M Authentication Function’s identifier (MAF-ID) is presumed to have been configured prior to the Credential Configuration phase.

Table 9.1.1.3-1		 Parameters configured to a M2M Authentication Functions during the Credential Configuration phase.

| Security Association Establishment Framework | Parameter | Mandatory /Optional for this Security Association Establishment Framework |
| --- | --- | --- |
| MAF-Based | A-to-MAF Authentication | Entity A’s CSE-ID or AE-ID (IdA) | Mandatory |
|  |  | Master Credential (Km) | Mandatory |
|  |  | Master Credential Identifier (KmId) | Mandatory |
|  |  | masterCredentialExpiry | Optional |
|  | B-to-MAF Authentication | Entity B and MAF shall be able to establish mutually-authenticated secure communication. The details are not specified in the present document | Mandatory |

The Credential Configuration of M2M Authentication Framework shall be achieved through either:

- Business logic of the Stakeholder operating the M2M Authentication Function, and the details are not described in this specification.

- Remote provisioning via one of the Remote Security Provisioning Frameworks in Clause 8.3.

### 9.1.2 	Association Configuration Procedures and Parameters

The following Association Configuration procedures are described in this clause:

- Association Configuration of Entity A and Entity B, see Clause 9.1.2.1,

- Association Configuration of M2M Authentication Functions, see Clause 9.1.2.2,and

- Association Configuration of Underlying Network Service Provider authentication servers (e.g. HLR, HSS or AAA), see Clause 9.1.2.3.

#### 9.1.2.1 	Association Configuration of Entity A and Entity B

Table 9.1.2.1-1 lists the parameters configured to Entity A and Entity B in the Credential Configuration phase.

Table 9.1.2.1-1	Parameters configured to Entity A and Entity B during the Credential Configuration phase.

| Security Association Establishment Framework | Parameters specific to the Security Association Establishment Frameworks | Mandatory /Optional for this Security Association Establishment Framework |
| --- | --- | --- |
| Pre-Provisioned M2M Secure Connection Key | None |  |
| Certificate Based | thisEntityIdentifier | Mandatory |
|  | otherEntityCertificateName | Mandatory |
|  | otherEntityRootOfTrust | Mandatory |
| Certificate Based | Other entity is authenticated using Raw Public Key Certificate | Other entity’s identity (IdA or IdB) | Mandatory |
|  |  | Other entity’s Public key identifier | Mandatory |
|  | Other entity is authenticated using Device Certificate | Other entity’s identity (IdA or IdB) | Mandatory |
|  |  | Other entity’s M2M Device ID OID | Mandatory |
|  |  | Other entity’s trust anchor certificates | Mandatory |
|  | Other entity is authenticated using CSE-ID Certificate | Other entity’s CSE-ID (IdA or IdB) | Mandatory |
|  |  | Other entity’s trust anchor certificates | Mandatory |
|  | Other entity is authenticated using AE-ID Certificate | Other entity’s AE-ID (IdA or IdB) | Mandatory |
|  |  | Other entity’s trust anchor certificates | Mandatory |
| MAF-Based | Configured to Entity A | Entity B’s CSE-ID or AE-ID (IdB) | Mandatory |
| GBA-Based | Configured to Entity A | Entity B’s CSE-ID or AE-ID (IdB) | Mandatory |

Mechanisms for Association Configuration of an entity shall authenticate the configuration source and provide integrity protection for the configured information communicated from the configuration source to the entity.

#### 9.1.2.2 	Association Configuration of M2M Authentication Functions

Table 9.1.2.2-1 lists the parameters configured to M2M Authentication Functions in the Association Configuration phase.

Table 9.1.2.2-1		 Parameters configured to a M2M Authentication Functions during the Association Configuration phase.

| Security Association Establishment Framework | Parameter | Mandatory /Optional for this Security Association Establishment Framework |
| --- | --- | --- |
| MAF-Based | A-to-MAF Authentication | Entity B’s CSE-ID or AE-ID (IdB) | Mandatory |
|  |  | associationConfigurationExpiry | Optional |
|  |  | securityAssociationLifespan | Optional |
|  | B-to-MAF Authentication | Editor’s note: FFS. |  |

This specification assumes that Association Configuration of the M2M Authentication Functions will utilize business logic of the Stakeholder that operates the M2M Authentication Function, and the details are not described in this specification.

#### 9.1.2.3 	Association Configuration of UNSP Authentication Servers

Table 9.1.2.3-1 lists the parameters configured to an Underlying Network Service Provider authentication server (e.g. HLR, HSS or AAA) in the Association Configuration phase.

Table 9.1.2.3-1		 Parameters configured to an Underlying Network Service Provider authentication server (e.g. HLR, HSS or AAA) during the Association Configuration phase.

| Security Association Establishment Framework | Parameter | Mandatory /Optional for this Security Association Establishment Framework |
| --- | --- | --- |
| GBA-Based. Parameters are configured to UE’s GBA User Security Settings (GUSS). GUSS details are specified in 3GPP 33.220 [13]. Where this description differs from [13], [13] takes precedence | Entity A’s CSE-ID or AE-ID (IdA) | Mandatory |
|  | Entity B’s CSE-ID or AE-ID (IdB) | Mandatory |
|  | associationConfigurationExpiry | Optional |
|  | securityAssociationLifespan | Optional |

The Association Configuration of the Underlying Network Service Provider authentication server is achieved by updating the GBA User Security Settings (GUSS) (3GPP 33.220 [13]) of the User Equipment (UE) upon which the Enrolee is executed. This specification assumes that this Association Configuration will utilize business logic of the Underlying Network Service Provider, and the details are not described in this specification.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Does this change request avoid conflict with the content of an already approved text, by modification, deletion or the addition of an editor’s note?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change  include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?