| CHANGE REQUEST |
| --- |
| Group Name:* | SEC#12 |
| Source:* | Qualcomm Inc. (TIA) |
| Format:* | Plenary |
| Date:* | 2014-07-31 |
| Contact:* | Philip Hawkes, Qualcomm, phawkes@qti.qualcomm.com, Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | Update clause 9.2 |
| CR against: | TS-0003 and 0.6.0 |
| Clauses/Sub Clauses Affected* | 9.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include the proposed changes in TS-0003 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Do not conflict with the content of an already approved text, by modification, deletion or the addition of an editor’s note.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Note that the following indicates a row/columns of tables that should be deleted by making the row/column background red, and striking through the text in the row/column, as shown below.

This cell should be deleted

### -----------------------Start of change 1-------------------------------------------

## 9. 2 	Remote Security Provisioning Framework Procedures and Parameters

### 9.2.1 	Bootstrap Credential Configuration Procedures and Parameters

The following Bootstrap Credential Configuration procedures are described in this clause:

- Bootstrap Credential Configuration of Enrolees and Enrolment Targets (except for the GBA-Based case as discussed below), see Clause 9.2.1.1,

- Bootstrap Credential Configuration of M2M Enrolment Functions (except for the GBA-Based case as discussed above), see Clause 9.2.1.2.

The following Bootstrap Credential Configuration procedures are specified by other organizations:

- Bootstrap Credential Configuration of Underlying Network Service Provider authentication servers (e.g. HLR, HSS or AAA) for the GBA-Based Security Association Establishment Framework. These details are specified by 3GPP, 3GPP2 and ETSI specifications.

- Bootstrap Credential Configuration of Enrolees for the GBA-Based Security Association Establishment Framework. These details are specified by 3GPP, 3GPP2 and ETSI specifications.

Editor’s Note: List any relevant 3GPP, 3GPP2 or IETF specifications.

#### 9.2.1.1 	Bootstrap Credential Configuration of Enrolee and Enrolment Targets

Table 9.2.1.1-1 lists the parameters configured to Enrolees and Enrolment Targets in the Bootstrap Credential Configuration phase for authentication with the M2M Enrolment Function in the Pre-Provisioned Symmetric Enrolee Key Remote Security Provisioning Framework and Certificate-Based Remote Security Provisioning Framework .

Table 9.2.1.1-1	 Parameters configured to Enrolees and Enrolment Targets during the Bootstrap Credential Configuration phase.

| Remote Security Provisioning Framework | Parameter | Mandatory /Optional for this Security Framework |
| --- | --- | --- |
| Pre-Provisioned M2M Secure Connection Key authentication. Not applicable to MAF. | Kpm | Mandatory |
|  | KpmId | Mandatory |
|  | MEF URI | Mandatory |
| Certificate Based | thisEntityPrivateKey | Mandatory |
|  | thisEntityCertificate | Mandatory |
|  | thisEntityCertificateChain | Optional |
| Certificate-Based authentication | Entity authenticates itself using a raw public key | Entity’s Private Key | Mandatory |
|  |  | Entity’s Raw Public Key Certificate | Mandatory |
|  | Entity authenticates itself using a device certificate | Entity’s Private Key | Mandatory |
|  |  | Entity’s Certificate and Chain | Mandatory |
|  | Entity authenticates itself using a CSE-ID or AE-ID certificate | Entity’s Private Key | Mandatory |
|  |  | Entity’s Certificate and Chain | Mandatory |

The Bootstrap Credential Configuration of an Enrolees or Field Domain Enrolment Target for the Pre-Provisioned Symmetric Enrolee Key Remote Security Provisioning Framework and Certificate-Based Remote Security Provisioning Framework shall authenticate the configuration source and shall provide confidentiality and integrity protection of the configured information communicated from the configuration source to the secured environment of the Enrolee or Field Domain Enrolment Target. The present document does not specify any such mechanisms.

The Bootstrap Credential Configuration of an Infrastructure Domain Enrolment Target (including an M2M Authentication Functions) expected to use business logic of the Stakeholder operating the Infrastructure Domain Enrolment, and the details are not described in this specification.

#### 9.2.1.2 	Bootstrap Credential Configuration of M2M Enrolment Functions

It is assumed that an M2M Enrolment Function already knows its FQDN.

Table 9.2.1.2-1 lists the parameters configured to M2M Enrolment Functions in the Bootstrap Credential Configuration phase for mutual authentication with Enrolees and Enrolment Targets using the Pre-Provisioned Symmetric Enrolee Key Remote Security Provisioning Framework and Certificate-Based Remote Security Provisioning Framework.

Table 9.2.1.2-1 Parameters configured to the M2M Enrolment Function during the Bootstrap Credential Configuration phase for mutual authentication with Enrolees and Enrolment Targets using the Pre-Provisioned Symmetric Enrolee Key Remote Security Provisioning Framework and Certificate-Based Remote Security Provisioning Framework.

| Remote Security Provisioning Framework | Parameters specific to the Remote Security Provisioning Frameworks | Mandatory /Optional for this Security Framework |
| --- | --- | --- |
| Pre-Provisioned Symmetric Enrolment Key authentication of Enrolee or Enrolment Target | Kpm | Mandatory |
|  | KpmId | Mandatory |
| Certificate Based authentication of Enrolee or Enrolment Target | MEF Private Key | Mandatory |
|  | MEF Certificate and Chain | Mandatory |
|  | mefCertificateChain | Mandatory |

The Bootstrap Credential Configuration of M2M Enrolment Functions is expected to use business logic of the stakeholder operating the M2M Enrolment Function, and the details are not described in this specification.

### 9.2.2 	Bootstrap Instruction Configuration Procedures and Parameters

The following Bootstrap Instruction Configuration procedures are described in this clause:

- Bootstrap Instruction Configuration of Enrolees, see Clause 9.2.2.1,

- Bootstrap Instruction Configuration of Enrolment Targets, see Clause 9.2.2.2,

- Bootstrap Instruction Configuration of M2M Enrolment Functions, see Clause 9.2.2.3

- Bootstrap Instruction Configuration of Underlying Network Service Provider authentication servers (e.g. HLR, HSS or AAA), see Clause 9.2.2.4.

#### 9.2.2.1 	Bootstrap Instruction Configuration of Enrolees

Table 9.2.2.1-1 lists the parameters configured to an Enrolee during the Bootstrap Instruction Configuration phase which are common to all Remote Security Provisioning Frameworks.

Table 9.2.2.1-1 Parameters configured to an Enrolee during the Bootstrap Instruction Configuration phase of which are common to all Remote Security Provisioning Frameworks.

| Parameter common to all Remote Security Provisioning Frameworks | Mandatory /Optional for this Remote Security Provisioning Framework |
| --- | --- |
| thisEntityIdentifier | Mandatory |
| Enrolment Target Identifier (Enrolee B’s AE-ID or CSE-ID, or MAF-ID) | Mandatory |

Table 9.2.2.1-2 lists the Remote Security Provisioning Framework–specific parameters configured an Enrolee in the Bootstrap Instruction Configuration phase of the Remote Security Provisioning Frameworks.

Table 9.2.2.1-2 Remote Security Provisioning Framework –specific parameters configured to an Enrolee during the Instruction Configuration phase of the Remote Security Provisioning Framework.

| Remote Security Provisioning Framework | Remote Security Provisioning Framework-specific Parameters | Mandatory /Optional for this Remote Security Provisioning Framework |
| --- | --- | --- |
| Pre-Provisioned Symmetric Enrolment Key | None |  |
| Certificate Based | MEFURI | Mandatory |
|  | Mef CertificateName | Mandatory |
|  | MEF TrustAnchor Certificates | Mandatory |
| GBA-Based | None |

Mechanisms for Bootstrap Instruction Configuration of Enrolees shall authenticate the configuration source and shall provide at least integrity protection of the configured information communicated from the configuration source to the Enrolee.

#### 9.2.2.2 	Bootstrap Instruction Configuration of Enrolment Targets

Table 9.2.2.2-1 lists the parameters configured to Enrolment Targets during the Bootstrap Instruction Configuration phase.

Table 9.2.2.2-1 Parameters configured to Enrolment Targets during the Bootstrap Instruction Configuration phase.

| Mechanism for authenticating the Enrolment Target | Remote Security Provisioning Framework-specific Parameters |
| --- | --- |
| Pre-Provisioned Symmetric Enrolment Key. Not applicable to MAF. | None |
| Certificate Based | MEF/BSF Trust Anchor Certificates |

Mechanisms for Bootstrap Instruction Configuration of Enrolment Targets shall authenticate the configuration source and shall provide at least integrity protection of the configured information communicated from the configuration source to the Enrolment Targets.

This specification assumes that Bootstrap Instruction Configuration of Infrastructure Domain Enrolment Targets (including M2M Authentication Functions) utilizes business logic of the Stakeholder that operates the M2M Authentication Function, and the details are not described in this specification.

#### 9.2.2.3 	Bootstrap Instruction Configuration of M2M Enrolment Functions

Editor’s Note: TO DO - list parameters that may be configured to this entity in this phase.

Table 9.2.2.3-1 lists the parameters configured to an M2M Enrolment Function during the Bootstrap Instruction Configuration phase which are common to the Pre-Provisioned Symmetric Enrolee Key Remote Security Provisioning Framework and Certificate-Based all Remote Security Provisioning Frameworks.

Table 9.2.2.3-1 Parameters configured to M2M Enrolment Functions during the Bootstrap Instruction Configuration phase of which are common to the Pre-Provisioned Symmetric Enrolee Key Remote Security Provisioning Framework and Certificate-Based Security BootstrapRemote Security Provisioning Frameworks.

| Parameter common to all Remote Security Provisioning Frameworks | Mandatory /Optional for all Remote Security Provisioning Frameworks |
| --- | --- |
| Enrolee’s assigned CSE-ID or AE -ID | Mandatory |
| Enrolment Target Identity (Enrolee B’s CSE-ID or AE-ID, or MAF-ID) | Mandatory |

Table 9.2.2.3-2 lists the Remote Security Provisioning Framework–specific parameters configured to an M2M Enrolment Functions in the Bootstrap Instruction Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Remote Security Provisioning Framework and Certificate-Based Remote Security Provisioning Framework.

Table 9.2.2.3-2 Remote Security Provisioning Framework–specific parameters configured to an M2M Enrolment Function during the Bootstrap Instruction Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Remote Security Provisioning Framework and Certificate-Based Remote Security Provisioning Framework.

| Remote Security Provisioning Framework | Remote Security Provisioning Framework-specific Parameters | Mandatory /Optional for this Remote Security Provisioning Framework |
| --- | --- | --- |
| Pre-Provisioned Symmetric Enrolment Key | None |  |
| Certificate Based | Enrolee is authenticated using a raw public key certificate | Enrolee’s Public key identifier | Mandatory |
|  | Enrolee is authenticated using a device certificate | Enrolee’s M2M Device ID | Mandatory |
|  |  | Enrolee’s Trust Anchor Certificates | Mandatory |
|  | Enrolee is authenticated using a CSE-ID or AE-ID certificate | Enrolee’s Trust Anchor Certificates | Mandatory |

Table 9.2.2.3-3 lists the parameters configured to an M2M Enrolment Functions for authentication of the Enrolment Target when the Enrolment Target is Enrolee B (a CSE or AE).

Table 9.2.2.3-3 Remote Security Provisioning Framework–specific parameters configured to an M2M Enrolment Function during the Bootstrap Instruction Configuration phase for authentication of the Enrolment Target when the Enrolment Target is Enrolee B (a CSE or AE)..

| Mechanism for Authenticating Enrolee B | Parameters specific to the mechanism for authenticating Enrolee B |
| --- | --- |
| Pre-Provisioned Symmetric Enrolment Key | None |
| Certificate Based | Enrolee B is authenticated using a raw public key certificate | Enrolee B’s Public key identifier |
|  | Enrolee B is authenticated using a device certificate | Enrolee B’s M2M Device ID |
|  |  | Enrolee B’s Trust Anchor Certificates |
|  | Enrolee B is authenticated using a CSE-ID or AE-ID certificate | Enrolee B’s Trust Anchor Certificates |

Table 9.2.2.2-4 lists the parameters configured to an M2M Enrolment Function for authenticating the Enrolment Target when the Enrolment Target is an M2M Authentication Function.

Table 9.2.2.2-4The parameters configured to an M2M Enrolment Function for identifying and authenticating the Enrolment Target when the Enrolment Target is an M2M Authentication Function.

Parameter common to all Remote Provisioning Frameworks

MAF Trust Anchor Certificates

This specification assumes that Bootstrap Instruction Configuration of the M2M Enrolment Functions utilizes business logic of the Stakeholder that operates the M2M Enrolment Function, and the details are not described in this specification.

#### 9.2.2.4 	Bootstrap Instruction Configuration of UNSP Authentication Server

Table 9.2.2.4-1 lists the parameters configured to an Underlying Network Service Provider authentication server (e.g. HLR, HSS or AAA) during the Bootstrap Instruction Configuration phase of the GBA-Based Remote Security Provisioning Framework.

Table 9.2.2.4-1 Parameters configured to M2M Enrolment Functions during the Bootstrap Instruction Configuration phase of the GBA-Based Remote Security Provisioning Framework.

| Parameter | Mandatory /Optional for all Remote Security Provisioning Frameworks |
| --- | --- |
| Enrolee’s assigned CSE-ID or AE-ID | Mandatory |
| Enrolment Target Identifier (Enrolee B’s CSE-ID or AE-ID, or MAF-ID) | Mandatory |

The Bootstrap Instruction Configuration of the Underlying Network Service Provider authentication server is achieved by updating the GBA User Security Settings (GUSS) (3GPP 33.220 [13]) of the User Equipment (UE) upon which the Enrolee is executed. This specification assumes that this Bootstrap Instruction Configuration utilizes business logic of the Underlying Network Service Provider, and the details are not described in this specification.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Does this change request avoid conflict with the content of an already approved text, by modification, deletion or the addition of an editor’s note?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change  include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

For release 1, I prefer to just delete this text as it just provides some examples.