| CHANGE REQUEST |
| --- |
| Group Name:* | SEC#15 at TP#15 |
| Source:* | Philip Hawkes, Qualcomm, phawkes@qti.qualcomm.com, Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Format:* | Plenary |
| Date:* | 2015-01-12 |
| Contact:* | As above |
| Reason for Change/s:* | This CR provides generic changes (not related to a specific authentication mechanism) to align with changes to the AE Registration process has been updated in TS-0001 clause 10.1.1.2.2. |
| CR against: | TS-0003 v0.8.1 |
| Clauses/Sub Clauses Affected* | 6.1.1, 8.2.1, 8.3.1.2, 9, new 10.4 “Credential-ID Details” |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Apply changes to TS-0003 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

For each change in this CR, there is a comment identifying one or more of the following reasons for the change:

- ALIGNMENT WITH TS-0001. Changes to align the Security Association Establishment Framework and Remote Security Provisioning Frameworks with changes in TS-0001 Functional Architecture clause 10.1.1.2.2.

- BUG: changes to correct technical information

- EDITORIAL: changes to improve readability. No technical changes.

- TYPO: changes to correct typographic errors. No technical changes

- DEVICE CERT ( oCID CERT: at SEC#14.2, Qualcomm introduced the concept of the object-identifier based “oneM2M-Certificate-ID” (abbreviated here to “oCID”). . It was necessary to generalize the device certificates to the oCID certificates in order to support the scenarios described in TS-0001 clause 10.1.1.2.2. oCID certificates may be associated with any of: a single CSE; a single AE; multiple AE with same App-ID on same Node; or multiple AE with multiple App-ID on same Node. Other mechanisms (e.g. TS-0001 clause 10.1.1.2.2) are used to associate the oCID with the CSE-ID, AE-ID, or AE-ID(s) that are authenticated using that certificates. Therefore these changes are indirectly “ALIGNMENT WITH TS-0001”.  oCID certificates are described in a parallel CR.

W apologise that the changes are showing under multiple user names – we endeavour to fix this in future releases!

### -----------------------Start of change 1-------------------------------------------

## 6.1.1 	Interactions between layers

Before any M2M Common Services layer procedure can take place, connectivity has to be established in the underlying Network Services Layer, which may involve independent provisioning and service registration procedures specified by the underlying network.

The Service Layer Security provisioning (security pre-provisioning or security bootstrapping) and Security Association Establishment procedures specified in the present document can take place independently (and generally consecutively) from any required Network Service Layer connectivity establishment procedures.

Finally, the security provisioning and security association establishment requirements imposed by M2M Application Service Providers have to be accounted for. At the service layer level, the security association establishment results in a TLS or DTLS session which protects messages being exchanged between adjacent AE/CSE, i.e. hop-by-hop. AEs that need to preserve the privacy of their information exchange from untrusted intermediate nodes may be provisioned to support a direct security association between them. Such security associations enable to encrypt the content of resources exchanged between AEs through the service layer.

A credential used in a TLS/DTLS session is either associated with a single CSE/AE on a Node, or with multiple AEs on the same Node: for example, multiple AEs with the same App-ID on the same Node.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 8.2.1	Overview on Security Association Establishment Frameworks

In the present document, security associations are restricted to single hop on Mcc, Mcc’ or Mca reference point.

The oneM2M system supports the following Security Association Establishment Frameworks:

Security Association Establishment Frameworks:

Provisioned Symmetric Key Security Association Establishment. A symmetric key is provisioned to the entities: this is called the Provisioned M2M Symmetric Key, and denoted Kpsa. The entities authenticate each other by verifying Message Integrity Codes (MIC) in the Security Handshake which were generated using the symmetric key.  For more details see clause 8.2.2.1.

Certificate-Based Security Association Establishment: The entities are each issued with

a Private Signing Key that is known only to that entity,

a Certificate containing the corresponding Public Verification Key, and

(Optionally) a Certificate Chain from the entity's Certificate to a Root Certificate.

The entities must validate each other's Certificate before trusting the Public Verification Keys in the Certificate. Within the Security Handshake, entity A creates a digital signature of the session parameters using its private signing key and entity B verifies the digital signature using entity A's public verification key. Then the roles are reversed: entity B creates a digital signature and entity A verifies it. For more details see clause 8.2.2.2.

M2M Authentication Function (MAF)-based Security Association Establishment. This Security Association Establishment Framework uses symmetric keys to authenticate the entity A and the M2M Authentication Function (MAF) and derive a M2M Secure Connection key (Kc) that the MAF delivers to entity B. Then entities then authenticate each other using the M2M Secure Connection key (Kc). For more details see clause 8.2.3.1.

For a more detailed description of the above Security Association Establishment Frameworks, it is useful to compare the following aspects of the Security Association Establishment Frameworks:

Credential Configuration:

For MAF-based Security Association Establishment Frameworks:

Entity A is configured with (or otherwise establishes) the Master Credential (Km) that the entity A will use to authenticate the entity A to the MAF.

The MAF is configured with the Master Credential (Km) that will be used to authenticate the MAF to entity A.

The details for the GBA-Based Security Association Establishment Framework are out of scope.

For the Provisioned Symmetric Key Security Association Establishment Framework, each entity is provisioned with the Provisioned M2M Symmetric Key that entities will use to authenticate each other using pre-provisioning or remote provisioning.

For the Certificate-Based Security Association Establishment Frameworks, each entity is pre-provisioned with the Credential that the entity will use to authenticate itself to the other entity.

Association Configuration:

Entity A shall be configured with IdB, the entity identifier (that is, CSE-ID or AE-ID) for Entity B.

Additionally,

In the case of Certificate-Based Authentication Framework: each entity is configured with the certificate information that the entity will use to verify the other entity. The necessary certificate information is dependent on the flavour of the certificates, with details provided in clause 8.1.2.4 “Information Needed for Certificate Authentication of another Entity”.

In the case of MAF-Based Authentication Framework: The MAF is provided with the identity of Entity B for which the MAF is authorized to facilitate establishing a security association with Entity A.

Association Security Handshake: Identification, authentication and security context establishment between the entities.

  - MAF Handshake: When a MAF-based Security Association Establishment Framework is used, entity A and the MAF perform mutual authentication and generate a M2M Secure Connection Key (Kc) which is then used in the Security Handshake for mutual authentication between entity A and entity B. This is not applicable to Certificate-based or Provisioned Symmetric Key-based Security Association Establishment Frameworks.

  - Entity A associates the resulting security context with IdB: the CSE-ID or AE-ID-Stem value for Entity B configured during Association Configuration.

  - Entity B associates the security context with identifying information for Entity A’s:

  - If Entity A is a CSE, then the identifying information is a CSE-ID.

  - If Entity A is an AE, then the identifying information is the list of allowed combination of (allowed AE-ID-Stem value and allowed App-ID value) which may be used by AEs authenticated using the credential.

  - There are a variety of approaches for providing Entity B with the identifying information prior to registration.

  - CSE-ID (and AE-ID certificates respectively) contain the identifying information for a CSE (or AE respectively). If Entity A authenticated using a CSE-ID certificate or AE-ID certificate, then Entity B associates the security context with identifying information in the certificate, as described in the certificate profile in Clause 10.1.1 “Certificate Profiles”.

  - In all other cases, Entity B forms a globally unique Credential-ID from the information obtained in the security association establishment mechanism, and Entity B subsequently applies a mapping from the Credential-ID to Entity A’s identifying information – where the mapping is managed separately from the security association establishment mechanism. The Credential-ID identifies one of a Kpsa (in the case of a PSK SAEF), certificate (in the case of a Certificate-Based SAEF) or the Km (in the case of an MAF-Based SAEF).

  - If Entity A’s entity identifier was assigned by Entity B, then Entity B shall maintain its own mapping from the Credential-ID to the identifying information.

  - If Entity A’s entity identifier(s) was assigned by the M2M SP, then the mapping to the identifying information shall made available to Entity B via one of the following approaches..

  - If the Security Association Establishment procedure is facilitated by an M2M Authentication Function, then the M2M Authentication Function can be provided with the identifying information and the M2M Authentication Function can provide this to Entity B at the same time as Kc is provided to Entity B. The M2M Authentication Function could have been provided with the identifying information during provisioning, including the case where the M2M Authentication Function is provided with the identifying information during remote provisioning by an M2M Enrolment Function (which is similar to the case described in the following bullet).

  - If the Security Association Establishment procedure uses a Provisioned Symmetric Key which was remotely provisioned to Entity A and Entity B, then the M2M Enrolment Function can provide Entity B with identifying information during the Remote Security Provisioning procedure.

  - If the M2M Service Provider assigns Entity A’s entity identifier(s), then the information may be securely configured by the M2M Service Provider to Entity B prior to the Association Security Handshake. For example, this information may be configured as part of Credential Configuration or Association Configuration. This specification permits using other mechanisms, with the proviso that the mechanism provides authentication, integrity protection and optionally confidentiality.

    - Example 1. If the M2M Service Provider has the opportunity to configure Entity B prior to deployment, then the M2M Service Provider could configure the identifying information to Entity B at this time.

    - Example 2. A secure remote management protocol could be used to configure Entity B with the identifying information. However, this is not currently an interoperable feature as there is no standardized management object facilitating this management.

  - NOTE:	In the case that the Entity is an AE and Entity B is a CSE, the identifying information may be obtained by retrieving the applicable <serviceSubscribedAppRule> resources which are linked to by the ruleLinks attribute of the Entity B’s <serviceSubscribedNode>  on the IN-CSE as described in clause 10.1.1.2.2 “Application Entity Registration procedure” in TS-0001 [1].

Figure 8.2.1-1 provides a summary of the above defined three Security Association Establishment Frameworks.

Figure 8.2.1-1: Overview of the Security Association Establishment Frameworks
supported by oneM2M.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3 (in Clause 8.3.1.2) -----------------

Certificate-Based Remote Security Provisioning Framework: The Enrolee and M2M Enrolment Function are each issued with

a Private Signing Key that is known only to that entity,

a Certificate containing the corresponding Public Verification Key, and

(In the case of an oneM2M Certificate ID (oCID) certificate, CSE-ID certificate or AE-ID certificate) a Certificate Chain from the entity's Certificate to a Trust Anchor Certificate.

The Enrolee and M2M Enrolment Function shall validate each other's Certificate before trusting the Public Verification Keys in the Certificate. Within the Security Handshake, the M2M Enrolment Function creates a digital signature of the session parameters using its private signing key and the Enrolee verifies the digital signature using the M2M Enrolment Function's public verification key. Then the roles are reversed: the Enrolee creates a digital signature and the M2M Enrolment Function verifies it. For more details see clause 8.3.2.2.

GBA-based Remote Security Provisioning Framework. In this case, the role of the M2M Enrolment Function is performed by a GBA Bootstrap Server Function. This framework uses 3GPP or 3GPP2 symmetric keys to authenticate the Enrolee and the M2M Enrolment Function (which is also a GBA BSF). The details are specified by 3GPP [13] and 3GPP2 [14]. For more details see clause 8.3.2.3.

For a more detailed description of the above Remote Security Provisioning Frameworks, it is useful to compare the following aspects of the Remote Security Provisioning Frameworks.

Bootstrap Credential Configuration: The Enrolee and M2M Enrolment Function are pre-provisioned with the Bootstrap Credential that the entity will use to authenticate itself to the other entity. The mechanisms for this pre-provisioning are not described in this specification.

Bootstrap Instruction Configuration:

The Enrolee is provided with either

  - The M2M Authentication Function Identifier (MAF-ID) identifying the M2M Authentication Function for which the Enrolee is to be remotely provisioned when used in conjunction with a MAF-based security association establishment framework; or

  - The identifier of Enrolee B (Enrolee B-ID), when used in conjunction with a Provisioned Symmetric Key Security Association Establishment.

NOTE 1:	The identity of the M2M Authentication Function or the Enrolee B is assumed to have been configured prior to the Bootstrap Instruction Configuration phase.

Additionally, in the case of Certificate-Based Remote Security Provisioning Framework:

The Enrolee is configured with the M2M Enrolment Function URI (for the purpose of routing the (D)TLS messages to the M2M Enrolment Function), and M2M Enrolment Function Trust Anchor information that the Enrolee will use to verify the M2M Enrolment Function.

The M2M Enrolment Function is configured with Enrolee’s certificate information that the M2M Enrolment Function will use to verify the Enrolee. The necessary certificate information is dependent on the flavour of the Enrolee’s certificate, with details provided in clause 8.1.2.4 “Information Needed for Certificate Authentication of another Entity”.

Bootstrap Enrolment Handshake: Identification, authentication and security context establishment between the Enrolee and M2M Enrolment Function.

Enrolment Key Generation: generating a symmetric Enrolment Key, (Ke) and corresponding Enrolment Key Identifier (KeId) shared by the Enrolee and M2M Enrolment Function, which is used for subsequent generation of the Master Credential (Km) or Provisioned M2M Symmetric Key (Kpsa).

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4 (in Clause 8.3.1.2) -----------------

-	The M2M Enrolment Function derives the Km from the Ke and MAF-ID. Details of the derivation are provided in clause 10.3.2	“Derivation of Master Credential from Enrolment Key”.

-	The M2M Enrolment Function returns the Km to the M2M Authentication Function. If the identifying information of the Enrolee is configured to the M2M Enrolment Function also passes the identifying information of the Enrolee. More details regarding identifying information can be found in clause 8.2.1 “Overview of Security Association Establishment Frameworks”.

### -----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5 (in Clause 8.3.1.2) -----------------

Figure 8.3.1.2-1 provides a summary of the above defined Remote Security Provisioning Frameworks.

Figure 8.3.1.2-1: Overview of the Remote Security Provisioning Frameworks supported by oneM2M

### -----------------------End of change 5---------------------------------------------

### -----------------------Start of change 6-------------------------------------------

#### 9.1.1.1	 Credential Configuration of Entity A and Entity B

Table 9.1.1.1-1 lists the parameters configured to a Field-Domain Security Association End-Points in the Credential Configuration phase.

Table 9.1.1.1-1	 Parameters configured to a Field Domain Security Association end-point during the Credential Configuration phase.

| Security Association Establishment Framework | Parameter |
| --- | --- |
| Provisioned Symmetric Key | Kpsa |
|  | KpsaId |
| Certificate Based | Entity authenticates itself using a Raw Public Key Certificate | Entity’s Private Key |
|  |  | Entity’s Raw Public Key Certificate |
|  | Entity authenticates itself using a oCID Certificate | Entity’s Private Key |
|  |  | Entity’s oCID Certificate and Chain |
|  | Entity authenticates itself using a CSE-ID Certificate | Entity’s CSE-ID |
|  |  | Entity’s Private Key |
|  |  | Entity’s CSE-ID Certificate and Chain |
|  | Entity authenticates itself using an AE-ID Certificate | Entity’s AE-ID |
|  |  | Entity’s Private Key |
|  |  | Entity’s AE-ID Certificate and Chain |
| MAF-Based | Entity A | MAF Identifier (MAF-ID) |
|  |  | Master Credential (Km Id) |
|  |  | Master Credential Identifier (KmId) |
|  | Entity B | Entity B and MAF shall be able to establish mutually-authenticated secure communication. The details are not specified in the present document |

The Credential Configuration of Entity A, Entity B and the MAF for the Provisioned Symmetric Key Security Association Establishment Framework, or the MAF-Based Security Association Establishment Framework is achieved through either:

- Pre-provisioning via mechanisms which are not specified in the present document.

- Remote provisioning via one of the Remote Security Provisioning Frameworks in Clause 8.3.

The Credential Configuration of Entity A and Entity B for the Certificate Security Association Establishment Frameworks is performed by pre-provisioning via mechanisms which are not specified in the present document.

#### 9.1.1.2 	Credential Configuration of M2M Authentication Functions

Table 9.1.1.2-1 lists the parameters configured to M2M Authentication Functions in the Credential Configuration phase. The M2M Authentication Function’s identifier (MAF-ID) is presumed to have been configured prior to the Credential Configuration phase.

Table 9.1.1.2-1		 Parameters configured to a M2M Authentication Functions during the Credential Configuration phase.

| Security Association Establishment Framework | Parameter |
| --- | --- |
| MAF-Based | A-to-MAF Authentication | Entity A’s CSE-ID or AE-ID (IdA) |
|  |  | masterCredential (Km) |
|  |  | masterCredentialIdentifier (KmId) |
|  | B-to-MAF Authentication | Entity B and MAF shall be able to establish mutually-authenticated secure communication. The details are not specified in the present document |

The Credential Configuration of M2M Authentication Framework shall be achieved through either:

- Business logic of the Stakeholder operating the M2M Authentication Function, and the details are not described in this specification.

- Remote provisioning via one of the Remote Security Provisioning Frameworks in Clause 8.3.

### 9.1.2 	Association Configuration Procedures and Parameters

The following Association Configuration procedures are described in this clause:

- Association Configuration of Entity A, see Clause 9.1.2.1.1,

- Association Configuration of Entity B, see Clause 9.1.2.1.2, and

- Association Configuration of M2M Authentication Functions, see Clause 9.1.2.2.

#### 9.1.2.1 	Association Configuration of Entity A and Entity B

#### 9.1.2.1.1 	Association Configuration of Entity A

Table 9.1.2.1.1-1 lists the parameters configured to an Entity A during the Association Configuration phase which are common to all security association establishment frameworks.

Table 9.1.2.1.1-1 Parameters configured to an Enrolee during the Association Configuration phase of which are common to all security association establishment frameworks.

Parameter common to all security association establishment frameworks

Enrolee B’s Identity (IdB)

Table 9.1.2.1.1-2 lists the parameters configured to Entity A in the Association Configuration phase which are specific to the security association establishment framework.

Table 9.1.2.1.1-2		 Parameters configured to Entity A during the Association Configuration phase which are specific to the security association establishment framework.

| Security Association Establishment Framework | Parameters specific to the Security Association Establishment Frameworks |
| --- | --- |
| Provisioned Symmetric Key | None |
| Certificate Based | Entity B is authenticated using Raw Public Key Certificate | Other entity’s identity (IdA or IdB) |
|  |  | Entity B’s Public key identifier |
|  | Entity B is authenticated using oCID Certificate | Other entity’s identity (IdA or IdB) |
|  |  | Entity B’s certificate’s oCID |
|  |  | Entity B’s trust anchor information |
|  | Entity B is authenticated using CSE-ID Certificate | Other entity’s identity (IdA or IdB) |
|  |  | Entity B’s trust anchor information |
|  | Entity B is authenticated using AE-ID Certificate | Other entity’s identity (IdA or IdB) |
|  |  | Entity B’s trust anchor information |
| MAF-Based |  | None |

Mechanisms for Association Configuration of Entity A shall authenticate the configuration source and provide integrity protection for the configured information communicated from the configuration source to the entity.

##### 9.1.2.1.2 	Association Configuration of Entity B

Table 9.1.2.1.2-1 lists the parameters configured to Registrar (Entity B) in the Association Configuration phase.

Table 9.1.2.1.2-1		 Parameters configured to Registrar (Entity B) during the Association Configuration phase.

| Security Association Establishment Framework | Parameters specific to the Security Association Establishment Frameworks |
| --- | --- |
| Provisioned Symmetric Key | None |
| Certificate Based | Entity A is authenticated using Raw Public Key Certificate | None |
|  | Entity A is authenticated using oneM2M-oCID certificate, CSE-ID certificate or AE-ID certificate | Entity A’s trust anchor information |
| MAF-Based | None |

Mechanisms for Association Configuration of Entity B shall authenticate the configuration source and provide integrity protection for the configured information communicated from the configuration source to the entity.

### -----------------------End of change 6---------------------------------------------

### -----------------------Start of change 7-------------------------------------------

### 9.2.1 	Bootstrap Credential Configuration Procedures and Parameters

The following Bootstrap Credential Configuration procedures are described in this clause:

- Bootstrap Credential Configuration of Enrolees and Enrolment Targets (except for the GBA-Based case as discussed below), see Clause 9.2.1.1,

- Bootstrap Credential Configuration of M2M Enrolment Functions (except for the GBA-Based case as discussed above), see Clause 9.2.1.2.

The following Bootstrap Credential Configuration procedures are specified by other organizations:

- Bootstrap Credential Configuration of Underlying Network Service Provider authentication servers (e.g. HLR, HSS or AAA) for the GBA-Based Security Association Establishment Framework. These details are specified by 3GPP TS 33.220 [13], 3GPP2 S.S0109-A [14].

- Bootstrap Credential Configuration of Enrolees for the GBA-Based Security Association Establishment Framework. These details are specified by 3GPP TS 33.220 [13], 3GPP2 S.S0109-A [14].

#### 9.2.1.1 	Bootstrap Credential Configuration of Enrolee

Table 9.2.1.1-1 lists the parameters configured to Enrolees in the Bootstrap Credential Configuration phase for authentication with the M2M Enrolment Function in the Pre-Provisioned Symmetric Enrolee Key Remote Security Provisioning Framework and Certificate-Based Remote Security Provisioning Framework.

Table 9.2.1.1-1	 Parameters configured to Enrolees during the Bootstrap Credential Configuration phase.

| Remote Security Provisioning Framework | Parameter |
| --- | --- |
| Pre-Provisioned Symmetric Enrolment Key authentication | Kpm |
|  | KpmId |
|  | MEF URI |
| Certificate-Based authentication | Enrolee authenticates itself using a raw public key | Enrolee’s Private Key |
|  |  | Enrolee’s Raw Public Key Certificate |
|  | Enrolee authenticates itself using a oCID certificate | Enrolee’s Private Key |
|  |  | Enrolee’s Certificate and Chain |
|  | Enrolee authenticates itself using a CSE-ID or AE-ID certificate | Enrolee’s Private Key |
|  |  | Enrolee’s Certificate and Chain |

The Bootstrap Credential Configuration of an Enrolee for the Pre-Provisioned Symmetric Enrolee Key Remote Security Provisioning Framework and Certificate-Based Remote Security Provisioning Framework shall authenticate the configuration source and shall provide confidentiality and integrity protection of the configured information communicated from the configuration source to the secured environment of the Enrolee. The present document does not specify any such mechanisms.

### -----------------------End of change 7---------------------------------------------

### -----------------------Start of change 8-------------------------------------------

### 9.2.2 	Bootstrap Instruction Configuration Procedures and Parameters

The following Bootstrap Instruction Configuration procedures are described in this clause:

- Bootstrap Instruction Configuration of Enrolees, see Clause 9.2.2.1,

- Bootstrap Instruction Configuration of M2M Enrolment Functions, see Clause 9.2.2.3

- Bootstrap Instruction Configuration of Underlying Network Service Provider authentication servers (e.g. HLR, HSS or AAA), see Clause 9.2.2.4.

#### 9.2.2.1 	Bootstrap Instruction Configuration of Enrolees

Table 9.2.2.1-1 lists the parameters configured to an Enrolee during the Bootstrap Instruction Configuration phase which are common to all Remote Security Provisioning Frameworks.

Table 9.2.2.1-1 Parameters configured to an Enrolee during the Bootstrap Instruction Configuration phase of which are common to all Remote Security Provisioning Frameworks.

Parameter common to all Remote Security Provisioning Frameworks

Enrolment Target Identifier (Enrolee B’s AE-ID or CSE-ID, or MAF-ID)

Table 9.2.2.1-2 lists the Remote Security Provisioning Framework–specific parameters configured an Enrolee in the Bootstrap Instruction Configuration phase of the Remote Security Provisioning Framework.

Table 9.2.2.1-2 Remote Security Provisioning Framework –specific parameters configured to an Enrolee during the Instruction Configuration phase of the Remote Security Provisioning Framework.

| Remote Security Provisioning Framework | Remote Security Provisioning Framework-specific Parameters |
| --- | --- |
| Pre-Provisioned Symmetric Enrolment Key | None |
| Certificate Based | MEF URI |
|  | MEF Trust Anchor information |
| GBA-Based | None |

Mechanisms for Bootstrap Instruction Configuration of Enrolees shall authenticate the configuration source and shall provide at least integrity protection of the configured information communicated from the configuration source to the Enrolee.

#### 9.2.2.2 	Void

#### 9.2.2.3 	Bootstrap Instruction Configuration of M2M Enrolment Functions

Table 9.2.2.3-1 lists the parameters configured to an M2M Enrolment Function during the Bootstrap Instruction Configuration phase which are common to the Pre-Provisioned Symmetric Enrolee Key Remote Security Provisioning Framework and Certificate-Based Remote Security Provisioning Framework.

Table 9.2.2.3-1 Parameters configured to M2M Enrolment Functions during the Bootstrap Instruction Configuration phase of which are common to the Pre-Provisioned Symmetric Enrolee Key Remote Security Provisioning Framework and Certificate-Based Remote Security Provisioning Framework.

Parameter common to all Remote Security Provisioning Frameworks

Enrolee’s assigned CSE-ID or AE -ID

Enrolment Target Identity (Enrolee B’s CSE-ID or AE-ID, or MAF-ID)

Table 9.2.2.3-2 lists the Remote Security Provisioning Framework–specific parameters configured to an M2M Enrolment Functions in the Bootstrap Instruction Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Remote Security Provisioning Framework and Certificate-Based Remote Security Provisioning Framework.

Table 9.2.2.3-2 Remote Security Provisioning Framework–specific parameters configured to an M2M Enrolment Function during the Bootstrap Instruction Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Remote Security Provisioning Framework and Certificate-Based Remote Security Provisioning Framework.

| Remote Security Provisioning Framework | Remote Security Provisioning Framework-specific Parameters |
| --- | --- |
| Pre-Provisioned Symmetric Enrolment Key | None |
| Certificate Based | Enrolee is authenticated using a raw public key certificate | Enrolee’s Public key identifier |
|  | Enrolee is authenticated using an oneM2M Certificate ID (oCID) certificate | Enrolee’s oneM2M Certificate ID (oCID) |
|  |  | Enrolee’s Trust Anchor information |
|  | Enrolee is authenticated using a CSE-ID or AE-ID certificate | Enrolee’s Trust Anchor information |

#### 9.2.2.4 	Bootstrap Instruction Configuration of UNSP Authentication Server

Table 9.2.2.4-1 lists the parameters configured to an Underlying Network Service Provider authentication server (e.g. HLR, HSS or AAA) during the Bootstrap Instruction Configuration phase of the GBA-Based Remote Security Provisioning Framework.

Table 9.2.2.4-1 Parameters configured to M2M Enrolment Functions during the Bootstrap Instruction Configuration phase of the GBA-Based Remote Security Provisioning Framework.

| Parameter | Mandatory /Optional for all Remote Security Provisioning Frameworks |
| --- | --- |
| (o) Enrolee’s assigned CSE-ID or AE-ID | Mandatory |
| Enrolment Target Identifier (Enrolee B’s CSE-ID or AE-ID, or MAF-ID) | Mandatory |

### -----------------------End of change 8---------------------------------------------

### -----------------------Start of change 9-------------------------------------------

## 10.4	Credential-ID Details

A Credential-ID is a globally unique identifier used to identify serviceSubscribedAppRules resources (TS-0001[1]).

The Credential-ID has two parts:

- A type-ID part. The type-ID part is a non-negative integer represented in hexadecimal ASCII characters (0-9, a-f, A-F).

- A value part which contains a globally-unique identifier for the entity’s credential. The value part may use the Roman alphabet, numerals, ‘.’, ‘-‘, and ‘@’.

The Credential-ID is formed by concatenating the type part, the character ‘-‘ and the value part.

Table 10.4.2-1 describes the format of the Credential-ID value for the supported values of Credential-ID type-ID..

Table 10.4.2-1 Supported Credential-ID Type-ID values, the corresponding security association establishment framework, a description of the Credential being identified, and the clause where the Credential-ID value format is specified.

| Credential-ID type-ID | Security Association Establishment Framework | Credential-ID Description | Credential-ID Value format defined in clause |
| --- | --- | --- | --- |
| 0 | Other | Other identifiers of any format for any type of credential. Intended for use in an isolated deployment wishes to use their identifiers other than those shown below. These identifiers are not guaranteed to be interoperable. | Not standardized |
| 1 | PSK | KpsaId | TBD |
| 2 | Certificate-Based | Public Key Identifier (for raw public key certificates) | 10.1.2 |
| 3 |  | oneM2M-Certificate-ID (oCID) | 10.1.4 |
| 4 | MAF-Based | KmId | TBD |

### -----------------------End of change 9---------------------------------------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

Credential-ID: A globally unique identifier for a credential that was used to authenticate a CSE or AE. This can be used to determine the CSE-ID or AE-ID(s) that may be associated with the entity (see clause 10.1.1.2.2. TS-0001 [1]).

oneM2M-Certificate-ID: An globally unique identifier for the certificate based on Object Identifiers (see Annex H.1 TS-0001 [1]).

<defined term>: <definition>

<defined term>[N]: <definition>

## 3.2	Symbols

<symbol>	<Explanation>

## 3.3	Abbreviations

<ABBREVIATION1>	<Explanation>

## 3.4	Acronyms

oCID	oneM2M-Certificate-ID

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

# Comments

Alignment with TS-0001

TYPO: deleted extra period ‘.’

Typo: deleted extra space

BUG: not incorrect, but details should have been left to the description of Certificate SAEF.

BUG: These additional details for MAF-Based case should have been included.

TYPO: deleted extra space

Some of these details had already been integrated to TS-001 AE Registration procedure, but it is better to specify the details here since they rely heavily on details of the security procedures.

ALIGNMENT WITH TS-0001. B no longer needs to be configured with IdA. 
EDITORIAL: Cosmetic changes to “Credential Configuration” Phase.

DEVICE CERT ( oCID CERT

BUG: Should not have referred to M2M Enrolment Function in this bullet – it is treated in a subsequent bullet

EDITORIAL: separation into bullets.

ALIGNMENT WITH TS-0001: MAF is not mandated to supply CSE-ID or AE-ID.

EDITORIAL: All text regarding configuring identifiers to MEF is now moved to clause 8.3.1.

BUG: not incorrect, but details should have been left to the description of Certificate RSPF.

TYPO: missing space

TYPO: delete repeaded “clause”

Minor changes: 
MEF TrustAnchorCert ( MEF Trust Anchor Info
Enrolee-ID ( (o) Enrolee CSE-ID/AE-ID

Enrolee’s assigned CSE-ID or AE-ID ( (o) Enrolee’s assigned CSE-ID or AE-ID

DEVICE CERT ( oCID CERT

DEVICE CERT ( oCID CERT

TYPO: removed extra space

ALIGNMENT WITH TS-0001: Delete this entry. This information is no longer consider part of a configuration phase, and is not described in clause 9.

ALIGNMENT WITH TS-0001: This clause is adjusted due to changes in AE Registration process – Entity B no longer needs to be provided with IdA in Association configuration before Entity A authenticates to Entity B.

ALIGNMENT WITH TS-0001: Added section specifically for Entity B since it is now treated differently from entity A.

TYPO

EDITORIAL: Delete the entries of these table with text shown in red strike-through font. Configuration of these parameters is no longer dealt with in clause 9.

DEVICE CERT ( oCID CERT

DEVICE CERT ( oCID CERT

EDITORIAL

EDITORIAL

COMMENT: I am not convinced that this option is possible, but I have left it in anyway

EDITORIAL

ALIGNMENT WITH TS-0001: This clause is adjusted due to changes in AE Registration process – Entity B no longer needs to be provided with IdA in Association configuration before Entity A authenticates to Entity B.

DEVICE CERT ( oCID CERT

EDITORIAL

TYPO: – deleting superfluous spaces.

BUG: No bootstrap credential configuration steps for Enrolment Targets.

BUG: No bootstrap credential configuration steps for Enrolment Targets.

BUG: No bootstrap credential configuration steps for Enrolment Targets.

BUG: Copying error – previous text was for an SAEF, not RSPF.

BUG: No bootstrap credential configuration steps for Enrolment Targets.

BUG: No bootstrap credential configuration steps for Enrolment Targets.

BUG: Enrolment Targets are not configured during Bootstrap Instruction Configuration. Authentication between Enrolment Target and MEF is currently out of scope. This clause should be deleted.

EDITORIAL

BUG: Enrolment Targets are not configured during Bootstrap Instruction Configuration. Authentication between Enrolment Target and MEF is currently out of scope. This clause should be deleted.

ALIGNMENT WITH TS-0001: Delete this entry. This information is not consider in clause 9.

Elsewhere, we say that mutual authentication of MEF and Enrolment Target is out of scope. We should delete this text.

ALIGNMENT WITH TS-0001: