| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#15 |
| Title:* | Group Authentication Requirements and Principles |
| Source:* | China Mobile |
| Contact: | Ziyao Cheng, China Mobile, chengziyao@chinamobile.com Minpeng Qi, China Mobile, qiminpeng@chinamobile.com Min Zuo, China Mobile, zuomin@chinamobile.com |
| Date:* | 2015-01-19 |
| Abstract:* | This contribution presents the requirements and principles of group authentication for the security TR-0012. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0016 |
| Document(s) Impacted* | Security TR (TS-0012) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into an appropriate section of the Security TR-0012. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

==================<Start of Change (New Text 1)>=================

# 7	Requirements and Principles

## 7.1	Assumptions

Editor’s note: this clause provides assumptions.

<Text>

## 7.2	Requirements on the Entities

### 7.2.1	Requirements on the Entities for Group Authentication

ADN/ASN:

- It shall support credential configuration (pre-provisioning or remote provisioning).

- It shall authenticate the MN and establish security association simultaneously.

- It shall authenticate the IN (via MN) and establish security association.

MN:

- It shall support credential configuration (pre-provisioning or remote provisioning).

- It shall authenticate the ADN/ASN and establish security association simultaneously.

- It shall authenticate the IN and establish security association simultaneously.

- It shall perform mutual authentication with the IN on behalf of each ADN/ASN in the group.

IN:

- It shall support credential configuration (pre-provisioning or remote provisioning).

- It shall authenticate the MN and establish security association simultaneously.

- It shall authenticate the ADN/ASN (via MN) and establish security association.

## 7.3	Requirements on the Reference Points

### 7.3.1	Requirements on Reference Points for Group Authentication

Reference point between the ADN/ASN and the MN:

- Mutual authentication is required.

- Security association is required.

Reference point between the MN and the IN:

- Mutual authentication is required.

- Security association is required.

==================<End of Change 1>========================