| CHANGE REQUEST |
| --- |
| Group Name:* | TP#15 |
| Source:* | Giesecke & Devrient |
| Format:* | Plenary Face-to-face |
| Date:* | 2015-01-15 |
| Contact:* | Claus Dietze, Giesecke & Devrient |
| Reason for Change/s:* | This contribution corrects figure 8.2.1-1 |
| CR against: Release* | Rel. 1 |
| CR against: TS/TR* | TS-0003 V-0.9.0 |
| Clauses/Sub Clauses* | 8.2.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution addresses received Public Review comments  related to the references in TS-0003.

### -----------------------Start of change 1-------------------------------------------

### 8.2.1	Overview on Security Association Establishment Frameworks

In the present document, security associations are restricted to single hop on Mcc, Mcc’ or Mca reference point.

The oneM2M system supports the following Security Association Establishment Frameworks:

Security Association Establishment Frameworks:

Provisioned Symmetric Key Security Association Establishment. A symmetric key is provisioned to the entities: this is called the Provisioned M2M Symmetric Key, and denoted Kpsa. The entities authenticate each other by verifying Message Integrity Codes (MIC) in the Security Handshake which were generated using the symmetric key.  For more details see clause 8.2.2.1.

Certificate-Based Security Association Establishment: The entities are each issued with

a Private Signing Key that is known only to that entity,

a Certificate containing the corresponding Public Verification Key, and

(Optionally) a Certificate Chain from the entity's Certificate to a Root Certificate.

The entities must validate each other's Certificate before trusting the Public Verification Keys in the Certificate. Within the Security Handshake, entity A creates a digital signature of the session parameters using its private signing key and entity B verifies the digital signature using entity A's public verification key. Then the roles are reversed: entity B creates a digital signature and entity A verifies it. For more details see clause 8.2.2.2.

M2M Authentication Function (MAF)-based Security Association Establishment. This Security Association Establishment Framework uses symmetric keys to authenticate the entity A and the M2M Authentication Function (MAF) and derive a M2M Secure Connection key (Kc) that the MAF delivers to entity B. Then entities then authenticate each other using the M2M Secure Connection key (Kc).. For more details see clause 8.2.3.1.

For a more detailed description of the above Security Association Establishment Frameworks, it is useful to compare the following aspects of the Security Association Establishment Frameworks:

Credential Configuration:

For MAF-based Security Association Establishment Frameworks:

Entity A is configured with (or otherwise establishes) the Master Credential (Km) that the entity A will use to authenticate the entity A to the MAF.

The MAF is configured with the Master Credential (Km) that will be used to authenticate the MAF to entity A.

The details for the GBA-Based Security Association Establishment Framework are out of scope.

For the Provisioned Symmetric Key Security Association Establishment Framework, each entity is provisioned with the Provisioned M2M Symmetric Key that entities will use to authenticate each other using pre-provisioning or remote provisioning.

For the Certificate-Based Security Association Establishment Frameworks, each entity is pre-provisioned with the Credential that the entity will use to authenticate itself to the other entity.

Association Configuration: Configuration of entity identifiers (that is, CSE-ID or AE-ID) for the entities to be authenticated.

Additionally, in the case of Certificate-Based Authentication Framework: each entity is configured with the Certificate Name and Root of Trust that the entity will use to verify the other entity.

Association Security Handshake: Identification, authentication and security context establishment between the entities.

  - MAF Handshake: When a MAF-based Security Association Establishment Framework is used, entity A and the MAF perform mutual authentication and generate a M2M Secure Connection Key (Kc) which is then used in the Security Handshake for mutual authentication between entity A and entity B. This is not applicable to  Certificate-based or Provisioned Symmetric Key-based Security Association Establishment Frameworks.

Figure 8.2.1-1 provides a summary of the above defined three Security Association Establishment Frameworks.

Figure 8.2.1-1: Overview of the Security Association Establishment Frameworks
supported by oneM2M.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?