| CHANGE REQUEST |
| --- |
| Group Name:* | TP#15 |
| Source:* | Giesecke & Devrient |
| Format:* | Plenary Face-to-face |
| Date:* | 2015-01-19 |
| Contact:* | Claus Dietze |
| Reason for Change/s:* | Incorporates changes according to EditHelp! Review result |
| CR against: Release* | Rel. 1 |
| CR against: TS/TR* | TS-0003 V-0.9.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution addresses received Public Review comments  related to the references in TS-0003.

### -----------------------Start of change 1-------------------------------------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M TS-0001 "oneM2M Architecture"

[2]	void

[3]	void

[4]	oneM2M TS-0004 “oneM2M Core Protocol”

[5]	IETF RFC 5246 "The Transport Layer Security (TLS) Protocol Version 1.2".

[6]	IETF RFC 6347 "Datagram Transport Layer Security Version 1.2"

[7]	ETSI TS 102 225 (V11.0.0) "Smart Cards; Secured packet structure for UICC based applications (Release 11)" URL:http://www.etsi.org/

[8]	ETSI TS 102 226 (V11.0.0) "Smart Cards; Remote APDU structure for UICC based applications (Release 11)" URL:http://www.etsi.org/

[9]	3GPP TS 31.115 (V10.1.0) "Remote APDU Structure for (U)SIM Toolkit applications (Release 10)"

[10]	3GPP TS 31.116 (V10.2.0) "Remote APDU Structure for (Universal) Subscriber Identity Module (U)SIM Toolkit applications (Release 10)"

[11]	3GPP2 C.S0078-0 (V1.0) "Secured packet structure for CDMA Card Application Toolkit (CCAT) applications"

[12]	3GPP2 C.S0079-0 (V1.0) "Remote APDU Structure for CDMA Card Application Toolkit (CCAT) applications"

[13]	 3GPP TS 33.220 "Digital cellular telecommunications system (Phase 2+); Universal Mobile Telecommunications System (UMTS); LTE; Generic Authentication Architecture (GAA); Generic Bootstrapping Architecture (GBA) (3GPP TS 33.220)"

[14]	3GPP2 S.S0109-A "Generic Bootstrapping Architecture (GBA) Framework"

[15]	IETF RFC 4279 "Pre-Shared Key Ciphersuites for Transport Layer Security (TLS) "

voidvoid[18]	IETF RFC 5705 "Keying Material Exporters for Transport Layer Security (TLS)"

[19]	IETF RFC 3629 "UTF-8, a transformation format of ISO 10646".

[20]	"Unicode Standard Annex #15; Unicode Normalization Forms", Unicode 5.1.0, March 2008. http://www.unicode.org

[21]	GlobalPlatform Device Technology TEE Administration framework, DRAFT

[22] 	GlobalPlatform Device Technology TEE System Architecture, Version 1.0

[23]	ETSI TS 102 671 "Smart Cards; Machine-to-Machine UICC; Physical and logical characteristics" URL:http://www.etsi.org/

[24]	ETSI TS 102 221 "Smart Cards; UICC-Terminal Interface; Physical and logical characteristics" URL:http://www.etsi.org/

[25]	ETSI TS 102 484 "Smart Cards; Secure channel between a UICC and an end-point terminal" URL:http://www.etsi.org/

[26]	ISO/IEC 7816-4: "Identification cards - Integrated circuit cards - Part 4: Organization, security and commands for interchange".

[27]	ETSI TS 101 220 "Smart Cards; ETSI numbering system for telecommunication application providers" URL:http://www.etsi.org/

[28]	void

[29]	void

[30]	void

[31]		IETF RFC 6655 "AES-CCM Cipher Suites for Transport Layer Security (TLS)"

[32]	IETF RFC 5289 "TLS Elliptic Curve Cipher Suites with SHA-256/384 and AES Galois Counter Mode (GCM) "

[33] 	IETF RFC 2104 "HMAC: Keyed-Hashing for Message Authentication"

[34]	IETF RFC 5280 "Internet X.509 Public Key Infrastructure Certificate and Certificate Revocation List (CRL) Profile”

[35]	IETF RFC 6960 "X.509 Internet Public Key Infrastructure Online Certificate Status Protocol - OCSP"

[36]	IETF RFC 6961 "The Transport Layer Security (TLS) Multiple Certificate Status Request Extension"

[37]	IETF RFC 7250 “Using Raw Public Keys in Transport Layer Security (TLS) and Datagram Transport Layer Security (DTLS)”

[38]	IETF RFC 7252 “The Constrained Application Protocol (CoAP)”

[39]	RECOMMENDED ELLIPTIC CURVES FOR FEDERAL GOVERNMENT USE, National Institute of Standards and Technology, July 1999. http://csrc.nist.gov/groups/ST/toolkit/documents/dss/NISTReCur.pdf

[40]	IETF RFC 6920 “Naming Things with Hashes”

[41]	IETF RFC 3548 "The Base16, Base32, and Base64 Data Encodings".

[42]	IETF RFC 5487 “Pre-Shared Key Cipher Suites for TLS with SHA-256/384 and AES Galois Counter Mode”

[43]			 IETF RFC 4492 “Elliptic Curve Cryptography (ECC) Cipher Suites for Transport Layer Security (TLS)”

[44]		IETF RFC 6066 "Transport Layer Security (TLS) Extensions: Extension Definitions”

[45]	IETF RFC 7251  “AES-CCM Elliptic Curve Cryptography (ECC) Cipher Suites for Transport Layer Security (TLS)”

[46]	IETF RFC 5480 "Elliptic Curve Cryptography Subject Public Key Information",

[47]	GlobalPlatform Device Technology Secure Element Remote Application Management, Version 1.0

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules

NOTE:	Available at http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc.

[i.2]	oneM2M-TR-0004 Definitions and abbreviations

[i.3]	void

[i.6]	oneM2M TR-0008, Security Analysis Technical Report

[i.7]	eXtensible Access Control Markup Language (XACML) Version 3.0. 22 January 2013. OASIS Standard.

[i.8]	Handbook of Applied Cryptography,  A. J. Menezes, P. C. van Oorschot, S. A. Vanstone, CRC Press, 1996

[i.9]	Recommendation  ITU T  X.509, Information technology - Open Systems Interconnection - The Directory: Public-key and attribute certificate frameworks, 10/2012.

[i.10]	void

[i.11]	OMA-TS-REST-NetAPI_TerminalLocation-V1_0-20130924-A: "RESTful Network API for Terminal Location", Version 1.0.

[i.12]	ISO 3166-1:2013, “Codes for the representation of names of countries and their subdivisions -- Part 1: Country codes”.

[i.13]	ISO/IEC 7816-5: "Identification cards - Integrated circuit cards - Part 5: Registration of Application Providers".

[i.14]	Guide to Attribute Based Access Control (ABAC) Definition and Considerations, NIST Special Publication 800-162 (http://nvlpubs.nist.gov/nistpubs/specialpublications/NIST.sp.800-162.pdf)

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in [i.2] and the following apply:

AE-ID Certificate: certificate with a certificate chain to a trust anchor certificate and containing an AE-ID in the subjectAltName extension.

NOTE:	An AE_ID certificate can be used to verify that an entity has been assigned the AE-ID in the certificate.

association configuration: phase of a Security Association Establishment Framework in which the entity establishing the Security Association (and the Central Key Distribution Server,  in the case of Centralized Security Frameworks), are provided with identities (and any other relevant credentials) to ensure that the security association is established between the intended entities

association security handshake: phase of a Security Association Framework in which the security association endpoints perform mutual authentication

bootstrap credential: pre-provisioned credential enabling mutual authentication of the Enrolee and the M2M Enrolment function

bootstrap credential configuration: phase of a Security Bootstrap Framework in which the Bootstrap Credentials are pre-provisioned to the Enrolee and the M2M Enrolment function

bootstrap enrolment handshake: phase of a Security Bootstrap Framework in which the Enrolee and M2M Enrolment Function perform mutual authentication

bootstrap instruction configuration: phase of a Security Bootstrap Framework in which the Enrolee and M2M Enrolment Function are provided with identities (and any other relevant credentials) to enable the M2M Enrolment function to establish a Master Credential between the intended Enrolee and M2M Authentication Function

bootstrap server function [13]: BSF is hosted in a network element under the control of a Mobile Network Operator. BSF, HSS, and UEs participate in GBA in which a shared secret is established between the network and a UE by running the bootstrapping procedure

NOTE:	The shared secret can be used between NAFs and UEs, for example, for authentication purposes.

bootstrapping transaction identifier [13]: bootstrapping transaction identifier (B-TID) is used to bind the subscriber identity to the keying material in GBA reference points Ua, Ub and Zn

CA-Certificate [ i.8]: certificate created by one certification authority (CA) certifying the public key of another CA

certificate: See Public Key Certificate.

certificate chain: sequence of one or more CA-certificates, where: the Public Verification Key in each CA-certificate is certified in the previous CA-certificate; and the public key of the first CA-Certificate is trusted a priori

NOTE:	Trust in the public key in each CA-certificate can be based on trust in the previous CA-Certificate.

certificate name: unique identifier in a name field of a Certificate (e.g. in the X.509 "Subject" or "Subject Alternative Name" attribute)

certificate verification: process necessary to trust an entity's Certificate

certification authority [i.8]: responsible for establishing and vouching for the authenticity of public keys

NOTE:	[This] includes binding public keys to distinguished names through signed certificates, managing certificate serial numbers, and certificate revocation.

credential configuration: phase of a Security Association Establishment Framework in which the Credentials necessary for the Security Association Establishment Framework are configured to the relevant entities and functions

CSE-ID certificate: certificate with a certificate chain to a root of trust and containing a CSE-ID in the subjectAltName extension.

NOTE:	A CSE_ID certificate can be used to verify that an entity has been assigned the CSE-ID in the certificate.

device certificate: certificate with a certificate chain to a root of trust and containing at least one globally unique hardware instance identifier in the subjectAltName extension.

NOTE:	A device certificate can be used to verify that an entity is executing on the identified hardware instance.

digital signature [i.9]: information is signed by appending to it an enciphered summary of the information

NOTE:	The summary is produced by means of a one-way hash function, while the enciphering is carried out using the private key of the signer.

enrolee: AE or CSE that requires remote provisioning of a symmetric key to be shared with an enrolment target

enrolment key: symmetric key established between an Enrolee and M2M Enrolment Function following successful mutual authentication

NOTE:	A symmetric key to be shared by the Enrolee and an Enrolment Target may be derived (at the Enrolee and M2M Enrolment Function) from the currently valid Enrolment Key, and the M2M Enrolment Function subsequently securely delivers the symmetric key to the Enrolment Target.

enrolment key generation: phase of remote security provisioning Framework in which the Enrolee and M2M Enrolment function establish an Enrolment Key and Enrolment Key identifier

enrolment phase: The step in the lifecycle of an M2M equipment where it becomes provisioned for operation with a specific M2M Service Provider.

enrolment target: A M2M Authentication Function, CSE, or AE with whom an Enrolee wishes to establish a symmetric key (master credential or pre-provisioned secure connection key) using remote security provisioning

entity identifier: CSE-ID (or AE-ID respectively) of a CSE (or AE respectively)

FQDN certificate: A certificate with a certificate chain to a root of trust and containing an FQDN.

generic bootstrap architecture: set of 3GPP and 3GPP2 specifications providing security features and a mechanism to bootstrap authentication and key agreement for application security from the 3GPP and 3GPP2 underlying network authentication mechanisms

message integrity code: tag computed from a message and a symmetric key, and attached to a message

NOTE 1:	The purpose of a messages integrity code is to facilitate, without the use of any additional mechanisms, assurances regarding both the source of a message and its integrity.

NOTE 2:	A Message Integrity Code is sometimes called a "Message Authentication Code" - we have used "Message Integrity Code" since the abbreviation of "Message Authentication Code" (MAC) might be misunderstood to refer to "Media Access Control". The definition is based on text from [i.8] (p323).

M2M secure connection key: key shared between two CSEs of M2M Nodes (e.g. ASN/MN-CSE and IN-CSE) in order to secure the communication between those two entities

NOTE:	This M2M Secure Connection Key results from a successful M2M Security Association Establishment procedure.

MAF handshake: Phase of a Security Association Establishment Framework in which an entity and the MAF perform mutual authentication and generate a Symmetric Key which can then be used in the Association Security Handshake for mutual authentication between that entity and other entities

master credentials: Credentials used to mutually authenticate between an ASN/MN-CSE and the MAF. This is done to secure access to the infrastructure of an M2M Service Provider

NOTE:	The Master Credentials are either pre-provisioned or remotely provisioned (without relying on those credentials).

Online Certificate Status Protocol: A protocol for requesting a report on the status of one or more X.509 certificates [RFC6960]

operational phase: The period in the lifecycle of an M2M equipment where it is actually used for providing M2M services.

policy decision point [i.7]: system entity that evaluates applicable policy and renders an authorization decision

policy enforcement point [i.7]: system entity that performs access control, by making decision requests and enforcing authorization decisions

policy information point [i.7]: system entity that acts as a source of attribute values

policy retrieval point: system entity that retrieves applicable policy or policy set

pre-provisioned secure connection key: Symmetric Key that is pre-provisioned to two entities (which may be AEs or CSEs) to be used for mutual authentication of those entities in Security Association Establishment

pre-provisioned secure connection key identifier: Identifier for a Pre-Provisioned Secure Connection Key

pre-provisioned symmetric enrolee key: Symmetric Key that is pre-provisioned to the Enrolee and M2M Enrolment Function

pre-provisioned symmetric enrolee key identifier: Identifier for a Pre-Provisioned Symmetric Enrolee Key

private signing key: secret key that can generate signatures that can be verified using a corresponding Public Verification Key

public key certificate: electronic document that uses a digital signature to bind a public key with an identity

NOTE:	[i.8] A public-key certificate is a data structure consisting of a data part and a signature part. The data part contains cleartext data including, as a minimum, a public [verification] key and a string identifying the part (subject entity) to be associated therewith. The signature part consists of the digital signature of a certification authority over the data part, thereby binding the subject entity's identity to the specified public key.

public key certificate flavour: A name describing the usage of a public key certificate within the scope of oneM2M.

public key infrastructure: set of hardware, software, people, policies, and procedures needed to create, manage, distribute, use, store, and revoke Public Key Certificates. For more details, see [i.8].

public verification key: Credential that can verify digital signatures generated by a corresponding Private Signing Key, but which cannot be used to generate digital signatures

raw public key certificate: A certificate comprising only the SubjectPublicKeyInfo structure of an X.509 certificate that carries the parameters necessary to describe the public key [37]

relative enrolment key identifier: part of the enrolment key identifier that is unique within the context of  a M2M Enrolment Function.

security association establishment: sequential processing of credential configuration, association configuration and association security handshake between two entities.

NOTE:	Credential configuration and/or association configuration can not be performed if those steps have already been executed before.

security association establishment framework: Security Framework for Security Association Establishment

security bootstrap framework: Security Framework for Remote security provisioning: a mechanism for remotely provisioning a Master Credential and Master Credential Identifier to a Enrolee and an M2M Authentication Function

security framework: set of procedures providing Security Association Establishment or Remote security provisioning

self-signed certificate: Public Key Certificate that is signed by the same entity whose identity it certifies

symmetric key: secret key that is shared between two entities

trust anchor certificate: a certificate that is trusted a priori

X.509: ITU-T recommendation for a Public Key Infrastructure

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

## 3.3	Abbreviations

For the purposes of the present document, the abbreviations given in [i.2] and the following abbreviations apply:

ACL	Access Control List

ACP		AccessControlPolicy Instance

API	Application Programming Interface

ASN	Application Service Node

BSF	Bootstrapping Server Function

B-TID		Bootstrapping Transaction Identifier

CA	Certification Authority

DTLS	Datagram Transport Layer Security (Protocol)

Enrolee-ID	Enrollee Identity

FQDN	Fully Qualified Domain Name

GBA	Generic Bootstrapping Architecture

GBA_ME	ME-based GBA

GBA_U	GBA with UICC-based enhancements

GUSS	GBA User Security Settings

HLR	Home Location Register

HSS	Home Subscriber System

HW	Hardware

IdA	Identifier for entity A

IdB	Identifier for entity B

Kc	M2M Secure Connection Key

KcId 	M2M Secure Connection Key identifier

Ke	Enrolment Key

KeId	Enrolment Key Identifier

Km	Master Credential

KmId	Master Credential Identifier

Kpm	pre-provisioned credential for Master Credential provisioning

KpmId	pre-provisioned credential for Master Credential provisioning Identifier

Kpsa	provisioned credential for M2M Security Association Establishment

KpsaId	provisioned credential for M2M Security Association Establishment Identifier

Ks	temporary Key material referred to in GBA

Ks_(ext/int)_NAF Derived key in GBA_ME or Derived key in GBA_U which remains on UICC

Ks_NAF	Derived key in the ME

Ks_ext_NAF 	Derived key in GBA_U sent to the ME

Ks_int_NAF	Derived key in GBA_U which remains on UICC

MAF	M2M Authentication Function

MAF-ID	M2M Authentication Function Identifier

MEF	M2M Enrolment Function

MIC	Message Integrity Code

MN	Middle Node

NAF	Network Application Function

OCSP	Online Certificate Status Protocol

PDP	Policy Decision Point

PEP	Policy Enforcement Point

PIP	Policy Information Point

PKI	Public Key Infrastructure

PRP	Policy Retrieval Point

RBAC	Role Based Access Control

RSPF			Remote Security Provisioning Framework

SAEF			Security Association Establishment Framework

SE	Secure Environment

SW	Software

TEE	Trusted Execution Environment

TLS	Transport Layer Security (Protocol)

(D)TLS-PSK	(D)TLS Pre-Shared Key (ciphersuites)

UE	(3GPP) User Equipment

USS	User Security Settings

URI	Uniform Resource Identifier

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 7.1.2.	Parameters of the Request message

This section specifies the parameters of a request message which are evaluated by the access control mechanism.

The data types applicable to these parameters are defined in clause 6.4 of TS-0004 [4].

The parameters are listed in Table 7.1.2-1.

Table 7.1.2-1: Parameters indicated in the request message

| Parameter | Description | Mandatory/ Optional | Usage in access control mechanism |
| --- | --- | --- | --- |
| to | URI of target resource | M | Selection of accessControlPolicy associated with the target resource |
| fr | Identifier representing the originator of the request | M | Evaluated against accessControlOriginators in privileges and selfPrivileges attributes |
| role | Role of the originator | O | Evaluated against accessControlOriginators in privileges and selfPrivileges attributes (see note) |
| op | Requested operation | M | Evaluated against accessControlOperations in privileges and selfPrivileges attributes |
| fc | Filter criteria | O | Differentiation between Retrieve and Discovery operations |
| NOTE: this parameter is for use in future Release(s). |

### -----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5-------------------------------------------

##### 8.1.2.2	Path Validation and Certificate Status Verification

If an entity is to authenticate another entity using a device certificate, CSE-ID certificate, AE-ID certificate or FQDN certificate, then the entity shall perform basic path validation (Section 6.1of RFC 5280 [34]) as part of verifying the other entity’s certificate (see clause 8.1.1.2.4 “Certificate Verification”).

Certificate authority certificates shall include the name constraint extensions (clause 4.2.1.10 “Name Constraints” of RFC 5280 [34]) and shall constrain the names (object identifier M2M Device IDs from Annex H “Object Identifier Based M2M Device Identifier” TS-0001 [1], CSE-ID URIs, AE-ID URIs or FQDNs respectively) which may be in the subsequent certificate used to authenticate the entity (device certificate, CSE-ID certificate, AE-ID certificate or FQDN certificate respectively).

- Clause 4.2.1.10 “Name Constraints” in RFC5280 [34] describes how the name constraint extension is used for constraining URIs and FQDNs.

- Clause 10.4.1.4.2 “Profile for Certificate Authority Certificates for Device Certificates” describes how the name constraint extension is used for constraining object identifier M2M Device IDs.

The trust anchor certificate containing the trust anchor information (Section 6.1.1 of RFC5280 [34]) is provided to the entity during Credential Configuration, Association Configuration, Bootstrap Credential Configuration or Bootstrap Instruction Configuration.

NOTE 1: Section 6.1.1 of RFC 5280 [34] states “The trust anchor information is trusted because it was delivered to the path processing procedure by some trustworthy out-of-band procedure”. Credential Configuration, Association Configuration, Bootstrap Credential Configuration and Bootstrap Instruction Configuration satisfy the requirements of being trustworthy out-of-band procedures.

Certificate status verification: In the case of an Infrastructure  Domain entity receiving an MEF certificate, the entity shall verify the status of the certificate using a Certificate Revocation List as described in RFC 5280 [34]. oneM2M support for certificate status checking in Field Domain entities requires further study. A mapping of the Online Certificate Status Protocol (OCSP) onto HTTP may be used, as described in Appendix A of RFC 6960 [35], however a mapping of OCSP onto CoAP is not currently defined. Furthermore, OCSP may also not be easily applicable in all environments. An alternative approach may be using the TLS Certificate Status Request extension (Section 8 of [44]; also known as "OCSP stapling") or preferably the Multiple Certificate Status Extension ([36]), if available.

NOTE 2: Most of the above paragraph is based on almost identical text in the CoAP specification RFC 7252 [38], a protocol with similar (if not identical) considerations to oneM2M deployments.

### -----------------------End of change 5---------------------------------------------

### -----------------------Start of change 6-------------------------------------------

### 8.3.2	Detailed Remote Security Provisioning Framework

#### 8.3.2.1	Pre-Provisioned Symmetric Key Remote Security Provisioning Framework

This clause describes the Pre-Provisioned Symmetric Key Remote Security Provisioning Framework. The Bootstrap Credential for this framework is a long-term symmetric key that has been pre-provisioned into the Enrolee and M2M Enrolment Function; this key is called a Pre-Provisioned Symmetric Enrolee Key and is denoted Kpm.

NOTE 1:	Long term Pre-Provisioned Symmetric Enrolee Keys can pose a security risk if not adequately secured, and for this reason it is recommended that Long term Pre-Provisioned Symmetric Enrolee Keys are stored in Secure Environments.

[…]

Bootstrap Credential Configuration: The Pre-Provisioned Symmetric Enrolee Key (Kpm) and the corresponding Pre-Provisioned Symmetric Enrolee Key Identifier, denoted KpmId, are pre-provisioned to both entities. The Enrolee is also provisioned with the M2M Enrolment Function's URI (MEF URI), for the purpose of routing the (D)TLS exchange.

NOTE 2:	This pre-provisioning (by definition) uses mechanisms not specified by oneM2M.

### -----------------------End of change 6---------------------------------------------

### -----------------------Start of change 7-------------------------------------------

## D.1.2	M2M Service Framework discovery for Access Network UICC

When a UICC Network Access application supports one or more M2M Service subscription, with a DF1M2M, the EFDIR entry corresponding to this UICC Network Access Application shall contain the following M2M related Data Objects:

oneM2M Service Framework DO: defining the association between the identifier of one M2M Service Subscription provisioned in the ADF and the related DF corresponding to this M2M subscription. Likewise, each M2M Service Subscription is associated to one DF. Each of these DFs is hereafter referred as DF1M2M.

There shall be as many oneM2M Service Framework Data Objects as there are M2M Service Subscriptions provisioned in the ADF.

Table D.1: Coding of oneM2M related DOs

| Bytes | Length | Description | Status |
| --- | --- | --- | --- |
| 1 | 1 | Discretionary template tag = '73' | M |
| 2 | 1 | Length of the discretionary template = X | M |
| 3 to (2+X) | X | Discretionary Template | X |

Table D.2: Coding of oneM2M Discretionary Template related DOs

| Bytes | Length | Description | Status |
| --- | --- | --- | --- |
| 1 | 1 | oneM2M service specific data content tag = ‘A2’ | M |
| 2 | 1 | M2M service specific data content length = Y | M |
| 3 to (2+Y) | Y | M2M service specific data content | M |

Table D.3: Coding of oneM2M Service Specific Data Content related DOs

| Bytes | Length | Description | Status |
| --- | --- | --- | --- |
| 1 | 1 | oneM2M supported service provisioning tag = '80' | M |
| 2 | 1 | Length of the M2M supported service provisioning tag = A | M |
| 3 to 4 | 2 | M2M Dedicated File Identifier for following M2M service subscription | M |
| 5 to (A+2) | (A-2) | M2M Subscription Identifier | M |

### -----------------------End of change 7---------------------------------------------

### -----------------------Start of change 8-------------------------------------------

### D.1.3.1	EF1M2MST (oneM2M Service Table)

This EF indicates which optional oneM2M services are available for the corresponding subscription. If a service is not indicated as available in the oneM2M DF, the hosting M2M field node shall not select this service. The presence of this file is mandatory if optional services are provided by the subscription.

| Identifier: '6F0A' | Structure: transparent | Mandatory |
| --- | --- | --- |
| SFI: '0A' |  |
| File size: X bytes, X ≥ 1 | Update activity: low |
| Access Conditions: READ ALW UPDATE ADM DEACTIVATE ADM ACTIVATE ADM |
| Bytes | Description | M/O | Length |
| 1 | Services n°1 to n°8 | M | 1 byte |
| 2 | Services n°9 to n°16 | O | 1 byte |
| 3 | Services n°17 to n°24 | O | 1 byte |
| 4 | Services n°25 to n°32 | O | 1 byte |
| etc. |  |  |  |
| X | Services n°(8X-7) to n°(8X) | O | 1 byte |

### -----------------------End of change 8---------------------------------------------

### -----------------------Start of change 9-------------------------------------------

## E.1	Suggested content of the EFs at pre-personalization

If EFs have an unassigned value, it may not be clear from the main text what this value should be. This annex suggests values in these cases.

Table E.1: Pre-personalised EF values

| File Identification | Description | Value |
| --- | --- | --- |
| '6F02' | 1M2M Service Subscription Identifier | '8000FF…FF' |
| '6F03' | 1M2M Service Provider Identifier | '8000FF…FF' |
| '6F04' | M2M Node Identifier | '8000FF…FF' |
| '6F05' | Local CSE Identifier | '8000FF...FF' |
| '6F06' | M2M Application Identifiers list | '00FF...FF' for each record |
| '6F07' | MEF Identifier | '00FF…FF' for each record |
| '6F08' | IN-CSE Identifiers list | '00FF...FF' for each record |
| '6F09' | MAF FQDN | '8000FF...FF' |
| '6F0A' | 1M2M Service Table | Operator/Service Provider dependant |

## E.2	EF changes via Data Download or CAT applications

This clause defines if changing the content of an EF by the UICC OTA protocol or by a CAT Application is advisable. Updating of certain EFs "over the air" or "over the Internet" could result in unpredictable behaviour of the UE; these are marked "Caution" in the table below. Certain EFs are marked "No"; under no circumstances should "over the air / over the internet" changes of these EFs be considered.

Table E.2: EF update behaviour

| File identification | Description | Change advised |
| --- | --- | --- |
| '6F02' | 1M2M Service Subscription Identifier | No |
| '6F03' | 1M2M Service Provider Identifier | No |
| '6F04' | M2M Node Identifier | Caution |
| '6F05' | Local CSE Identifier | Caution |
| '6F06' | M2M Application Identifiers list | Caution |
| '6F07' | MEF Identifier | Caution |
| '6F08' | IN-CSE Identifiers list | Caution |
| '6F09' | MAF FQDN | Caution |
| '6F0A' | 1M2M Service Table | Caution |

## E.3	List of SFI values at the ADFM2MSM or DFM2M level

Table E.3: SFI values

| File Identification | SFI | Description |
| --- | --- | --- |
| '6F02' | '02' | M2M Service Subscription Identifier |
| '6F03' | '03' | M2M Service Provider Identifier |
| '6F04' | '04' | M2M Node Identifier |
| '6F05' | '05' | Local CSE Identifier |
| '6F06' | '06' | M2M Application Identifiers list |
| '6F0A' | '0A' | 1M2M Service Table |

All other SFI values are reserved for future use.

## E.4	UICC related tags defined in annex J

Table E.4: UICC tags

| Tag | Name of Data Element | Usage |
| --- | --- | --- |
| '80' | MAF FQDN TLV data object | EFMAFFQDN |
| ‘80’ | M2M-Node-ID TLV Data Object | EFM2MNID |
| '80' | Local CSE-ID TLV data object | EFCSEID |
| '80' | M2M-SP-ID TLV data object | EF1M2MSPID |
| '80' | M2M Subscription Identifier TLV data object | EF1M2MSID |
| NOTE: The value 'FF' is an invalid tag value. |

### -----------------------End of change 9---------------------------------------------

### -----------------------Start of change 10-------------------------------------------

##### 8.1.2.4	Information Needed for Certificate Authentication of another Entity

An entity should trust the following information in order to authenticate another entity using certificates:

- An indication of the public key certificate flavour of other entity’s Certificate (that is, raw public key certificate, device certificate, CSE-ID certificate, AE-ID certificate, or an MEF certificate).

- In the case where other entity’s certificate is a raw public key certificate:

  - A public key identifier for the raw public key in the certificate (see clause 10.1.2 “Public Key Identifiers”). The public key identifier can be available

### -----------------------End of change 10---------------------------------------------

### -----------------------Start of change 11-------------------------------------------

### 8.2.1	Overview on Security Association Establishment Frameworks

In the present document, security associations are restricted to single hop on Mcc, Mcc’ or Mca reference point.

The oneM2M system supports the following Security Association Establishment Frameworks:

Security Association Establishment Frameworks:

Provisioned Symmetric Key Security Association Establishment. A symmetric key is provisioned to the entities: this is called the Provisioned M2M Symmetric Key, and denoted Kpsa. The entities authenticate each other by verifying Message Integrity Codes (MIC) in the Security Handshake which were generated using the symmetric key.  For more details see clause 8.2.2.1.

Certificate-Based Security Association Establishment: The entities are each issued with

a Private Signing Key that is known only to that entity,

a Certificate containing the corresponding Public Verification Key, and

(Optionally) a Certificate Chain from the entity's Certificate to a Root Certificate.

The entities shall validate each other's Certificate before trusting the Public Verification Keys in the Certificate. Within the Security Handshake, entity A creates a digital signature of the session parameters using its private signing key and entity B verifies the digital signature using entity A's public verification key. Then the roles are reversed: entity B creates a digital signature and entity A verifies it. For more details see clause 8.2.2.2.

### -----------------------End of change 11---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?