| CHANGE REQUEST |
| --- |
| Meeting:* | SEC#16 at TP#16 |
| Source:* | Philip Hawkes, Qualcomm, phawkes@qti.qualcomm.com, Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2015-03-16 |
| Contact:* | As above |
| Reason for Change/s:* | This CR provides essential corrections defining the format of Credential-ID, KmId and KpsaId. |
| CR against: Release* | Release 1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003 v1.0.1 |
| Clauses/Sub Clauses* | New 10.4 “Credential-ID Details”, 10.5 “KmId format”, 10.6 “KpsaId Format” |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

These essential correction are for defining the format of Credential-ID, KpsaId and KmId.

This text was previously in revisions of

- SEC-2015-0003,

- SEC-2015-0448,

- SEC-2015-0452

but has been moved into a separate CR so it is easier to discuss separately.

R01: Changed to latest template. No change to content.

### -----------------------Start of change 1-------------------------------------------

## 10.4	Credential-ID Details

The Credential-ID has two parts:

- A type-ID part. The type-ID part is a non-negative integer represented in a sequence of 2 hexadecimal ASCII characters (0-9, a-f, A-F).

- A value part which contains a globally-unique identifier for the entity’s credential. The value part may use the Roman alphabet, numerals, ‘.’, ‘_’, ‘-‘, and ‘@’.

The Credential-ID is formed by concatenating the type part, the character ‘-‘ and the value part.

NOTE: A Credential-ID is a globally unique identifier used to identify serviceSubscribedAppRules resources (TS-0001[1]).

Table 10.4.2-1 describes the format of the Credential-ID value for the supported values of Credential-ID type-ID..

Table 10.4.2-1 Supported Credential-ID Type-ID values, the corresponding security association establishment framework, a description of the Credential being identified, and the clause where the Credential-ID value format is specified.

| Credential-ID type-ID | Security Association Establishment Framework | Credential-ID Description | Credential-ID Value format defined in clause |
| --- | --- | --- | --- |
| 00 | Other | Other identifiers of any format for any type of credential. If isolated deployment wishes to use their identifiers other than those shown below, then this type of Credential-ID type can be appropriate. These identifiers are not guaranteed to be interoperable. | Not standardized |
| 01 | PSK | KpsaId | 10.5 |
| 02 | Certificate-Based | For Raw Public Key Certificate: Public Key Identifier | 10.1.2 |
| 03 |  | For Device Certificate: globally unique hardware instance identifier | 10.1.1.4 |
| 04 |  | For CSE-ID Certificate: CSE-ID | TS-0001 [1] |
| 05 |  | For AE-ID Certificate: AE-ID | TS-0001 [1] |
| 06 | MAF-Based | KmId | 10.6 |
| 07 to FF | - | reserved | - |

## 10.5	KpsaId

The KpsaId part shall be of the form

KpsaId = Issuer_Relative_KpsaId@Issuer_FQDN

where

- Issuer_Relative_KpsaId is composed of the Roman alphabet, numerals, ‘.’, ‘_’ and ‘-‘ characters. The issuer of KpsaId shall ensure that no two Kpsa have identical Issuer_Relative_KpsaId.

- Issuer_FQDN is an FQDN representing the stakeholder that provisioned Kpsa.

## 10.6	KmId Format

The KmId shall be of the form

KmId = MAF_RELATIVE_KmId@MAF_FQDN

where

- MAF_RELATIVE_ KmId is composed of the Roman alphabet, numerals, ‘.’, ‘_’ and ‘-‘ characters. The MAF_RELATIVE_KmId is not case sensitive. The MAF shall ensure that no two Km have identical MAF_RELATIVE_ KmID.

- MAF_FQDN denotes the FQDN of the M2M Authentication Function.

NOTE: This format for KmId allows the identity of the M2M Authentication Function to be extracted from KmId.

### -----------------------End of change 1---------------------------------------------

# Comments

I did minor editorial correction here from previous version – delta is not shown.