| Input Contribution |
| --- |
| Meeting ID* | SEC#17 |
| Title:* | TR-0016 Resource Definition for Supporting User-Defined ACP |
| Source:* | Wei Zhou, Datang, zhouwei@catt.cn Hui Xu, Datang, xuhui@catt.cn |
| Uploaded Date:* | 2015-03-16 |
| Document(s) Impacted* | SEC WI-0023, oneM2M-TR-0016 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TR-0016. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Header

1	Introduction

This contribution proposes to redefine the <accessControlPolicy> resource in order to support used-defined access control policies. This contribution also proposes a solution for enforcing privacy policies.

2	Proposal

### 7.3.x	Proposal Z: Solution of Supporting Heterogeneous Access Control Policies

#### 7.3.x.1	Introduction

According to the description in the clause 9.6.2 of oneM2M TS-0001 [1] and in the clause 7.1 of oneM2M TS-0003 [2], the current authorization solution does not support heterogeneous access control policies. As it is difficult to predicate all the authorization requirements of oneM2M system and then design a versatile authorization system to satisfy all authorization requirements, it is reasonable for the oneM2M authorization system to support heterogeneous access control policies.

This clause describes a solution that extends current oneM2M authorization system to support heterogeneous access control policies.

In oneM2M authorization system there are two types of access control policies. One type is evaluated in PDP, another type is enforced in PEP such as privacy related access control policies. Access control policies enforced in PEP is also called obligation policy.

#### 7.3.x.2	Redefined Resource Type accessControlPolicy

The redefined <accessControlPolicy> resource is shown in the Figure 7.3.x.2-1.

Figure 7.3.x.2-1: Redefined <accessControlPolicy> resource

In the redefined <accessControlPolicy> resource the modified and the new defined attributes are specified in table 7.3.x.2-1.

Table 7.3.x.2-2: New defined/modified attributes of <accessControlPolicy> resource

| Attributes of <accessControlPolicy> | Multiplicity | RW/ RO/ WO | Description | <accessControlPolicyAnnc> Attributes |
| --- | --- | --- | --- | --- |
| privileges | 0..1 | RW | A set of access control rules that applies to resources referencing this <accessControlPolicy> resource using the accessControlPolicyID attribute. | MA |
| policyRef | 0..1 | RW | A reference to an access control policy, from which access control policy can be retrieved. | MA |
| policyCategory | 1 | RW | Authorization system uses this attribute for selecting a suitable policy evaluator to evaluate the access control policy specified in privileges or policyRef attribute. | MA |
| policyType | 1 | RW | This attribute indicates the access control policy specified in policyRef attribute shall be evaluated in a PDP or in a PEP. | MA |

#### 7.3.x.2	General Procedure of Evaluating Heterogeneous  Access Control Policies

The general procedure of evaluating heterogeneous access control policies are describe as follows:

- For each applicable <accessControlPolicy> resource the PRP retrieves access control policy from either privileges attribute or policyRef attribute, values of policyCategory and policyType attributes are also retrieved. All these values are returned to the PDP.

- The PDP evaluates the access control policies which are not used for obligation purpose according to the policyType attribute. The PDP returns the access control decision to the PEP. The returned access control decision result may be accompanied with obligation policies if they are exist.

- The PEP enforces the access control decision, and fulfill the obligation policies if they accompany the access control decision.