| Input Contribution |
| --- |
| Meeting ID* | SEC 19 |
| Title:* | TS-0016_sensitive_data_storage_resource |
| Source:* | Giesecke & Devrient, Claus [dot] Dietze [@] gi-de[dot]com |
| Uploaded Date:* | 2015-09-04 |
| Document(s) Impacted* | WI-0021; TS-0016 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | For discussion and decision to be included into TS-0016 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Header

# 1	Introduction

This contribution provides a proposal for a secure storage resource and its related procedures.

# 2	Proposal

# 3	Definitions, symbols and abbreviations

Delete from the above heading the word(s) which is/are not applicable.

## 3.1	Definitions

SE-resource: A resource that resides within the Secure Environment and that does not have a representation within a CSE.

## 7.6	Sensitive Data Storage

### 7.6.1	<sensitiveDataObject> resource

Secure Environments provide a service to store and protect sensitive data. Sensitive data objects are represented as SE-resources and are created and managed within the Secure Environment. Requests to SE-resources are using absolute addressing. A <sensitiveDataObject> resource shall represent sensitive data and related information owned by a creator as shown in figure 7.6-1.

Figure 7.6-1: <sensitiveDataObject>representation

Table 7.6-1: Child Resources of <sensitiveDataObject>

| Child Resources of <sensitiveDataObject> | Child Resource Type | Multiplicity | Description | <sensitiveDataObjectAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <sensitiveData> | 1 | Contains sensitive data and required information to access and manage sensitive data owned by a dedicated creator | none |
| [variable] | <seAccessPrivileges> | 1 | Is used to control access to the resource. | none |

Attributes in <sensitiveDataObject> are shown in table 7.6-2.

Table 7.6-2: Attributes of <sensitiveDataObject> resource

| Attributes of <sensitiveDataObject> | Multiplicity | RW/ RO/ WO | Description | <sensitiveDataObjectAnnc> (MA/OA/NA) |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. | NA |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. | NA |
| creationTime | 1 | RO | Time/date of creation of the resource. | NA |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated or its direct child resources are created/deleted. | NA |
| creator | 1 | RO | The App-ID of the AE creating the resource. | NA |
| currentByteSize | 1 | RO | Current size in bytes of sensitive data. | NA |

### 7.6.2	<sensitiveDataObject> Resource Procedures

#### 7.6.2.1	CREATE <sensitiveDataObject>

This procedure shall be used for creating a <sensitiveDataObject> resource.

Table 7.6.2.1-1: <sensitiveDataObject> CREATE

| <sensitiveDataObject> CREATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the Create request: Operation To: contains M2M-SE-ID From Registree AE Request Identifier Content: <sensitveData> Name: name of resource |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their App-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = CREATE; Unsuccessful Operation = C; Request Identifier |
| Processing at Originator after receiving Response | n/a |
| Exceptions | According to [2] |

#### 7.6.2.2	RETRIEVE <sensitiveDataObject>

This procedure shall be used for retrieving a <sensitiveDataObject> resource.

Table 7.6.2.2-1: <sensitiveDataObject> RETRIEVE

| <sensitiveDataObject> RETRIEVE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the RETRIEVE request: Operation To: contains M2M-SE-ID From Registree AE Request Identifier |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their App-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = RETRIEVE; Unsuccessful Operation = R; Request Identifier Content = Sensitive Data |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

#### 7.6.2.3	UPDATE <sensitiveDataObject>

This procedure shall be used for updating the attributes and actual data of a <sensitiveDataObject> resource.

Table 7.6.2.3-1: <sensitiveDataObject> UPDATE

| <sensitiveDataObject> UPDATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the UPDATE request: Operation To: contains M2M-SE-ID From Registree AE Request Identifier Name Content = sensitive data and / or attributes |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their App-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = UPDATE; Unsuccessful Operation = R; Request Identifier |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

#### 7.6.2.4	DELETE <sensitiveDataObject>

This procedure shall be used for deleting a <sensitiveDataObject> resource.

Table 7.6.2.4-1: <sensitiveDataObject> DELETE

| <sensitiveDataObject> DELETE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the DELETE request: Operation To: contains M2M-SE-ID From Registree AE Request Identifier Name |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their App-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = DELETE; Unsuccessful Operation = D; Request Identifier |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |