| Input Contribution |
| --- |
| Meeting ID* | SEC 20 |
| Title:* | TR-0019_Dynamic_Authorization_Solution_Proposal |
| Source:* | vinod.choyi@interdigital.com dale.seed@interdigital.com |
| Uploaded Date:* | 2015-10-30 |
| Document(s) Impacted* | TR-0019 – Dynamic Authorization |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | For discussion and decision to be included into TR-0019 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------Start of change 1----------------------------------------------

## 3.3	Abbreviations

For the purposes of the present document, the abbreviations given in oneM2M TS-0011 [i.4] and oneM2M TS-0003 [i.3] and the following apply:

AS		Authorization Server

DAA	(oneM2M) Dynamic Authorization Architecture

Daga	DAA Authorization Grant Approval reference point

Dagd 	DAA Authorization Grant Data reference point

Dagi	DAA Authorization Grant Issuance reference point

Datd	DAA Access Token Data reference point

Dati 	DAA Access Token Issuance reference point

Datu	DAA Access Token Usage reference point

OAuth	Web Authorization Protocol (denotes an IETF Working Group and specifications produced by that working group)

RO		Resource Owner

RPT		Requesting Party Token

RS		Resource Server

SLDA	Service Layer Dynamic Authorization

SLDA-PA	Service Layer Dynamic Authorization Policy Administration

SLDA-PD	Service Layer Dynamic Authorization Policy Determination

SLDA-PE	Service Layer Dynamic Authorization Policy Enforcement

SLDA-PI	Service Layer Dynamic Authorization Policy Information

UMA		User Managed Access

### -----------------------End of change 1----------------------------------------------

### -----------------------Start of change 2----------------------------------------------

## 6.*	Dynamic Authorization Architecture Proposal 4 (DAA4) Reference Model

### 6.*.1 Overall Description

Figure 6.*.1-1 shows the oneM2M Dynamic Authorization Architecture proposal 4 (DAA4) reference model. The DAA4 reference model is based on oneM2M messaging that is used for dynamic authorization.

Figure 6.*.1-1 oneM2M Dynamic Authorization Architecture Proposal 4 (DAA4) Reference Model.

Table 6.*.1-1 lists the functional roles in the DAA4 reference model. Clause 6.* describes the functions associated with these functional roles.

| DAA4 Functional Role | Description | Details in clause |
| --- | --- | --- |
| Subject | The entity requiring authorization to access resources on the Hosting Entity. The Subject would be authorized dynamically by an Authorization Entity in order to access resources. | 6.*.2.1 |
| Hosting Entity | This entity interacts with the Subject in order to obtain information about the Subject that can be used for authorization checks. This entity interacts with an Authorization entity to provide information about the Subject and request dynamic authorization checks on the Subject. | 6.*.2.2 |
| Authorization Entity | This entity performs dynamic authorization checks of the Subject based on the information that was forwarded by a Hosting Entity. This entity sends a response indicating authorization results and additional information that can be used to update the access control policies at the Hosting Entity. This entity can belong to a different operator than the Hosting Entity and could be multiple hops away from the Hosting Entity. | 6.*.2.3 |

Table 6.*.1-1 List of DAA4 functional roles

The DAA4 reference model assumes the following sequence of events take place.

- Setup

  - The Authorization Entity is provided with policies governing processing of authorization requests and policies governing the issuing of authorization responses.

  - The Authorization Entity is pre-configured with Subject’s identity and information that can be used for performing the authorization checks.

  - The Authorization Entity is provided with policies governing the authorization checks that will have to be carried out on the Subject.

  - The Hosting Entity is provided with the information about the Authorization Entity and pre-configured with credentials that can be used to perform mutual authentication between the Hosting Entity and the Authorization Entity. Similarly the Authorization Entity is pre-configured with the information associated with the Hosting Entity and associated credentials that can be used to perform mutual authentication between the Hosting and the Authorization entities.

  - The Hosting Entity is provided with dynamic authorization policies, that governs decisions on requesting dynamic authorization request, processing dynamic authorization results from the Authorization Entity and updating of access control policies based on the authorization results.

  - The Subject is optionally provided with security parameters that can be used for authorization checks

- Accessing a resource. Subject sends a resource access request to the Hosting Entity. The Hosting Entity checks the access control policies and if there is no access policies associated with the subject then the Hosting Entity initiates a dynamic authorization check and as per the set policies forwards an authorization request to the Authorization Entity

- Authorization Checks: Based on the authorization request forwarded by the Hosting Entity, the Authorization Entity performs one or more authorization checks based on the Subject’s information that was provided within the authorization request. The results of the authorization checks are then forwarded to the Hosting Entity by the Authorization Entity containing information about the resource, type of operation(s) and the validity of the authorization. The Hosting Entity updates the ACPs accordingly based on the results provided to it by the Authorization Entity.

## 6.*.2	DAA4 Functional Roles

### 6.*.2.1	Subject

A Subject performs the following functions within the scope of DAA4:

- Perform a resource access with a Hosting Entity.

- (Optional) The Subject can be involved in authorization checks with an Authorization Entity based on the type of authorization checks that will have to be carried out.

### 6.*.2.2	Hosting Entity

Within the scope of DAA4, a Hosting Entity is able to perform the following functions:

- Initiate a dynamic authorization check if an access control policy associated with the Subject does not exist. The initiation of the dynamic authorization check is determined by pre-provisioned policies

- The Hosting Entity communicates with an Authorization Entity in order to request for dynamic authorization of the Subject’s request for a resource access. The request created contains information about the Subject, including the Subject’s identity, and optionally, the resource, resource type and the type of operations.

- The Hosting Entity processes the response containing the results of the authorization check from the Authorization Entity and updates the relevant access control policies accordingly based on the results. The Hosting Entity is able to verify the authenticity of the authorization response message.

### 6.*.2.3	Authorization Entity

Within the scope of DAA4, an Authorization Entity is able to perform the following functions:

- It is able to process the authorization request sent by the Hosting Entity.

- Based on the dynamic authorization policies as well as the Subject’s information that was provided as well as the information provided with regards to the resource and associated operations, the Authorization Entity initiates one or more authorization checks of the Subject.

- Ability to create an authorization response containing the results of the authorization checks and send it to the Hosting Entity. The Authorization Entity may include an authentication tag (e.g. MIC) or a digital signature vouching for the authenticity of the authorization.

## 6.*.3	DAA4 Reference Points

## The DAA4 uses the oneM2M standardized reference points:

## Mca: Used for communications between the Subject and the Hosting Entity. This reference point is optionally protected by means of a (D)TLS connection

## Mcc: Used for communications between the Hosting Entity and the Authorization Entity. This reference point is protected by means of hop-by-hop (D)TLS connection. In addition, end-to-end security protections can be used if the Hosting Entity and the Authorization Entity belongs to different service provider domains or if the Entities are multiple hops away.

### 6.*.4	Example Procedure of Dynamic Authorization using oneM2M reference points and primitives

This clause provides example message flow for DAA4. The oneM2M reference points and primitives are used with having very little impact on the overall oneM2M messaging and associated resource for dynamic authorization.

Figure 6.*.4-1 General Proposal for Dynamic Authorization 4 (DAA4) Reference Model.

The generic procedure for dynamic authorization based on oneM2M reference points and primitives shown in Figure 6.*.4-1. The detailed procedure is as follows:

- A Subject issues a Resource Access Request to a Hosting Entity over the Mca reference point.

- The Hosting Entity checks the ACPs associated with the Subject and if there does not exist an ACP associated with the request, then the Hosting Entity checks the Dynamic Authorization Policy (DynAuthPolicy). If there is a dynamic authorization policy that can be identified based on the request, then the Hosting Entity initiates a dynamic authorization process.

- The Hosting Entity sends an Authorization Request to an Authorization Entity, requesting for authorization of the Subject and optionally the resource information, the resource-type, type of operations etc. are included within the Authorization Request.

- The Authorization Entity based on the Authorization Request can perform one or more authorization checks such as Subject authentication, payment verification, subscription information etc. and then generates an authorization result.

- The Authorization Entity sends the authorization results to the Hosting Entity using an authorization response message. The authorization results can contain the duration of the validity of the authorization. The message is provided with an authentication tag or digital signature particularly if the Authorization Entity is either multiple hops away from the Hosting Entity or if the Authorization Entity belongs to a different service provider domain.

- The Hosting Entity verifies the authenticity of the message and then processes the authorization response. The Hosting Entity updates the local ACP and includes an optional time validity associated with the access control rule.

- If the authorization results provided by the Authorization Entity matched the resource access request, then the Hosting Entity sends a Resource Access Response message to the Subject that indicates a successful authorization.

-----------------------End of change 2----------------------------------------------

### -----------------------Start of change 3----------------------------------------------

# 8.3	Proposal 4: oneM2M-based SLDA

The following sub-sections propose an architecture, procedures, and resource definitions for enabling the oneM2M system to support Service Layer Dynamic Authorization (SLDA) functionality.

A summary of the proposed oneM2M enhancements include:

- Enhancements to the oneM2M architecture to support SLDA functionality and to show which types of oneM2M entities SLDA functionality can be included within (e.g. MEF, MAF and CSEs).

- The definition of several oneM2M procedures providing message sequence level descriptions of how different types of dynamic authorization functionality can be supported within a oneM2M system.

- The definition of a oneM2M <dynAuthPolicy> resource and attributes to support configuration of service layer dynamic authorization policies.

- The definition of a oneM2M <consult> resource and corresponding request and response message formats to support the ability to perform consultation-based dynamic authorization.

- Some proposed enhancements to the existing oneM2M defined <accessControlPolicy> resource to include an identifier for an individual privilege within the privilege list that enables partial addressing of individual privileges within privileges list, an expiration time for each individual privilege, and the definition of new types of authorization context that support use cases involving payment-based, reputation-based, and security assessment-based dynamic authorization.

## 8.3.1	Architecture

SLDA functionality can optionally be hosted on various oneM2M defined entities including a CSE, a MEF or a MAF.  SLDA functionality can be centralized and hosted in its entirety on one of these oneM2M defined entities, or alternatively, the SLDA functionality can be partitioned such that its sub-functions (SLDA-PA, SLDA-PD, SLDA-PE and SLDA-PI) can be hosted in a distributed manner across multiple oneM2M entities.  For example, the SLDA-PI sub-function can be hosted on a MEF, the SLDA-PD and SLDA-PA sub-functions on a MAF and the SLDA-PE sub-function on a CSE.  When hosted in a distributed manner, the SLDA sub-functions can coordinate with one another to perform dynamic authorization functions.

Figure 8.3.1-1: SLDA deployment distributed across oneM2M MEF, MAF and CSE Entities

## 8.3.2	General Procedure for Dynamic Authorization Policy Provisioning and Configuration, Policy Evaluation and Enforcement

### 8.3.2.1			Configuration of Dynamic Authorization Policies

Dynamic authorization policies can be configured via creating/updating/deleting the dynAuthRules attribute of a targeted <dynAuthPolicy> resource.   Once configured, an SLDA function can make use of these policies to perform dynamic authorization request handling.

Step 1 – A oneM2M entity (e.g. AE) determines the type of dynamic authorization rule it would like to configure and the corresponding values for this rule (such as consultation-based rules, payment-based rules, security-assessment-based rules and reputation-based rules).

Step 2 – A oneM2M entity (e.g. AE) sends request targeting a second oneM2M entity (e.g. CSE, MEF or MAF) that hosts a SLDA function.  The request contains a <dynAuthPolicy> resource representation, where the dynAuthRules attribute of the <dynAuthPolicy> resource can be configured with dynamic authorization policy rules from Step 1.

Step 3 – The SLDA function hosted on the oneM2M entity receives the request and checks whether the requester has the proper privileges to perform the specified operation on the targeted <dynAuthPolicy> resource.  This check is performed by confirming whether the requester has configured privileges within the corresponding <accessControlPolicy> resource associated with the targeted <dynAuthPolicy>.  If yes, the SLDA function continues with processing the request, otherwise the SLDA function returns an error to the requester indicating lack of privileges to perform this operation to the requester.

Step 4 – The SLDA function processes the request and based on the operation either creates, updates or deletes the specified rules to / from the dynAuthRules attribute of the targeted <dynAuthPolicy> resource

Step 5 – The receiving oneM2M entity returns a response to the requester indicating whether or not the request to create, update, or delete the specified rules in the dynAuthRules attribute of the targeted <dynAuthPolicy> resource was successful or not.

### 8.3.2.2			Service Layer Dynamic Authorization

Service Layer Dynamic Authorization may be triggered and performed autonomously by a oneM2M entity that hosts a SLDA function.   Via this procedure an SLDA function may support autonomously granting or denying privileges on-the-fly during the processing of requests made to access resources which a requester does not have existing privileges to access.  By supporting this procedure, burden is removed from requesters since they do not have to explicitly request access privileges for resources they do not have privileges established for.  Via this procedure, service layer dynamic authorization may be performed without requesters being aware that it is being performed.   This reduces the overhead on requesters especially for use cases involving resource constrained devices (e.g. sensor applications hosted on IoT devices).

This procedure is also beneficial for the service layer itself since it offers a mechanism for access control policies to be dynamically created or updated on-the-fly leveraging SLDA results rather than having to have an external management entity in the network statically pre-configure access control policies with a set of privileges in advance.   Pre-configuring access control policies in advance can be burdensome, inflexible and not very scalable.

Step #1- A requesting oneM2M entity (e.g. AE or CSE) issues a request (i.e. Create / Retrieve / Update / Delete / Subscribe / Discover) to another oneM2M entity.

Step #2 – The receiving oneM2M entity (e.g. CSE) detects access to targeted resource.  The receiving entity checks the corresponding <accessControlPolicy> resource(s) applicable to the targeted resource (if any) to determine whether the requester has sufficient privileges configured to allow it to perform the desired type of access.  In this example, the requester lacks sufficient access privileges.

Step #3 – Rather than immediately returning an ‘access denied’ error to the requester, the receiving entity triggers dynamic authorization processing to be performed by the SLDA functionality that may either be hosted on the receiving entity or on another entity in the system.  SLDA functionality may also be split across multiple entities with some functionality hosted on the receiving entity.

Step #4 – The receiving entity, if enabled with SLDA functionality, begins to perform dynamic authorization processing.  Depending on whether the receiving entity hosts SLDA functionality itself will determine whether the SLDA processing is performed completely local or whether the receiving entity will communicate with other oneM2M entities in the system to assist it with performing SLDA.  If no SLDA functionality is found the SLDA processing is stopped and an ‘access denied’ error is returned to the requester.  If SLDA functionality is found to be hosted on either the receiving entity and / or other entities in the system, then this functionality is triggered to attempt to locate <dynAuthPolicy> resources applicable to the targeted resource.  If a <dynAuthPolicy> is not found, the SLDA discontinues dynamic authorization processing and returns an ‘access denied’ error to the requester.  If one or more <dynAuthPolicy> resources are found, the SLDA functionality uses the dynAuthRules attribute for each resource found to evaluate against the requester’s request and determines whether privileges can be dynamically granted.

Step #5 (Optional) – While evaluating the dynAuthRules of the applicable <dynAuthPolicy> resources, the SLDA function may need to consult with other entities in the system depending on the type of dynAuthRules specified.  Consultation may be needed to gather the proper information the SLDA function requires to determine whether or not to grant or deny access privileges to the requester.  This consultation is performed using the <consult> resource and its corresponding request and response primitives.

Step #6 – Based on the results of evaluating the request against the dynAuthRules and possibly consulting with other entities in the system to obtain additional information that it factors into its decision making, the SLDA functionality decides to grant access to the requester.  As a result, the receiving entity performs the request on the targeted resource and returns a successful response to the requester.  The requester, is unaware that autonomous SLDA was performed.  All it is aware of is its request completed successfully.

Step #7 (Optional) – Using the dynamic authorization results, the SLDA function may optionally update the privileges attribute within the <accessControlPolicy> resource(s) associated with the targeted resource to add access control privileges for the requester.  This decision may be controlled via a dynAuthRule defined within a <dynAuthPolicy> resource.  For example, the dynAuthRule may support a rule (e.g. privilege lifetime rule) to control whether or not the SLDA function adds or updates the static privileges of the <accessControlPolicy> resources and if so what the expiration time of this privilege is.  As a result, the SLDA function may use this rule to control whether it updates or adds a privilege and if so the expiration time (e.g. this can be done using the accessControlExpirationTime component of the privilege).  Based on these rules, the SLDA function determines whether or not to add / update privileges and their respective lifetimes.  By choosing to update the privileges, the requester may be granted access to the resource and perform the same operation without dynamic authorization having to be repeated.

Step #8- A requesting oneM2M entity (e.g. AE or CSE) issues a request (i.e. Create / Retrieve / Update / Delete / Subscribe / Discover) to the same resource on the same oneM2M entity.

Step #9 – The receiving oneM2M entity (e.g. CSE) detects access to a targeted resource.  The receiving entity checks the corresponding <accessControlPolicy> resource(s) applicable to the targeted resource and detects that the requester now has sufficient access privileges as a result of the SLDA function having added these privileges  as part of Step 7.

Step #10 – The receiving entity performs the request on the targeted resource and returns a successful response to the requester.

### 8.3.2.2.1			Dynamic Authorization Process – Based on Subscription

The SLDA may consult with an entity in the system (e.g. CSE, MAF, MEF) to determine whether or not a requesting entity has a proper service subscription that allows it privileges to gain access to a targeted resource.

Step 1 – The SLDA function is triggered either by an explicit request (i.e. access to <dynAuthRequest resource) or autonomously via the SLDA function itself (e.g. via detection of a request that failed checks on existing <accessControlPolicy> static privileges).

Step 2 – The SLDA locates applicable <dynAuthPolicy> resources (if any) and evaluates the dynAuthPolicy attribute to determine what rules have been configured.  In this example, the dynAuthPolicy attribute has been configured with a rule specifying ‘Requires Service Subscription Verification’.   This rule triggers the SLDA function to either perform local service subscription verification processing (i.e. check m2mServiceSubscriptionProfile resources) or consult with a Subscription Verification Function in the system to have it perform this verification on behalf of the SLDA.

Step 3 – The SLDA function forms a consultation request message.  The message is targeted to the <consult> resource hosted by the Subscription Verification Function.   The consultSubject is configured with the AE-ID or CSE-ID of the requester for which the verification is being performed.  The payload of the request is configured with any service subscription information of the requester that is available (e.g. service layer IDs) as well as the service subscription policy rule defining requirements such as the required service provider and/or service plan that a requester must have to be granted access privileges.

Step 4 – The Subscription Verification Function assesses the subscription requirements defined by the policy against the requester’s service subscription to determine whether the requester meets the requirements defined by the policy.  The Subscription Verification Function then returns the result back to the SLDA via a consult response containing a verification status and a list of requirements that have been met as well as any that have not.

Step 5 – SLDA functionality checks the subscription verification results and factors this outcome into its dynamic authorization decision making to determine whether or not to grant or deny requester access privileges.

### 8.3.3			Resource Definitions

### 8.3.3.1			Resource Type <dynAuthPolicy>

The <dynAuthPolicy> resource serves as the interface to configure the SLDA function with dynamic authorization rules.  This resource is used to create, retrieve, update and delete SLDA policies.  Once configured with one or more <dynAuthPolicy> resources, the SLDA function uses the rules defined within the policies to perform dynamic authorization decision making.

Various types of dynamic authorization rules can be supported such as (but not limited to) multi-factor authentication-based, payment-based, security assessment-based, consultation-based and reputation-based policies.  The representation of the resources are described further below.

In addition to dynamic authorization rules, the <dynAuthPolicy> resource also supports a selfAccessControlPolicyIDs attribute.  This attribute is used to reference access control policies that define the access privileges for the <dynAuthPolicy> resource itself.   These privileges are used to control which entities are allowed to access (e.g. retrieve, update or delete) the <dynAuthPolicy> resource and its attributes.

Optionally, the <dynAuthPolicy> resource can also support an accessControlPolicyIDs attribute that can be configured with a list of links to one or more <accessControlPolicy> resources whose static privileges a SLDA function may dynamically create, update or delete using this <dynAuthPolicy> resource.

Figure 8.3.3.1-1: Structure of <dynAuthPolicy> resource

The  <dynAuthPolicy> resource shall contain the attributes specified in table 8.3.3.1-1.

Table 8.3.3.1-1: Attributes of <dynAuthPolicy> resource

| Attribute Name | Multiplicity | RW / RO/ WO | Description |
| --- | --- | --- | --- |
| selfAccessControlPolicyIDs | 1(L) | RO | Links to authorization policy(s) defining which entities have the privilege to perform CRUD operations to this <dynAuthPolicy> resource. |
| accessControlPolicyIDs | 0..1(L) | RW | Links to one or more access control policies whose privileges can be dynamically created, updated or deleted by an SLDA function based on the rules defined by this <dynAuthPolicy> resource. |
| dynAuthRules | 1(L) | RW | List of one or more rules used by a SLDA function to perform dynamic authorization. These rules are used to determine whether or not the SLDA function is to dynamically grant access privileges to an entity attempting to access a resource or service that the entity does not currently have proper privileges to access. Each rule can be specified as a list of criteria that must be met by an originator of a request before access privileges are dynamically granted. The following is a list of types of criteria: Note – Additional types can be defined. Allowed Originators (ar) – A list of IDs of originators that are candidates for dynamic authorization. Wildcard characters such as a ‘*’ can be used to Blocked Originators (br) - A list of IDs of originators that are NOT candidates for dynamic authorization. Wildcard characters such as a ‘*’ can be used to Allowed Operations (aop) – A list of allowed operations that are candidates for dynamic authorization Blocked Operations (bop) – A list of operations that are NOT candidates for dynamic authorization Allowed Locations (al) – A list of locations originator is allowed to be in to be considered a candidate for dynamic authorization Blocked Locations (bl) - A list of locations originator is forbidden to be in to be considered a candidate for dynamic authorization Allowed Time Schedule (ats) – A list of times that requests are allowed to be considered a candidate for dynamic authorization Blocked Time Schedule (bts) – A list of times that requests are NOT allowed to be considered a candidate for dynamic authorization Allowed IP addresses (aia) - A list of originator IP addresses that are allowed to be considered candidates for dynamic authorization Blocked IP addresses (aia) - A list of originator IP addresses that are NOT allowed to be considered candidates for dynamic authorization Allowed Requester Roles (arr) – A list of requester roles that are allowed to be considered candidates for dynamic authorization Blocked Requester Roles (brr) – A list of requester roles that are NOT candidates for dynamic authorization Allowed Apps (aa) – A list of classes of apps or App-IDs that are allowed to be considered candidates for dynamic authorization Blocked Apps (ba) – A list of classes of apps or App-IDs that are NOT candidates for dynamic authorization Requires Payment Verification (rpv) – Originator’s payment information must first be verified before it can be considered a candidate for dynamic authorization. If a payment consultation contact is specified in the consultationContact list, then the SLDA function can consult with it. Requires Service Subscription Verification (rsv) - If present, then originator’s service subscription must first be verified to be valid before it can be considered a candidate for dynamic authorization. If a service subscription consultation contact is specified in the consultationContact list, then the SLDA function can consult with it. Requires Security Assessment (rsa) - If present, SLDA must perform security assessment-based authorization to verify that originator meets a certain level of security. If an authorization consultation contact is specified in the consultationContact list, then the SLDA function can consult with it. Required Platform Validation Level (rpv) – A required level of validation an originator’s platform must have to be considered a candidate for dynamic authorization. E.g. High (H), Average (A), Low (L). If a contact is specified in the consultationContact list for a platform validation function, the SLDA function can consult with it. Required Pre-Requisites (rpr) - A list of required credentials, subscriptions, actions or other arrangements an originator must have established / completed to be considered a candidate for dynamic authorization. Requires Consultation-based Authorization (rca) - If present, SLDA must perform consultation-based authorization. If an authorization consultation contact is specified in the consultationContact list, then the SLDA function can consult with it. Requires Payment Verification (rpv) – Originator’s payment information must first be verified before it can be considered a candidate for dynamic authorization. If a payment consultation contact is specified in the consultationContact list, then the SLDA function can consult with it. For example a list of dynAuthRules can be expressed as follows: ar:AE1,AE2,AE3; aop:U,R,S; boo:C,D; rsv; |

### 8.3.3.2			<consult> Resource

The <consult> resource is a virtual resource having no attributes.  The URI of this resource functions as a consultation point of contact which an SLDA function uses when performing dynamic authorization to consult with another entity in the network.  For example, when a <dynAuthPolicy> is configured with a consultation-based rule that defines a consultationContact, the URI of a <consult> resource is used.   A <consult> resource may be hosted by various oneM2M defined entities such as CSEs, AEs, MEFs and MAFs.   In addition, this resource may also be hosted by other types of entities not yet defined by oneM2M such as a location function, reputation verification function (e.g. social media servers), platform validation and assessment function, payment function, security function and service subscription verification function.

Figure 8.3.3.2-1: <consult> Virtual Resource

To perform consultation, an SLDA function constructs a consult request message and targets this message towards a <consult> resource hosted by an entity within the system.  Upon receiving this request, the entity processes it according to the type of consult, constructs a corresponding response message with the consult results, and returns the response to the SLDA function.

Table 8.3.3.2-1: Parameters of Consult Request Message

| Parameter Name | Description |
| --- | --- |
| consultantAddr | This is the address which this request is targeted at. For example, the URI of the <consult> resource. |
| consulterID | A oneM2M service layer ID of the originator issuing this consult request (E.g. AE-ID, CSE-ID, App-ID, etc). For example, the CSE-ID hosting an SLDA function. |
| consultType | The type of consult request. Several different types of consultation can be supported including one or more of the following types. Request for Consultation-based Dynamic Authorization Request for a Dynamic Authorization Credential Request for the location of an specified entity Request to verify payment info/token of a specified entity Request to verify reputation of a specified entity Request to verify service layer subscription of a specified entity Request to validate platform entity is hosted on Request to assess security of a specified entity |
| consultationInfo | Each type of consult request has corresponding information associated with it. This information may be sourced from an explicit dynamic authorization request or from an SLDA that is performing autonomous dynamic authorization. Some types of information include the following: consultSubject – Identifier of an entity which is the subject being consulted on behalf of. For example, a oneM2M AE-ID for which an SLDA function is consulting on behalf of and issuing a location consult request to a location server to determine the AE’s location. In this example, the AE-ID would be the consultSubject. Security context / assessment information of the consultSubject which the SLDA can collect and track Type of request Requested privileges Payment Info Service Subscription Info Security context information Security assessment requirements |

Table 8.3.3.2-2: Parameters of Consult Response Message

| Parameter Name | Description |
| --- | --- |
| consultStatus | The status of the consult request: Consultation Rejected Consultation Successful Consultation Error |
| consultResults | Each type of consult response can have corresponding results associated with it. Some of the results are generic and applicable to all the different types of consult requests, while some results are specific to a particular type as described below. List of privileges granted to requested resource or service and corresponding lifetime of privileges List of denied privileges to requested resource or service that were not granted and reasons why List of privileges that were pro-actively granted to resources or services that were not requested but the requester may be interested in. A dynamic authorization credential A location of the requester A payment verification status Reputation reviews/ranking Platform validation assessment results Security assessment level (e.g. trusted, un-trusted, etc) |

### 8.3.3.3			Enhancements to  <accessControlPolicy>

Current oneM2M specifications only support an <accessControlPolicy> resource having a set of defined privileges based on an ACL.  This ACL is a set of access-control-rule tuples that can be stored within the privileges attribute, where each tuple is comprised of three components consisting of 1) accessControlOriginators, 2) accessControlOperations and 3) accessControlContext.

Three enhancements to the existing privileges attribute of the <accessControlPolicy> resource are described below.

- An additional component has been added to privileges access-control-rule tuple called an accessControlPrivilegeID.  This component may be used to identify and address an individual privileges access-control-rule tuple.  This identifier is useful when supporting updating or deleting of an individual tuple.  Otherwise, an update or delete of an individual tuple requires updating the entire privileges access-control-rule tuple list which is less efficient.

- Another component has been added to the privileges access-control-rule tuple called an accessControlExpirationTime.  This component may be used to define a lifetime associated with a particular access-control-rule tuple.  In addition, it enables access-control-rule tuples to have different lifetimes with respect to one another, which can provide more flexibility from a privileges perspective.

- Three additional types of accessControlContext have also been defined:

- accessControlPaymentTerms – List of payment terms that must be established before an entity is allowed to access resources associated with this authorization policy.

- accessControlReputationLevel – Required reputation level that an entity must have before it is allowed to access resources associated with this authorization policy

- accessControlSecurityAssessment - Required level of security that an entity must have before it is allowed to access resources associated with this authorization policy

### -----------------------End of change 2----------------------------------------------