| CHANGE REQUEST |
| --- |
| Meeting:* | SEC#19 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2015-11-02 |
| Contact:* | As above |
| Reason for Change/s:* | Provides the ESF Preparation Layer and ESF Integration Layer Processing for ESF Target Data Class 1 |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenace / < Work Portion number(optional)> STE Small Technical Enhancements / < Work Portion number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0012 and v0.6.0 |
| Clauses/Sub Clauses* | New Clause 6.2. “End-to-End Security Framework (ESF) Proposal 1”, |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution is one of a series on the End-to-End Security Framework (ESF). For details on this series, see introduction to SEC-2015-0633-CR_TR-0012_ESF_Intro.

The present contribution provides the ESF Preparation Layer and ESF Integration Layer Processing for ESF Target Data Class 1.

NOTE TO RAPPORTEUR: The references in the text currently use short labels (e.g. [RFC6749]), and the assignment of proper reference labels (e.g. [i.7]) is currently left to the rapporteur. The references are currently highlighted in yellow, to assist in finding the references within the proposed text.

### -----------------------Start of change 1-------------------------------------------

### 6.3	ESF Preparation Layer and ESF Integration Layer Processing

### 6.3.1	ESF Specifications for ESF Target Data Class 1

#### 6.3.1.1	Profile for ESF Target Data Class 1

Table 6.3.1.1-1 “Profile for ESF Target Data Class 1” contains the profile for ESF Target Data Class 1.

| Aspect | Description |
| --- | --- |
| ESF Target Data Class Identifier | 1 |
| Input item | A request or response |
| Target data | A serialization of the entire request or response |
| Treated Item | A new encapsulating request or response whose Content parameter is the envelope produced by the ESF Security Layer. The Originator and Hosting CSE of the encapsulating message are the ESF End-Points for this message. |
| EEP Constraints | The present document allows an EEP to be the Originator or Hosting CSE of the input message or any other CSE on the oneM2M path between the Originator and Hosting CSE of the input message. |
| Security Layer Constraints | There can be only one Target EEP. |
| Target Data-class specific parameters for ESF Policy | Parameters for the encapsulating message (e.g. To, From) |

Table 6.3.1.1-1 Profile for ESF Target Data Class 1

#### 6.3.1.2	ESF Target Data Class 1 Processing at the Sending EEP

The follow steps occur at a Sending EEP when applying this ESF Target Data Class to an outbound request or response

- The EEP’s Preparation Function serializes the request or response into a binary data object.

- The EEP’s Preparation Function passes to the EEPs Security Function

  - The applicable ESF Target Data Class identifier.

  - Target data set to the binary data object and

  - There is no additional data for this ESF Target Data Class.

- The EEPs Security Function applies the applicable processing according to the security session type, generating an envelope.

NOTE: If ESF-Sm is applied, and the security session is not yet established, then at the ESF-Sm handshake phase must be applied prior to transmitting any target data. Consequently, the first two outbound envelopes in this case will typically contain handshake phase key exchange parameters, and not the message.

- The EEPs Security Function provides the envelope and applicable ESF Target Data Class identifier to the EEP’s Integration Function. The envelope is serialized as is XML or JSON.

- The EEP’s Integration Function forms a request or response (according to if the protected message was a request or response) including the envelope in the content:

- The EEP’s Integration Function passes the request or response to the next step in processing outbound messages.

#### 6.3.1.3	ESF Target Data Class 1 Processing at the Receiving EEP

The follow steps occur at a Receiving EEP when applying this ESF Target Data Class to an inbound request or response

  - The EEP’s Integration Layer parses the received message to identify the sending EEP and extract the envelope which is the Content parameter of the message. The envelope is serialized as is XML or JSON.

- The EEP’s Integration Function passes to the EEPs Security Function

  - The applicable ESF Target Data Class identifier.

  - Envelope.

  - There is no additional data for this ESF Target Data Class.

- The EEPs Security Function applies the applicable processing according to the security session type, generating a verified target data. This processing includes verification that the provided ESF Target Data Class identifier is correct.

NOTE: If ESF-Sm is applied, and the security session is not yet established, then at the ESF-Sm handshake phase must be applied prior to transmitting any target data. Consequently, the first two inbound envelopes in this case will typically contain handshake phase key exchange parameters, and not the message.

- The EEPs Security Function provides the verified target data and to the EEP’s Preparation Layer.

- The EEP’s Preparation Function parses the binary data object to form the verified request or response.

- The EEP’s Preparation Function passes the request or response to the next step in processing inbound messages.

### -----------------------End of change 1---------------------------------------------