| Input Contribution |
| --- |
| Meeting ID* | SEC 20 |
| Title:* | TS-0016 AE discovery and selection |
| Source:* | Sungcheol Park, KT, sungcheol.park@kt.com |
| Uploaded Date:* | 2015-11-11 |
| Document(s) Impacted* | WI-0021; TS-0016 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | For discussion and decision to be included into TS-0016 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 1	Introduction

This contribution provides a proposal for Application Entity discovery and selection. The document(TS-0016) has getSecureEnvironment, getSEFunctions and getSecureEnvironment, but there is no functions for AEs. A field domain node may have one or more SEs, and a SE may be removable. So we need to get a list of available SEs, to select a SE, and to use the functions of the SE. A SE may have one or more AE_SECs. An AE_SEC issuer may create, activate, deactivate, delete AE_SECs. And each AE_SEC may be issued by different issuers. So each AE_SEC may have different sensitive functions. And also, a CSE and an AE need to check what AE_SECs are available when a new SE connected. Because of these, an application for an AE_SEC needs to get a list of available AE_SECs, to select an AE_SEC, and to use the functions of the AE_SEC.

A SE may has its sensitive functions to access control of the SE and to management AE_SECs. For example, an access control function of a SE may permit based on its access control policy and data. And a remote application management function may load, activate, deactivate and delete AE_SECs.

An AE_SEC may has dedicated sensitive functions, such access control function, application dedicated cipher function and sensitive application data management function.

# 2	Proposal

## 7.X	AE Discovery and Selection

### 7.X.1	getApplicationEntity

#### 7X.1.1	Description

This service provides a list of available AE_SEC provided by a given SE. A SE may have one or more AE_SECs. A SE may be inserted and be removed physically. Application provider which issued AE_SECs may create, update and delete the AE_SECs. Because of these, CSE or an application for the AE need to check available AE_SECs.

#### 7.X.1.2	Pre-Conditions

M2M-SE-ID is known to the calling entity (getSecureEnvironment).

#### 7.X.1.3	Signature – getApplicationEntity

Table 7.3.1.3-1: getApplicationEntity

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| seId | IN | NO | M2M-SE-Identifier |
| applicationId | IN | NO | Application Identifier (App-ID) for the AE |
| responseType | OUT | NO | Response types: List of available AE_SEC include their M2M-AE-IDs and their provided security level No AE_SEC available (but SE exists) AE_SEC do not exist |

### 7.X.2	getAEFunctions

#### 7.X.2.1	Description

This service provides a list of available sensitive functions provided by a given AE_SEC. Unlike getSEFunctions is related with the functions of SE, getAEFunctions is related with dedicated functions to the AE_SEC. For example, a mobile TV application shall get permission to access a SE from the access control function of the SE, and then the application should request the multimedia content decryption to the decoding function of the AE_SEC.

#### 7.X.2.2	Pre-Conditions

M2M-AE-ID is known to the calling entity (getApplicationEntity).

#### 7.X.2.3	Signature – getAEFunctions

Table 7.3.2.3-1: getAEFunctions

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO | M2M-AE-Identifier |
| applicationId | IN | NO | Application Identifier (App-ID) for the AE_cse |
| responseType | OUT | NO | Response types: List of available sensitive functions No sensitive function available (but AE_SEC exists) AEs do not exist |

### 7.X.3	selectApplicationEntity

#### 7.X.3.1	Description

Selects a particular Application Entity available within the present entity.

#### 7.X.3.2	Pre-Conditions

Not applicable.

#### 7.X.3.3	Signature – selectApplicationEntity

Table 7.4.1.3-1: selectApplicationEntity

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | conditional | M2M-AE-ID |
| secLevel | IN | conditional | Types: AE_SEC with highest available security level to be selected AE_SEC with a particular security level to be selected |
| responseType | OUT | NO | Response types: Security level of selected AE_SEC together with aeId Security level or selected AE_SEC does not exist |
| Note: conditional is to be interpreted as mandatory if no other conditional parameter does exist. |