| CHANGE REQUEST |
| --- |
| Meeting:* | SEC 20.3 |
| Source:* | Colin Blanchard BT Group colin.blanchard@bt.com |
| Date:* | 2016-01-22 |
| Contact:* | Colin Blanchard BT Group colin.blanchard@bt.com |
| Reason for Change/s:* | The Privacy Policy Protection Architecture from SEC-2015-0589R06 is now incorporated in oneM2M-TR-0016-V-0.4.1 TR-0016 Authorization Architecture and Access Control Policy in clause 9.3.2.2 “Subscription to an ASP’s service” However, the architecture and stage 2 numbered processing steps are not yet reflected in the TS-0003 Security solutions specification. It was agreed at the last conference call SEC 20.1 to create a CR to bring the agreed list of privacy attributes in SEC-2015-0627 into TS 00003 The current text in clause 9.3.2.2 of TR 0016 needs to be added into the TS 0003 and the text stating areas are “for further study” replaced with references to the clauses on management of privacy attributes in SEC-2015-0627 This CR implements 1 and 2 above |
| CR against: Release* | Release 2 |
| CR against: WI* | Active WI-0045 MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003-V1.3.0 |
| Clauses/Sub Clauses* | 11 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M. Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The Privacy Policy Protection Architecture from SEC-2015-0589R06 is now incorporated in oneM2M-TR-0016-V-0.4.1 TR-0016 Authorization Architecture and Access Control Policy in clause 9.3.2.2 “Subscription to an ASP’s service” However, the architecture and stage 2 numbered processing steps are not yet reflected in the TS-0003 Security solutions specification.

- It was agreed at the last conference call SEC 20.1 to create a CR to bring the agreed list of privacy attributes in SEC-2015-0627 into TS 00003

- The current text in clause 9.3.2.2 of TR 0016 needs to be added into the TS 0003 and the text stating areas are “for further study” replaced with references to the clauses on management of privacy attributes in SEC-2015-0627

This CR implements 1 and 2 above

This contribution corresponds to following requirements. (Requirements from TS-0002 Requirements)

| SEC-052 | The oneM2M System shall store and process privacy preferences in an interoperable manner. | Targeted for Release 2 |
| --- | --- | --- |
| SEC-053 | The oneM2M System shall support privacy profiles at various levels to care for conditions of legal requirements, manufacturers, and data subjects. | Targeted for Release 2 |
| SEC-054 | The oneM2M System shall be able to prioritise privacy profiles where there is a conflict between profiles (legal profile takes priority over data subject profile, for example). | Targeted for Release 2 |

### -----------------------Start of change 1-------------------------------------------

# 11	Privacy Protection Architecture using Privacy Policy Manager（PPM)

This clause provides an architecture for the  Privacy Policy Manager (PPM). PPM is a distributed authorization privacy protection architecture using user’s privacy preference.

## 11.1	Introduction

The PPM is a personal data management framework based on the user’s privacy preferences. The PPM creates access control policies from the user’s privacy preference and protects the user’s Personally Identifiable Information (PII) from unauthorized parties. If the Service Provider provides the user’s Personally Identifiable Information to third party, the Service Provider needs the user’s acceptance. In case that the user accepted a privacy policy which indicates provision to third party, the Service Provider can provides the Personally Identifiable Information to third party. However, if the privacy policy didn’t include provision to third party, the Service Provider needs to update the privacy policy and get the user’s consent to it.

## 11.2	Relationship between components of PPM and oneM2M

The PPM shall have the following components. Detail of each component is explained in TR-0001-Use_Cases_Collection. This clause provides the relationship between the components and components of oneM2M.

- Sophisticated consent mechanism for privacy policy

When an end user subscribes to a service which uses an application provided by an IN-AE, the end user becomes a data subject, and the data subject creates a privacy preference and registers it on the PPM

This function is described in clause 11.4.1.2

- Functions of the  Policy Decision Point (PDP) and Policy Retrieval Point (PRP)

PDP

When an application requests personal data from an  IN-CSE, the PPM replies with an access decision that is decided from access control policies based on the user’s privacy preference.

PRP

When an application requests personal data from an IN-CSE, PDP requests access control policies to the PPM. The PPM replies with the access control policies based on the user’s privacy preference.

Components of PDP and PRP are defined in the following oneM2M documents

TS-0003 6.2.2 Authorization Architecture

TS-0003 7.1 Access Control Mechanism

- Traceability of personal data usage

PPM shall store the access log that records which IN-AE accessed which kind of collected data

This function is for further study of oneM2M, but this function can be implemented using components that are defined in oneM2M.

## 11.3	Privacy Policy Management in oneM2M Architecture

There are four procedures in the use of PPM. This clause explains relationships between steps in the PPM scenario and components of oneM2M.

A data subject joins an IN-CSE such as M2M Platform

A data subject subscribes to a service by an IN-AE

An IN-AE requests personal data that is stored in an ASN-CSE, MN-CSE or IN-CSE

The data subject checks the access log of his/her own personal data and requests the deletion to the IN-AE.

### 11.3.1	Involved Entities

Data subject

An end user can make use of services on an IN-CSE by subscribing to a service of an IN-AE which provides applications which controls access to the IN-CSE.

When an end user subscribes to a service by an IN-AE, the end user becomes a data subject.

AE

An AE collects various kinds of data, such as sensor.

An AE sends the data to an ASN-CSE, MN-CSE or IN-CSE

ASN-CSE or MN-CSE

Policy Enforcement Point (PEP)

  - PEP is one of the functions in the CSE.

Policy Decision Point (PDP)

  - PDP is one of the functions in the CSE.

Personal Data

  - Personal data is information that can be used on its own or with other information to identify an individual to form Personally Identifiable Information (PII).

  - A field domain CSE collects and stores personal data.

  - Examples of personal data: Sensor data, Electrical power consumption, Operating state of air conditioner, etc.…

IN-AE

An IN-AE provides services to an end user who joins the IN-CSE.

An IN-AE requests personal data from an IN-CSE in order to provide services.

IN-CSE

Portal

  - A portal is a kind of Web site or Web application in an IN-CSE.

  - An end user accesses a portal to join an IN-CSE. A data subject accesses the portal to subscribe to a service by an IN-AE.

PPM

The PPM shall store access control policies based on user’s privacy preference

A MN-CSE uses the PPM as PDP or PRP, so the PPM shall need both PDP and PRP

  - A portal is a kind of Web site or Web application in the PPM

  - An end user accesses a portal to configure the end user’s privacy preference

### 11.3.2 Management Flow in PPM Architecture

This clause describes the case where an ASN-CSE or MN-CSE stores personal data.

#### 11.3.2.1	Join to an IN-CSE

When a data subject joins an IN-CSE, the data subject configures a privacy preference using the PPM. A privacy preference explains what kind of data are allowed to be accessed by IN-AE. Figure 11.3.2.1 illustrates the overview of this process.

# Figure 11.3.2.1 a data subject joins an IN-CSE

- A data subject accesses the portal in an IN-CSE.

This process is equivalent to protocols of Web access such as HTTP, HTTPS and so on.

This process is described in clause 11.4.1.2.

- A data subject configures a privacy preference and registers it on the PPM. Then, the PPM shall create access control policies based on it.

A data subject accesses the PPM or the IN-CSE redirects the data subject to the PPM. This process is equivalent to protocols of Web access.

This process is described in clause 11.4.1.2

- An ASN-CSE or MN-CSE collects and stores data from AE.

#### 11.3.2.2	Subscription to a service by IN-AE

The data subject can subscribe to various kinds of services provided by IN-AEs through the IN-CSE. Service lists are registered on a portal and the data subject can select services to subscribe to. When the data subject subscribes to a service, the data subject needs to accept a privacy policy. In order for the data subject to easily understand this policy, the PPM shall create the customized privacy policy based on the privacy policy provided by the IN-AE and the data subject’s privacy preference. Therefore, the data subject can control personal data and agreement implies understanding of  the privacy policy. Figure 11.3.2.2 shows the overview of this process.

# Figure: 11.3.2.2 The data subject subscribes to an IN-AE’s service

- The data subject accesses the portal and select an IN-AE’s service to subscribe.

This process is equivalent to protocols of Web access such as HTTP, HTTPS and so on,

This process is described in clause 11.4.1.1

- The data subject needs to accept a privacy policy to subscribe to the IN-AE’s service. The PPM shall create the customized privacy policy for each data subject based on the data subject’s privacy preference. It is easy for the data subject to confirm differences between the privacy preference and the privacy policy and to understand what kind of personal data are collected by the IN-AE. After the data subject accepts the privacy policy, the data subject can subscribe to the IN-AE’s service.

The function of creating a customized privacy policy is described in clause 11.4.1.3

- The PPM shall create or update access control policies using the privacy policy that the data subject accepted.

The function of creating or updating access control policies in the PPM is for further study.

#### 11.3.2.3	Request for personal data to the IN-CSE

If the IN-AE needs personal data to provide the service, the IN-AE requests the data from the IN-CSE. The PPM shall work as PDP or PRP. If the PPM works as PDP, PEP receives access decision from the PPM and controls the data access using them. Figure 11.3.2.3.1 illustrates the overview of this process. If the PPM works as PRP, PDP retrieves access control policies from the PPM and controls the data access using them. Figure 11.3.2.3.2 illustrates the overview of this process.

A. The PPM works as PDP

# Figure 11.3.2.3.1 Request for personal data to the IN-CSE (the PPM works as PDP)

- An IN-AE requests personal data from the IN-CSE.

- PEP in the ASN-CSE or MN-CSE requests “Decision Request” from the PPM. The PPM shall decide to permit/deny access to personal data using control policies. Then, the PPM shall reply “Decision Response” to the ASN-CSE or MN-CSE.

In this case, the PPM shall need to provide an interface that enables access control for personal data using the PPM as PDP.

- If accessing personal data is permitted, PEP accesses the personal data and sends the personal data to the IN-AE as a response.

B. The PPM works as PRP

# Figure: 11.3.2.3.2 Request for personal data to the IN-CSE (the PPM works as PRP)

- An IN-AE requests personal data from the IN-CSE.

- PEP in the ASN-CSE or MN-CSE requests “Decision Request” from PDP. PDP requests “Policy Request” from the PPM. The PPM shall collect access control policies about “Policy Request” and send the access control policies as “Policy Response” to PDP in the ASN-CSE or MN-CSE. Then, PDP decides to permit or deny access to the personal data using the access control policies and sends a result as “Decision Response” to PEP.

In this case, the PPM shall provide an interface that enables access control for personal data using the PPM as PRP.

- If accessing personal data is permitted, PEP accesses the personal data and sends the personal data to the IN-AE as a response.

## 11.4	Privacy Policy Manager Implementation Models

### 11.4.1	 Using Terms and Conditions Mark-up Language

# Figure: 11.4.1   Privacy Policy Manager Implementation Model   Using Terms and Conditions Mark-up Language

The above model views the components of the Privacy Policy Manager (PPM) for one end user (#1) and one ASP (Provider 1), arranged as a number of selected/not selected filters in a series of stackable Filter Frames.

Four mandatory Filter Frames are defined:-

- Descriptor Filter Frame

- At least one “Provider Terms and Conditions” Filter Frame

- User Preferences Filter Frame

- At least one “Presented to user” Filter Frame

Within each Filter Frame, there are grids representing the Privacy Tags in the Mark-up Language vertically and the applications and or devices horizontally.

For the Provider Terms and Condition Filter Frame and User Preferences Filter Frame, each attribute represented by the privacy tag configured as being “selected” or “not selected” for a particular application/device is modelled by “dropping in” an appropriate coloured filter disc.

Discs at the same positions within one or more similarly structured “Presented to user Filter Frames” detect clear paths through the Filter Frame stack.

- Where provider terms and conditions and user preferences are in agreement, these discs turn green.

- Where the paths are blocked by one or more conflicts, similar detectors turn the discs red.

For example, if the Application Service Provider expects the user to agree to location information to be collected and shared with a 3rd party, then the ASP selects those two attributes (clear discs) If the end user has set a preference that they don’t want location information to be collected and shared, then there will be black discs in the User Preferences Filter Frame and path through the stack will be blocked.

Optional additional Filter Frames may be placed in the stack to “select” or “not select” those same features again by “dropping in” an appropriate coloured filter disc. For example, a country legal mandate may overrule an application Service Provider or end user selection.  The position of these optional Filter Frames determines the precedence with those at the front overruling those at the back.

The assumption with this model is that the vast majority of the provider attributes selected by the application Service Provider will not conflict with user preferences and will show green. However, there will be a very large numbers of devices, applications and frequency of software updates and additions replacements of devices. While most will not result in a conflict, those that do will be instantly identified by one or more red discs which are only displayed to the end user, thus avoiding the need to constantly read and reread hundreds of pages of detailed T&C’s.

There will be an instance of this stack for each end user who is registered with the PPM and an instance for each Application Service Provider for which they have subscribed.  However, the Descriptor Filter Frame and optional city/state/country/region Filter Frames may be shared resources for these instances.

While the description software implementation of this model is outside the scope of this stage 2 specifications, sample code for implementation of the logic is shown in Annex Y (informative).

#### 11.4.1.1 Registration of Application Service Provider Privacy Policy

- Optional registration of an applications Privacy Policy shall be part of the process of obtaining a Registered App-ID for each application and version and presenting a security certificate to the oneM2M Registration Authority that is used to authenticate the application and version.

- The ASP shall download an application T&C import template from the oneM2M App-ID Registry server, if they do not already have the correct application T&C import template.

- The application T&C import template shall list in numeric order the tags in normative Annex X.

- For each tag in the list, the ASP shall provide a value for all devices and applications in the scope of the application that the ASP is registering in the format defined in normative Annex X

- The ASP shall process the application T&C import template using their local systems and procedures with input from devices vendors and third parties who provide components of their application to create one or more provider T&C’s

- The oneM2M App-ID Registry shall, at a minimum, also provide the ASP with the “descriptors list” in the language of the oneM2M partner to support the ASP in completing the T&C import templates to form the set of Provider T&C for that ASP.

- The security certificate that was used during the App-ID registration process shall also be used to ensure integrity and protect the completed application T&C import template in subsequent storage and transmission.

- The oneM2M App-ID Registry shall check the authenticity and integrity of the ASP T&C’s by verifying the signature with the ASP public key certificate during App-ID Registration.

- Each ASP or software vendor T&C completed shall be associated to the App-ID in the oneM2M App-ID Registry.

#### 11.4.1.2	Registration of End User Privacy Preferences

- When an end user subscribes to a service provided by an application service provider, the end user becomes a data subject, and the data subject downloads or views the end user privacy preferences template from the PPM Portal

- The template used by the end user to state their privacy preferences shall align with the template used by the Application Service Provider i.e. the tags as listed in normative Annex X shall be displayed in the same order

- The end user selects and deselects attributes to state their privacy preferences which are then registered on the PPM using the same portal.

#### 11.4.1.3	Creating a customised Privacy Policy for each end user

- To make it easy for the data subject to confirm differences between the privacy preference and the privacy policy:

  - If the ASP’s selection of the feature represented by the tag value matches the privacy preference selected by the user for that Application/Device, then the corresponding “presented to user” indicator shall be set to green

  - If the ASP’s non selection of the feature represented by the tag value matches the privacy preference set by the user for that Application/Device, then the corresponding “presented to user” indicator shall be set to green

  - If the ASP’s value selected for the feature represented by the tag value matches the privacy preference selected by the user for that Application/Device, then the corresponding “presented to user” indicator shall be set to green

  - If the ASP’s selection of the feature represented by the tag value does not match the privacy preference selected by the user for that Application/Device, then the corresponding “presented to user” indicator shall be set to red

  - If the ASP’s non selection of the feature represented by the tag value does not match the privacy preference selected by the user for that Application/Device, then the corresponding “presented to user” indicator shall be set to red

  - If the ASP’s value set for the feature represented by the tag value does not match the privacy preference set by the user for that Application/Device, then the corresponding “presented to user” indicator shall be set to green

- The above rules shall be overridden if one or more optional preference profiles are present

- The order of precedence shall be

- Legal Region

- Legal Country

- Legal City

- Legal State

- Parental Control

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

# Annex X List of Privacy Attributes (Normative)

| Tag ID | Tag Name | Value | Parameter | Tag description (short form) | full Tag description | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| 1.0 | Who | Null | Null | Name of party | The trading name of the device or service provider asking for access to the users smart devices/network/data |  |
|  |  | variable | Txt | company name | The name of the company that is requesting access to the user's smart devices and specifying their terms |  |
|  |  | variable | Country code | Location | The country where the device or service provider is located |  |
|  |  | variable | Txt | Company Registration number | Company Registration number |  |
| 1.1 | ID |  |  |  | Options for how applications and devices are uniquely identified |  |
|  |  |  | Txt | Model number | These are the mobile number(s) of the device(s) if included in the ASP’s service |  |
|  |  |  | Txt | Version | These are the version number(s) of the device(s) if included in the ASP’s service |  |
|  |  |  | oneM2M Defined format | Registered App ID | These are the Registered App ID of the apps if included in the ASP’s service |  |
|  |  |  | Country codes | Country codes where approval has been granted ( if needed | Device or app accreditation may only be valid in certain countries |  |
| 2.0 | What |  |  | Data Classification Type | What is the type of data that the device/service will access? With the higher the value the more sensitive the data is. |  |
|  |  | NA | Yes/No | No data gathered | the device does not gather any data, this could be output device, such as a light switch, that only receives instructions |  |
|  |  | Non personal data | Yes/No | data not linked to a person | The data cannot be linked to a person, this could be applicable if the device was a door sensor that can only report then it was opened or closed. |  |
|  |  | Anonymised data | Yes/No | Data is collected about a person but anonymised | Data is collected about a person but anonymised to remove or summarise any data that would allow an individual to the identified/profiled |  |
|  |  | Personal data | Yes/No | Data that can be directly linked to an identify | The data gather can be linked to an identifier that is unique to an individual or small group (e.g. family members in the same home) |  |
|  |  | Sensitive personal data | Yes/No | Data that can be linked to identify, of a more sensitive nature. | The EU DPA defines certain types of sensitive person data. Additional types such as banking should also be considered to see if they fall within this area. |  |
|  |  | Medical data | Yes/No | Data related to an individual's health/fitness etc. | Data about illnesses, treatments or general wellbeing. |  |
| 3.0 | When | Null | null | When the data is collected | How often data is sent |  |
|  |  | NA | Yes/No | Not data collected | The device/service does not collect data, e.g. an end device such as a light |  |
|  |  | Event based | Yes/No | Triggered by an event | Device only gathers data when triggered, such as a door sensor triggering a camera |  |
|  |  | Variable Monthly | 1 to 12 | data Is sent monthly | The device/services only gathers the data as a monthly transfer. For example a smart fridge, sending a routine operational status report. |  |
|  |  | Weekly | Yes/No | data is sent weekly | The device/service only gathers the data as a weekly transfer. For example a diagnostic status report from your fire detection system, including sensor test results, predicted remaining battery life. |  |
|  |  | Daily | Yes/No | data is sent daily | The device/service only gathers the data on a daily transfer. For example a smart fridge sending the items that have run out as a Grocery list to the users preferred retailer so the retailer can short list them for inclusion in the users shopping basket. |  |
|  |  | hourly | 1 to 24 | Data is sent every X hours | The device/service only gathers the data on an hourly transfer. For example a house alarm reporting it is armed and all sensors have reported they are active. So user alarm app/alarm monitoring service knows that system is still operational and someone has not been able to disable the alarm ability to send an alert. |  |
|  |  | minutes | 1 to 60 | data is sent every X minutes | The device/service only gathers the data every 15th minutes. For example smart meters reporting back their usage figures. |  |
|  |  | Real time-triggered | Yes/No | The data is sent continuously then triggered. | The data is sent in real time, when a specific event triggers it. E.g. The house alarm reports an internal door opening while alarm it set, this triggers the streaming of security cameras. |  |
|  |  | Real time-full | Yes/No | The data is sent continuously at all times | The data is sent in real time for the duration of the device being active. For example CCTV data being sent to offsite storage. |  |
| 3.1 | Time period | Null |  | time period of data | When data is sent, does it cover a time period |  |
|  |  | NA | Yes/No | Not data collected | The device/service does not collect data, e.g. an end device such as a light |  |
|  |  | summary/current status | Yes/No | The device send its current status | The Device sends the current status data, with no history e.g. the current status of a door sensor (open/closed) and not the log of when the door was opened and closed. |  |
|  |  | Sample | Yes/No | The data covers a short period of time. | The data covers a sample of data from a short period of time, such a periodic sampling of heart rhythm being sampled several times a day. |  |
|  |  | full history | Yes/No | The full data captured by the device is provided | The full data captured by the device is provided, either sent in real time (3.0) or history uploaded retrospectively. |  |
| 3.2 | Sample rate | Null |  | the time period between data sampling | How long in seconds between samples been taken. |  |
|  |  | NA | Yes/No | Not data collected | The device/service does not collect data, e.g. an end device such as a light |  |
|  |  | Variable |  | value is seconds between data capture points | How long between readings that the device takes measured in seconds. |  |
|  |  | Streamed data | Yes/No | Data is captured continuously | Data is captured continuously, such as a smart security camera able to stream the feed to the user. |  |
| 4.0 | Where -stored | Null |  | Where the data is stored | Were the data created by the device or used by the service is stored |  |
|  |  | NA | Yes/No | Not data collected | The device/service does not collect data, e.g. an end device such as a light |  |
|  |  | Local | Yes/No | The data is only stored locally | The data is stored within the network of smart devices (e.g. within the home) |  |
|  |  | variable |  | Nation/block | The nation were the data stored, or if part of a wider framework (such as the EU) |  |
| 4.1 | Where -collected |  |  | Where the data is collected from. | Where is the data collected from -note this may be redundant for consumer, but could be used for external feeds such as weather reports. May also be relevant to services so they can state the tries of devices they will pull data from, as they may not want access to all smart devices in the location. |  |
|  |  | NA | Yes/No | Not data collected | The device/service does not collect data, e.g. an end device such as a light |  |
|  |  | Device | Yes/No | Data is collected just the specific device covered by T&C | The terms & conditions (also well as users privacy settings) are only be evaluated against the data collected by the specific device. |  |
|  |  | Smart device network | Yes/No | Data is collect from all devices on the users network | The data is collected from all the devices* that form the users smart device network. |  |
|  |  | variable |  | External feed | Data comes from an external feed, and is combined with data gather. E.g. Weather forecasts combined with users building utilisation patens to predict, then to turn heating up so the building is at the desired temperature when the user arrives. | Note: this would be descriptive and the user would have two options. Disable or substitute (e.g. they have their own compatible weather station, instead of getting a feed from the meteorological office. |
| 4.2 | Where -Processed | Null |  | Where is the data processed | Where (physical location) the data is processed. This may be different from the storage location |  |
|  |  | NA | Yes/No | Not data collected | The device/service does not collect data, e.g. an end device such as a light |  |
|  |  | Local | Yes/No | The data is only processed locally | The data in only processed on the device, or with the user's network of smart devices. |  |
|  |  | Variable |  | Nation/block | The nation were the data stored, or if part of a wider framework (such as the EU) |  |
| 4.3 | Where -Accessed | Hull |  | Were the data is accessible from | Where the supplier/vendor/legal restrictions allow the data stored to be accessed from. |  |
|  |  | NA | Yes/No | Not data collected | The device/service does not collect data, e.g. an end device such as a light |  |
|  |  | Local | Yes/No | The data is only processed locally | The data in only processed on the device, or with the user's network of smart devices. |  |
|  |  | Variable |  | Nation/block | The nation were the data stored, or if part of a wider framework (such as the EU) |  |
| 5.0 | Why | Null |  |  | The prime reason why personal data is being collected and to allow any change of use to be notified to the user |  |
|  |  | Yes/No | Yes/No | For Direct Delivery of the service | The ASP collects information for the direct delivery of the service | E.g. using location for paging from a base station that the user is currently registered at |
|  |  | Yes/No | Yes/No | To improve ASP’s and their partners products and services | The ASP collects information to improve ASP’s and their partners products and services |  |
|  |  | Yes/No | Yes/No | To personalize services | The ASP collects information to personalize ASP’s and their partners products and services | “ our customers that selected this also selected these” |
|  |  | Yes/No | Yes/No | A legal requirement | The ASP collects information to meet a legal requirement | E.g. Minimum age of intended user used to determine access to resources |
| 6.0 | Retention | Null |  | How long is data retained | How long the data (defined above) is kept in its current level of detail |  |
|  |  | NA | Yes/No | Not data collected | The device/service does not collect data, e.g. an end device such as a light |  |
|  |  | Zero retention | Yes/No | Zero data retention | After processing data, its immediately deleted |  |
|  |  | Minutes | 1 to 60 | Data is kept for X minutes | Data is kept for 15 minutes before being deleted. E.g. the device only holds the last set of readings and collects new ones every 15 minutes. |  |
|  |  | hour | 1 to 24 | Data is kept for X hour | Data is kept for X hours |  |
|  |  | Day | 1 to 7 | data is kept for X day |  |  |
|  |  | week | 1 to 4 | Data is kept for X week |  |  |
|  |  | Month | 1 to 12 | Data is kept for X month |  |  |
|  |  | Year | 1 to 10 | data is kept for X year |  |  |
|  |  | forever |  | The data will be kept for ever | The data will be stored without a defined retention/deletion policy. |  |
| 6.1 | retention -anonymised | null |  | how long anonymised data is kept | How long any anonymised or other derived data that is not directly linked to a unique identify is kept. E.g. stats on power usage by geo location |  |
|  |  | Zero retention | Yes/No | Zero data retention | After processing data, its immediately deleted |  |
|  |  | Minutes | 1 to 60 | Data is kept for X minutes | Data is kept for 15 minutes before being deleted. E.g. the device only holds the last set of readings and collects new ones every 15 minutes. |  |
|  |  | hour | 1 to 24 | Data is kept for X hour | Data is kept for X hours |  |
|  |  | Day | 1 to 7 | data is kept for X day |  |  |
|  |  | week | 1 to 4 | Data is kept for X week |  |  |
|  |  | Month | 1 to 12 | Data is kept for X month |  |  |
|  |  | Year | 1 to 10 | data is kept for X year |  |  |
|  |  | forever |  | The data will be kept for ever | The data will be stored without a defined retention/deletion policy. |  |
| 6.2 | retention -summary | Null |  | how long summary data is kept | How long summary data is kept, e.g. how much total power was used per month based on meter readings taken every 15 minutes. |  |
|  |  | Zero retention | Yes/No | Zero data retention | After processing data, its immediately deleted |  |
|  |  | Minutes | 1 to 60 | Data is kept for X minutes | Data is kept for 15 minutes before being deleted. E.g. the device only holds the last set of readings and collects new ones every 15 minutes. |  |
|  |  | hour | 1 to 24 | Data is kept for X hour | Data is kept for X hours |  |
|  |  | Day | 1 to 7 | data is kept for X day |  |  |
|  |  | week | 1 to 4 | Data is kept for X week |  |  |
|  |  | Month | 1 to 12 | Data is kept for X month |  |  |
|  |  | Year | 1 to 10 | data is kept for X year |  |  |
|  |  | forever |  | The data will be kept for ever | The data will be stored without a defined retention/deletion policy. |  |
| 7.0 | Sharing -full | Null |  | Who the full data is shared with. | Who outside the company has access to the full data by type |  |
|  |  | NA | Yes/No | Data is not shared outside the company | Data is not shared outside the company providing the device/service with not processing contracted out |  |
|  |  | Group | No/scope and reason | Data is only shared with companies in the same group | Data is only shared within other companies in the same group. |  |
|  |  | Infrastructure provider | Yes/No | Data is stored on 3rd party infrastructure | The data is stored on a separate company's servers e.g. the company providing the device/service uses a cloud provider for storage or processing. | Note: the answers for where reflect the 3rd party as well as the company offering the service/device. |
|  |  | Subcontractor | Yes/No | Data is shared with subcontractor(s) | Data is shared with one or more subcontractors who provide part of the service. | Note: the answers about location etc. reflect all subcontractors used. |
|  |  | Other contracted parties ancillary functions | No/scope and reason | Data is shared with other parties under contract | Data is shared with other parties under contract that provide additional (non-core) functions to use/operation of device. Such as providing newsletters, marketing offers etc. Local warranty repair places etc. |  |
|  |  | Affiliate | No/scope and reason | Data is shared with other private entities | Data is shared with other parties who have no direct or indirect involvement in the device/service. E.g. device suppliers sharing data with channel partners so they can target campaigns. |  |
|  |  | Public bodies | No/scope, reason, bodies | Data is shared with key public bodies | Data is shared then certain conditions with certain bodies. E.g. on triggering of an alarm, data for your security devices is shared with police so they can respond in a suitable fashion. Or if a medical alarm goes off the ambulance service/hospital etc. are sent details so they can respond. |  |
| 7.1 | Sharing -anonymised | Null |  | Who the data is shared with. | Who outside the company has access to anonymised data by type of user |  |
|  |  | NA | Yes/No | Data is not shared outside the company | Data is not shared outside the company providing the device/service with no processing contracted out |  |
|  |  | Group | No/scope and reason | Data is only shared with companies in the same group | Data is only shared within other companies in the same group. |  |
|  |  | Infrastructure provider | Yes/No | Data is stored on 3rd party infrastructure | The data is stored on a separate company's servers. E.g. the company providing the device/service uses a cloud provider for storage or processing. |  |
|  |  | Subcontractor | Yes/No | Data is shared with subcontractor(s) | Data is shared with one or more subcontractors who provide part of the service. |  |
|  |  | Other contracted parties ancillary functions | No/scope and reason | Data is shared with other parties under contract | Data is shared with other parties under contract that provide additional (non-core) functions to use/operation of device. Such as providing newsletters, marketing offers etc. Local warranty repair places etc. |  |
|  |  | Affiliate | No/scope and reason | Data is shared with other private entities | Data is shared with other parties who have no direct or indirect involvement in the device/service. E.g. device suppliers sharing data with channel partners so they can target campaigns. |  |
|  |  | Public bodies | No/scope, reason, bodies | Data is shared with key public bodies | Data is shared then certain conditions with certain bodies. E.g. on triggering of an alarm, data for your security devices is shared with police so they can respond in a suitable fashion. Or if a medical alarm goes off the ambulance service/hospital etc. are sent details so they can respond. |  |
| 7.2 | Sharing -summary | Null |  | Who the data is shared with. | Who outside the company has access to summary data by type of user |  |
|  |  | NA | Yes/No | Data is not shared outside the company | Data is not shared outside the company providing the device/service with no processing contracted out |  |
|  |  | Group | No/scope and reason | Data is only shared with companies in the same group | Data is only shared within other companies in the same group. |  |
|  |  | Infrastructure provider | Yes/No | Data is stored on 3rd party infrastructure | The data is stored on a separate company's servers. E.g. the company providing the device/service uses a cloud provider for storage or processing. |  |
|  |  | Subcontractor | Yes/No | Data is shared with subcontractor(s) | Data is shared with one or more subcontractors who provide part of the service. |  |
|  |  | Other contracted parties ancillary functions | No/scope and reason | Data is shared with other parties under contract | Data is shared with other parties under contract that provide additional (non-core) functions to use/operation of device. Such as providing newsletters, marketing offers etc. Local warranty repair places etc. |  |
|  |  | Affiliate | No/scope and reason | Data is shared with other private entities | Data is shared with other parties who have no direct or indirect involvement in the device/service. E.g. device suppliers sharing data with channel partners so they can target campaigns. |  |
|  |  | Public bodies | No/scope, reason, bodies | Data is shared with key public bodies | Data is shared then certain conditions with certain bodies. E.g. local councils gathering average water usage by geo-location. |  |
| 8.0 | informing | Null |  |  |  |  |
|  |  | Y/N | Y/N | T&C’s sent to email address registered by the end user | The device vendor application providers send their tag values in this table to an email address registered by the end user |  |
|  |  | URL | ACME.com/English / device type/model/T&C | T&C’s by displayed URL | The device vendor application providers make their tag values in this table available at a URL | Could be automatically processed by the PPM portal |
|  |  | URL | ACME.com/English / device type/model/T&C | T&C’s by URL stored in device | The device vendor application providers make their tag values in this table available at a URL stored in the device | Could be automatically processed by the PPM portal and or device |
|  |  | Y/N | Y/N | T&C;s on local Screen ( if present ) | The device vendor application providers make their tag values in this table available on the device screen ( if present) |  |
|  |  | Y/N | Y/N | On remote screen associated with user | The device vendor application providers make their tag values in this table available on remote screen associated with user |  |
|  |  | Y/N | Y/N | By post | The device vendor application providers send their tag values in this table to an postal address registered by the end user |  |
|  |  | Y/N | Y/N | SMS ( txt) | The device vendor application providers send their tag values in this table to an SMS number registered by the end user |  |
| 9.0 | Obtaining consent | Null |  |  |  |  |
|  |  |  | Y/N | Consent by In app default | User has to accept default by a single click in the app |  |
|  |  |  | Y/N | Consent by End user signed document | Summary XML signed with end users private key e.g. digital signature |  |
|  |  |  | Y/N | Consent by oneM2M recommended method | A oneM2M recommended method {TBA} | If this is defined in the future |
| 10.0 | Protection | Null |  |  | Five levels to describe how well that the end user privacy and security is protected are defined. Level 1 is the lowest and Level 5 the highest. Each of these levels provides requirements expected for a claim at that level | These levels align with those already proposed by oneM2M WG4 |
|  |  | Protection level claimed | 1 | Protection level claimed = 1 | Level 1: lowest level with minimal claims that the end user privacy and security is protected. This level is used when minimum risk is associated with a breach of end user security and privacy |  |
|  |  | Protection level claimed | 2 | Protection level claimed = 2 | Level 2: provides some level of confidence that the end user privacy and security is protected. Entities prove, through a secure authentication protocol, that the entity has control of the sensitive data / credentials. Controls are in place to protect against attacks on stored sensitive data / credentials. |  |
|  |  | Protection level claimed | 3 | Protection level claimed = 3 | Level 3: provides high confidence that the end user privacy and security is protected. This level is needed when substantial risk is associated with breach of end user security and privacy. Multi-factor authentication is used. Any sensitive data or information exchanged in authentication protocols is cryptographically protected in transit and at rest. |  |
|  |  | Protection level claimed | 4 | Protection level claimed= 4 | Level 4: provides very high confidence that the end user privacy and security is protected. This level is used when high risk is associated with a breach of end user security and privacy. This level provides the highest level of end user security and privacy. In addition to Level 3 this level requires the usage of tamper resistant hardware devices for the storage of all sensitive data such as cryptographic keys |  |
|  |  | Protection level claimed | 5 | Protection level claimed = 5 | As level 4 but evidence of external accreditation/ assurance available | May depend on work of oneM2M on device certification |
| 11.0 | Age | Null |  |  | When relevant to privacy settings options for how the end users age can be determined e.g. DOB age range etc. |  |
|  |  | DD/MM/YYY |  | Date Of Birth | Claimed Date Of Birth of the end user to determine access to resources |  |
|  |  | Numeric value or range of values |  | Minimum age of intended user | Minimum age of intended user used to determine access to resources |  |
|  |  | DD/MM/YYY |  | Maximum age of device ( shelf life) | Maximum age of device ( shelf life) used to determine access to resources | For devices with embedded batteries that have a shelf life or chemicals in medical devices etc. |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

# Annex Y Terms and Conditions Mark-up Language implementation rules (Informative)

Typical implementation rules are shown below and are repeated for each row.

Note on conventions: {} identifies the answers to earlier if statement, [] identifies the Filter Frame and () contain comments. The logic has been shown with indents to better show the nesting of the statements. The logic works by checking the same rows on the Filter Frames being checked.

To generate the summary value for each row the follow logic is used.

If [Current Filter Frame] Value, is not equal to NA (Not applicable= No preference or limit set)?

{Yes} Is [Current Filter Frame] value equal to [Previous Filter Frame] summary value (compound value) of?

{Yes} [Current Filter Frame] Summary value equals Value set.

{No} is [current Filter Frame] Value set =”Yes”?

{Yes}  [Current Filter Frame] Summary value set as [Previous Filter Frame] Summary value

{No} [Current Filter Frame] Summary value set as [Current Filter Frame] Summary value.

{No} [Current Filter Frame] summary value set as [Previous Filter Frame] Summary value

To generate the T&C acceptable symbol the following logic is used.

If [Current Filter Frame] Value equals “Yes”?

{Yes] [Current Filter Frame] T&C Acceptable set as “(” (the smiley is used so the result displayed to the user is language agnostic as well as only requiring a small amount of screen space).

{No} [Current Filter Frame] Value equal [Previous Filter Frame]?

{Yes} [Current Filter Frame] T&C acceptable set as “(”

{No} [Current Filter Frame] T&C Acceptable set as “(”

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

## 2.2	Informative references

[i.X]	National Institute of Standards and Technology: “Guide to Protecting the Confidentiality of Personally Identifiable Information (PII)"

### -----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5-------------------------------------------

# 3	Definitions and abbreviations

## 3.1	Definitions

PersonallyIdentifiable Information [i.X]: Any information about an individual maintained by an agency, including (1) any information that can be used to distinguish or trace an individual‘s identity, such as name, social security number, date and place of birth, mother‘s maiden name, or biometric records; and (2) any other information that is linked or linkable to an individual, such as medical, educational, financial, and employment information.

## 3.3	Abbreviations

App-ID                       Application Identifier

PII	 Personally Identifiable Information

### -----------------------End of change 5---------------------------------------------