| CHANGE REQUEST |
| --- |
| Meeting:* | SEC#21 |
| Source:* | InterDigital |
| Date:* | 2015-10-29 |
| Contact:* | Vinod Choyi, vinod.choyi@interdigital.com , Dale Seed, dale.seed@interdigital.com |
| Reason for Change/s:* | M2M Enrolment Function shall impose authorization on Enrolment Target. M2M Enrolment Function is configured with which Enrolee can be provisioned to the Enrolment Target in Bootstrap Instruction Configuration phase. M2M Enrolment Function shall use this information to validate Enrolment Target against the requested Enrolee. M2M Enrolment Function shall derive Km or Kpsa only if the authorization is successful. |
| CR against: Release* | Rel-1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003 v1.3.0 |
| Clauses/Sub Clauses* | 8.3.1.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

### TS -0003_V1.3.0 Security Solutions, in section 8.3.2, Bootstrap Instruction Configuration mentions that the M2M Enrolment Function is configured with the Enrolment Target Identity -“Identifying the Enrolment Target for which the Enrolee is to be provisioned.”.  In Integration to the Security Association Handshake phase, Enrolment Target retrieves the key Km or Kpsa from M2M Enrolment Function by passing KeId (i.e. KeId is associated with an Enrolee). M2M Enrolment Function shall authorize the Enrolment Target before deriving Keys.

The proposal is to impose authorization functionality in M2M Enrolment Function. Enrolment Target passes (securely) KeId to MEF to retrieve the keys of an Enrolee. M2M Enrolment Function shall validate whether the requested Enorlee’s keys can be provisioned to the Enrolment Target based on the information provisioned during Bootstrap Instruction Configuration phase.

----------------------- Start of change 1 -----------------------

#### 8.3.1.2	Overview on Remote Security Provisioning Frameworks

An AE or CSE that requires remote provisioning of a Master Credential and Master Credential Identifier or a Provisioned Secure Connection Key (Kpsa) and Provisioned Secure Connection Key Identifier (KpsaId) is called an Enrolee. The AE or CSE with whom the enrolee is to establish a security association is called Enrolee B. The AE or CSE or M2M Authentication Function with whom the enrolee is to establish a shared key is called an Enrolment Target.

The oneM2M system supports the following Security Bootstrap Frameworks:

Pre-Provisioned Symmetric Enrolee Key Remote Security Provisioning Framework: A symmetric key is pre-provisioned to the Enrolee and M2M Enrolment Function for the mutually authentication of those entities. For more details, see clause 8.3.2.1.

Certificate-Based Remote Security Provisioning Framework: The Enrolee and M2M Enrolment Function are each issued with:

a Private Signing Key that is known only to that entity;

a Certificate containing the corresponding Public Verification Key; and

(In the case of a device certificate, CSE-ID certificate or AE-ID certificate) a Certificate Chain from the entity's Certificate to a Trust Anchor Certificate.

The Enrolee and M2M Enrolment Function shall validate each other's Certificate before trusting the Public Verification Keys in the Certificate. Within the Security Handshake, the M2M Enrolment Function creates a digital signature of the session parameters using its private signing key and the Enrolee verifies the digital signature using the M2M Enrolment Function's public verification key. Then the roles are reversed: the Enrolee creates a digital signature and the M2M Enrolment Function verifies it. For more details see clause 8.3.2.2.

GBA-based Remote Security Provisioning Framework. In this case, the role of the M2M Enrolment Function is performed by a GBA Bootstrap Server Function. This framework uses 3GPP or 3GPP2 symmetric keys to authenticate the Enrolee and the M2M Enrolment Function (which is also a GBA BSF). The details are specified by 3GPP TS 33.220 [13] and 3GPP2 S.S0109-A [14]. For more details see clause 8.3.2.3.

For a more detailed description of the above Remote Security Provisioning Frameworks, it is useful to compare the following aspects of the Remote Security Provisioning Frameworks.

Bootstrap Credential Configuration: The Enrolee and M2M Enrolment Function are pre-provisioned with the Bootstrap Credential that the entity will use to authenticate itself to the other entity. The mechanisms for this pre-provisioning are not described in the present document.

Bootstrap Instruction Configuration:

The Enrolee and M2M Enrolment Function are provided with either:

  - M2M Authentication Function Identifier (MAF-ID) identifying the M2M Authentication Function for which the Enrolee is to be remotely provisioned when used in conjunction with a MAF-based security association establishment framework; or

  - The identifier of Enrolee B (Enrolee B-ID), when used in conjunction with a Provisioned Symmetric Key Security Association Establishment.

NOTE 1:	The identity of the M2M Authentication Function or the Enrolee B is assumed to have been configured prior to the Bootstrap Instruction Configuration phase.

Additionally, in the case of Certificate-Based Remote Security Provisioning Framework:

The Enrolee is configured with the M2M Enrolment Function URI (for the purpose of routing the (D)TLS messages to the M2M Enrolment Function) and M2M Enrolment Function Trust Anchor information that the Enrolee will use to verify the M2M Enrolment Function.

- The M2M Enrolment Function is configured with the Enrolee’s certificate information that the M2M Enrolment Function will use to verify the Enrolee. The necessary certificate information is dependent on the Enrolee’s certificate’s flavour, with details provided in clause 8.1.2.4 “Information Needed for Certificate Authentication of another Entity”.

Bootstrap Enrolment Handshake: Identification, authentication and security context establishment between the Enrolee and M2M Enrolment Function.

Enrolment Key Generation: generating a symmetric Enrolment Key,(Ke) and corresponding Enrolment Key Identifier (KeId) shared by the Enrolee and M2M Enrolment Function, which is used for subsequent generation of the Master Credential (Km) or Provisioned M2M Symmetric Key (Kpsa).

Integration to the Association Security Handshake:

For MAF-based symmetric Key Security Association, the following steps occur during the MAF Handshake of the MAF-Based Security Association Establishment:

The Enrolee derives the Master Credential (Km) from the Enrolment Key (Ke) and M2M Authentication Function Identifier (MAF-ID). Details of the derivation are provided in clause 9.4.

The Enrolee generates the Master Credential Identifier (KmId) from Master Credential (Km) as described in clause 9.1, and stores Km and KmId.

The Enrolee passes the Enrolment Key Identifier (KeId)  to the M2M Authentication Function (see "MAF Handshake" in clause 8.2.2.3).

NOTE 2:	When the Enrolee first communicates with the M2M Authentication Function, then the M2M Authentication Function has not yet retrieved the Km from the M2M Enrolment Function. Consequently, the Enrolee provides the KeId to the M2M Authentication function, which is then passed to the M2M Enrolment Function to identify the Enrolment Key. The M2M Enrolment Function then returns the Km from which the M2M Authentication Function can derive the KmId. In subsequent Security Establishments, the Enrolee may provide the KmId or the KeId, and the M2M Authentication Function will know that both identifiers indicate the retrieved Km. For more details, see "MAF Handshake" in clause 8.2.2.3.

Upon receipt of the KeId, the M2M Authentication Function determines if it already has the corresponding Km and CSE-ID or AE-ID of the Enrolee:

If the M2M Authentication Function already has the corresponding Km and CSE-ID or AE-ID of the Enrolee, then the Km is used for mutual authentication (see "MAF Handshake" in clause 8.2.2.3).

If the M2M Authentication Function does not have the corresponding Master Credential (Km) and CSE-ID or AE-ID of the Enrolee, then the following steps are followed:

-	The M2M Authentication Function (securely) passes the KeId to the M2M Enrolment Function, along with the M2M Authentication Function's URI.

-	The M2M Authentication Function initiates establishing a mutually-authenticated TLS Session with the M2M Enrolment Function:

*	The M2M Authentication Function authenticates itself to the M2M Enrolment Function using an FQDN certificate containing the FQDN of the M2M Authentication Function.

*	The M2M Enrolment Function authenticates itself to the M2M Authentication Function using an FQDN certificate containing the FQDN of the M2M Enrolment Function.

- The M2M Enrolment Function authorizes M2M Authentication Function, i.e. the M2M Enrolment Function shall verify whether the requested Enrolee(i.e. KeId associated with an Enrolee) information and credentials can be provisioned to M2M Authentication Function.

NOTE 3:	 During Bootstrap Instruction Configuration phase, M2M Enrolment Function is provisioned with the information about the M2M Authentication Functions or the Enrolment Targets for which the M2M Enrolment Function is authorized to provide the credentials of the Enrolee. So when an Enrolment Target requests for credentials of the Enrolee, then the M2M Enrolment Function verifies if the Enrolment Target is indeed authorized to be provisioned with the Enrolee’s credentials.

-	The M2M Enrolment Function derives the Km from the Ke and MAF-ID. Details of the derivation are provided in clause clause 10.3.2	"Derivation of Master Credential from Enrolment Key".

-	The M2M Enrolment Function returns the Km to the M2M Authentication Function. If the CSE-ID or AE-ID of the Enrolee is configured to the M2M Enrolment Function, then the M2M Enrolment Function also passes this CSE-ID or AE-ID to the M2M Authentication Function.

-	The M2M Authentication Function generates the Master Credential Identifier (KmId) from Master Credential (Km) as described in clause 9.1, and stores Km and KmId.

-	The Master Credential (Km) is used for mutual authentication and generation of Kc and KcId as described in MAF-Based Security Association Establishment Framework (see "MAF Handshake" in clause 8.2.2.3).

-	The Enrolee and M2M Authentication Function set Master Credential Identifier (KmId) to the value of the Enrolment Key Identifier (KeId).

-	The Enrolee and M2M Authentication Function store Km and KmId.

For Provisioned Symmetric Key Security Association Establishment, similar procedure applies where Enrolee B plays the role of M2M Authentication Function, Kpsa plays the role of Km, KpsaId is generated instead of KmId. Generation of Kpsa is described in 10.3.3 	"Derivation of Provisioned Secure Connection Key from Enrolment Key".

----------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?