| CHANGE REQUEST |
| --- |
| Meeting:* | SEC21 |
| Source:* | Giesecke & Devrient |
| Date:* | 2015-01-11 |
| Contact:* | Dirk.Wacker[at]gi-de.com, Giesecke & Devrient |
| Reason for Change/s:* | Pseudo CR to add missing features to TS-0016 |
| CR against: Release* | 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0016 v0.3.0 |
| Clauses/Sub Clauses* | 7.9 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This pseudo-CR introduces an Identity resource within the Secure Environment together with its associated procedures.

### -----------------------Start of change 1-------------------------------------------

## 7.9	Authentication and Identification

### 7.9.1	<Identity> resource

Secure Environments provide a service to AEs or CSEs to establish a Identity and provide authentication of this Identity. The <Identity> resource shall represent the services offered by the Secure Environment to enable the establishment of a secure Identity. The services include the following:

- generation of an Identity and associated key material within the secure environment

- using the associated key material for authenticating the generated Identity

The <Identity> resource is shown in figure 7.9-1.

Figure 7.9-1: <Identity> representation

Attributes in <Identity> are shown in table 7.9-1.

Table 7.9-1: Attributes of <Identity> resource

| Attributes of <sensitiveDataObject> | Multiplicity | RW/ RO/ WO | Description | <sensitiveDataObjectAnnc> (MA/OA/NA) |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. | NA |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. | NA |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. | NA |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. | NA |
| creator | 1 | RO | The AE-ID or CSE-ID of the entity creating the resource. | NA |
| seAccessPrivileges | 1 | WO | Is used to control access to the resource. | NA |
| idName | 1 | WO | Contains the name of the identity | NA |
| idData | 1 | RW | Contains information associated to the identity and which is necessary for the authentication protocol. The detailed structure depends on the authentication protocol and could comprise among others key material, protocol identifier, certificates | NA |
| originatorAuthenticationData | 1 | RW | Contains information provided by the Originator and which is necessary for the authentication protocol. The detailed structure depends on the authentication protocol and could comprise among others nonces, certificates, signatures | NA |
| receiverAuthenticationData | 1 | RO | Contains information provided by the Receiver and which is necessary for the authentication protocol. The detailed structure depends on the authentication protocol and could comprise among others nonces, certificates, signatures | NA |

Editor’s note:

- usage of resourceType attribute is for further study

### 7.9.2	<Identity> Resource Procedures

#### 7.9.2.1	CREATE <Identity>

This procedure shall be used for creating a <Identity>  resource.

Table 7.9.2.1-1: <Identity> CREATE

| <Identity> CREATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the Create request: To: contains M2M-SE-ID or M2M-AE-ID From: Registree AE, Registree CSE Request Identifier Content: idData |
| Processing at Originator before sending Request | Establish security association between creator and SE or AE_Sec Requests from an AE includes their AE-ID Requests from a CSE include their CSE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = CREATE; Unsuccessful Operation = C; Request Identifier |
| Processing at Originator after receiving Response | n/a |
| Exceptions | According to [2] |

#### 7.9.2.2	RETRIEVE <Identity>

This procedure shall be used for retrieving the identity and retrieve authentication data according the used authentication protocol.

Table 7.9.2.2-1: <Identity> RETRIEVE

| <Identity> RETRIEVE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the RETRIEVE request: To: contains M2M-SE-ID or M2M-AE-ID From: Registree AE or Registree CSE Request Identifier |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID Requests from a CSE include their CSE-ID Conducting authentication protocol |
| Processing at Receiver | Check seAccessPrivileges and validate request Conducting authentication protocol |
| Information in Response message | Response status codes: ack; successful operation = RETRIEVE; Unsuccessful Operation = R; Request Identifier Content = idName, receiverAuthenticationData |
| Processing at Originator after receiving Response | Conducting authentication protocol |
| Exceptions | As defined in [2] |

#### 7.9.2.3	UPDATE <Identity>

This procedure shall be used for updating IDData and sending authentication data according the used authentication protocol.

Table 7.8.2.3-1: <Identity> UPDATE

| <Identity> UPDATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the UPDATE request: To: contains M2M-SE-ID From: Registree AE or Registree CSE Request Identifier Content = idData, originatorAuthenticationData |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID Requests from a CSE include their CSE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = UPDATE; Unsuccessful Operation = U; Request Identifier |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

#### 7.9.2.4	DELETE <Identity >

This procedure shall be used for deleting a <Identity> resource.

Table 7.9.2.4-1: < Identity> DELETE

| <Identity> DELETE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the DELETE request: To: contains M2M-SE-ID From Registree AE Request Identifier |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID Requests from a CSE include their CSE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = DELETED; Unsuccessful Operation = D; Request Identifier |
| Processing at Originator after receiving Response | n/a |
| Exceptions | As defined in [2] |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

## 2.2	Informative references

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

### -----------------------End of Changes to References  -------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

<defined term>: <definition>

<defined term>[N]: <definition>

## 3.2	Symbols

<symbol>	<Explanation>

## 3.3	Abbreviations and Acronyms

<ABBREVIATION/ACRONYM>	<Explanation>

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?