| CHANGE REQUEST |
| --- |
| Meeting:* | SEC21 |
| Source:* | Giesecke & Devrient |
| Date:* | 2016-02-09 |
| Contact:* | Dirk.Wacker[at]gi-de.com, Giesecke & Devrient |
| Reason for Change/s:* | Pseudo CR to add missing features to TS-0016 |
| CR against: Release* | 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0016 v0.3.0 |
| Clauses/Sub Clauses* | 7.9 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This pseudo-CR introduces an Identity resource within the Secure Environment together with its associated procedures.

### -----------------------Start of change 1-------------------------------------------

## 7.9	Authentication and Identification

### 7.9.1	<identity> resource

Secure Environments provide a service to AEs or CSEs to establish a Identity and provide authentication of this Identity. The <identity> resource shall represent the services offered by the Secure Environment to enable the establishment of a secure Identity. The services include the following:

- generation of an Identity and associated key material within the secure environment

- using the associated key material for authenticating the generated Identity

The <identity> resource is shown in figure 7.9-1.

Figure 7.9-1: <identity> representation

The <identity> resource shall contain the child resources specified in table 7.9-1.

Table 7.9-1: Child resources of <identity> resource

| Child Resources of <identity> | Child Resource Type | Multiplicity | Description | <identityAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| authenticate | <authenticate> | 0..1 | See clause 7.9.3 | None |
| generateKey | <generateKey> | 0..1 | See clause 7.9.4 | None |

Attributes in <Identity> are shown in table 7.9-2.

Table 7.9-2: Attributes of <Identity> resource

| Attributes of <sensitiveDataObject> | Multiplicity | RW/ RO/ WO | Description | <sensitiveDataObjectAnnc> (MA/OA/NA) |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. | NA |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. | NA |
| resourceName | 1 | WO | This attribute is the name for the resource that is used for 'hierarchical addressing method' to represent the parent-child relationships of resources. | NA |
| parentID | 1 | RO | This attribute is the resourceID of the parent of this resource. | NA |
| expirationTime | 1 | RW | Time/date after which the resource will be deleted by the Hosting CSE. | NA |
| accessControlPolicyIDs | 0..1 (L) | RW | Is used to control access to the resource. If no accessControlPolicyIDs are provided at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute | NA |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. | NA |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. | NA |
| idName | 1 | WO | Contains the name of the identity | NA |
| keyData | 0..1 | WO | Contains the value of a key | NA |
| idData | 0..1 | RW | Contains information associated to the identity and which is necessary for the authentication protocol. The detailed structure depends on the authentication protocol and could comprise among others public key material, protocol identifier, certificates | NA |
| originatorAuthenticationData | 0..1 | RW | Contains information provided by the Originator and which is necessary for the authentication protocol. The detailed structure depends on the authentication protocol and could comprise among others nonces, certificates, signatures | NA |
| receiverAuthenticationData | 0..1 | RO | Contains information provided by the Receiver and which is necessary for the authentication protocol. The detailed structure depends on the authentication protocol and could comprise among others nonces, certificates, signatures | NA |

### 7.9.2	<identity> Resource Procedures

#### 7.9.2.1	CREATE <identity>

This procedure shall be used for creating a <identity>  resource.

Table 7.9.2.1-1: <identity> CREATE

| <identity> CREATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | All parameters defined in table 8.1.2-3 of [2] apply with the specific details for: To: contains M2M-SE-ID or M2M-AE-ID Content: The resource content shall provide the information as defined in clause 7.9.1 |
| Processing at Originator before sending Request | According to clause 10.1.1.1.of [2] |
| Processing at Receiver | According to clause 10.1.1.1.of [2] |
| Information in Response message | All parameters defined in table 8.1.3-1 of [2] apply with the specific details for: • Content: Address of the created <identity> resource, according to clause 10.1.1.1.of [2] |
| Processing at Originator after receiving Response | According to clause 10.1.1.1. of [2] |
| Exceptions | According to clause 10.1.1.1. of [2] |

If <generateKey> is created, the key to be used will be generated  and stored in keyData, in such a case keyInformation is filled with the public part of the generated key.

#### 7.9.2.2	RETRIEVE <identity>

This procedure shall be used for retrieving the identity and retrieve authentication data according the used authentication protocol.

Table 7.9.2.2-1: <identity> RETRIEVE

| <identity> RETRIEVE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | According to clause 10.1.2. of [2] with the specific details for: To: contains M2M-SE-ID or M2M-AE-ID |
| Processing at Originator before sending Request | According to clause 10.1.2. of [2] |
| Processing at Receiver | According to clause 10.1.2. of [2] |
| Information in Response message | All parameters defined in table 8.1.3-1 of [2] apply with specific details for: Content: Attributes of the <identity> resources as defined in clause 7.9.1. |
| Processing at Originator after receiving Response | According to clause 10.1.2. of [2] |
| Exceptions | According to clause 10.1.2. of [2] |

#### 7.9.2.3	UPDATE <identity>

This procedure shall be used for updating the <identity resource> and sending authentication data according the used authentication protocol.

Table 7.8.2.3-1: <identity> UPDATE

| <identity> UPDATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | All parameters defined in table 8.1.2-3 of [2] apply with the specific details for: To: contains M2M-SE-ID or M2M-AE-ID Content = attributes of the <cipher> resource as defined in clause 7.7.1 which need be updated |
| Processing at Originator before sending Request | According to clause 10.1.3. of [2] |
| Processing at Receiver | According to clause 10.1.3. of [2] |
| Information in Response message | According to clause 10.1.3. of [2] |
| Processing at Originator after receiving Response | According to clause 10.1.3. of [2] |
| Exceptions | According to clause 10.1.3. of [2] |

#### 7.9.2.4	DELETE <identity >

This procedure shall be used for deleting a <identity> resource.

Table 7.9.2.4-1: < identity> DELETE

| <Identity> DELETE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | All parameters defined in table 8.1.2-3 of [2] apply with the specific details for:To: contains M2M-SE-ID or M2M-AE-ID |
| Processing at Originator before sending Request | According to clause 10.1.4.1 of [2] |
| Processing at Receiver | According to clause 10.1.4.1 of [2] |
| Information in Response message | According to clause 10.1.4.1 of [2] |
| Processing at Originator after receiving Response | According to clause 10.1.4.1 of [2] |
| Exceptions | According to clause 10.1.4.1 of [2] |

#### 7.9.3	<authenticate> Resource

The <authenticate> resource is a virtual resource because it does not have a representation. It is the child resource of a <identity> resource. When a RETRIEVE request addresses the <authenticate>  resource, the originatorAuthenticationData, keyData and idData is used to calculate a value which is stored in retrieverAuthenticationData.

Depending on the authentication protocol it may be necessary to repeat the process of UPDATE originatorAuthenticationData , RETRIEVE <authenticate> and RETRIEVE retrieverAuthenticationData  several times.

The <authenticate>  resource inherits access control policies that apply to the parent <identity> resource.

#### 7.9.4	<generateKey> Resource

The <generateKey> resource is a virtual resource because it does not have a representation. When a RETRIEVE request addresses the <generateKey> resource, the keyData attribute is filled with a key generated according the algorithm attrbute.

The <generateKey> resource inherits access control policies that apply to the parent resource.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

## 2.2	Informative references

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

### -----------------------End of Changes to References  -------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

<defined term>: <definition>

<defined term>[N]: <definition>

## 3.2	Symbols

<symbol>	<Explanation>

## 3.3	Abbreviations and Acronyms

<ABBREVIATION/ACRONYM>	<Explanation>

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?