| CHANGE REQUEST |
| --- |
| Meeting:* | SEC22 |
| Source:* | Giesecke & Devrient |
| Date:* | 2016-03-14 |
| Contact:* | Dirk.Wacker[at]gi-de.com, Giesecke & Devrient |
| Reason for Change/s:* | CR to clarify the usage of algorithm specific parameters |
| CR against: Release* | 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0016 v0.4.0 |
| Clauses/Sub Clauses* | 7.7.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR replaces the attribute keyInformation with the child resource algorithmSpecificParameter and details the expected content for the different algorithm. Further more a algorithm was removed which is not used in oneM2M.

### -----------------------Start of change 1-------------------------------------------

### 7.7.1	<cipher> resource

Secure Environments provide a service for cryptographic operations. A <cipher> resource shall represent sensitive data and related information owned by a creator as shown in figure 7.7.1-1.

Figure 7.7.1-1: <cipher> representation

The <cipher> resource shall contain the child resources specified in table 7.7.1-1.

Table 7.7.1-1: Child resources of <cipher> resource

| Child Resources of <cipher> | Child Resource Type | Multiplicity | Description | <cipherAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| encrypt | <encrypt> | 1 | See clause 7.7.1.2 | None |
| decrypt | <decrypt> | 1 | See clause 7.7.1.3 | None |
| generateKey | <generateKey> | 0..1 | See clause 7.7.1.4 | None |
| algorithmSpecificParameter | <algorithmSpecificParameter> | 0..1 | See clause 7.10 | None |

Attributes in <cipher> are shown in table 7.7.1-2.

Table 7.7-2: Attributes of <cipher> resource

| Attributes of <cipher> | Multiplicity | RW/ RO/ WO | Description | <cipherAnnc> (MA/OA/NA) |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. | NA |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. | NA |
| resourceName | 1 | WO | This attribute is the name for the resource that is used for 'hierarchical addressing method' to represent the parent-child relationships of resources. | NA |
| parentID | 1 | RO | This attribute is the resourceID of the parent of this resource. | NA |
| expirationTime | 1 | RW | Time/date after which the resource will be deleted by the Hosting CSE. | NA |
| accessControlPolicyIDs | 0..1 (L) | RW | Is used to control access to the resource. If no accessControlPolicyIDs are provided at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute | NA |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. | NA |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. | NA |
| maxByteSize | 0..1 | RW | Maximum size in bytes of data | NA |
| currentByteSize | 0..1 | RO | Current size in bytes of sensitive data. | NA |
| sensitiveData | 0..1 | RW | Contains the input data to be either encrypted or decrypted. | NA |
| calculatedData | 0..1 | RO | Contains the result of the encryption/decryption | NA |
| algorithm | 1 | WO | Contains the algorithm type of the resource instance | NA |
| keyData | 0..1 | RW | Contains the value of a key | NA |

The following types are defined for the algorithm attribute:

- ALG_AEAD_AES_128_GCM: The AEAD_AES_128_GCM authenticated encryption algorithm works as specified in [RFC5116], using AES-128 as the block cipher, by providing the key, nonce, and plaintext, and associated data to that mode of operation.

- ALG_AEAD_AES_256_GCM: This algorithm is identical to AEAD_AES_128_GCM, but with the following differences: K_LEN is 32 octets, instead of 16 octets, and AES-256 GCM is used instead of AES-128 GCM.

- ALG_AEAD_AES_128_CCM: The AEAD_AES_128_CCM authenticated encryption algorithm works as specified in [RFC5116], using AES-128 as the block cipher, by providing the key, nonce, associated data, and plaintext to that mode of operation.

- ALG_AEAD_AES_256_CCM: This algorithm is identical to AEAD_AES_128_CCM, but with the following differences: K_LEN is 32 octets, instead of 16, and AES-256 CCM is used instead of AES-128 CCM.

- ALG_AEAD_AES_128_CCM_8: The AEAD_AES_128_CCM_8 authenticated encryption algorithm is identical to the AEAD_AES_128_CCM algorithm (see Section 5.3 of  [RFC 5116]), except that it uses 8 octets for authentication, instead  of the full 16 octets used by AEAD_AES_128_CCM (see Section 6.1 of  [RFC 6655]).

- ALG_AEAD_AES_256_CCM_8: The AEAD_AES_256_CCM_8 authenticated encryption algorithm is identical to the AEAD_AES_256_CCM algorithm (see Section 5.4 of [RFC 5116]), except that it uses 8 octets for authentication, instead of the full 16 octets used by AEAD_AES_256_CCM (see Section 6.2 of  [RFC 6655]).

- ALG_AES_BLOCK_128_CBC_NOPAD : Cipher algorithm ALG_AES_BLOCK_128_CBC_NOPAD provides a cipher using AES with block size 128 in CBC mode and does not pad input data.

- ALG_AES_CBC_ISO9797_M1: Cipher algorithm ALG_AES_CBC_ISO9797_M1 provides a cipher using AES with block size 128 in CBC mode, and pads input data according to the ISO 9797 method 1 scheme.

- ALG_AES_CBC_ISO9797_M2: Cipher algorithm ALG_AES_CBC_ISO9797_M2 provides a cipher using AES with block size 128 in CBC mode, and pads input data according to the ISO 9797 method 2 (ISO 7816-4, EMV'96) scheme.

- ALG_AES_CBC_PKCS5: Cipher algorithm ALG_AES_CBC_PKCS5 provides a cipher using AES with block size 128 in CBC mode, and pads input data according to the PKCS#5 scheme.

#### 7.7.1.1	<cipher> Resource Procedures

##### 7.7.1.1.1	CREATE <cipher>

This procedure shall be used for creating a <cipher>  resource.

Table 7.7.1.1.1-1: <cipher> CREATE

| <cipher> CREATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | All parameters defined in table 8.1.2-3 of [2] apply with the specific details for: To: contains M2M-SE-ID or M2M-AE-ID Content: The resource content shall provide the information as defined in clause 7.7.1. |
| Processing at Originator before sending Request | According to clause 10.1.1.1.of [2] |
| Processing at Receiver | According to clause 10.1.1.1.of [2] |
| Information in Response message | All parameters defined in table 8.1.3-1 of [2] apply with the specific details for: • Content: Address of the created <cipher> resource, according to clause 10.1.1.1.of [2] |
| Processing at Originator after receiving Response | According to clause 10.1.1.1. of [2] |
| Exceptions | According to clause 10.1.1.1. of [2] |

If <generateKey> is created, the key to be used will be generated  and stored in keyData.

##### 7.7.1.1.2	RETRIEVE <cipher>

This procedure shall be used for retrieving the generated output from all/last input data of the <Cipher> resource.

Table 7.7.1.1.2-1: <cipher> RETRIEVE

| <cipher> RETRIEVE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | According to clause 10.1.2. of [2] with the specific details for: To: contains M2M-SE-ID or M2M-AE-ID |
| Processing at Originator before sending Request | According to clause 10.1.2. of [2] |
| Processing at Receiver | According to clause 10.1.2. of [2] |
| Information in Response message | All parameters defined in table 8.1.3-1 of [2] apply with specific details for: Content: Attributes of the <cipher> resources as defined in clause 7.7.1. |
| Processing at Originator after receiving Response | According to clause 10.1.2. of [2] |
| Exceptions | According to clause 10.1.2. of [2] |

##### 7.7.1.1.3	UPDATE <cipher>

This procedure shall be used for updating the <cipher> resource with data to encrypt or decrypt. It may be necessary to use this procedure several times until all data is transmitted.

Table 7.7.1.1.3-1: <cipher> UPDATE

| <cipher> UPDATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | All parameters defined in table 8.1.2-3 of [2] apply with the specific details for: To: contains M2M-SE-ID or M2M-AE-ID Content = attributes of the <cipher> resource as defined in clause 7.7.1 which need be updated |
| Processing at Originator before sending Request | According to clause 10.1.3. of [2] |
| Processing at Receiver | According to clause 10.1.3. of [2] |
| Information in Response message | According to clause 10.1.3. of [2] |
| Processing at Originator after receiving Response | According to clause 10.1.3. of [2] |
| Exceptions | According to clause 10.1.3. of [2] |

##### 7.7.1.1.4	DELETE <cipher>

This procedure shall be used for deleting a <cipher> resource.

Table 7.7.1.1.4-1: <cipher> DELETE

| <cipher> DELETE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | All parameters defined in table 8.1.2-3 of [2] apply with the specific details for:To: contains M2M-SE-ID or M2M-AE-ID |
| Processing at Originator before sending Request | According to clause 10.1.4.1 of [2] |
| Processing at Receiver | According to clause 10.1.4.1 of [2] |
| Information in Response message | According to clause 10.1.4.1 of [2] |
| Processing at Originator after receiving Response | According to clause 10.1.4.1 of [2] |
| Exceptions | According to clause 10.1.4.1 of [2] |

#### 7.7.1.2	<encrypt> Resource

The <encrypt> resource is a virtual resource because it does not have a representation. It is the child resource of a <cipher> resource. When a RETRIEVE request addresses the <encrypt> resource, the sensitiveData of the <cipher> resource is encrypted and the result shall be stored in calculatedData.

The <encrypt> resource inherits access control policies that apply to the parent <cipher> resource.

#### 7.7.1.3	<decrypt> Resource

The <decrypt> resource is a virtual resource because it does not have a representation. It is the child resource of a <cipher> resource. When a RETRIEVE request addresses the <decrypt> resource, the sensitiveData of the <cipher> resource is decrypted and the result shall be stored in calculatedData.

The <decrypt> resource inherits access control policies that apply to the parent <cipher> resource.

#### 7.7.1.4	<generateKey> Resource

The <generateKey> resource is a virtual resource because it does not have a representation. When a RETRIEVE request addresses the <generateKey> resource, the keyData attribute is filled with a key generated according the algorithm attrbute.

The <generateKey> resource inherits access control policies that apply to the parent resource.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 7.10	<algorithmSpecificParameter> Resource

The <algorithmSpecificParameter> contains parameter required for the different algorithm.

The <algorithmSpecificParameter> resource inherits the same access control policies of the parent <cipher> resource, and does not have its own accessControlPolicyIDs attribute.

The <algorithmSpecificParameter> resource is shown in figure 7.10-1.

Figure 7.10-1: <algorithmSpecificParameter> representation

Attributes in <algorithmSpecificParameter> are shown in table 7.10-1.

| Attributes of <algorithmSpecificParameter> | Multiplicity | RW/ RO/ WO | Description | <algorithmSpecificParameterAnnc> (MA/OA/NA) |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. | NA |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. | NA |
| resourceName | 1 | WO | This attribute is the name for the resource that is used for 'hierarchical addressing method' to represent the parent-child relationships of resources. | NA |
| parentID | 1 | RO | This attribute is the resourceID of the parent of this resource. | NA |
| expirationTime | 1 | RW | Time/date after which the resource will be deleted by the Hosting CSE. | NA |
| accessControlPolicyIDs | 0..1 (L) | RW | Is used to control access to the resource. If no accessControlPolicyIDs are provided at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute | NA |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. | NA |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. | NA |
| initialVector | 0..1 | RW | AES algorithms, except for ALG_AES_CMAC_128, in CBC mode expect a 16-byte parameter value for the initial vector(IV). | NA |
| nonce | 0..1 | RW | AEAD algorithms expect a value for the nonce | NA |
| associatedData | 0..1 | RW | The associated data for AEAD algorithm, which contains the data to be authenticated, but not encrypted. | NA |
| label | 0..1 | RW | "EXPORTER-oneM2M-Bootstrap" for TLS Key Export for Enrolment Key. "EXPORTER-oneM2M-Connection" for TLS Key Export for M2M Secure Connection Key. |  |

Table 7.7.1.5-1: Attributes of <algorithmSpecificParameter> resource

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 7.8.3	<connectionInstance> resource

The <connectionInstance> resource represents a data instance in the <secureConnection> resource.

The <connectionInstance> resource inherits the same access control policies of the parent <secureConection> resource, and does not have its own accessControlPolicyIDs attribute.

The services include the following:

- generation of key material within the secure environment that can be used for the establishment of a secure connection by the requesting entity (creator) outside of the secure environment

- acting as secure connection endpoint and sending the data provided by the requesting entity (creator) from within the secure environment with the key material generated and kept inside the secure environment

The <connectionInstance> resource is shown in figure 7.8.3-1.

Figure 7.8.3-1: <connectionInstance> representation

The <connectionInstance> resource shall contain the child resources specified in table 7.8.3-1.

Table 7.8.3-1: Child resources of <connectionInstance> resource

| Child Resources of <connectionInstance> | Child Resource Type | Multiplicity | Description | <connectionInstance Annc> Child Resource Types |
| --- | --- | --- | --- | --- |
| algorithmSpecificParameter | <algorithmSpecificParameter> | 0..1 | See clause 7.10 | None |
| connect | <connect> | 1 | See clause 7.8.5 | None |
| send | <send> | 1 | See clause 7.8.6 | None |

Attributes in <connectionInstance> are shown in table 7.8.3-2.

| Attributes of <connectionInstance> | Multiplicity | RW/ RO/ WO | Description | <connectionInstance Annc> (MA/OA/NA) |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. | NA |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. | NA |
| resourceName | 1 | WO | This attribute is the name for the resource that is used for 'hierarchical addressing method' to represent the parent-child relationships of resources. | NA |
| parentID | 1 | RO | This attribute is the resourceID of the parent of this resource. | NA |
| expirationTime | 1 | RW | Time/date after which the resource will be deleted by the Hosting CSE. | NA |
| accessControlPolicyIDs | 0..1 (L) | RW | Is used to control access to the resource. If no accessControlPolicyIDs are provided at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute | NA |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. | NA |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. | NA |
| destinationURI | 1 | RW | Specifies the end point to which the secure connection shall be established | NA |
| outgoingPayloadData | 0..1 | RW | Contains the data that has to be sent via the established secure connection | NA |
| incomingPayloadData | 0..1 | RO | Contains the data that has to be sent via the established secure connection | NA |
| negotiatedKey | 0..1 | RO | Contains the negotiated key e.g. the pairwiseE2EKey using TLS Exporter specification (RFC 5705). | NA |
| negotiatedCipherSuite | 0..1 | RO | Is the cipher suite negotiated between the Secure Environment and the remote entity | NA |

Table 7.8.3-2: Attributes of <connectionInstance> resource

### 7.8.4	<connectionInstance> Resource Procedures

#### 7.8.4.1	CREATE <connectionInstance>

This procedure shall be used for creating a <connectionInstance> resource.

Table 7.8.4.1-1: <connectionInstance> CREATE

| <connectionInstance> CREATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | All parameters defined in table 8.1.2-3 of [2] apply with the specific details for:To: contains M2M-SE-ID or M2M-AE-ID Content: : The resource content shall provide the information as defined in clause 7.8.3. |
| Processing at Originator before sending Request | According to clause 10.1.1.1.of [2] |
| Processing at Receiver | According to clause 10.1.1.1.of [2] |
| Information in Response message | All parameters defined in table 8.1.3-1 of [2] apply with the specific details for: • Content: Address of the created <connectionInstance> resource, according to clause 10.1.1.1.of [2] |
| Processing at Originator after receiving Response | According to clause 10.1.1.1. of [2] |
| Exceptions | According to clause 10.1.1.1. of [2] |

#### 7.8.4.2	RETRIEVE <connectionInstance>

This procedure shall be used for retrieving payload data from a communication partner or to retrieve the negotiated key.

Table 7.8.4.2-1: <connectionInstance> RETRIEVE

| <connectionInstance> RETRIEVE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | According to clause 10.1.2. of [2] with the specific details for: To: contains M2M-SE-ID or M2M-AE-ID |
| Processing at Originator before sending Request | According to clause 10.1.2. of [2] |
| Processing at Receiver | According to clause 10.1.2. of [2] |
| Information in Response message | All parameters defined in table 8.1.3-1 of [2] apply with specific details for: Content: Attributes of the <connectionInstance> resources as defined in clause 7.8.3. |
| Processing at Originator after receiving Response | According to clause 10.1.2. of [2] |
| Exceptions | According to clause 10.1.2. of [2] |

#### 7.8.4.3	UPDATE <connectionInstance>

This procedure shall be used for sending payload data via an established secure connection.

Table 7.8.4.3-1: <connectionInstance> UPDATE

| <connectionInstance> UPDATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | All parameters defined in table 8.1.2-3 of [2] apply with the specific details for: To: contains M2M-SE-ID or M2M-AE-ID Content = attributes of the <connectionInstance> resource as defined in clause 7.8.3 which need be updated |
| Processing at Originator before sending Request | According to clause 10.1.3. of [2] |
| Processing at Receiver | According to clause 10.1.3. of [2] |
| Information in Response message | According to clause 10.1.3. of [2] |
| Processing at Originator after receiving Response | According to clause 10.1.3. of [2] |
| Exceptions | According to clause 10.1.3. of [2] |

#### 7.8.4.4	DELETE <connectionInstance>

This procedure shall be used for deleting a <connectionInstance> resource. Deleting a <connectionInstance> resource closes an established secure connection between the originator (creator) and the destination.

Table 7.8.4.4-1: <connectionInstance> DELETE

| <connectionInstance> DELETE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | All parameters defined in table 8.1.2-3 of [2] apply with the specific details for: To: contains M2M-SE-ID or M2M-AE-ID |
| Processing at Originator before sending Request | According to clause 10.1.4.1 of [2] |
| Processing at Receiver | According to clause 10.1.4.1 of [2] |
| Information in Response message | According to clause 10.1.4.1 of [2] |
| Processing at Originator after receiving Response | According to clause 10.1.4.1 of [2] |
| Exceptions | According to clause 10.1.4.1 of [2] |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of Changes to References Section -------------

### -----------------------End of Changes to References  -------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

Figure is changed