| CHANGE REQUEST |
| --- |
| Meeting:* | SEC23 |
| Source:* | Datang |
| Date:* | 2016-05-15 |
| Contact:* | Wei Zhou, Datang, zhouwei@catt.cn Hui Xu, Datang, xuhui@catt.cn |
| Reason for Change/s:* | TS-0003 CR Role Based Access Control |
| CR against: Release* | 2 |
| CR against: WI* | Active WI MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003-V2.1.0 |
| Clauses/Sub Clauses* | 7.4 Role Based Access Control |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution proposes the role based authorization architecture and procedures.

This contribution is rewritten based on the contribution “ SEC-2016-0059R04-CR_for_Role_Based_Access_Control” that are discussed in TP 22 and SEC-ARC 22.2 joint meeting.

### -----------------------Start of change 1-------------------------------------------

## 7.4	Role Based Access Control

### 7.4.1	Role Based Access Control Architecture

Figure 7.4.1-1 provides a high level overview of the role based access control architecture in the oneM2M System. The entities related to role issuance and role based access control are described as follows:

- Authorization Authority: It is responsible for assigning roles to Originators through creating <role> and/or <token> resources in Role and/or Token Repositories.

- Role Repository: It is a CSE that is responsible for storing <role> resources.

- Token Repository: It is a CSE that is responsible for storing <token> resources.

- NOTE 1:	The arrows shown in the figure 7.4.1-1 are the logical relations among the entities and not the registration relations that form the real data paths.

- NOTE 2:	The functions of PDP and PIP are combined in the Hosting CSE for oneM2M Release 2.

# Figure 7.4.1-1. Role based access control architecture

The generic procedure of this architecture is described as follows:

Step 001:	An Originator applies for a role from an Authorization Authority.

Step 002:	The Authorization Authority checks if the applied role can be assigned to the Originator. If it is permitted, the Authorization Authority assigns the requested role to the Originator. A token that holds the assigned role may also be issued.

Step 003:	The Authorization Authority creates a <role> and/or <token> resource in a Role Repository and/or a Token Repository from which the Originator’s role assignment information can be retrieved.

Step 004:	The Originator may retrieve the assigned roles and/or tokens from Role and/or Token Repositories in order to get detailed information about the assigned roles and/or tokens.

Step 005:	The Originator sends an access request to the target resource in the Hosting CSE. The request shall contain the role information that may be the Role-IDs, Tokens or Token-IDs.

Step 006:	The Hosting CSE may send an access control decision request to a PDP.

Step 007:	The PDP may need to retrieve the Originator’s role assignment information according to the Role-IDs and/or Token-IDs from the Role and/or Token Repositories.

Step 008:	The PDP verifies the Originator’s roles and/or tokens, and then makes an access control decision according to the access control policies and roles.

NOTE 1:	Some steps described here may not be needed in some applications, e.g. if an Originator already has the role information from the Authorization Authority, it does not need to do the step 4.

### 7.4.2	Role Issuing Procedure

There are two ways to assign roles to an Originator.

- One way is to create a <role> resource that describes what role is assigned to the originator. The <role> resources are stored in role repositories from which the AEs and CSEs can retrieve <role> resources in order to get an Originator’s role assignment information.

- Another way is to issue a token that describes what role is assigned to the token holder (i.e. the Originator). The issued token may also be stored in a <token> resource in a token repository from which the issued token can be retrieved.

A <role> resource may also point to a <token> resource in which the token that holds the assigned role is stored through the tokenlink attribute.

The general procedure of issuing a role to an Originator is shown in the Figure 7.4.2-1 and described as follows:

# Figure 7.4.2-1: Procedure of issuing a role

- The Originator shall send a role application request via a <role> resource CREATE request to an Authorization Authority. In the request at least the Role-ID that the Originator wants to apply for shall be provided in the Content parameter.

- The Authorization Authority shall check if the applied role can be assigned to the Originator according to the role assignment policies that are however out of scope of present document. After passing the role assignment policy check, the Authorization Authority shall assign the role to the Originator through creating a <role> resource in a Role Repository. The Authorization Authority may also issue a token that holds the assigned role to the Originator. In this case a <token> resource shall be created in a Token Authority. The <role> resource creation and <token> resource creation are described in the following two steps.

- In case a token that holds the assigned role is issued to the Originator, the Authorization Authority shall create a <token> resource in a Token Repository. The <token> CREATE request shall provide the mandatory and optional attributes as specified in clause 9.6.39 of TS-0001 [1].

- The Authorization Authority shall create a <role> resource in a Role Repository. The <role> resource CREATE request shall provide the mandatory and optional attributes as specified in clause 9.6.38 of TS-0001 [1].

- The Authorization Authority shall return the result of role assignment information back to the Originator via a <role> resource creation response. The returned Content parameter in the response dependents on the setting of the Result Content parameter in the <role> resource CREATE request.

- The Originator may send a <role> resource retrieve request to a Role Repository in order to get the details of role assignment information.

- The Originator may send a <token> resource retrieve request to a Token Repository in order to get the details of token issuance information, including the issued token.

### 7.4.3	Role Based Access Control Procedure

The general procedure of using a role in an authorization process is shown in the Figure 7.4.3-1 and described as follows:

# Figure 7.4.3-1: Role based access control procedure

- The Originator shall include the applicable Role-IDs, Token-IDs or tokens  into the request sent to the Hosting CSE.

- In case of Role-IDs or Token-IDs, the Hosting CSE (acting the role of PIP) shall send a <role> or <token> resource retrieve request to the Role or Token Repository.

- The Role Repository or Token Repository shall return the attributes of <role> or <token> resource back to the Hosting CSE..

- The Hosting CSE (acting the role of PDP) shall verify the received roles and/or tokens, the verification shall include: if a role/token is issued by a valid Authorization Authority, if holder of the role/token is equal to the Originator, and if the role/token is still valid. Only valid roles/tokens shall be used for access control.

- The Hosting CSE (acting the role of PDP) shall evaluate the access request of the Originator using access control policies and/or Role-IDs for making an access control decision as described in clause 7.1.

- The Hosting CSE shall enforce the access control decision, i.e. either perform the resource access on behalf the Originator or deny the resource access.

- The Hosting CSE shall return the result of resource access back to the Originator.

### -----------------------End of change 1-------------------------------------------