| CHANGE REQUEST |
| --- |
| Meeting:* | SEC23 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2016-05-16 |
| Contact:* | As above |
| Reason for Change/s:* | Add stage 3 details for End-to-End Security of Primitives |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003 and 2.0.1 |
| Clauses/Sub Clauses* | * 2.1 Normative References. * New 8.4.3 “End-to-End-Security of Primitives Protocol Details” * New 10.x oneM2M Security data type definitions |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

ADD references

### -----------------------Start of change 1-------------------------------------------

### 8.4.3	End-to-End Security of Primitives (ESPrim) Protocol Details

#### 8.4.3.1	End-to-End Security of Primitives (ESPrim) Parameter Definitions

##### 8.4.3.1.1	originatorESPrimRandObject parameter definition

The structure of the originator2ERandObject parameter is shown in Table 8.4.3.1.1-1. This parameter is used in establishing sessionESPrimKey as part of End-to-End Security of Primitives (ESPrim), described in clause 8.4.2. The data type of the originatorESPrimRandObject parameter is specified in clause 10.x.3.2.

Table 8.4.3.1.1-1: Structure of the originatorESPrimRandObject parameter

| Element Path | Multiplicity | Description |
| --- | --- | --- |
| esprimRandID | 1 | An identifier for the originatorESPrimRandObject, assigned by the CSE or AE generating the originatorESPrimRandObject |
| esprimRandValue | 1 | A 128-bit randomly-generated value. |
| esprimRandExpiry | 1 | Time when the originatorESPrimRandObject expires |
| esprimKeyGenAlgID | 1 | The enumerated identifier of the algorithm selected for sessionESPrimKey generation by the CSE or AE generating the originatorESPrimRandObject |
| esprimProtocolAndAlgIDs | 1 | A list of enumerated identifiers for AEAD Algorithms supported by the CSE or AE generating the originatorESPrimRandObject |

##### 8.4.3.1.2	receiverESPrimRandObject parameter definition

The structure of the receiver2ERandObject parameter is shown in Table 8.4.3.1.2-1. This parameter is used in establishing sessionESPrimKey as part of End-to-End Security of Primitives (ESPrim), described in clause 8.4.2. The data type of the receiverESPrimRandObject parameter is specified in 10.x.3.3.

Table 8.4.3.1.2-1: Structure of the receiverESPrimRandObject parameter

| Element Path | Multiplicity | Description |
| --- | --- | --- |
| esprimRandID | 1 | An identifier for the receiverESPrimRandObject, assigned by the CSE or AE generating the receiverESPrimRandObject |
| esprimRandValue | 1 | A 128-bit randomly-generated value. |
| esprimRandExpiry | 1 | Time when the receiverESPrimRandObject expires. |
| esprimKeyGenAlgIDs | 1 | A list of enumerated identifiers for algorithms supported for sessionESPrimKey generation by the CSE or AE generating the receiverESPrimRandObject |
| esprimProtocolAndAlgIDs | 1 | A list of enumerated identifiers for AEAD Algorithms supported by the CSE or AE generating the receiverESPrimRandObject |

#### 8.4.3.2	ESPrim Object formatting and processing using the JWE Compact Serialization

Background: JSON Web Encryption (JWE) specified in RFC 7516 [RFC7516], provides a simple format for encrypting any data object.  Two JWE serializations are provided: a compact, URI-safe serialization, and a JSON serialization.

The JW End-to-End Security of Primitives (ESPrim)E Compact Serialization uses a small amount of JSON serialize a few parameters, but the necessary formatting and parsing can be easily encoded without generic tools for formatting or parsing JSON.

In the JWE Compact Serialization, a JWE is represented as the concatenation of five JWE parameters:

BASE64URL(UTF8(JWE Protected Header)) || ’.’ ||

BASE64URL(JWE Encrypted Key) || ’.’ ||

BASE64URL(JWE Initialization Vector) || ’.’ ||

BASE64URL(JWE Ciphertext) || ’.’ ||

BASE64URL(JWE Authentication Tag)

where BASE64URL(OCTETS) denotes the base64url encoding of OCTETS, per section 2 of the JSON Web Signature specification RFC 7515 [RFC7515].

NOTE: 	If OCTETS is an empty octet sequence, then RFC 7515 [RFC7515] defines BASE64URL(OCTETS) to be the empty string.

NOTE: 	The JWE Compact Serialization is not as flexible as the JWE JSON serialization, however the JWE compact serialization provides sufficient flexibility for ESPrim Objects. Moreover ease of formatting and parsing JWE Compact Serialization provides a simple solution for both XML and JSON representations of primitives

JWE Parameter definitions for ESPrim: Table 8.4.3.2-1, specifies these values of the five JWE parameters when the JWE Compact Serialization

Table 8.4.3.2-1: JWE Components used in ESPrim Objects

| JWE value | element type | Empty | Component Content |
| --- | --- | --- | --- |
| JWE Protected Header | JSON | Never | See Table 8.4.3.2-2 JWE Protected Header Parameters |
| JWE Encryption Key | Binary value | Always | This value is empty for the key management mode (used for ESPrim |
| JWE Initialization Vector | Binary value | Conditional | As per RFC 7516 [RFC7516] |
| JWE Ciphertext | Binary value | Never |  |
| JWE Authentication Tag | Binary value | Conditional |  |
| NOTE: whether these components are empty or not is conditional on the algorithm selected for encryption. |

Table 8.4.3.2-2 “JWE Protected Header Parameters” describes the parameters in the JWE Protected Header when using JWE for ESPRrim.

Table 8.4.3.2-2: JWE Protected Header Parameters

| Element path | Multiplicity for ESPrim | Purpose | Specification of element | Description of assigned value |
| --- | --- | --- | --- | --- |
| “alg” | 1 | Key management mode | [RFC7516] | “dir” indicating Direct Encryption. |
| “enc” | 1 | Encryption Algorithm |  | The options available here are the same as for ESData use of JWE. See clause 8.7.3 “ESData Protocol Details” |
| “kid” | 1 | Key identifier | [RFC7516] | Identifier for pairwiseESPrimKey |
| “cty” | 0..1 | Media type of the secured Content | [RFC7516] | Dictated by the serialization of the primitive (XML or JSON) selected by the Originator. |
| “ori” | 1 | Identify originators input to session key generation | Clause 8.4.3.1.1 | esprimRandID of the originatorESPrimRandObject used to generate sessionESPrimKey for this ESPrim Object. |
| “rri” | 1 | Identify receiver’s input to session key generation | Clause 8.4.3.1.2 | esprimRandID of the receiverESPrimRandObject used to generate sessionESPrimKey for this ESPrim Object. |
| “oro” | 0..1 | originatorESPrimRandObject | Clause 8.4.3.1.1 using JSON serialization | JSON representation of an originatorESPrimRandObject generated by the Originator. Sent only by the Originator. |
| “rro” | 0..1 | receiverESPrimRandObject | Clause 8.4.3.1.2 using JSON serialization | JSON representation of an receiverESPrimRandObject generated by the Receiver. Sent only by the Receiver. |

The following text provides further explanation of the parameters in the JWE Protected Header when using JWE for ESPRrim.

Recall that an ESPrim Object is formed by encrypting the inner primitive using the symmetric key sessionESPrimKey. The generation of sessionESPrimKey from a pairwiseESPrimKey, originatorESPrimRandObject and receiverESPrimRandObject is separate from the key management available through JWE – from the perpective of JWE, sessionESPrimKey is simply a secret symmetric key value shared between Originator and Receiver. JWE uses the Direct Encryption key management mode in this scenario. The JWE serialization will be required to transport the pairwiseESPrimKey identifier, the esprimRandIDs of the originatorESPrimRandObject identifier, and optionally a receiverESPrimRandObject or originatorESPrimRandObject  so that the Originator and Receiver can generate the correct sessionESPrimKey.

- The “alg” (Algorithm) JWE header parameter [RFC7516] shall be set to the value of “dir” to indicate Direct Encryption key management mode.

- The “enc” (Encryption Algorithm) JWE header parameter [RFC7516] may be selected by the sender of the ESPrimObject. The encryption algorithm shall agrees with the esprimProtocolAndAlgIDs in identified originatorESPrimRandObject and the esprimProtocolAndAlgIDs in the identified receiverESPrimRandObject.

- The “kid” (Key ID) JWE header parameter [RFC7516] shall be set to the pairwiseESPrimKey identifier.

- The “cty” shall identify the media type of the representation (JSON or XML) of the inner primitive.

- The esprimRandIDs of the originatorESPrimRandObject and receiverESPrimRandObject shall be communicated in the “ori” (Originator Rand ID) and “rri” (Receiver Rand ID) parameters included in the JWE Protected header. These parameters are specific to oneM2M and shall conform to the definition of the esprimRandID in clauses 8.4.3.1.2 and  8.4.3.1.2.

- The originator may include a originatorESPrimRandObject in an “oro” (Originator Rand Object) parameter – either at the beginning of an ESPrim session or to refresh the session keys “in-band” during an existing ESPrim session. In the former case, “ori” shall match the esprimRandID in the originatorESPrimRandObject, but this restriction does not apply in the latter case. This parameter is defined in clauses 8.4.2 and 8.4.3.1.1, and the JSON representation shall be used.

- The receiver may include a receiverESPrimRandObject in an “rro” (Receiver Rand Object) – either at the to refresh the session keys “in-band” during an existing ESPrim session. This parameter is defined in clauses 8.4.2 and 8.4.3.1.1, and the JSON representation shall be used.

Forming an ESPrim Object: The inner primitive representation shall be encrypted as specified for message encryption in [RFC7516], with the following clarification

- The JWE Protected Header shall be composed as described above.

  - The Content Encryption Key (CEK) shall be the sessionESPrimKey generated using the pairwiseESPrimKey, originatorESPrimRandObject and receiverESPrimRandObject identified in the JWE Protected Header.

- The plaintext shall be the inner primitive representation.

- The JWE Initialization Vector, JWE Ciphertext and JWE Authentication Tag shall be generated from the Protected JWE Header, the plaintext and CEK as specified in RFC 7516 [RFC7516], according to the identified encryption algorithm

- The JWE Compact Serialization shall be composed from the JWE parameters.

The ESPrim Object is the JWE Compact Serialization.

Processing an ESPrim Object: The JWE Compact Serialization shall be processed as specified for message decryption in [RFC7516], with the following clarification

- The JWE Protected Header shall be composed as described above.

  - If originatorESPrimRandObject or receiverESPrimRandObject is included, then these shall be recorded.

  - The Content Encryption Key (CEK) shall be the sessionESPrimKey generated using the pairwiseESPrimKey, originatorESPrimRandObject and receiverESPrimRandObject identified in the JWE Protected Header. The generation of SessionESPrimKey is specified in clause 8.4.2.

- The plaintext shall be generated from the JWE Initialization Vector, JWE Ciphertext, JWE Authentication Tag  and CEK as specified in RFC 7516 [RFC7516], according to the identified encryption algorithm.

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2  (new clause)---------------

## 10.x oneM2M Security data type definitions

### 10.x.1	oneM2M Security simple data types

Table 6.3.3-1 describes oneM2M-security-specific simple data type definitions. XML Schema data type definitions for these data types can be found in the XSD file called CDT-commonTypes-v2_4_0.xsd.

The types in table 10.x.1 are either:

- Atomic data types derived from XML Schema data types by restrictions other than enumeration

- List data types constructed from other XML Schema or oneM2M-defined atomic data types.

The oneM2M-defined enumeration data types are defined in clause 10.x.2.

Table 6.3.3-1: oneM2M Simple Data Types

| XSD type name | Type Name | Examples | Description |
| --- | --- | --- | --- |

### 10.x.2	oneM2M Security Enumeration data types

#### 10.x.2.1	Introduction

The oneM2M-Security Enumeration Types are extensions of the oneM2M Enumeration Types defined in TS-0004 [4].

##### 10.x.2.2	m2msec:esprimKeyGenAlgID

Used in m2msec:receiverESPrimRandObject and m2m:originatorESPrimRandObject.

Table 10.x.2.2.1-1: Interpretation of esprimKeyGenAlgID

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | sessionESPrimKey Key Generation Algorithm 1 |  |
| NOTE: Further sessionESPrimKey Key Generation Algorithms are anticipated to be added in the future. |

##### 10.x.2.3 m2msec:esprimProtocolAndAlgID

Used in m2msec:receiveEr2ERandObject and m2msec:originatorESPrimRandObject.

NOTE: This enumeration uses a structure with two identifiers separated by the ‘-‘ character. The most significant numeral identifies an object security technology (that is, a protocol) such as XML Encryption v1.1 [XML-ENCv1.1] or JSON Web Encryption (JWE) [RFC7516]. The least significant numeral identifies an Authenticated Encryption option for that object security technology.

Table 10.x.2.2.3-1: Interpretation of esprimProtocolAndAlgID

| Value | Interpretation | Note |
| --- | --- | --- |
| 0-0 | XML-ENCv1.1 with AES128-GCM | AES GCM using 128-bit key. See [XML-ENCv1.1] |
| 0-1 | XML-ENCv1.1 with AES192-GCM | AES GCM using 192-bit key. See [XML-ENCv1.1] |
| 0-2 | XML-ENCv1.1 with AES256-GCM | AES GCM using 256-bit key. See [XML-ENCv1.1] |
| 1-0 | JWE with “enc” = “A128CBC-HS256” | AES_128_CBC_HMAC_SHA_256. See [RFC7516, RFC7518] |
| 1-1 | JWE with “enc” = “A192CBC-HS256” | AES_192_CBC_HMAC_SHA_256. See [RFC7516, RFC7518] |
| 1-2 | JWE with “enc” = “A256CBC-HS256” | AES_256_CBC_HMAC_SHA_256. See [RFC7516, RFC7518] |
| 1-3 | JWE with “enc” = “A128GCM” | AES GCM using 128-bit key. See [RFC7516, RFC7518] |
| 1-4 | JWE with “enc” = “A192GCM” | AES GCM using 192-bit key See [RFC7516, RFC7518] |
| 1-5 | JWE with “enc” = “A256GCM” | AES GCM using 256-bit key. See [RFC7516, RFC7518] |

### 10.x.3	oneM2M Security Complex data types

#### 10.x.3.1	Introduction

The present clause defines structured information for specific use in oneM2M security features.  These types are defined to be xs:sequence complex types, unless specified otherwise. XML Schema data type definitions for these data types can be found in the XSD file called  CDT-commonTypes-v2_4_0.xsd.

#### 10.x.3.2	m2msec:originatorESPrimRandObject

Used for originatorESPrimRandObject parameter in End-to-End Security of Primitives.

Table 10.x.3.2-1: Type Definition of m2m:receiverESPrimRandObject

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| esprimRandID | xs:NCName | 1 |  |
| esprimRandValue | xs:NCName | 1 |  |
| esprimRandExpiry | m2m:absRelTimestamp | 1 | See clause 10.x.1 |
| esprimKeyGenAlgIDs | List of m2msec:esprimKeyGenAlgID | 1 | See clause 10.x.2.2 |
| esprimProtocolAndAlgIDs | List of m2msec:esprimProtocolAndAlgID | 1 | See clause 10.x.2.3 |

#### 10.x.3.3	m2msec:receiverESPrimRandObject

Used for receiverESPrimRandObject parameter in End-to-End Security of Primitives.

Table 10.x.3.3-1: Type Definition of m2m:receiverESPrimRandObject

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| esprimRandID | xs:NCName | 1 |  |
| esprimRandValue | xs:NCName | 1 |  |
| esprimRandExpiry | m2m:absRelTimestamp | 1 | See clause 10.x.1 |
| esprimKeyGenAlgID | m2msec:esprimKeyGenAlgID | 1 | See clause 10.x.2.2 |
| esprimProtocolAndAlgIDs | List of m2msec:esprimProtocolAndAlgID | 1 | See clause 10.x.2.3 |

### -----------------------Start of change 2  (new clause)---------------

### ------------Add the following normative references to clause 2.1  -------------

[XML-ENCv1.1]	W3C Recommendation “XML Encryption Syntax and Processing v1.1”, 2013, http://www.w3.org/TR/xmlenc-core1/

[RFC7516]	IETF RFC 7516: “JSON Web Encryption (JWE)”, 2015

[RFC7518]	IETF RFC 7518: “JSON Web Algorithms (JWA)”, 2015

### ------------End of changes  to clause 2.1  -------------