| CHANGE REQUEST |
| --- |
| Meeting:* | SEC 23.4 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2016-06-28 |
| Contact:* | As above |
| Reason for Change/s:* | Provides the reference point between an CSE/AE and a MEF or MAF, reusing oneM2M primitives. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003 and 2.2.0 |
| Clauses/Sub Clauses* | New clause “TEF Interface” |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

There is a need for a protocol for request/response exchanges with MEF and MAF.

The authors originally proposed a specific protocol for the MAF interface in SEC-2016-0128, but it made little sense to specify an additional protocol for the MAF interface.

This CR proposes using a simplified version of the oneM2M primitives used on the Mcc/Mca reference points with a separates set of resources and limited set of parameters. The present contribution makes SEC-2016-0128 obsolete.

### -----------------------Start of change 1-------------------------------------------

# X.	TEF Interface

## X.1	Introduction to the TEF Interface

The TEF Interface is a simple variant of the Mcc/Mca reference points specifying the interaction of CSEs and AEs with the TEFs used for enrolment (an MEF) and authentication (an MAF). The present document does not specify the operation and management of the TEF required to support these procedures.

The TEF Interface specification has no impact on the specifications in TS-0001 [1] and TS-0004 [4].

The TEF Interface incorporates the following concepts from the Mcc/Mca

- The concept of operations acting on resources: The present TEF Interface supports only CREATE and RETRIEVE operations.

NOTE: The present specification does not specify how resources are updated or deleted. Future versions of the TEF Interface may include support for updating or deleting resource.

- The resource addressing from Mcc/Mca is used.

- The resources contain the universal attributes (TS-0001 [1])

The TEF Interface differs from Mcc/Mca in the following ways:

- The TEF Client can only communicates directly with the TEF – there are no transited CSE. Only Blocking Mode communication method is supported.

- None of the mcc/mca resource definitions are used.

  - Access management is no longer specified by <accessControlPolicy> resources. A separate mechanism is specified for access control.

  - The <subscription> resource and NOTIFY operations are not supported.

  - There is no AE registration or CSE registration.

  - There are no announced resources.

The hierarchy of resources is very simple.

- <TEF> resource type is the base resource of the TEF. This resource is implicitly created by the TEF.

  - <enrolment> resource contains information about the TEF Client’s (AE or CSE)  enrolment to an M2M SP or M2M Trust Enabler

    - <mgmtObj> specializations configuring security-related information to the TEF Client. These are created by the M2M SP or M2M Trust Enabler. These <mgmtObj> specializations are specified in the oneM2M Device Configuration TS-0022 [DevCfgTS]

    - <symmetricKey> resources created by the TEF Client, containing symmetric keys for retrieval by another TEF Client(s) or a MAF.

## X.2	TEF Interface Overview

This TEF Interface overview is based on the specification in clause 6 of oneM2M TS-0004 [4].

The resources use the M2M-SP-ID, App-ID, AE-ID and CSE-ID as defined in 6.2.3 of [14]. M2M Trust Enablers (MTEs) are identified using an M2M-SP-ID.

Resources are addressed as specified in clause 6.2.4 in [4].

Common data types are inherited from clause 6.3 [4], although only a few data types are used.

Table X.2-1 lists the request primitive parameters inherited from clause 6.4.1 [4]; the data types of these parameters is unchanged.

Table X.2-1: TEF Interface request primitive parameters

| Parameter | Multiplicity | Notes |
| --- | --- | --- |
| Operation | 1 |  |
| To | 1 |  |
| From | 0..1 |  |
| Request Identifier | 1 |  |
| Resource Type | 0..1 |  |
| Content | 1 |  |
| Result Content | 0..1 |  |
| Filter Criteria | 0..1 |  |

Table X.2-2 lists the response primitive parameters inherited from clause 6.4.2 [4]; the data types of these parameters is unchanged.

Table X.2-2: TEF Interface response primitive parameters

| Parameter | Multiplicity | Notes |
| --- | --- | --- |
| Response Status Code | 1 |  |
| Request Identifier | 1 |  |
| Content | 0..1 |  |

Editor’s note: Unclear which of the resource data types in clause 6.5 [4] are supported.

Table X.2-3 lists the response status codes from clause 6.6 [4] which are supported by the TEF Interface.

Table X.2-3: Response status codes supported by the TEF Interface

| Response status codes | Interpretation |
| --- | --- |
| 2000 | OK |
| 2001 | CREATED |
| 4000 | BAD_REQUEST |
| 4004 | NOT_FOUND |
| 4005 | OPERATION_NOT_ALLOWED |
| 4103 | ACCESS_DENIED |
| 5000 | INTERNAL_SERVER_ERROR |

Editor’s note: Unclear which of the oneM2M specific MIME media types from clause 6.6 [4] are supported.

Virtual resources (clause 6.8 [4]) are not supported by the TEF Interface.

## X.3	TEF Processing and Representation of Primitives

This clause is based on the specification in clause 7 and 8 of oneM2M TS-0004 [4].

The TEF Interface request primitive format conforms to clause 7.2.1.1 [4], constrained to the Create and Retrieve operations, with request parameters listed in Table X.2-1.

The TEF Interface response primitive format conforms to clause 7.2.1.2 [4], constrained to the Create and Retrieve operations, with request parameters listed in Table X.2-2.

The TEF Interface generic resource request procedure for originators and receivers conforms to clauses 7.2.2.1 and 7.2.2.2 of [4], with the following clarification:

- The TEF Client acts as the originator, and the TEF acts as the receiver and hosting CSE.

- The operation shall be one of the Create and Retrieve operations,

- The request and response parameters shall conform to Table X.2-1 and Table X.2-2.

- “Blocking Mode” communication method shall be used.

- Recv-6.3: “Check authorization of the Originator” shall be replaced with the process in clause YYYY “TEF Interface Authorization”

The originator actions, receiver actions and Hosting CSE actions conform to clause 7.3 [4], with clause 7.3.3.17 [4] replaced by the process in clause YYYY “TEF Interface Authorization”.

The management common operations in clause 7.3.4 [4] do not apply to the TEF Interface.

The resource-type-specification conventions apply to the specification in clause XXXXX “Resource Type-specification procedures and definitions”, but the remainder of clause 7.4 [4] does not apply to the TEF Interface.

Clause 7.5.1 [4] (regarding Notification) does not apply to the TEF Interface. Elements contained in the Content primitive parameter conform to clause 7.5.2 [4], constrained to the Create and Retrieve operations.

The representation of TEF Interface primitives in data transfer conforms to Clause 8. Clause AAAA contains additional short names specific to the TEF Interface.

## X.4	Resource definitions

### X.4.1 Resource Type <TEF>

The <TEF> resource shall represent a TEF.

The <TEF> resource shall contain the child resources specified in table X.4.1-1.

Table X.4.1-1: Child resources of <TEF> resource

| Child Resources of <TEF> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <enrolment> | 0..n | See clause X.4.2 |

The <TEF> resource shall contain no attributes.

### X.4.2 Resource Type <enrolment>

The <enrolment> resource shall represent a TEF Client enrolled with an M2M SP or M2M Trust Enabler (MTE).

NOTE: A single TEF Client may be enrolled with at most one M2M SP and any number of MTEs (typically enabling end-to-end security to TEF Clients outside the TEF Client’s M2M SP’s domain). Consequently, a TEF Client may be associated with multiple <enrolment> resources on multiple TEFs.

The <enrolment> resource shall contain the child resources specified in table X.4.2-1.

Table X.4.2-1: Child resources of <enrolment> resource

| Child Resources of <TEF> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <symmetrickey> | 0..n | See clause X.4.3 |
| [variable] | <mgmtObj> | 0..n | Management objects used in device configuration [DevCfgTS] |

The <enrolment> resource shall contain the attributes specified in table X.4.2-2.

Table X.4.2-2: Attributes of <enrolment> resource

| Attributes of <serviceSubscribedAppRule> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceID | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceName | 1 | RO | See clause 9.6.1.3 of [1]. |
| parentID | 1 | RO | See clause 9.6.1.3 of [1]. |
| expirationTime | 1 | WO | See clause 9.6.1.3 of [1]. |
| creationTime | 1 | WO | See clause 9.6.1.3 of [1]. |
| fqdn | 1 | WO | FQDN of the M2M SP or MTE associated with this enrolment |
| AE-ID | 0..1 | WO/RO | AE-ID of the TEF Client when the TEF Client is a AE |
| CSE-ID | 0..1 | WO/RO | CSE-ID of the TEF Client when the TEF Client is a CSE |
| credentialID | 1 | RO | CredentialID of the credential used to authenticate the TEF Client to the TEF. Assigned by the TEF |

### X.4.3 Resource Type <symmetricKey>

The <symmetricKey> resource shall represent a symmetric key that the TEF Client has established with the TEF for distributing to authorized Targets. The TEF Client provides list of authorized Targets when the resource is created – the present document does not specify how the TEF associates the list with the resource. The TEF, is coordination with the M2M SP or MTE, can modify the list of authorized Targets and the time of expiry.

The <symmetricKey> resource shall contain no child resources.

The <symmetricKey> resource shall contain the attributes specified in table X.4.3-1.

Table X.4.3-1: Attributes of <symmetricKey> resource

| Attributes of <serviceSubscribedAppRule> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceID | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceName | 1 | RO | See clause 9.6.1.3 of [1]. |
| parentID | 1 | RO | See clause 9.6.1.3 of [1]. |
| expirationTime | 1 | WO | See clause 9.6.1.3 of [1]. |
| creationTime | 1 | WO | See clause 9.6.1.3 of [1]. |
| relKeyID | 1 | RO | To do |
| SUID | 1 | WO | To do |
| keyValue | 1 | WO/RO | To do |

## X.5	TEF Interface resource-type specific procedures and definitions

### X.5.1 Resource Type <TEF>

#### X.5.1.1 Introduction

A <TEF> resource shall represent a TEF. This <TEF> resource shall be the root for all the resources that are residing on the TEF.

The <TEF> resource has no attributes.

Table X.5.1.1-1: Child resources of <TEF> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to in Resource Type Definition |
| --- | --- | --- | --- |
| <enrolment> | [variable] | 0..n | Clause X.5.2 |

#### X.5.1.2 <TEF> resource specific procedures on Create and Retrieve operations

##### X.5.1.2.1 Create

Originator:

The <TEF> resource shall not be created via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

If the request is received, the Receiver CSE shall execute the following steps in order.

- "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

- "Send the Response primitive".

##### X.5.1.2.2 Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1 of [4] with clarified discussed in clause X.3.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [4] with clarified discussed in clause X.3, and with following difference regarding access control.

Editor’s note: difference regarding access control needs completing.

### X.5.2 Resource Type <enrolment>

#### X.5.2.1 Introduction

A <enrolment> resource shall represent a TEF Client (AE or CSE) enrolled with an M2M Service Provider or M2M Trust Enabler for whom the TEF is acting as MEF or MAF. A <enrolment> resource shall be a child resource of the TEF’s <TEF> resource.

Table X.5.2.1-1: Universal/Common Attributes of <enrolment> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create |
| @resourceName | NP |
| resourceType | NP |
| resourceID | NP |
| parentID | NP |
| creationTime | NP |
| expirationTime | O |

Table X.5.2.1-2: Resource Specific Attributes of <enrolment> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create |  |  |
| provider | M | FQDN Editors’note: ask PRO | No default |
| AE-ID | O | m2m:ID | No default |
| CSE-ID | O | m2m:ID | No default |
| credentialID | NP | sec:credentialID Editors’ note: to define |  |

Table X.5.2.1-1: Child resources of <enrolment> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to in Resource Type Definition |
| --- | --- | --- | --- |
| <symmetricKey> | [variable] | 0..n | Clause X.5.3 |
| <mgmtObj> | [variable] | 0..n | See [DevCfgTS] |

#### X.5.2.2 <enrolment> resource specific procedures on Create and Retrieve operations

##### X.5.2.2.1 Create

Originator:

No change from the generic procedures in clause 7.2.2.1 of [4] with clarified discussed in clause X.3.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [4] with clarified discussed in clause X.3, and with following difference regarding access control.

Editor’s note: difference regarding access control needs completing.

##### X.5.1.2.1 Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1 of [4] with clarified discussed in clause X.3.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [4] with clarified discussed in clause X.3, and with following difference regarding access control.

Editor’s note: difference regarding access control needs completing.

### X.5.3 Resource Type <symmetricKey>

#### X.5.3.1 Introduction

A <symmetricKey> resource shall represent a TEF Client (AE or CSE) enrolled with an M2M Service Provider or M2M Trust Enabler for whom the TEF is acting as MEF or MAF. A <symmetricKey> resource shall be a child resource of an <enrolment> resource.

Table X.5.3.1-1: Universal/Common Attributes of <symmetricKey>resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create |
| @resourceName | NP |
| resourceType | NP |
| resourceID | NP |
| parentID | NP |
| creationTime | NP |
| expirationTime | M |

Table X.5.3.1-2: Resource Specific Attributes of <symmetricKey>  resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create |  |  |
| relKeyID | NP | sec:relKeyID Editor’s note: to define. | No default |
| SUID | M | m2m:suid | No default |
| keyValue | O | xs:base64binary | No default |

The <symmetricKey> resource shall contain no child resources.

#### X.5.3.2 <symmetricKey> resource specific procedures on Create and Retrieve operations

##### X.5.3.2.1 Create

Originator:

No change from the generic procedures in clause 7.2.2.1 of [4] with clarified discussed in clause X.3.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [4] with clarified discussed in clause X.3, and with following difference regarding access control.

Editor’s note: difference regarding access control needs completing.

##### X.5.1.2.1 Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1 of [4] with clarified discussed in clause X.3, and with following difference regarding generation of the keyValue when not explicitly provided by the TEF Client.

Editor’s note: generation of keyValue needs completing.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [4] with clarified discussed in clause X.3, and with following difference regarding access control and generation of the keyValue when not explicitly provided by the TEF Client

Editor’s note: difference regarding access control needs completing.

Editor’s note: generation of keyValue needs completing.