| CHANGE REQUEST |
| --- |
| Meeting:* | SEC 24 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2016-07-10 |
| Contact:* | As above |
| Reason for Change/s:* | Provides the reference point between a CSE/AE and a MEF or MAF, reusing oneM2M primitives. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003 and 2.3.0 |
| Clauses/Sub Clauses* | New clause “TEF Interface” |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

There is a need for a protocol for request/response exchanges with MEF and MAF.

The authors originally proposed a specific protocol for the MAF interface in SEC-2016-0128, but it made little sense to specify an additional protocol for the MAF interface.

This CR proposes using a simplified version of the oneM2M primitives used on the Mcc/Mca reference points with a separates set of resources and limited set of parameters. The present contribution makes SEC-2016-0128 obsolete.

R01 delta from R00

- Added support for Update and Delete operations

- Added further details.

- The <symmtericKey> resource is renamed to <symmKeyReg> (Symmetric key registration), since it includes the registered metadata in addition to the value of the symmetric key.

- Changed hierarchy, <symmKeyRegg> is no longer a child of <tefClientReg>, and the resourceName is used as the relative part of the identifier of the symmetric key. This allows constructing the resource address directly from the symmetric key identifier, whereas previously a filtered retrieve would have been required.

- Added the notion of the administrating stakeholder (M2M SP or M2M Trust Enabler), who authorizes creation and updating of resources. In particular, the administrating stakeholder can change the list of authorized targets who may retrieve the registered key. The FQDN of the administrating stakeholder is included in the <tefClientReg> and <symmKeyReg> resources

- Added the universal attributes to all resources

- Used the creator attribute to record the identifier of the Source TEF Client.

R02 delta from R01

- Added some introductory text on administrating stakeholders

- Minor corrections suggested during SEC 23.5.

- Corrected values in some “Request Optionality” and “RW/RO/WO” columns.

### -----------------------Start of change 1-------------------------------------------

# X.	TEF Interface

## X.1	Introduction to the TEF Interface

The TEF Interface is a simple variant of the Mcc/Mca reference points specifying the interaction of CSEs and AE s with TEFs used for enrolment (an MEF) and authentication (an MAF), acting on behalf of an administrating stakeholder such as an M2M SP or third party M2M Trust Enabler (MTE) . The present document does not specify the operation and management of the TEF required to support these procedures.

The CSEs and AEs interacting with the TEF are called TEF Clients. The interface can also be used by another TEF using the services of the TEF and an administrating stakeholder, although it is assumed that the TEF will provide separate APIs to other TEFs and administrating stakeholders.

The administrating stakeholder authorizes the TEF’s services to TEF clients, and oversee authorizing the distribution of symmetric keys. A TEF may provide its services on behalf of multiple administrating stakeholders. A TEF Client may be associated with multiple administrating stakeholders, each administrating the use of the TEF within a different scope.

NOTE 1: 	The administrating stakeholder could be an M2M SP administrating the registration and distribution of credentials used for SAEFs and ESPrim within the M2M SP’s Domain.

NOTE 2:	The administrating stakeholder could be an MTE administrating the registration and distribution of credentials for ESPrim and ESData to MAF Clients belonging to a particular Application Service Provider, where the MAF Clients could be distributed over multiple M2M SP domains.

The TEF Interface specification has no impact on the specifications in TS-0001 [1] and TS-0004 [4]. However, the TEF Interface uses much of the specification in TS-0004 [4] and in particular allows use of the HTTP binding in TS-0008 [TS0008], the CoAP binding in TS-0009 [TS0009] and the WebSocket binding in TS-0020 [TS0020].

NOTE: 	The MQTT binding in TS-0010 [TS0010] is not suitable for the TEF Interface, because the TEF Interface assumes a TLS or DTLS connection from the TEF Client to the TEF – which is not possible using the MQTT binding

The TEF Interface incorporates the following concepts from the Mcc/Mca reference points:

- The concept of operations acting on resources.

- The resource addressing from Mcc/Mca is used.

- The universal attributes and some common attributes of resources.

The TEF Interface differs from Mcc/Mca in the following ways:

- The TEF Client can only communicate directly with the TEF – there are no transited CSE. Only Blocking Mode communication method is supported.

- None of the resource types applicable on Mcc/Mca are used.

  - Access control decisions use simple access control list for Retrieve access, and <accessControlPolicy> resources are not used for resources hosted by the TEF. A consequence of this is that the accessControlPolicyIDs attributes are not needed in the resources hosted by the TEF.

  - The <subscription> resource and NOTIFY operations are not supported.

  - There is no AE registration or CSE registration, but a similar process where a TEF Client creates a <tefClientReg> (TEF Client registration record) resource on the TEF.

  - There are no announced resources.

The hierarchy of resources hosted by a TEF shall be as follows:

- <TEF> resource type is the structural root for all the resources that are residing on a TEF. This resource is implicitly created by the TEF and uses the fixed resource name “tef” and contains following child resources:

  - <tefClientReg> resource. It confirms the TEF Client’s (AE or CSE)  registration to an administrating stakeholder, and can contain configuration information to be returned to the TEF Client.

  - <symmKeyReg> resources. It is created by the TEF Client, and contains symmetric keys for retrieval by another TEF Client(s) or another TEF.

## X.2	TEF Interface Overview

This TEF Interface overview is based on the specification in clause 6 of oneM2M TS-0004 [4].

Identifiers such as M2M-SP-ID, AE-ID and CSE-ID as defined in 6.2.3 of [14] also apply to the TEF Interface. M2M Trust Enablers (MTEs) are identified using an M2M-SP-ID.

Resources are addressed as specified in clause 6.2.4 in [4].

Common data types applicable to the TEF Interface are inherited from clause 6.3 [4].

Table X.2-1 and X.2-2 list the request and response primitive parameters inherited from clauses 6.4.1 and 6.4.2 in  [4], respectively; the data types of these parameters are unchanged.

NOTE:	All other optional request and response primitive parameters defined in clause 6.4.1 [4] are not used on the TEF Interface.

Table X.2-1: TEF Interface request primitive parameters

| Parameter | Multiplicity | Notes |
| --- | --- | --- |
| Operation | 1 |  |
| To | 1 |  |
| From | 0..1 |  |
| Request Identifier | 1 |  |
| Resource Type | 0..1 |  |
| Content | 0..1 |  |
| Result Content | 0..1 |  |

Table X.2-2: TEF Interface response primitive parameters

| Parameter | Multiplicity | Notes |
| --- | --- | --- |
| Response Status Code | 1 |  |
| Request Identifier | 1 |  |
| Content | 0..1 |  |

Data types associated with resources applicable to the TEF Interface are defined in clause X.4.

Table X.2-3 lists the response status codes from clause 6.6 [4] which are supported by the TEF Interface.

Table X.2-3: Response status codes supported by the TEF Interface

| Response status codes | Interpretation |
| --- | --- |
| 2000 | OK |
| 2001 | CREATED |
| 2002 | DELETED |
| 2004 | UPDATED |
| 4000 | BAD_REQUEST |
| 4004 | NOT_FOUND |
| 4005 | OPERATION_NOT_ALLOWED |
| 4103 | ACCESS_DENIED |
| 5000 | INTERNAL_SERVER_ERROR |

Editor’s note: Unclear which, if any, of the oneM2M specific MIME media types from clause 6.7 [4] are supported.

Virtual resources (clause 6.8 [4]) are not supported by the TEF Interface.

## X.3	TEF Processing and Representation of Primitives

This clause is based on the specification in clause 7 and 8 of oneM2M TS-0004 [4].

The TEF Interface request primitive format conforms to clause 7.2.1.1 [4], constrained to the CRUD operations, with request parameters listed in Table X.2-1.

The TEF Interface response primitive format conforms to clause 7.2.1.2 [4], constrained to the CRUD operations, with response parameters listed in Table X.2-2.

The TEF Interface generic resource request procedure for originators and receivers conforms to clauses 7.2.2.1 and 7.2.2.2 of [4], with the following clarification:

- The TEF Client acts as the originator, and the TEF acts as the receiver and hosting CSE.

- The operation shall be one of the CRUD operations.

- The request and response parameters shall conform to Table X.2-1 and Table X.2-2.

- “Blocking Mode” communication method shall be used.

- The step Recv-6.3: “Check authorization of the Originator” is replaced by the authorization processes described in the TEF Interface resource-type specific procedures in clause X.5.

The originator actions, receiver actions and Hosting CSE actions conform to clause 7.3 [4], with clause 7.3.3.17 [4] replaced by the authorization processes described in the TEF Interface resource-type specific procedures in clause X.5.

The management common operations in clause 7.3.4 [4] do not apply to the TEF Interface.

The resource-type-specification conventions apply to the specification in clause X.5, but the remainder of clause 7.4 [4] does not apply to the TEF Interface.

Clause 7.5.1 [4] (regarding Notification) does not apply to the TEF Interface. Elements contained in the Content primitive parameter conform to clause 7.5.2 [4].

The representation of TEF Interface primitives in data transfer conforms to Clause 8. Clause AAAA contains additional short names specific to the TEF Interface.

Editor’s note: a table of short names is required.

## X.4	Resource definitions

### X.4.1 Resource Type <TEF>

The <TEF> resource shall represent a TEF.

The <TEF> resource shall contain the child resources specified in table X.4.1-1.

Table X.4.1-1: Child resources of <TEF> resource

| Child Resources of <TEF> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <tefClientReg> | 0..n | See clause X.4.2 |
| [variable] | <symmKeyReg> | 0..n | See clause X.4.3 |

The <TEF> resource shall contain the attributes specified in table X.4.1-2.

Table X.4.1-2: Attributes of <TEF> resource

| Attributes of <TEF> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceID | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceName | 1 | RO | See clause 9.6.1.3 of [1]. Shall be fixed to “tef”. |
| expirationTime | 1 | RO | See clause 9.6.1.3 of [1]. |
| creationTime | 1 | RO | See clause 9.6.1.3 of [1]. |

### X.4.2 Resource Type <tefClientReg>

The <tefClientReg> resource shall represent a TEF Client enrolled with an M2M SP or M2M Trust Enabler (MTE).

NOTE: 	A single TEF Client may be enrolled with at most one M2M SP and any number of MTEs (typically enabling end-to-end security to TEF Clients outside the TEF Client’s M2M SP’s domain). Consequently, a TEF Client may be associated with multiple <tefClientReg> resources on multiple TEFs.

The <tefClientReg> resource shall contain the child resources specified in table X.4.2-1.

Table X.4.2-1: Child resources of <tefClientReg> resource

| Child Resources of <tefClientReg> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <mgmtObj> | 0..n | Management objects used in device configuration [DevCfgTS] |

The <tefClientReg> resource shall contain the attributes specified in table X.4.2-2.

Table X.4.2-2: Attributes of <tefClientReg> resource

| Attributes of <tefClientReg> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceID | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceName | 1 | RO | See clause 9.6.1.3 of [1]. |
| parentID | 1 | RO | See clause 9.6.1.3 of [1]. |
| expirationTime | 1 | WO | See clause 9.6.1.3 of [1]. |
| creationTime | 1 | RO | See clause 9.6.1.3 of [1]. |
| labels | 1 | RW | See clause 9.6.1.3 of [1]. |
| creator | 1 | WO | See clause 9.6.1.3 of [1]. |
| fqdn | 1 | WO | FQDN of the M2M SP or MTE who is the administrating stakeholder of this enrolment |
| assignedSymmKeylID | 0..1 | RO | When the Enrolee uses a symmetric key to authenticate to the Enrolee, then the TEF may use this attribute to provide a symmetry key identifier within the domain of the TEF. Assigned by the TEF. |
| tefClientCfg | 0..1 | RO | TEF Client configuration information. The administrating stakeholder arranges for the TEF to include this attribute in the resource for retrieval by the TEF Client. |
| NOTE: At least one of AE-ID and CSE-ID shall be present. |

### X.4.3 Resource Type <symmKeyReg>

The <symmKeyReg> resource shall represent a symmetric key that a source TEF Client has established with the TEF for distributing to authorized Target TEF Clients and/or another TEF. The TEF Client provides a list of authorized Targets when the resource is created – the present document does not specify how the TEF associates the list with the resource. The TEF, is coordination with the identified administrating stakeholder (M2M SP or MTE), can modify the list of authorized Targets and the expirationTime.

The <symmKeyReg> resource shall contain no child resources.

The <symmKeyReg> resource shall contain the attributes specified in table X.4.3-1.

Table X.4.3-1: Attributes of <symmKeyReg> resource

| Attributes of <symmKeyReg> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceID | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceName | 1 | RO | See clause 9.6.1.3 of [1]. This value is used as the relative part of the identifier for the symmetric key in security protocols. |
| parentID | 1 | RO | See clause 9.6.1.3 of [1]. |
| expirationTime | 1 | WO | See clause 9.6.1.3 of [1]. |
| creationTime | 1 | RO | See clause 9.6.1.3 of [1]. |
| labels | 0..1 | RW | See clause 9.6.1.3 of [1]. |
| creator | 1 | RO | See clause 9.6.1.3 of [1]. |
| fqdn | 1 | WO | FQDN of the administrating stakeholder (M2M SP or MTE) associated with this enrolment. |
| SUID | 1 | WO | An SUID constraining the use of the symmetric key associated with this resource |
| targetIDs | 1 (L) | RW | List of AE-ID(s) and/or CSE-ID(s) and/or TEF-FQDN identifying the AE(s) and/or CSE(s) and/or TEF(s) authorized to retrieve the resource. Only the creator and administrating stakeholder (identified by fqdn) are authorized to access this attribute. |
| keyValue | 1 | WO | The value of the key to be provided to the identifier targets. May be provided in the Create request or derived by the TEF Client and TEF from the TLS handshake parameters. |

## X.5	TEF Interface resource-type specific procedures and definitions

### X.5.1 Resource Type <TEF>

#### X.5.1.1 Introduction

A <TEF> resource shall represent a TEF. This <TEF> resource shall be the root for all the resources that are residing on the TEF.

The <TEF> resource has no attributes.

Table X.5.1.1-1: Child resources of <TEF> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to Resource Type Definition |
| --- | --- | --- | --- |
| <tefClientReg> | [variable] | 0..n | Clause X.5.2 |
| <symmKeyReg> | [variable] | 0..n | Clause X.5.3 |

#### X.5.1.2 <TEF> resource specific procedures on CRUD operations

##### X.5.1.2.1 Create

Originator:

The <TEF> resource shall not be created via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

If the request is received, the Receiver CSE shall execute the following steps in order.

- "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

- "Send the Response primitive".

##### X.5.1.2.2 Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1 of [4] with clarifications discussed in clauses X.2 and X.3.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [4] with clarifications discussed in clauses X.2 and X.3, and performing the following step in the place of step Recv-6.3: “Check authorization of the Originator”:

The Receiver shall allow all Originator’s to retrieve this resource.

##### X.5.1.2.3 Update

Originator:

The <tefClientReg> resource shall not be updated via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

- If the request is received, the Receiver CSE shall execute the following steps in order.

- "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error .

- "Send the Response primitive".

##### X.5.1.2.4 Delete

Originator:

The <TEF> resource shall not be DELETEed via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

- If the request is received, the Receiver CSE shall execute the following steps in order.

- "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

- "Send the Response primitive".

### X.5.2 Resource Type <tefClientReg>

#### X.5.2.1 Introduction

A <tefClientReg> resource shall represent a TEF Client (AE or CSE) enrolled with the TEF on behalf of an M2M Service Provider or M2M Trust Enabler. A <tefClientReg> resource shall be a child resource of the TEF’s <TEF> resource.

Table X.5.2.1-1: Universal/Common Attributes of <tefClientReg> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | NP | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| creationTime | NP | NP |
| expirationTime | M | M |
| creator | NP | NP |

Table X.5.2.1-2: Resource Specific Attributes of <tefClientReg> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| fqdn | M | NP | xs:anyURI | No default |
| assignedSymmKeyID | NP | NP | sec:credentialID | No default |
| tefClientCfg | NP | NP | sec:tefClientCfg | No default |

The <tefClientReg> resource shall contain no child resources.

#### X.5.2.2 <tefClientReg> resource specific procedures on CRUD operations

##### X.5.2.2.1 Create

Originator:

No change from the generic procedures in clause 7.2.2.1 of [4] with clarifications discussed in clauses X.2 and X.3, and with following differences:

In step Orig-6.0: “Process Response primitive”, if the Originator used a symmetric key to authenticate to the TEF, and the <tefClientReg> resource in the response contained an assignedSymmKeyID then the originator shall use the assignedSymmKeyID to identify this symmetric key when it is subsequently used in authenticating to the TEF.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [4] with clarifications discussed in clauses X.2 and X.3, and with following differences:

The Receiver shall performing the following steps in order in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized to register with the administrating stakeholder (M2M SP or MTE) identified by fqdn attribute. The present document does not specify how the Receiver makes this determination.

  - If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

  - If the Originator is authorized, then the Receiver shall allow the request.

The Receiver shall perform the following steps in order as part of “Create the resource” (clause 7.3.3.5)” during Step Recv-6.5: “Create/Update/Retrieve/Delete/Notify operation is performed”:

- If the Originator authenticated using symmetric key with a key identifier which does not use the Receiver’s FQDN, then

  - The Receiver shall assign a symmetric key identifier with the Receiver’s FQDN and with relative part which is unique within the scope of symmetric key identifiers issued by the Receiver. The Receiver shall associate this symmetric key identifier with the symmetric key used for authenticating the Originator.

  - The Receiver shall set the assignedSymmKeyID attribute to be the Credential-ID formed from the assigned symmetric key identifier as specified in clause 10.4.

- If the Originator authenticated using a symmetric key with a key identifier which does not use the Receiver’s FQDN, or if the Originator authenticated using a certificate, then the Receiver shall not include an assignedSymmKeyID attribute in the created resource.

- The Receiver shall assign the creator attribute to an AE-ID or CSE-ID on instructions from the administrating stakeholder. The present document does not specify any details of how the AE-ID or CSE-ID is determined.

- The Receiver may assign the tefClientCfg attribute on instructions from the administrating stakeholder.

##### X.5.2.2.2 Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1 of [4] with clarifications discussed in clauses X.2 and X.3.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [4] with clarifications discussed in clauses X.2 and X.3, performing the following steps in order in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized by checking if the Originator is the creator of the resource.

- If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

- If the Originator is authorized, then the Receiver shall allow the request.

##### X.5.2.2.3 Update

Originator:

The <tefClientReg> resource shall not be updated via API.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [4] with clarifications discussed in clauses X.2 and X.3, and with the following differences:

The Receiver shall perform the following step in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized by checking if the Originator is the creator of the resource.

- If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

- If the Originator is authorized, then the Receiver shall allow the request.

The Receiver shall perform the following steps in order as part of “Update the resource” (clause 7.3.3.7)” during Step Recv-6.5: “Create/Update/Retrieve/Delete/Notify operation is performed”:

- If the Originator was the Creator of the resource, then the Receiver shall perform steps 2 and 3 in clause X.5.2.2.1.

##### X.5.2.2.4 Delete

Originator:

No change from the generic procedures in clause 7.2.2.1 of [4] with clarifications discussed in clauses X.2 and X.3.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [4] with clarifications discussed in clauses X.2 and X.3, performing the following step in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized by checking if the Originator is the creator of the resource.

- If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

- If the Originator is authorized, then the Receiver shall allow the request.

### X.5.3 Resource Type <symmKeyReg>

#### X.5.3.1 Introduction

A <symmKeyReg> resource shall represent a symmetric key registered with the TEF and administrated by the identified administrating stakeholder. A <symmKeyReg> resource shall be a child resource of an <TEF> resource.

Table X.5.3.1-1: Universal/Common Attributes of <symmKeyReg>resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | NP | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| creationTime | NP | NP |
| expirationTime | M | M |
| creator | NP | NP |
| labels | O | O |

Table X.5.3.1-2: Resource Specific Attributes of <symmKeyReg>  resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| fqdn | M | NP | xs:anyURI | No default |
| SUID | M | NP | m2m:suid | No default |
| targetIDs | O | O | m2m:listOfM2MID | No default |
| keyValue | O | NP | xs:base64binary | No default |

The <symmKeyReg> resource shall contain no child resources.

#### X.5.3.2 <symmKeyReg> resource specific procedures on CRUD operations

##### X.5.3.2.1 Create

Originator:

No change from the generic procedures in clause 7.2.2.1 of [4] with clarifications discussed in clauses X.2 and X.3, and with following differences:

In step Orig-1.0: “Compose of a Request primitive”, the

- Originator shall select to either use a key derived from the TLS handshake or use another key provided by the Originator.

  - If the Originator selects to use a key derived from the TLS handshake, then the Originator shall not include the keyValue attribute in the <symmKeyReg> resource of the request.

  - If the Originator selects to provide a key other than a key derived from the TLS handshake, the Originator shall include the value of this key in the keyValue attribute in the <symmKeyReg> resource of the request.

In step Orig-6.0: “Process Response primitive”, the following steps shall be performed

- If the Originator selected to use a key derived from the TLS handshake (see difference to step Orig-1.0 above), then the Originator shall perform the following steps in order to generate the value for the keyValue attribute

  - The Originator shall apply the TLS export mechanism described in clause 10.3.1 to generate a TLS-export-key.

  - The Originator shall apply the usage-constrained key derivation algorithm in clause 10.3.7 to derive the keyValue from TLS-export-key, fqdn, SUID and the resourceName assigned by the Receiver to the created resource.

- The originator shall record the resourceName attribute of the created resource as the relative part of the key identifier for the symmetric key which is to be assigned to the value for the keyValue attribute.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [4] with clarifications discussed in clauses X.2 and X.3, and with following differences:

The Receiver shall perform the following steps in order in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall ensure that the following criteria are satisfied, with administrating stakeholder being the stakeholder matching the fqdn attribute of the <symmKeyReg> resource in the Create request:

  - The Originator is enrolled with the administrating stakeholder; that is, there is a non-expired <tefClientReg> resource whose creator attribute matches the Originator’s AE-ID or CSE-ID, and whose fqdn attribute identifies the administrating stakeholder.

  - The Receiver determines that the administrating stakeholder allows the creation of the resource. The present document does not specify how the Receiver makes this determination.

- If these criteria are not met, then the Receiver shall shall execute the following steps in order.

  - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

  - "Send the Response primitive".

- Otherwise, then the Receiver shall allow the request.

The Receiver shall perform the following steps in order as part of “Create the resource” (clause 7.3.3.5)” during Step Recv-6.5: “Create/Update/Retrieve/Delete/Notify operation is performed”:

- If the keyValue attribute is not present in the <symmKeyReg> resource in the request, then the Receiver shall perform the following steps in order to generate the value for the keyValue attribute

  - The Receiver shall apply the TLS export mechanism described in clause 10.3.1 to generate a TLS-export-key.

  - The Receiver shall apply the usage-constrained key derivation algorithm in clause 10.3.7 to derive the value for the keyValue attribute from TLS-export-key, fqdn, SUID and the resourceName assigned by the Receiver to the created resource.

##### X.5.3.2.2 Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1 of [4] with clarifications discussed in clauses X.2 and X.3.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [4] with clarifications discussed in clauses X.2 and X.3, and with following differences:

The Receiver shall perform the following steps in order in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized by checking if the Originator is the creator of the resource or the Originator is identified in the targetIDs.

- If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

- If the Originator is authorized, then the Receiver shall allow the request.

##### X.5.3.2.3 Update

Originator:

No change from the generic procedures in clause 7.2.2.1 of [4] with clarifications discussed in clauses X.2 and X.3.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [4] with clarifications discussed in clauses X.2 and X.3, and performing the following step in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized by checking if the Originator is the creator of the resource.

- If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

- If the Originator is authorized, then the Receiver shall allow the request.

##### X.5.3.2.4 Delete

Originator:

No change from the generic procedures in clause 7.2.2.1 of [4] with clarifications discussed in clause X.2 and X.3.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [4] with clarifications discussed in clauses X.2 and X.3, and performing the following step in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized by checking if the Originator is the creator of the resource.

- If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

- If the Originator is authorized, then the Receiver shall allow the request.

### -----------------------End of change 1-------------------------------------------