| CHANGE REQUEST |
| --- |
| Meeting:* | SEC 24 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 206-07-11 |
| Contact:* | As above |
| Reason for Change/s:* | MAF Interface stage 3 specification |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-006 End-to-End Security and Group Authentication MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003 and 2.3.0 |
| Clauses/Sub Clauses* | 8.8 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 205 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR provides the stage 3 details for the MAF Procedures, using the TEF Interface proposed in SEC-206-0131.

### Add the following text to the end of clause 8.8.1, just before text explaining the organization of clause 8.8

### -----------------------Start of change 1 (8.8.1)--------------------------------

The MAF Security Framework uses the TEF Interface, with the MAF Client acting as a TEF Client and the MAF acting as a TEF. A MAF may provide its services on behalf of multiple administrating stakeholders, and a MAF Client may be associated with multiple administrating stakeholders, each administrating stakeholder administering the use of the MAF within a different scope. See clause X.1 for further discussion on the relationship between administrating stakeholders, MAF Clients and the MAF.

The MAF Procedures, with the exception of the MAF Handshake, use the TEF Interface primitives and resources specified in clause X. Table 8.8.1-2 lists the TEF Interface resource type and primitive operation for each MAF Procedure. Figure 8.8.1-2 translates Figure 8.8.1-1 into TEF Interface primitives.

Table 8.8.1-2: Mapping of MAF Procedures to TEF Interface procedures

| MAF Procedure | TEF Interface Procedure |
| --- | --- |
|  | Resource type | Primitive Operation |
| MAF Client Registration | <tefClientReg> | Create |
| MAF Client Configuration Retrieval | <tefClientReg> | Retrieve |
| MAF Client Registration Update | <tefClientReg> | Update |
| MAF Client De-Registration | <tefClientReg> | Delete |
| MAF Key Registration | <symmKeyReg> | Create |
| MAF Key Retrieval | <symmKeyReg> | Retrieve |
| MAF Key Registration Update | <symmKeyReg> | Update |
| MAF Key De-Registration | <symmKeyReg> | Delete |

Figure 8.8.1-2: The sequence of events when using the MAF Security Framework as part of a security feature, described using the TEF Interface primitives and resources

### -----------------------End of change  1 -------------------------------------------

### Change 2 provides new text

### -----------------------Start of change  2 -------------------------------------------

### 8.8.3	MAF Security Framework Message Definitions

#### 8.8.3.1	Introduction to the MAF Security Framework Messages

Clause 8.8.3 defines the MAF Security Framework messages: that is, parameters of the request (from the MAF Client to the MAF) and a corresponding response (from the MAF to the MAF Client) for the MAF procedures. With the exception of the MAF Handshake, the MAF Procedures are defined using the TEF Interface primitives and resources defined in clause X.

#### 8.8.3.2	MAF Handshake Procedure Details

Editor’s note: Unclear if there are any details to add here. It is helpful to have this clause here to align the numbering of related sub-clauses of 8.8.2 and 8.8.3.

#### 8.8.3.3	MAF Client Registration Procedure Message Definitions

The processing for this procedure is specified in clause 8.8.2.3.

The MAF Client Registration Procedure messages correspond to performing a Create operation of a <tefClientReg> resource, described in clause X.5.3.2.1.

NOTE: 	This procedure serves a similar purpose to creating a <remoteCSE> (CSE Registration) or creating a <AE> resource (AE Registration) on a CSE.

Table 8.8.3.3-1 describes the TEF Interface request primitive corresponding to the MAF Client Registration request message.

Table 8.8.3.3-1: The TEF Interface request primitive corresponding to the MAF Client Registration request message

| TEF Request Primitive Parameter | Multiplicity | Value | Notes |
| --- | --- | --- | --- |
| Operation | 1 | Create |  |
| To | 1 | {MAF-FQDN}/tef | See Table 8.8.2.3-1 |
| From | 0 | - |  |
| Request Identifier | 1 | Randomly selected by MAF client | [1,4] |
| Resource Type | 1 | <tefClientReg> resource Editor’s note: To Do |  |
| Content = <tefClientReg> Resource | Attributes | 1 |  |  |
|  | @resourceName | 0 | - |  |
|  | resourceType | 0 | - |  |
|  | resourceID | 0 | - |  |
|  | parentID | 0 | - |  |
|  | creationTime | 0 | - |  |
|  | expirationTime | 1 | expirationTime | See Table 8.8.2.3-1 |
|  | creator | 0 | - |  |
|  | labels | 0..1 | labels | See Table 8.8.2.3-1 |
|  | fqdn | 1 | adminFQDN | See Table 8.8.2.3-1 |
|  | assignedSymmKeyID | 0 | - |  |
| Result Content | 1 | “4” attributes and child resources, or “5” attributes and child resource references | [1,4] |

Table 8.8.3.3-2 describes the TEF Interface response primitive corresponding to the MAF Client Registration response message.

Table 8.8.3.3-2: The TEF Interface response primitive corresponding to the MAF Client Registration response message

| TEF Request Primitive Parameter | Multiplicity | Value | Notes |
| --- | --- | --- | --- |
| Response Status Code | 1 | “2001” CREATED | [1,4] |
| Request Identifier | 1 | Copied from request | [1,4] |
| Content = <tefClientReg> Resource | Attributes | 1 |  |  |
|  | @resourceName | 1 | tefClientRegID | See Table 8.8.2.3-2 |
|  | resourceType | 1 | <tefClientReg> resource Editor’s note: To Do |  |
|  | resourceID | 0 | Assigned by MAF | [1,4] |
|  | parentID | 1 | resourceID of <TEF> resource | [1,4] |
|  | creationTime | 1 | Assigned by MAF | [1,4] |
|  | expirationTime | 1 | expirationTime | See Table 8.8.2.3-2 |
|  | creator | 0 | creator | See Table 8.8.2.3-2 |
|  | labels | 0..1 | labels | See Table 8.8.2.3-2 |
|  | fqdn | 1 | adminFQDN | See Table 8.8.2.3-2 |
|  | assignedSymmKeyID | 0..1 | assignedSymmKeyID | See Table 8.8.2.3-2 |
|  | tefClientCfg | 0..1 | config | See Table 8.8.2.3-2 |

#### 8.8.3.4	MAF Client Configuration Retrieval Procedure Details

The processing for this procedure is specified in clause 8.8.2.4.

The MAF Client Configuration Retrieval Procedure messages correspond to performing a Retrieve operation on a <tefClientReg> resource, described in clause X.5.3.2.2.

Table 8.8.3.4-1 describes the TEF Interface request primitive corresponding to the MAF Client Configuration Retrieval request message.

Table 8.8.3.4-1: The TEF Interface request primitive corresponding to the MAF Client Configuration Retrieval request message

| TEF Request Primitive Parameter | Multiplicity | Value | Notes |
| --- | --- | --- | --- |
| Operation | 1 | Retrieve |  |
| To | 1 | {MAF-FQDN}/tef/{tefClientRegID} | See Table 8.8.2.4-1 |
| From | 0 | Target MAF Client’s AE-ID or CSE-ID | [1,4] |
| Request Identifier | 1 | Randomly selected by MAF client | [1,4] |
| Resource Type | 0 | - | - |
| Content | 0 | - | - |
| Result Content | 1 | “1” attributes | [1,4] |

Table 8.8.3.4-2 describes the TEF Interface response primitive corresponding to the MAF Client Configuration Retrievaresponse message.

Table 8.8.3.4-2: The TEF Interface response primitive corresponding to the MAF Client Configuration Retrieval response message

| TEF Request Primitive Parameter | Multiplicity | Value | Notes |
| --- | --- | --- | --- |
| Response Status Code | 1 | 2000” OK | [1,4] |
| Request Identifier | 1 | Copied from request | [1,4] |
| Content = <tefClientReg> Resource | Attributes | 1 |  |  |
|  | @resourceName | 1 | tefClientRegID | See Table 8.8.2.4-2 |
|  | resourceType | 1 | <tefClientReg> resource Editor’s note: To Do |  |
|  | resourceID | 0 | Assigned by MAF | [1,4] |
|  | parentID | 1 | resourceID of <TEF> resource | [1,4] |
|  | creationTime | 1 | Assigned by MAF | [1,4] |
|  | expirationTime | 1 | expirationTime | See Table 8.8.2.4-2 |
|  | creator | 0 | creator | See Table 8.8.2.4-2 |
|  | labels | 0..1 | labels | See Table 8.8.2.4-2 |
|  | fqdn | 1 | adminFQDN | See Table 8.8.2.4-2 |
|  | assignedSymmKeyID | 0..1 | assignedSymmKeyID | See Table 8.8.2.4-2 |
|  | tefClientCfg | 0..1 | config | See Table 8.8.2.4-2 |

#### 8.8.3.5	MAF Client Registration Update Procedure Details

The processing for this procedure is specified in clause 8.8.2.5.

The MAF Client Registration Update Procedure messages correspond to performing an Update operation on an <tefClientReg> resource, described in clause X.5.3.2.3.

Table 8.8.3.5-1 describes the TEF Interface request primitive corresponding to the MAF Client Registration Update request message.

Table 8.8.3.5-1: The TEF Interface request primitive corresponding to the MAF Client Registration Update request message

| TEF Request Primitive Parameter | Multiplicity | Value | Notes |
| --- | --- | --- | --- |
| Operation | 1 | Update |  |
| To | 1 | {MAF-FQDN}/tef/{tefClientRegID} | See Table 8.8.2.5-1 |
| From | 0 | - |  |
| Request Identifier | 1 | Randomly selected by MAF client | [1,4] |
| Resource Type | 0 | - |  |
| Content = attributes of <tefClientReg> Resource | Attributes | 1 |  |  |
|  | @resourceName | 0 | - |  |
|  | resourceType | 0 | - |  |
|  | resourceID | 0 | - |  |
|  | parentID | 0 | - |  |
|  | creationTime | 0 | - |  |
|  | expirationTime | 0..1 | expirationTime | See Table 8.8.2.5-1 |
|  | creator | 0 | - |  |
|  | labels | 0..1 | labels | See Table 8.8.2.5-1 |
|  | fqdn | 0 | - |  |
|  | assignedSymmKeyID | 0..1 | assignedSymmKeyID | See Table 8.8.2.5-1 |
| Result Content | 1 | “4” attributes and child resources, or “5” attributes and child resource references | [1,4] |

Table 8.8.3.5-2 describes the TEF Interface response primitive corresponding to the MAF Client Registration Update response message.

Table 8.8.3.5-2: The TEF Interface response primitive corresponding to the MAF Client Registration Update response message

| TEF Request Primitive Parameter | Multiplicity | Value | Notes |
| --- | --- | --- | --- |
| Response Status Code | 1 | “2004” UPDATED | [1,4] |
| Request Identifier | 1 | Copied from request | [1,4] |
| Content = attributes of <tefClientReg> Resource | Attributes | 1 |  |  |
|  | @resourceName | 0 | - |  |
|  | resourceType | 0 | - |  |
|  | resourceID | 0 | - |  |
|  | parentID | 0 | - |  |
|  | creationTime | 0 | - |  |
|  | expirationTime | 0..1 | expirationTime | See Table 8.8.2.5-2 |
|  | creator | 0 | - |  |
|  | labels | 0..1 | labels | See Table 8.8.2.5-2 |
|  | fqdn | 1 | - |  |
|  | assignedSymmKeyID | 0..1 | assignedSymmKeyID | See Table 8.8.2.5-2 |

#### 8.8.3.6	MAF Client De-Registration Procedure Details

The processing for this procedure is specified in clause 8.8.2.6.

The MAF Client De-Registration Procedure messages correspond to performing an Delete operation on an <tefClientReg> resource, described in clause X.5.2.2.4.

Table 8.8.3.6-1 describes the TEF Interface request primitive corresponding to the MAF Client De-Registration request message.

Table 8.8.3.6-1: The TEF Interface request primitive corresponding to the MAF Client De-Registration request message

| TEF Request Primitive Parameter | Multiplicity | Value | Notes |
| --- | --- | --- | --- |
| Operation | 1 | Delete |  |
| To | 1 | {MAF-FQDN}/tef/{tefClientRegID} | See Table 8.8.2.6-1 |
| From | 0 | - |  |
| Request Identifier | 1 | Randomly selected by MAF client | [1,4] |
| Resource Type | 0 | - | - |
| Content | 0 | - | - |
| Result Content | 0 | - | - |

Table 8.8.3.6-2 describes the TEF Interface response primitive corresponding to the MAF Client De-Registration response message.

Table 8.8.3.6-2: The TEF Interface response primitive corresponding to the MAF Client De-Registration response message

| TEF Request Primitive Parameter | Multiplicity | Value | Notes |
| --- | --- | --- | --- |
| Response Status Code | 1 | “2002” DELETED | [1,4] |
| Request Identifier | 1 | Copied from request | [1,4] |
| Content | 0 | - | - |

#### 8.8.3.7	MAF Key Registration Procedure Details

The processing for this procedure is specified in clause 8.8.2.7.

The MAF Client Registration Procedure messages correspond to performing a Create operation on a <symmKeyReg> resource, described in clause X.5.3.2.1.

Table 8.8.3.7-1 describes the TEF Interface request primitive corresponding to the MAF Key Registration request message.

Table 8.8.3.7-1: The TEF Interface request primitive corresponding to the MAF Key Registration request message

| TEF Request Primitive Parameter | Multiplicity | Value | Notes |
| --- | --- | --- | --- |
| Operation | 1 | Create |  |
| To | 1 | {MAF-FQDN}/tef | See Table 8.8.2.7-1 |
| From | 0 | - |  |
| Request Identifier | 1 | Randomly selected by MAF client | [1,4] |
| Resource Type | 1 | <symmKeyReg> resource Editor’s note: To Do |  |
| Content = <Key Registration> Resource | Attributes | 1 |  |  |
|  | @resourceName | 0 | - |  |
|  | resourceType | 0 | - |  |
|  | resourceID | 0 | - |  |
|  | parentID | 0 | - |  |
|  | creationTime | 0 | - |  |
|  | expirationTime | 1 | expirationTime | See Table 8.8.2.7-1 |
|  | creator | 0 | - |  |
|  | labels | 0..1 | labels | See Table 8.8.2.7-1 |
|  | fqdn | 1 | adminFQDN | See Table 8.8.2.7-1 |
|  | SUID | 1 | SUID | See Table 8.8.2.7-1 |
|  | targetIDs | 0..1 | targetIDs | See Table 8.8.2.7-1 |
|  | keyValue | 0..1 | Key Value | See Table 8.8.2.7-1 |
| Result Content | 1 | “1” attributes | [1,4] |

Table 8.8.3.7-2 describes the TEF Interface response primitive corresponding to the MAF Key Registration response message.

Table 8.8.3.7-2: The TEF Interface response primitive corresponding to the MAF Key Registration response message

| TEF Request Primitive Parameter | Multiplicity | Value | Notes |
| --- | --- | --- | --- |
| Response Status Code | 1 | “2001” CREATED | [1,4] |
| Request Identifier | 1 | Copied from request | [1,4] |
| Content = <Key Registration> Resource | Attributes | 1 |  |  |
|  | @resourceName | 1 | RelKeyID | See Table 8.8.2.7-2 |
|  | resourceType | 1 | <symmKeyReg> resource Editor’s note: To Do |  |
|  | resourceID | 0 | Assigned by MAF | [1,4] |
|  | parentID | 1 | resourceID of <TEF> resource | [1,4] |
|  | creationTime | 1 | Assigned by MAF | [1,4] |
|  | expirationTime | 1 | expirationTime | See Table 8.8.2.7-2 |
|  | creator | 0 | Source MAF Client ID | See Table 8.8.2.7-2 |
|  | labels | 0..1 | labels | See Table 8.8.2.7-2 |
|  | fqdn | 1 | adminFQDN | See Table 8.8.2.7-2 |
|  | SUID | 1 | SUID | See Table 8.8.2.7-2 |
|  | targetIDs | 1 | targetIDs | See Table 8.8.2.7-2 |
|  | keyValue | 0 | - |  |

#### 8.8.3.8	MAF Key Retrieval Procedure Details

The processing for this procedure is specified in clause 8.8.2.8.

The MAF Key De-Registration Procedure messages correspond to performing an Retrieve operation on an <symmKeyReg> resource, described in clause X.5.3.2.2.

Table 8.8.3.8-1 describes the TEF Interface request primitive corresponding to the MAF Key Retrieval request message.

Table 8.8.3.8-1: The TEF Interface request primitive corresponding to the MAF Key Retrieval request message

| TEF Request Primitive Parameter | Multiplicity | Value | Notes |
| --- | --- | --- | --- |
| Operation | 1 | Retrieve |  |
| To | 1 | {MAF-FQDN}/tef/{RelKeyID} | See Table 8.8.2.8-1 |
| From | 0 | Target MAF Client’s AE-ID or CSE-ID | [1,4] |
| Request Identifier | 1 | Randomly selected by MAF client | [1,4] |
| Resource Type | 0 | - | - |
| Content | 0 | - | - |
| Result Content | 1 | “1” attributes | [1,4] |

Table 8.8.3.8-2 describes the TEF Interface response primitive corresponding to the MAF Key Retrieval response message.

Table 8.8.3.7-2: The TEF Interface response primitive corresponding to the MAF Key Retrieval response message

| TEF Request Primitive Parameter | Multiplicity | Value | Notes |
| --- | --- | --- | --- |
| Response Status Code | 1 | “2000” OK | [1,4] |
| Request Identifier | 1 | Copied from request | [1,4] |
| Content = <Key Registration> Resource | Attributes | 1 |  |  |
|  | @resourceName | 1 | RelKeyID | See Table 8.8.2.8-2 |
|  | resourceType | 1 | <symmKeyReg> resource Editor’s note: To Do | [1,4] |
|  | resourceID | 1 | Assigned by MAF | [1,4] |
|  | parentID | 1 | resourceID of <TEF> resource | [1,4] |
|  | creationTime | 1 | Assigned by MAF | [1,4] |
|  | expirationTime | 1 | expirationTime | See Table 8.8.2.8-2 |
|  | creator | 1 | Source MAF Client ID | See Table 8.8.2.8-2 |
|  | labels | 0..1 | labels | See Table 8.8.2.8-2 |
|  | fqdn | 1 | adminFQDN | See Table 8.8.2.8-2 |
|  | SUID | 1 | SUID | See Table 8.8.2.8-2 |
|  | targetIDs | 0 | - | targetIDs is never returned to Target MAF Clients. |
|  | keyValue | 1 | Key Value | See Table 8.8.2.8-2 |

#### 8.8.3.9	MAF Key Registration Update Procedure Details

The processing for this procedure is specified in clause 8.8.2.9.

The MAF Key Registration Update messages correspond to performing a Update operation on a <symmKeyReg> resource, described in clause X.5.3.2.3.

Table 8.8.3.7-1 describes the TEF Interface request primitive corresponding to the MAF Key Registration Update request message information.

Table 8.8.3.7-1: The TEF Interface request primitive corresponding to the MAF Key Registration Update request message

| TEF Request Primitive Parameter | Multiplicity | Value | Notes |
| --- | --- | --- | --- |
| Operation | 1 | Update |  |
| To | 1 | {MAF-FQDN}/tef/{RelKeyID} | See Table 8.8.2.9-1 |
| From | 1 | Source MAF Client’s AE-ID or CSE-ID | [1,4] |
| Request Identifier | 1 | Randomly selected by MAF client | [1,4] |
| Resource Type | 0 | - |  |
| Content = <Key Registration> Resource | Attributes | 1 |  |  |
|  | @resourceName | 0 | - |  |
|  | resourceType | 0 | - |  |
|  | resourceID | 0 | - |  |
|  | parentID | 0 | - |  |
|  | creationTime | 0 | - |  |
|  | expirationTime | 0..1 | expirationTime | See Table 8.8.2.9-1 |
|  | creator | 0 | - |  |
|  | labels | 0..1 | labels | See Table 8.8.2.9-1 |
|  | fqdn | 0 | - |  |
|  | SUID | 0 | - |  |
|  | targetIDs | 0..1 | targetIDs | See Table 8.8.2.9-1 |
|  | keyValue | 0 | - | See Table 8.8.2.9-1 |
| Result Content | 1 | “1” attributes | [1,4] |

Table 8.8.3.9-2 describes the TEF Interface response primitive corresponding to the MAF Key Registration response message.

Table 8.8.3.9-2: The TEF Interface response primitive corresponding to the MAF Key Registration Update response message

| TEF Request Primitive Parameter | Multiplicity | Value | Notes |
| --- | --- | --- | --- |
| Response Status Code | 1 | “2004” UPDATED | [1,4] |
| Request Identifier | 1 | Copied from request | [1,4] |
| Content = <Key Registration> Resource | Attributes | 1 |  |  |
|  | @resourceName | 0 | - |  |
|  | resourceType | 0 | - |  |
|  | resourceID | 0 | - |  |
|  | parentID | 0 | - |  |
|  | creationTime | 0 | - |  |
|  | expirationTime | 0..1 | expirationTime | See Table 8.8.2.9-2 |
|  | creator | 0 | - |  |
|  | labels | 0..1 | labels | See Table 8.8.2.9-2 |
|  | fqdn | 0 | - |  |
|  | SUID | 0 | - |  |
|  | targetIDs | 0..1 | targetIDs | See Table 8.8.2.9-2 |
|  | keyValue | 0 | - |  |

#### 8.8.3.10	MAF Key De-Registration Procedure Details

The processing for this procedure is specified in clause 8.8.2.10.

The MAF Key De-Registration Procedure messages correspond to performing an Delete operation on an <symmKeyReg> resource, described in clause X.5.3.2.4.

Table 8.8.3.10-1 describes the TEF Interface request primitive corresponding to the MAF Key De-Registration request message.

Table 8.8.3.10-1: The TEF Interface request primitive corresponding to the MAF Key De-Registration request message

| TEF Request Primitive Parameter | Multiplicity | Value | Notes |
| --- | --- | --- | --- |
| Operation | 1 | Delete |  |
| To | 1 | {MAF-FQDN}/tef/{RelKeyID} | See Table 8.8.2.10-1 |
| From | 1 | Source MAF Client’s AE-ID or CSE-ID | [1,4] |
| Request Identifier | 1 | Randomly selected by MAF client | [1,4] |
| Resource Type | 0 | - | - |
| Content | 0 | - | - |
| Result Content | 0 | - | - |

Table 8.8.3.10-2 describes the TEF Interface response primitive corresponding to the MAF Key De-Registration response message.

Table 8.8.3.10-2: The TEF Interface response primitive corresponding to the MAF Key De-Registration response message

| TEF Request Primitive Parameter | Multiplicity | Value | Notes |
| --- | --- | --- | --- |
| Response Status Code | 1 | “2002” DELETED | [1,4] |
| Request Identifier | 1 | Copied from request | [1,4] |
| Content | 0 | - | - |

### -----------------------End of change  2 -------------------------------------------

# Comments

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values

These are not field values