| CHANGE REQUEST |
| --- |
| Meeting:* | SEC24 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2016-07-11 |
| Contact:* | As above |
| Reason for Change/s:* | Provides data type definitions for parameters used only within oneM2m security specifications |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003 and 2.3.0 |
| Clauses/Sub Clauses* | New clause Y (to be chosen by the rapporteur and/or SEC WG) |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR provides data type definitions and short name assignments for resources and complex data types which are used only within the scope of security specifications (which currently include only TS-0003).

### -----------------------Start of change 1 ------------------------

## 10.4	Credential-ID Details

The Credential-ID has two parts:

A type-ID part. The type-ID part is a positive integer defined by datatype sec:credIDTypeID.

A value part which contains a globally-unique identifier for the entity's credential. The value part may use the Roman alphabet, numerals, '.', '_', '-', and '@'.

The Credential-ID is formed by concatenating the type part, the character '-' and the value part.

NOTE:	A Credential-ID is a globally unique identifier used to identify serviceSubscribedAppRule resources (oneM2M TS-0001[1]) and identify credentials in security configuration information.

### -----------------------End of change 1 ------------------------

### -----------------------Start of change 2 ------------------------

# Y	Security-Specific oneM2M Data Type Definitions

## Y.1 Introduction

Clause Y contains data type definitions used only within the oneM2M security specifications.

Any data types of XML elements defined for use only within oneM2M security specifications shall use the namespace:

http://www.onem2m.org/xml/securityProtocols.

The present document, and any XML or XML Schema Documents produced by oneM2M shall use the prefix “sec:” to refer to that namespace

## Y.2 Simple Security-Specific oneM2M Data Types

Table Y.2-1 describes simple data type definitions specific to security. The types in table Y.2-1 are either:

Atomic data types derived from XML Schema data types by restrictions other than enumeration

List data types constructed from other XML Schema or oneM2M-defined atomic data types.

Table Y.2-1: Security-specific oneM2M simple data types

| XSD type name | Used for | Examples | Description |
| --- | --- | --- | --- |
| sec:relKeyID | Relative part of symmetric key Identifiers | 1he83he, my-key_name, firstname.lastname | Any combination of the Roman alphabet, numerals, '.', '_' and '-' characters |
| sec:credentialID | Credential Identifier | 10-thiskey@mymef.com | A sec:credIDTypeID and a xs:anyURI separated by the ‘-‘ character. See clause 10.4. The xs:anyURI is the value part of the credential-lD |

## Y.3 Enumerated Security-Specific oneM2M Data Types

### Y.3.1	Introduction

The enumerated security-specific oneM2M data types are treated identically to the enumerated oneM2M data types defined in clause 6.3.4 of TS-0004 [4]. These data types are based on <xs:integer>, with the numeric values interpreted as specified in clause Y.3.2

### Y.3.2	Enumeration type definitions

#### Y.3.2.1	sec:credIDTypeID

The sec:credIDTypeID enumeration type is used in sec:credentialID to identify the type of the identified credential.

Table X.32.1-1: Interpretation of the sec:credIDTypeID enumeration type.

| Value | Interpretation | Note |
| --- | --- | --- |
| 10 | Symmetric key used to authenticate to a MEF (KpmID) | See clause 8.3.2.1 |
| 11 | Symmetric key used to authenticate to a MAF (KmID) | See clause 8.8.3.1 |
| 12 | Symmetric key used to authenticate in an SAEF (KpsaID or KcID) | See clauses 8.2.2.1, 8.2.2.3 |
| 13 | Symmetric key used to authenticate in ESPrim (pairwiseESPrimKeyID) | See clauses 8.4.2 |
| 14 | Symmetric key used for direct encryption in the ESData Encryption-only or Nested-Sign-then-encrypt security classes (generic symmetric key identifier format) | See clause 8.5.2 |
| 15 | Symmetric key used for symmetric key wrap in the ESData Encryption-only or Nested-Sign-then-encrypt security classes (generic symmetric key identifier format) | See clause 8.5.2 |
| 16 | Symmetric key used for HMAC in the ESData Signature-only security class (generic symmetric key identifier format) | See clause 8.5.2 |
| 30 | Raw Public Key Certificate used in TLS: (Public Key Identifier) | 10.1.2 |
| 31 | Device Certificate used in TLS (globally unique hardware instance identifier) | 10.1.1.4 |
| 32 | CSE-ID Certificate used in TLS (CSE-ID) | oneM2M TS-0001 [1] |
| 33 | AE-ID Certificate used in TLS (AE-ID) | oneM2M TS-0001 [1] |
| 41 | Raw Public Key Certificate used for RSA or ECDH Key management in the ESData Encryption-only or Nested-Sign-then-encrypt security classes: (Public Key Identifier) | 10.1.2 |
| 42 | Device Certificate used for RSA or ECDH Key management in the ESData Encryption-only or Nested-Sign-then-encrypt security classes (globally unique hardware instance identifier) | 10.1.1.4 |
| 43 | CSE-ID Certificate used for RSA or ECDH Key management in the ESData Encryption-only or Nested-Sign-then-encrypt security classes (CSE-ID) | oneM2M TS-0001 [1] |
| 44 | AE-ID Certificate used for RSA or ECDH Key management in the ESData Encryption-only or Nested-Sign-then-encrypt security classes (AE-ID) | oneM2M TS-0001 [1] |
| 51 | Raw Public Key Certificate used for RSA or ECDH Key management in the ESData Signature-only security class: (Public Key Identifier) | 10.1.2 |
| 52 | Device Certificate used for RSA or ECDSA signatures in the ESData Signature-only security class (globally unique hardware instance identifier) | 10.1.1.4 |
| 53 | CSE-ID Certificate used for RSA or ECDH Key management in the ESData Signature-only security class (CSE-ID) | oneM2M TS-0001 [1] |
| 54 | AE-ID Certificate used for RSA or ECDH Key management in the ESData Signature-only security class (AE-ID) | oneM2M TS-0001 [1] |
| NOTE: The form of the identifier for the credential type is described in brackets. |

## Y.3	Complex Security-Specific oneM2M Data Types

### Y.3.1	sec:tefClientCfg

Used for the tefClientCfg attribute of the <tefClientReg> resource. See clause X.5.2.1.

Table Y.2.1-1: Type definition of sec:tefClientCfg.

| Element Path | Element Type | Multiplicity | Notes |
| --- | --- | --- | --- |
| tefClientRegCfg | sec:tefClientRegCfg | 0..1 | See clause Y.4.2 |
| tefKeyRegCfg | sec:tefKeyRegCfg | 0..1 | See clause Y.4.3 |
| NOTE 1: Only one element shall be present |

### Y.4.2	sec:tefClientRegCfg

Used for tefClientRegCfg in sec:tefClientCfg. See clause 8.8.3.2.

Table Y.4.2-1: Type definition of sec:tefClientRegCfg.

| Element Path | Element Type | Multiplicity | Notes |
| --- | --- | --- | --- |
| expirationTime | m2m:timestamp | 0..1 | oneM2M TS-0004 [4] |
| labels | m2m:labels | 0..1 | oneM2M TS-0004 [4] |
| adminFQDN | xs:anyURI | 1 |  |
| URI | xs:anyURI | 1 |  |
| httpPort | xs:unsignedByte | 0..1 |  |
| coapPort | xs:unsignedByte | 0..1 |  |
| websocketPort | xs:unsignedByte | 0..1 |  |
| ppsk | anonymous | 0..1 |  |
| ppsk/credID | sec:credentialID | 0..1 | See Note 1. See clause Y.2 |
| ppsk/fqdn | xs:anyURI | 0..1 | See Note 1 |
| rpsk | sec:tefKeyRegCfg | 0..1 | See clause Y.4.2.3 |
| certAuth | anonymous | 0..1 |  |
| certAuth/credID | sec:credentialID | 1 | See clause Y.2 |
| certAuth/caCerts | xs:base64binary | 1 |  |
| NOTE 1: If the ppsk element is present, then exactly one of ppsk/credID and ppsk/mafID shall be present |

#### Y.4.2.3	sec:tefKeyRegCfg

Used for tefKeyRegCfg in sec:tefClientCfg. See clause 8.8.3.3

Table Y.4.3-1: Type definition of sec:tefKeyRegCfg.

| Element Path | Element Type | Multiplicity | Notes |
| --- | --- | --- | --- |
| expirationTime | m2m:timestamp | 0..1 | oneM2M TS-0004 [4] |
| labels | m2m:labels | 0..1 | oneM2M TS-0004 [4] |
| adminFQDN | xs:anyURI | 1 |  |
| SUID | m2m:suid | 1 | oneM2M TS-0004 [4] |
| targetIDs | m2m:listOfM2MIDs | 0..1 | oneM2M TS-0004 [4] |

### -----------------------End of change 2 -------------------------

### -----------------------Start of change 3 -------------------------

# Z. Security-specific oneM2M Short Names

## Z.2 Introduction

The short names are introduced in clause 8.2.1 of oneM2M TS-0004 [4]. The short names in oneM2M TS-0004 [4] shall apply in addition to the short names defined here.

## Z.2 Security-specific oneM2M Resource attributes

In protocol bindings resource attributes names shall be translated into short names of Table Z.2-1. And in Table 8.2.3-1 of oneM2M TS-0004 [4].

Table Z.2-1: Security-specific oneM2M Attribute Short Names.

| Attribute Name | Occurs in | Short Name | Notes |
| --- | --- | --- | --- |
| resourceType | All | ty* | Defined in oneM2M TS-0004 [4]. |
| resourceID | All | ri | Defined in oneM2M TS-0004 [4]. |
| resourceName | All | rn | Defined in oneM2M TS-0004 [4]. |
| parentID | tefClientReg, tefKeyReg | pi | Defined in oneM2M TS-0004 [4]. |
| expirationTime | All | et | Defined in oneM2M TS-0004 [4]. |
| creationTime | All | ct | Defined in oneM2M TS-0004 [4]. |
| labels | tefClientReg, tefKeyReg | lbl | Defined in oneM2M TS-0004 [4]. |
| creator | tefClientReg, tefKeyReg | cr | Defined in oneM2M TS-0004 [4]. |
| fqdn | tefClientReg, tefKeyReg | fq |  |
| assignedSymmKeylID | tefClientReg | aski |  |
| tefClientCfg | tefClientReg | ccfg |  |
| targetIDs | tefKeyReg | tgis |  |
| keyValue | tefKeyReg | kv |  |
| NOTE: Marked short names have been already assigned for primitive parameters in oneM2M TS-0004 [4] |

## Z.3 Security-specific oneM2M Resource types

In protocol bindings resource type names shall be translated into short names of Table Z.3-1.

Table Z.3-1: Security-specific Resource Type Short Names

| Attribute Name | Short Name |
| --- | --- |
| TEF | tef |
| tefClientReg | tcr |
| tefKeyReg | tkr |

## Z.4 Security-specific oneM2M Complex data type members

In protocol bindings complex data types member names shall be translated into short names of Table Z.4-1.

Table Z.4-1: Security-specific oneM2M Complex data type member short names

| Member Name | Occurs in | Short Name | Notes |
| --- | --- | --- | --- |
| tefClientRegCfg | tefClientCfg | tcrc |  |
| tefKeyRegCfg | tefClientCfg | tkrc |  |
| expirationTime | tefClientRegCfg, tefKeyRegCfg | et* | Defined in oneM2M TS-0004 [4]. |
| labels | tefClientRegCfg, tefKeyRegCfg | lbl* | Defined in oneM2M TS-0004 [4]. |
| fqdn | tefClientRegCfg, tefKeyRegCfg | fq* |  |
| URI | tefClientRegCfg | uri | Defined in oneM2M TS-0004 [4]. |
| httpPort | tefClientRegCfg | hpt |  |
| coapPort | tefClientRegCfg | cpt |  |
| websocketPort | tefClientRegCfg | wpt |  |
| ppsk | tefClientRegCfg | pk |  |
| rpsk | tefClientRegCfg | rk |  |
| certAuth | tefClientRegCfg | cert |  |
| credID | tefClientRegCfg | crdi |  |
| caCerts | tefClientRegCfg | cact |  |
| SUID | tefKeyRegCfg | suid |  |
| targetIDs | tefKeyRegCfg | tgis |  |
| NOTE: * marked short names have been already assigned to an attribute in Table Z.2-1. |

### -----------------------End of change 3 -------------------------

# Comments

Not a field

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value

This reference is not a field value