| oneM2M Technical Specification |
| --- |
| Document Number | oneM2M-TS-00xx-V-0.1.0 Editor's note: The TS number will be assigned once this initial version is approved by WG4 SEC. |
| Document Name: | MAF and MEF Interface Specification |
| Date: | 2016-12-09 |
| Abstract: | This specification defines the reference points Mmaf and Mmef of oneM2M nodes (ADN, ASN, MN, IN) with the M2M Authentication Function (MAF) and the M2M Enrolment Function (MEF) |
| Template Version: 08 September 2015 (Dot not modify) |

This Specification is provided for future development work within oneM2M only. The Partners accept no liability for any use of this Specification.

The present document has not been subject to any approval process by the oneM2M Partners Type 1.  Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices.

About oneM2M

The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide.

More information about oneM2M may be found at:  http//www.oneM2M.org

Copyright Notification

© 2016, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSTDI, TTA, TTC).

All rights reserved.

The copyright extends to reproduction in all media.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

# Contents

Contents	3

1	Scope	4

2	References	4

2.1	Normative references	4

2.2	Informative references	4

3	Definitions and abbreviations	4

3.1	Definitions	4

3.2	Abbreviations	5

4	Conventions	5

5	General Description	5

5.1	Introduction to the MAF Interface	5

5.2	MAF Interface Overview	6

6	Processing and Representation of Primitives	7

7	Resource types definitions	8

7.1	Resource Type <MAFBase>	8

7.2	Resource Type <mafClientReg>	9

7.3	Resource Type <symmKeyReg>	9

8	Resource-type specific procedures and definitions	10

8.1	Resource Type <MAFBase>	10

8.1.1	Introduction	10

8.1.2	<MAFBase> resource specific procedures on CRUD operations	10

8.1.2.1	Create	10

8.1.2.2	Retrieve	11

8.1.2.4	Delete	11

8.2	Resource Type <mafClientReg>	12

8.2.1	Introduction	12

8.2.2	<mafClientReg> resource specific procedures on CRUD operations	12

8.2.2.1	Create	12

8.2.2.2	Retrieve	13

8.2.2.3	Update	13

8.2.2.4	Delete	14

8.3	Resource Type <symmKeyReg>	14

8.3.1	Introduction	14

8.3.2	<symmKeyReg> resource specific procedures on CRUD operations	15

8.3.2.1	Create	15

8.3.2.2	Retrieve	16

8.3.2.3	Update	17

8.3.2.4	Delete	17

9	Short Names	17

Proforma copyright release text block	18

Annexes	18

History	19

# 1	Scope

The present document specifies communication between the M2M Authentication Function (MAF) and MAF clients on the reference point Mmaf and between the M2M Enrolment Function (MEF) and MEF clients on the reference point Mmef.

# 2	References

## 2.1	Normative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the reference document (including any amendments) applies.

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M TS-0001: "Functional Architecture".

[2]	oneM2M TS-0003: "Security Solutions".

[3]	oneM2M TS-0004: "Service Layer Core Protocol Specification”

[4]	oneM2M TS-0008: " CoAP Protocol Binding”.

[5]	oneM2M TS-0009: " HTTP Protocol Binding”.

[6]	oneM2M TS-0010: " MQTT Protocol Binding”.

[7]	oneM2M TS-0020: " WebSocket Protocol Binding”.

## 2.2	Informative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the reference document (including any amendments) applies.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules.

NOTE:	Available at http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf.

# 3	Definitions and abbreviations

For the purposes of the present document, the terms and definitions given in oneM2M TS-0011 [TS-0011], oneM2M TS-0003 [2] and the following apply:

## 3.1	Definitions

MAF Client: functionality for performing MAF procedures on behalf of an associated CSE or AE, or on behalf of CSE or AE(s) present on an associated Node.

MAF interface: Communication interface between a MAF and a MAF Client identified by reference point Mmaf

## 3.2	Abbreviations

MAF	M2M Authentication Function

MEF	M2M Enrolment Function

# 4	Conventions

The key words “Shall”, ”Shall not”, “May”, ”Need not”, “Should”, ”Should not” in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1]

# 5	General Description

Editor’s Note: The subclauses below will be updated when the MEF interface will be introduced

## 5.1	Introduction to the MAF Interface

The MAF Interface is a simple variant of the Mcc/Mca reference points specifying the interaction of MAF Clients with a M2M Authentication Function (MAF), acting on behalf of an administrating stakeholder such as an M2M SP or third party M2M Trust Enabler (MTE). The present document does not specify the operation and management of the MAF required to support these procedures.

A MAF Client interacts with the MAF on behalf of Node (ADN, ASN, IN or MN), or a CSE or an AE.

Figure 5.1-1 defines the reference point Mmaf between MAF clients and a MAF.

Figure 5.1-1: Reference Architecture for MAF

The administrating stakeholder authorizes the MAF’s services to MAF clients, and oversees authorizing the distribution of symmetric keys. A MAF may provide its services on behalf of multiple administrating stakeholders. A MAF Client may be associated with multiple administrating stakeholders, each administrating the use of the MAF within a different scope.

NOTE 1: 	The administrating stakeholder could be an M2M SP administrating the registration and distribution of credentials used for SAEFs and ESPrim within the M2M SP’s Domain.

NOTE 2:	The administrating stakeholder could be an MTE administrating the registration and distribution of credentials for ESPrim and ESData to MAF Clients belonging to a particular Application Service Provider, where the MAF Clients could be distributed over multiple M2M SP domains.

The present specification has no impact on the specifications in TS-0001 [1] and TS-0004 [3]. However, the MAF Interface uses much of the specification in TS-0004 [3] and in particular allows use of the HTTP binding in TS-0008 [4], the CoAP binding in TS-0009 [5] and the WebSocket binding in TS-0020 [7].

NOTE 3: 	The MQTT binding in TS-0010 [6] is not suitable for the MAF Interface, because the MAF Interface assumes a TLS or DTLS connection from the MAF Client to the MAF – which is not possible using the MQTT binding

The MAF Interface incorporates the following concepts from the Mcc/Mca reference points:

- The concept of operations acting on resources.

- The resource addressing from Mcc/Mca is used.

- The universal attributes and some common attributes of resources.

The MAF Interface differs from Mcc/Mca in the following ways:

- The MAF Client can only communicate directly with the MAF – there are no transited CSEs. Only Blocking Mode communication method is supported.

- None of the resource types applicable on Mcc/Mca are used.

  - Access control decisions use simple access control list for Retrieve access, and <accessControlPolicy> resources are not used for resources hosted by the MAF. A consequence of this is that the accessControlPolicyIDs attributes are not needed in the resources hosted by the MAF.

  - The <subscription> resource and NOTIFY operations are not supported.

  - There is no AE registration or CSE registration, but a similar process where a MAF Client creates a <mafClientReg> (MAF Client registration record) resource on the MAF.

  - There are no announced resources.

The hierarchy of resources hosted by a MAF shall be as follows:

- <MAFBase> resource type is the structural root for all the resources that are residing on a MAF. This resource is implicitly created by the MAF and uses the fixed resource name “maf” and contains following child resources:

  - <mafClientReg> resource. It confirms the MAF Client’s registration to an administrating stakeholder, and can contain configuration information to be returned to the MAF Client.

  - <symmKeyReg> resources. It is created by the MAF Client, and contains symmetric keys for retrieval by another MAF Client.

## 5.2	MAF Interface Overview

This MAF Interface overview is based on the specification in clause 6 of oneM2M TS-0004 [3].

Identifiers such as M2M-SP-ID, AE-ID and CSE-ID as defined in 6.2.3 of [3] also apply to the MAF Interface. M2M Trust Enablers (MTEs) are identified using an M2M-SP-ID.

Resources are addressed as specified in clause 6.2.4 in [3].

Common data types applicable to the MAF Interface are inherited from clause 6.3 of [3].

Table 5.2-1 and 5.2-2 list the request and response primitive parameters inherited from clauses 6.4.1 and 6.4.2 in [3], respectively; the data types of these parameters are unchanged.

NOTE:	All other optional request and response primitive parameters defined in clause 6.4.1 of [3] are not used on the MAF Interface.

Table 5.2-1: MAF Interface request primitive parameters

| Parameter | Multiplicity | Notes |
| --- | --- | --- |
| Operation | 1 |  |
| To | 1 |  |
| From | 0..1 | If not present, the MAF internally assigns From to be the identity of the Node, CSE or AE associated with the credential used for the MAF Handshake procedure. |
| Request Identifier | 1 |  |
| Resource Type | 0..1 |  |
| Content | 0..1 |  |
| Result Content | 0..1 |  |

Table 5.2-2: MAF Interface response primitive parameters

| Parameter | Multiplicity | Notes |
| --- | --- | --- |
| Response Status Code | 1 |  |
| Request Identifier | 1 |  |
| Content | 0..1 |  |

Data types associated with resources applicable to the MAF Interface are defined in clause 7.

Table 5.2-3 lists the response status codes from clause 6.6 [3] which are supported by the MAF Interface.

Table 5.2-3: Response status codes supported by the MAF Interface

| Response status codes | Interpretation |
| --- | --- |
| 2000 | OK |
| 2001 | CREATED |
| 2002 | DELETED |
| 2004 | UPDATED |
| 4000 | BAD_REQUEST |
| 4004 | NOT_FOUND |
| 4005 | OPERATION_NOT_ALLOWED |
| 4103 | ACCESS_DENIED |
| 5000 | INTERNAL_SERVER_ERROR |

Editor’s note: Unclear which, if any, of the oneM2M specific MIME media types from clause 6.7 [3] are supported.

Virtual resources (clause 6.8 [3]) are not supported by the MAF Interface.

# 6	Processing and Representation of Primitives

Editor’s Note: This clause will be updated when the MEF interface will be introduced

This clause is based on the specification in clause 7 and 8 of oneM2M TS-0004 [3].

The MAF Interface request primitive format conforms to clause 7.2.1.1 [3], constrained to the CRUD operations, with request parameters listed in Table 5.2-1.

The MAF Interface response primitive format conforms to clause 7.2.1.2 [3], constrained to the CRUD operations, with response parameters listed in Table 5.2-2.

The MAF Interface generic resource request procedure for originators and receivers conforms to clauses 7.2.2.1 and 7.2.2.2 of [3], with the following clarification:

- The MAF Client acts as the originator, and the MAF acts as the receiver and resource hosting entity.

- The MAF Handshake procedure (clause 8.8.2.2 of oneM2M TS-0003 [3]) is used for mutual authentication of the MAF Client and MAF.

- The operation shall be one of the CRUD operations.

- The request and response parameters shall conform to Table 5.2-1 and Table 5.2-2.

- “Blocking Mode” communication method shall be used.

- The step Recv-6.3: “Check authorization of the Originator” is replaced by the authorization processes described in the MAF Interface resource-type specific procedures in clause 8.

The originator actions, receiver actions and Hosting CSE actions conform to clause 7.3 [3], with clause 7.3.3.17 [3] replaced by the authorization processes described in the MAF Interface resource-type specific procedures in clause 8.

The management common operations in clause 7.3.4 [3] do not apply to the MAF Interface.

The resource-type-specification conventions apply to the specification in clause 8, but the remainder of clause 7.4 [3] does not apply to the MAF Interface.

Clause 7.5.1 [3] (regarding Notification) does not apply to the MAF Interface. Elements contained in the Content primitive parameter conform to clause 7.5.2 [3].

The representation of MAF Interface primitives in data transfer conforms to Clause 8. Clause 9 (tbc.) contains additional short names specific to the MAF Interface.

Editor’s note:  the clause that defines the short names will be added

# 7	Resource types definitions

## 7.1	Resource Type <MAFBase>

The <MAFBase> resource shall represent a MAF.

The <MAF> resource shall contain the child resources specified in table 7.1-1.

Table 7.1-1: Child resources of <MAFBase> resource

| Child Resources of <MAFBase> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <mafClientReg> | 0..n | See clause 7.2 |
| [variable] | <symmKeyReg> | 0..n | See clause 7.3 |

The <MAF>Base resource shall contain the attributes specified in table 7.1-2.

Table 7.1-2: Attributes of <MAFBase> resource

| Attributes of <MAFBase> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceID | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceName | 1 | RO | See clause 9.6.1.3 of [1]. Shall be fixed to “maf”. |
| expirationTime | 1 | RO | See clause 9.6.1.3 of [1]. |
| creationTime | 1 | RO | See clause 9.6.1.3 of [1]. |

## 7.2	Resource Type <mafClientReg>

The <mafClientReg> resource shall represent a MAF Client enrolled with an M2M SP or M2M Trust Enabler (MTE).

NOTE: 	A single MAF Client may be enrolled with at most one M2M SP and any number of MTEs (typically enabling end-to-end security to MAF Clients outside the MAF Client’s M2M SP’s domain). Consequently, a MAF Client may be associated with multiple <mafClientReg> resources on multiple MAFs.

The <mafClientReg> resource shall contain no child resources.

The <mafClientReg> resource shall contain the attributes specified in table 7.2-1.

Table 7.2-1: Attributes of <mafClientReg> resource

| Attributes of <mafClientReg> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceID | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceName | 1 | RO | See clause 9.6.1.3 of [1]. |
| parentID | 1 | RO | See clause 9.6.1.3 of [1]. |
| expirationTime | 1 | WO | See clause 9.6.1.3 of [1]. |
| creationTime | 1 | RO | See clause 9.6.1.3 of [1]. |
| labels | 1 | RW | See clause 9.6.1.3 of [1]. |
| creator | 1 | WO | See clause 9.6.1.3 of [1]. Editor's note: a new attribute may need to be defined which allows Node-ID in addition to CSE-ID and AE-ID |
| fqdn | 1 | WO | FQDN of the M2M SP or MTE who is the administrating stakeholder of this enrolment |
| assignedSymmKeylID | 0..1 | RO | When the MAF Client uses a symmetric key to authenticate to the MAF, then the MAF may use this attribute to provide a symmetry key identifier within the domain of the MAF. Assigned by the MAF. |

## 7.3	Resource Type <symmKeyReg>

The <symmKeyReg> resource shall represent a symmetric key that a source MAF Client has established with the MAF for distributing to authorized Target MAF Clients and/or another MAF. The MAF Client provides a list of authorized Targets when the resource is created – the present document does not specify how the MAF associates the list with the resource. The MAF, is coordination with the identified administrating stakeholder (M2M SP or MTE), can modify the list of authorized Targets and the expirationTime.

The <symmKeyReg> resource shall contain no child resources.

The <symmKeyReg> resource shall contain the attributes specified in table 7.3-1.

Table 7.3-1: Attributes of <symmKeyReg> resource

| Attributes of <symmKeyReg> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceID | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceName | 1 | RO | See clause 9.6.1.3 of [1]. This value is used as the relative part of the identifier for the symmetric key in security protocols. |
| parentID | 1 | RO | See clause 9.6.1.3 of [1]. |
| expirationTime | 1 | WO | See clause 9.6.1.3 of [1]. |
| creationTime | 1 | RO | See clause 9.6.1.3 of [1]. |
| labels | 0..1 | RW | See clause 9.6.1.3 of [1]. |
| creator | 1 | RO | See clause 9.6.1.3 of [1]. |
| fqdn | 1 | WO | FQDN of the administrating stakeholder (M2M SP or MTE) associated with this enrolment. |
| SUID | 1 | WO | An SUID constraining the use of the symmetric key associated with this resource |
| targetIDs | 1 (L) | RW | List of AE-ID(s) and/or CSE-ID(s) and/or and/or Node-ID(s) identifying the AE(s) and/or CSE(s) and/or Node(s) authorized to retrieve the resource. Only the creator and administrating stakeholder (identified by fqdn) are authorized to access this attribute. |
| keyValue | 1 | WO | The value of the key to be provided to the identifier targets. May be provided in the Create request or derived by the MAF Client and MAF from the TLS handshake parameters. |

# 8	Resource-type specific procedures and definitions

## 8.1	Resource Type <MAFBase>

### 8.1.1	Introduction

A <MAFBase> resource shall represent a MAF. This <MAFBase> resource shall be the root for all the resources that are residing on the MAF.

The <MAFBase> resource has no attributes.

Table 8.1.1-1: Child resources of <MAFBase> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to Resource Type Definition |
| --- | --- | --- | --- |
| <mafClientReg> | [variable] | 0..n | Clause 7.2 |
| <symmKeyReg> | [variable] | 0..n | Clause 7.3 |

### 8.1.2	<MAFBase> resource specific procedures on CRUD operations

#### 8.1.2.1	Create

Originator:

The <MAFBase> resource shall not be created via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

If the request is received, the MAF shall execute the following steps in order.

- "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

- "Send the Response primitive".

#### 8.1.2.2	Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1 of [3] with clarifications discussed in clauses 5.2 and 6.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [3] with clarifications discussed in clauses 5.2 and 6, and performing the following step in the place of step Recv-6.3: “Check authorization of the Originator”:

The Receiver shall allow all Originator’s to retrieve this resource.

##### 8.1.2.3	Update

Originator:

The <MAFBase> resource shall not be updated via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

- If the request is received, the MAF shall execute the following steps in order.

- "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

- "Send the Response primitive".

#### 8.1.2.4	Delete

Originator:

The <MAFBase> resource shall not be DELETEed via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

- If the request is received, the MAF shall execute the following steps in order.

- "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

- "Send the Response primitive".

## 8.2	Resource Type <mafClientReg>

### 8.2.1	Introduction

A <mafClientReg> resource shall represent a MAF Client enrolled with the MAF on behalf of an M2M Service Provider or M2M Trust Enabler. A <mafClientReg> resource shall be a child resource of the MAF’s <MAFBase> resource.

Table 8.2.1-1: Universal/Common Attributes of <mafClientReg> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | NP | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| creationTime | NP | NP |
| expirationTime | M | M |
| labels | O | O |
| creator | NP | NP |

Table 8.2.1-2: Resource Specific Attributes of <mafClientReg> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| Fqdn | M | NP | xs:anyURI | No default |
| assignedSymmKeyID | NP | NP | sec:credentialID | No default |

The <mafClientReg> resource shall contain no child resources.

### 8.2.2	<mafClientReg> resource specific procedures on CRUD operations

#### 8.2.2.1	Create

Originator:

No change from the generic procedures in clause 7.2.2.1 of [3] with clarifications discussed in clauses 5.2 and 6, and with following differences:

In step Orig-6.0: “Process Response primitive”, if the Originator used a symmetric key to authenticate to the MAF, and the <mafClientReg> resource in the response contained an assignedSymmKeyID then the originator shall use the assignedSymmKeyID to identify this symmetric key when it is subsequently used in authenticating to the MAF.

Editor's note: May need specific text to allow for Node-ID in From.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [3] with clarifications discussed in clauses 5.2 and 6, and with following differences:

The Receiver shall performing the following steps in order in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized to register with the administrating stakeholder (M2M SP or MTE) identified by fqdn attribute. The present document does not specify how the Receiver makes this determination.

  - If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

  - If the Originator is authorized, then the Receiver shall allow the request.

The Receiver shall perform the following steps in order as part of “Create the resource” (clause 7.3.3.5)” during Step Recv-6.5: “Create/Update/Retrieve/Delete/Notify operation is performed”:

- If the Originator authenticated using symmetric key with a key identifier which does not use the Receiver’s FQDN, then

  - The Receiver shall assign a symmetric key identifier with the Receiver’s FQDN and with relative part which is unique within the scope of symmetric key identifiers issued by the Receiver. The Receiver shall associate this symmetric key identifier with the symmetric key used for authenticating the Originator.

  - The Receiver shall set the assignedSymmKeyID attribute to be the Credential-ID formed from the assigned symmetric key identifier as specified in clause 10.4.

- If the Originator authenticated using a symmetric key with a key identifier which does not use the Receiver’s FQDN, or if the Originator authenticated using a certificate, then the Receiver shall not include an assignedSymmKeyID attribute in the created resource.

- The Receiver shall assign the creator attribute to an AE-ID or CSE-ID or Node-ID on instructions from the administrating stakeholder. The present document does not specify any details of how the AE-ID or CSE-ID or Node-ID is determined.

- The Receiver may assign the mafClientCfg attribute on instructions from the administrating stakeholder.

#### 8.2.2.2	Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1 of [3] with clarifications discussed in clauses 5.2 and 6.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [3] with clarifications discussed in clauses 5.2 and 6.3, performing the following steps in order in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized by checking if the Originator is the creator of the resource.

Editor's note: May need specific text to allow for Node-ID in From and the creator attribute.

- If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

- If the Originator is authorized, then the Receiver shall allow the request.

#### 8.2.2.3	Update

Originator:

The <mafClientReg> resource shall not be updated via API.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [3] with clarifications discussed in clauses 5.2 and 6, and with the following differences:

The Receiver shall perform the following step in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized by checking if the Originator is the creator of the resource.

Editor's note: May need specific text to allow for Node-ID in From and the creator attribute.

- If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

- If the Originator is authorized, then the Receiver shall allow the request.

The Receiver shall perform the following steps in order as part of “Update the resource” (clause 7.3.3.7)” during Step Recv-6.5: “Create/Update/Retrieve/Delete/Notify operation is performed”:

- If the Originator was the Creator of the resource, then the Receiver shall perform steps 2 and 3 in clause 8.2.2.1.

#### 8.2.2.4	Delete

Originator:

No change from the generic procedures in clause 7.2.2.1 of [3] with clarifications discussed in clauses 5.2 and 6.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [3] with clarifications discussed in clauses 5.2 and 6, performing the following step in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized by checking if the Originator is the creator of the resource.

Editor's note: May need specific text to allow for Node-ID in From and the creator attribute.

- If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

- If the Originator is authorized, then the Receiver shall allow the request.

## 8.3	Resource Type <symmKeyReg>

### 8.3.1	Introduction

A <symmKeyReg> resource shall represent a symmetric key registered with the MAF and administrated by the identified administrating stakeholder. A <symmKeyReg> resource shall be a child resource of an <MAFBase> resource.

Table 8.3.1-1: Universal/Common Attributes of <symmKeyReg>resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | NP | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| creationTime | NP | NP |
| expirationTime | M | M |
| creator | NP | NP |
| labels | O | O |

Table 8.3.1-2: Resource Specific Attributes of <symmKeyReg> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| fqdn | M | NP | xs:anyURI | No default |
| SUID | M | NP | m2m:suid | No default |
| targetIDs | O | O | m2m:listOfM2MID | No default |
| keyValue | O | NP | xs:base64binary | No default |

The <symmKeyReg> resource shall contain no child resources.

### 8.3.2	<symmKeyReg> resource specific procedures on CRUD operations

#### 8.3.2.1	Create

Originator:

No change from the generic procedures in clause 7.2.2.1 of [3] with clarifications discussed in clauses 5.2 and 6, and with following differences:

In step Orig-1.0: “Compose of a Request primitive”, the

- Originator shall select to either use a key derived from the TLS handshake or use another key provided by the Originator.

  - If the Originator selects to use a key derived from the TLS handshake, then the Originator shall not include the keyValue attribute in the <symmKeyReg> resource of the request.

  - If the Originator selects to provide a key other than a key derived from the TLS handshake, the Originator shall include the value of this key in the keyValue attribute in the <symmKeyReg> resource of the request.

In step Orig-6.0: “Process Response primitive”, the following steps shall be performed

- If the Originator selected to use a key derived from the TLS handshake (see difference to step Orig-1.0 above), then the Originator shall perform the following steps in order to generate the value for the keyValue attribute

  - The Originator shall apply the TLS export mechanism described in clause 10.3.1 of [2] to generate a TLS-export-key.

  - The Originator shall apply the usage-constrained key derivation algorithm in clause 10.3.7 of [2] to derive the keyValue from TLS-export-key, fqdn, SUID and the resourceName assigned by the Receiver to the created resource.

- The originator shall record the resourceName attribute of the created resource as the relative part of the key identifier for the symmetric key which is to be assigned to the value for the keyValue attribute.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [3] with clarifications discussed in clauses 5.2 and 6, and with following differences:

The Receiver shall perform the following steps in order in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall ensure that the following criteria are satisfied, with administrating stakeholder being the stakeholder matching the fqdn attribute of the <symmKeyReg> resource in the Create request:

  - The Originator is enrolled with the administrating stakeholder; that is, there is a non-expired <mafClientReg> resource whose creator attribute matches the Originator’s AE-ID or CSE-ID or Node-ID, and whose fqdn attribute identifies the administrating stakeholder.

Editor's note: May need specific text to allow for Node-ID in From and the creator attribute.

  - The Receiver determines that the administrating stakeholder allows the creation of the resource. The present document does not specify how the Receiver makes this determination.

- If these criteria are not met, then the Receiver shall shall execute the following steps in order.

  - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

  - "Send the Response primitive".

- Otherwise, then the Receiver shall allow the request.

The Receiver shall perform the following steps in order as part of “Create the resource” (clause 7.3.3.5)” during Step Recv-6.5: “Create/Update/Retrieve/Delete/Notify operation is performed”:

- If the keyValue attribute is not present in the <symmKeyReg> resource in the request, then the Receiver shall perform the following steps in order to generate the value for the keyValue attribute

  - The Receiver shall apply the TLS export mechanism described in clause 10.3.1 of [2] to generate a TLS-export-key.

  - The Receiver shall apply the usage-constrained key derivation algorithm in clause 10.3.7 of [2] to derive the value for the keyValue attribute from TLS-export-key, fqdn, SUID and the resourceName assigned by the Receiver to the created resource.

#### 8.3.2.2	Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1 of [3] with clarifications discussed in clauses 5.2 and 6.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [3] with clarifications discussed in clauses 5.2 and 6, and with following differences:

The Receiver shall perform the following steps in order in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized by checking if the Originator is the creator of the resource or the Originator is identified in the targetIDs.

Editor's note: May need specific text to allow for Node-ID in From, and the creator attribute.

- If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

- If the Originator is authorized, then the Receiver shall allow the request.

#### 8.3.2.3	Update

Originator:

No change from the generic procedures in clause 7.2.2.1 of [3] with clarifications discussed in clauses 5.2 and 6.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [3] with clarifications discussed in clauses 5.2 and 6, and performing the following step in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized by checking if the Originator is the creator of the resource.

Editor's note: May need specific text to allow for Node-ID in From, and the creator attribute.

- If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

- If the Originator is authorized, then the Receiver shall allow the request.

#### 8.3.2.4	Delete

Originator:

No change from the generic procedures in clause 7.2.2.1 of [3] with clarifications discussed in clause 5.2 and 6.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [3] with clarifications discussed in clauses 5.2 and 6, and performing the following step in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized by checking if the Originator is the creator of the resource.

Editor's note: May need specific text to allow for Node-ID in From, and the creator attribute.

- If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

- If the Originator is authorized, then the Receiver shall allow the request.

# 9	Short Names

# Proforma copyright release text block

This text box shall immediately follow after the heading of an element (i.e. clause or annex) containing a proforma or template which is intended to be copied by the user. Such an element shall always start on a new page.

Notwithstanding the provisions of the copyright clause related to the text of the present document, oneM2M grants that users of the present document may freely reproduce the <proformatype> proforma in this {clause|annex} so that it can be used for its intended purposes and may further publish the completed <proformatype>.

<PAGE BREAK>

## Annexes

Each annex shall start on a new page (insert a page break between annexes A and B, annexes B and C, etc.).

Use the Heading 9 style for the title and the Normal style for the text.

Annex <A> (Informative/Normative):Remove Informative or Normative as appropriatTitle of annex (style H9)

<Text>

<PAGE BREAK>

Annex <B>(Informative/Normative): Remove Informative or Normative as appropriateTitle of annex (style H9)

<Text>

B.1	First clause of the annex (style H1)

<Text>

B.1.1	First subdivided clause of the annex (style H2)

<Text>

<PAGE BREAK>

The following text is to be used when appropriate:

Annex <y>:
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself

It shall not include references mentioned in the document.

Use the Heading 9 style for the title and B1+ or Normal for the text.

<Publication>: "<Title>".

OR

<Publication>: "<Title>".

<PAGE BREAK>

# History

This clause shall be the last one in the document and list the main phases (all additional information will be removed at the publication stage).

| Publication history |
| --- |
| V1.1.1 | <dd-Mmm-yyyy> | <Milestone> |

| Draft history (to be removed on publication) |
| --- |
| V0.1.0 | 09-Dec-2016 | Initial skeleton, scope and content agred at SEC#26: SEC-2016-0166R01-TEF_Interface_Specification_skeleton SEC-2016-0167R01-TEF_Interface_Specification_Scope SEC-2016-0168R01-TEF_Interface_Specification_main_body |