| Input Contribution |
| --- |
| Meeting ID* | SEC #28 |
| Title:* | Remote Security Provisioning Issue for Decentralized Authentication |
| Source:* | Jie Shi, Huawei, shi.jie1@huawei.com Guilin Wang, Huawei, wang.guilin@huawei.com Yanjiang Yang, Huawei, yang.yanjiang@huawei.com |
| Date:* | 2017-03-15 |
| Input related to* | TR-0041 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TS-0003 |
| Decision requested or recommendation:* | It is proposed to agree the content in this contribution |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### ----------------------start of change 1 ----------------------------------------------

# 6	Issues and Requirements

6.1 Decentralized Authentication Requirement

Clause 6.5 of TR-0026, Vehicular Domain Enabler, is “Use Cases for Electronic Toll Collection (ETC) service”. Two security requirements are set out in 6.5.10 of TR-0026 as follows:

…

- The M2M System shall enable each of many M2M devices to perform mutual authentication with each of many M2M gateways.

- The M2M System shall enable mutual authentication of M2M devices and M2M gateways in a timely manner.

Fulfilling these two requirements demands an efficient and flexible decentralized authentication solution for peer-to-peer communications.

6.2 IBC Credential Remote Provisioning Issue for Decentralized Authentication

Decentralized authentication is used to enable each entity to perform mutual authentication with many other entities in a timely manner, where all of these entities only have one credential.

Certificate-based mutual authentication and IBC (identity-based cryptography) based mutual authentication can both be used to realize decentralized authentication. Certificate-based mutual authentication may not be suitable for some IoT scenarios (e.g., V2V in smart vehicle), as the communication overhead compared to the message needed to be transmitted is high. So, IBC-based mutual authentication can be used in such scenarios.

In order to perform decentralized authentication using IBC based mutual authentication techniques, IBC credentials need to be provisioned to entities. Thus, the M2M System needs to provide mechanisms for remote provisioning of IBC credentials to entities that require IBC based mutual authentication.

### ----------------------end of change 1 -------------------------------------------------