| Input Contribution |
| --- |
| Meeting ID* | SEC #28 |
| Title:* | Pre-provisioned Symmetric Key Remote Security Provisioning Framework for Decentralized Authentication |
| Source:* | Jie Shi, Huawei, shi.jie1@huawei.com Guilin Wang, Huawei, wang.guilin@huawei.com Yanjiang Yang, Huawei, yang.yanjiang@huawei.com |
| Date:* | 2017-03-15 |
| Input related to* | TR-0041 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TS-0003 |
| Decision requested or recommendation:* | It is proposed to agree the content in this contribution |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### ----------------------start of change 1 ----------------------------------------------

# 2	References

The following text block applies.

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative references

As a Technical Report (TR) is entirely informative it shall not list normative references.

The following referenced documents are necessary for the application of the present document.

[1]					oneM2M TS-0003 Security Solutions.

[2]					IETF RFC 4279: “Pre-Shared Key Ciphersuites for Transport Layer Security (TLS)”.

[3]					IETF RFC 5705: “Keying Material Exporters for Transport Layer Security (TLS)”.

## 2.2	Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	Dan Boneh, Matthew K. Franklin: “Identity-Based Encryption from the Weil Pairing”, Proceedings of CRYPTO 2001.

[i.2]	RFC 6507: “Elliptic Curve-Based Certificateless Signatures for Identity-Based Encryption (ECCSI)”, February, 2012.

### ----------------------end of change 1 ----------------------------------------------

### ----------------------start of change 2 ----------------------------------------------

## 3.2	Symbols

||:  Concatenation

IdA: Identity of entity A

IdB: Identity of entity B

MPK: Master public key

MSK: Master secret key

SkA: Private key of entity A

SkB: Private key of entity B

## 3.3	Abbreviations

DH: Diffie-Hellman

DTLS: Datagram Transport Layer Security

IBC: Identity Based Cryptography

PKG: Private Key Generator

PKI: Public Key Infrastructure

PSK: Pre-shared Key

RSPF: Remote Security Provisioning Framework

TLS: Transport Layer Security

### ----------------------end of change 2 ----------------------------------------------

### ----------------------start of change 3 ----------------------------------------------

## 7.2 Pre-Provisioned Symmetric Key Remote Security Provisioning Framework for Decentralized Authentication

### 7.2.1 Introduction

This clause is proposed to solve the issue proposed in Clause 6.2.

Remote Security Provisioning Frameworks (RSPFs) provision credentials to an Enrollee (CSE or AE), which are introduced in Clause 8.3 of [1] to provision credentials to an Enrollee where the credentials include a symmetric key or a certificate. In this Clause, Pre-Provisioned Symmetric Key RSPFs are used to provision identity-based cryptography (IBC) credential to an Enrolee for decentralized authentication.

An IBC credential includes three elements, denoted by (Id, Sk, MPK), where Id and Sk are the identity and the corresponding private key of an Enrolee, MPK is the master public key which is a public system parameter.

IBC credential may also be pre-provisioned; that is, provisioned using means other than a Remote Security Provisioning Framework. The method for pre-provisioning can be deployed dependent.

### 7.2.2 Detailed solution

This clause describes the Pre-Provisioned Symmetric Key Remote Security Provisioning Framework for Decentralized Authentication, which is adapted from Clause 8.3.2.1 of [1].

The Bootstrap Credential for this framework is a long-term symmetric key that has been pre-provisioned into the Enrolee and M2M Enrolment Function; this key is called a Pre-Provisioned Symmetric Enrolee Key and is denoted Kpm.

NOTE 1:	Long term Pre-Provisioned Symmetric Enrollee Keys can pose a security risk if not adequately secured, and for this reason it is recommended that Long term Pre-Provisioned Symmetric Enrollee Keys are stored in Secure Environments.

Figure 7.2.2-1 illustrates the sequence of events when using the Pre-Provisioned Symmetric Enrolee Key Remote Security Provisioning Framework for Decentralized Authentication.

Figure 7.2.2-1: The sequence of events when using the Pre-Provisioned Symmetric Key Remote Security Provisioning Framework for Decentralized Authentication

Bootstrap Credential Configuration: The Pre-Provisioned Symmetric Enrolee Key (Kpm) and the corresponding Pre-Provisioned Symmetric Enrolee Key Identifier, denoted KpmID, are pre-provisioned to both entities.

NOTE 2:	This pre-provisioning (by definition) uses mechanisms not specified by oneM2M.

Bootstrap Instruction Configuration: The Enrolee and M2M Enrolment Function are configured with the information needed for authorizing the remote provisioning:

The Enrolee is configured with (or otherwise obtains) the following arguments to initiate remote provisioning:

MEF URI: URI of M2M Enrolment Function for the purpose of routing the (D)TLS exchange.

The Enrolee associates these arguments with the M2M Enrolment Function. The M2M Enrolment Function can be identified to the Enrolee using the Pre-Provisioned Symmetric Enrolee Key Identifier (KpmID) or the M2M Enrolment Function URI.

M2M Enrolment Function is configured with the following arguments to authorize the M2M Enrolment Function to remotely provision the Enrolee for decentralized authentication:

Enrolee's assigned CSE-ID or AE-ID (Enrolee-ID). The M2M Enrolment Function is to provide this entity identity for the Enrolee with the Km or Kpsa.

Enrolment Expiry: Life Time to be applied for the IBC credential generated.

The M2M Enrolment Function associates these arguments with an Enrolee. The Enrolee can be identified to the M2M Enrolment Function using the Pre-Provisioned Symmetric Enrolee Key Identifier (KpmID).

Bootstrap Security Handshake:

- The Enrolee and M2M Enrolment Function shall perform a (D)TLS-PSK handshake [2] to establish a secure session.

The "psk_identity" parameter [2] is set to the value of the Pre-Provisioned Symmetric Enrolee Key Identifier (KpmID).

The "psk" parameter [2] is set to the value of the Pre-Provisioned Symmetric Enrolee Key (Kpm).

The (D)TLS cipher suite profile is specified in clause 10.2.2 of [1] "TLS and DTLS Ciphersuites for TLS-PSK-Based Security Frameworks".

Enrolment Key Generation:

- The Enrolment Key (Ke), RelativeKeID, and Enrolment Re-authentication Key (Ker) are generated from the (D)TLS session secrets by the Enrolee and M2M Enrolment Function using TLS Key Export (IETF RFC 5705 [3]), as described in clause 10.3.1 of [1] "TLS Key Export Details".

- The Enrolment Key Identifier (KeID) is generated from the RelativeKeID and the M2M Enrolment Function's FQDN by the Enrolee and M2M Enrolment Function, as described in clause 10.3.4 of [1] "Generating KeID".

- The Enrolee and M2M Enrolment Function store the Enrolment Key (Ke) and Enrolment Key Identifier (KeID), and Enrolment Re-Authentication Key (Ker).

NOTE 3:	The Enrolment Key Generation for the Pre-Provisioned Symmetric Enrollee Key Remote Security Provisioning Framework is identical to the Enrolment Key Generation for the Certificate-Based Remote Security Provisioning Framework.

Enrolment Exchange:

- The Enrolee shall compose a request of notifying MEF to execute IBC credential enrolment and shall send the request to the MEF’s Enrolment Exchange URI.

- The MEF shall process this request to determine how the Enrolee is to be provisioned.

- The MEF shall compose a response with an indication of IBC credential enrolment and send it to the Enrolee.

- After receiving the response, the Enrolee shall perform IBC credential enrolment procedure as described below:

Note: The Enrolee and the MEF have successfully established a TLS session and communication between the MEF and the PKG is protected by existing secure channel.

  - The Enrolee shall send a request with its identity ID1 (CSE-ID or AE-ID) to the MEF;

  - The MEF shall generate a new identity ID2 for the enrolee based on the received identity and the expiry time for this IBC credential (e.g., adding FQDN and expired time before the received identity) to make sure the new identity is exclusive and forward the new identity to Private Key Generator (PKG);

  - The PKG shall generate private key Sk for the received identity ID2 based on the master public MPK and the master secret key MSK; and send the Sk and MPK back to the MEF;

  - The MEF shall send (ID2, Sk, MPK) to the Enrolee.

- The Enrolee shall store the IBC credential (ID2, Sk, MPK) and shall send a request to the MEF indicating success.

- The MEF shall send a response indicating the end of the enrolment exchange.

- The MEF shall close the TLS/DTLS session.

Use of Remotely Provisioned Credential:

If the Enrolee is remotely provisioned with an IBC credential, then the Enrolee may use the credential to preform decentralized authentication with other entities (CSE or AE) in oneM2M system.

### 7.2.3 Evaluation

The proposed pre-provisioned symmetric key remote security provisioning framework is similar to the pre-provisioned symmetric key remote security provisioning framework in clause 8.3.2.1 of [1]. The communications between the Enrollee and the MEF are transmitted through secure channels (e.g., built by (D)TLS) based on the pre-provisioned symmetric key, so the IBC credential can be securely provisioned to the Enrollee.

### ----------------------end of change 3 -------------------------------------------------