| CHANGE REQUEST |
| --- |
| Meeting ID:* | SEC 30 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Date:* | 2017-07-03 |
| Reason for Change/s:* | Adding details for MEF Client Command processing |
| CR against: Release* | 2A |
| CR against: WI* | Active WI-0057 MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003v2_9_1 |
| Clauses * | 8.3.x (new section) |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | TS-0032 (see related CRs) |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR describes the MEF Client Command processing and includes some editorial corrections to clause 12.

R01:

- Completed MEF Client Command Retrieve/Update Procedures (8.3.x.2/3).

- Completed NO_MORE_COMMANDS MEF Client Command Class-specific Processes (moved from 8.3.x5.1 to 8.3.x.6)

- Added MEF_CLIENT_CMD_ REPEATED_CMD_ID command status (clause 8.3.x.5.5) and corresponding cmdStatusCode (clause 12.3.2.4).

- Rearranged the order of some clauses.

### -----------------------Start of change 1-------------------------------------------

## 8.3.x MEF Client Command Processing

#### 8.3.x.1 Introduction

Purpose: The MEF Client Commands are used by an MEF to control the sequence of Enrolment Exchange procedures executed by the MEF Client.

A MEF Client Command is issued, or reissued, by the MEF to the MEF Client in the response of a MEF Client Command Retrieve procedure (clause 8.3.x.2) or MEF Client Command Update procedure (clause 8.3.x.2). The resulting status, following the attempt to parse and execute the command, is reported to the MEF Client in the request of a MEF Client Command Update procedure (clause 8.3.x.2).

A MEF Client Command Retrieve response or MEF Client Command Update response includes cmdID, cmdDescription, and initial cmdStatus of a MEF Client Command being issued, or reissued, by the MEF to the MEF Client. A MEF Client Command Update request, sent from the MEF Client to MEF, includes cmdID and cmdStatus indicating the result of attempting to pars and execute the command.

These three elements serve the following purposes:

- cmdID: disambiguates between sequential MEF Client Commands issued within the context of an MEF Client Registration (which, in some cases, may be one of multiple MEF Client Registrations on the MEF).  The cmdID serving two purposes: ensuring that a command is not accidentally executed twice; and correlating a MEF Client Command status to the corresponding issued command.

- cmdDescription: providing a description of the command to be executed.

- cmdStatusCode: enables the MEF to indicate if a command is a reissued command or not, and enables the MEF Client to indicate the result of attempting to parse and execute the command.

MEF Client Command procedures are performed within the context of a (non-expired) MEF Client Registration with the MEF.

#### 8.3.x.2 MEF Client Command Retrieve Procedure

Triggering the Procedure: See clause 8.3.4.6 for mechanisms which can trigger MEF Client Command procedures.

Pre-Conditions:

- The MEF and MEF Client have performed an MEF Handshake, see clause 8.3.5.2.2.

- The MEF Client Registration is not expired, and the MEF Client has obtained the MEFClientRegID for the registration.

- The MEF Client shall not send an MEF Client Command Retrieve in between the time when an MEF Client receives an MEF Client Command from the MEF and the time when the MEF Client sends a corresponding MEF Client Command Update to report on the status.

- The MEF Client shall not initiate an MEF Client Command Retrieve while waiting for a MEF Client Command Response from the MEF, unless the MEF takes too long to respond. The time duration for waiting for a response from the MEF is an implementation-specific decision of the MEF Client.

Procedure:

- The MEF Client shall send a MEF Client Command Retrieve request including the information shown in Table 8.3.5.2.4-1.

Table 8.3.x.2-1: MEF Client Command Retrieve Request message information

| Element | Description | Multiplicity |
| --- | --- | --- |
| MEFClientRegID | Identifier for the MEF Client registration record for which the MEF Client Command is being requested. See Pre-Condition B. | 1 |

- Upon receiving the request, the MEF shall process the request. If error cases are encountered, then the MEF shall send an error response.

- If the request is processed successfully, then the MEF shall attempt to retrieve the MEF Client Command currently associated with the identified MEF Client registration record.

  - If there are currently no more MEF Client Command to be issued to the MEF Client, then the MEF forms the cmdDescription as specified in clause 8.3.x.6.

  - If MEF Client Command will trigger a Certificate Provisioning procedure, then the MEF forms the cmdDescription as specified in clause 8.3.x.7.

  - If MEF Client Command will trigger Device Configuration, then the MEF forms the cmdDescription as specified in clause 8.3.x.8.

  - In the case of an MO_NODE MEF Client Command, then the MEF forms the cmdDescription, as specified in clause 8.3.x.9.

- The MEF shall compose a MEF Client Command Retrieval response a containing the following parameters.

Table 8.3.x.2-2: MEF Client Command Retrieve Response message information

| Element | Description | Multiplicity |
| --- | --- | --- |
| cmdID | MEF Client Configuration currently associated with the identified MEF Client registration record | 1 |
| cmdDescription | Description of the MEF Client Command being issued or reissued. | 1 |
| cmdStatusCode | cmdStatusCode set to MEF_CLIENT_CMD_ISSUED or MEF_CLIENT_CMD_REISSUED as appropriate (see clauses 8.3.x.5.2 and 8.3.x.5.3) | 1 |

The MEF shall send the response to the MEF Client.

- The MEF Client shall attempt to parse and execute the response information

  - The MEF Client attempts to parse the Response message information into cmdID, cmdDescription and cmdStatusCode elements; and parse cmdDescription into its constituent cmdClassID and cmdArgs elements. If parsing succeeds, then the MEF client proceeds to step 5b. If parsing fails, then the MEF Client may choose to exit the procedure, or may return to step 1.

  - The MEF Client compares the cmdID of the Response message with cmdID sent in the most recent MEF Client Command Update procedure. If the cmdID values are distinct, then the MEF Client proceeds to step 5.c.  If the cmdID values are identical then the  then the MEF_Client exits the procedure, triggering MEF Client Command Update procedure for this cmdID with cmdStatusCode set to the value for MEF_CLIENT_CMD_REPEATED_CMD_ID.

  - The MEF Client interprets cmdClassID, to determine the corresponding MEF Client Command Class. If the MEF Client supports the MEF Client Command Class then the MEF Client proceeds to step 5.d. If the MEF Client does not support the MEF Client Command Class then the MEF Client exits the procedure, triggering MEF Client Command Update procedure for this cmdID with cmdStatusCode set to the value for MEF_CLIENT_CMD_CLASS_NOT_SUPPORTED.

  - The MEF Client initiates the MEF Client Command Class-specific procedures:

    - The NO_MORE_COMMANDS MEF Client Command Class-specific procedures are specified in clause 8.3.x.5.1.

    - The CERT_PROV MEF Client Command Class-specific procedures are specified in clause 8.3.x.7.

    - The DEV_CFG MEF Client Command Class-specific procedures are specified in clause 8.3.x.8.

    - The MO_NODE MEF Client Command Class-specific procedures are specified in clause 8.3.x.9.

#### 8.3.x.3 MEF Client Command Update procedure

Triggering: The MEF Client shall initiate MEF Client Command Update procedure only when triggered from within the MEF Client Command Retrieve procedure (clause 8.3.x.2), or MEF Client Command Update procedure (the present clause) or a MEF Client Command Class-specific procedure (clauses 8.3.x.5.1, 8.3.x.7, 8.3.x.8, 8.3.x.9). The trigger includes the values for cmdID and cmdStatusCode.

Pre-Conditions:

- The MEF and MEF Client have performed an MEF Handshake, see clause 8.3.5.2.2.

- The MEF Client Registration is not expired, and the MEF Client has obtained the MEFClientRegID for the registration.

Procedure:

- The MEF Client shall send a MEF Client Command Update request including the information shown in Table 8.3.5.2.4-1.

Table 8.3.x.3-1: MEF Client Command Update Request message information

| Element | Description | Multiplicity |
| --- | --- | --- |
| MEFClientRegID | Identifier for the MEF Client registration record for which the MEF Client Command is being requested. See Pre-Condition B. | 1 |
| cmdID | Provided when the procedure was triggered | 1 |
| cmdStatusCode | Provided when the procedure was triggered | 1 |

- Upon receiving the request, the MEF shall process the request.

  - The MEF attempts to parse the request message information into MEFClientRegID, cmdID and cmdStatusCode elements. If parsing succeeds, then the MEF proceeds to step 2b. If parsing fails, then the MEF shall send an MEF Client Command Update response with the BAD_REQUEST request Status Code from Table 5.1.2-3 in TS-0032 [58], and no further steps are performed.

  - The MEF compares the cmdID in the request to the cmdID of the most recently issued MEF Client Commands. If there is no match then the cmdID and cmdStatusCode are discarded. If there is a match, then the MEF can records the cmdID and cmdStatusCode.

- The MEF determines the next MEF Client Command to issue to the MEF Client, as described in step 3 of clause 8.3.x.2.

- The MEF shall compose a MEF Client Command Update response containing the same elements as an MEF Client Command Retrieve response, shown in table 8.3.x.2-2 in step 4 of clause 8.3.x.2. The MEF shall send the response to the MEF Client.

- The MEF Client shall attempt to parse and execute the response message information, as specified in step 5 of clause 8.3.x.2.

#### 8.3.x.4 The cmdDescription element

The cmdDescription elements has type  is comprised of the following elements:

- cmdClassID: identifying a class of MEF Client Commands

- (conditional on cmdClassID) cmdArgs: containing arguments specific to the cmdClass

- (optional) targetID: When the MEF Client is a Node acting on behalf of a CE and/or multiple AE, then the targetID identifies Certificate Provisioning can be  for the cmdClass CERT_PROV

MEF Client Command processing supports the following classes of MEF Client Commands:

- NO_MORE_COMMANDS: indicating that the MEF has no more MEF Client Commands for the MEF Client. The NO_MORE_COMMANDS MEF Client Command is specified in clause 8.3.x.5.2.

- CERT_PROV: for triggering Certificate Provisioning procedures. The CERT_PROV MEF Client Commands are specified in clause 8.3.x.8.

- DEV_CFG: for triggering Device Configuration. The DEV_CFG MEF Client Commands are specified in clause 8.3.x.9.

- MO_NODE: for triggering procedures. The CERT_PROV MEF Client Commands are specified in clause 8.3.x.10.

#### 8.3.x.5 The cmdStatus element

##### 8.3.x.5.1 Introduction

The cmdStatus is used by the MEF and MEF Client to indicate the status of an issued Command. The value in the cmdStatus element is of datatype sec:cmdStatusCode, specified in clause 12.3.2.x, which maps to an interpretation. Table 8.3.x.5.1-1 provides an informative summary of the cmdStatus, with normative description in the remaining sub clauses of 8.3.x.5..

Table 8.3.x.5.1 -1: Overview of the cmdStatus element

| cmdStatus | Assigned by | cmdClass of issued MEF Client Command | Clause |
| --- | --- | --- | --- |
| MEF_CLIENT_CMD_ISSUED | MEF | Any | 8.3.x.5.2 |
| MEF_CLIENT_CMD_REISSUED | MEF | Any | 8.3.x.5.3 |
| MEF_CLIENT_CMD_OK | MEF Client | Any. See NOTE 1. | 8.3.x.5.4 |
| MEF_CLIENT_CMD_REPEATED_CMD_ID | MEF Client | Any | 8.3.x.5.5 |
| MEF_CLIENT_CMD_CLASS_NOT_SUPPORTED | MEF Client | Any. See NOTE 1. | 8.3.x.5.6 |
| MEF_CLIENT_CMD_BAD_ ARGUMENTS | MEF Client | Any. | 8.3.x.5.7 |
| MEF_CLIENT_CMD_UNACCEPTABLE_ARGUMENTS | MEF Client | CERT_PROV, DEV_CFG, MO_NODE | 8.3.x.5.8 |
| MEF_CLIENT_CMD_CERT_PROV_SERVER_ERROR | MEF Client | CERT_PROV | 8.3.x.5.9 |
| MEF_CLIENT_CMD_CERT_PROV_CLIENT_ERROR | MEF Client | CERT_PROV | 8.3.x.5.10 |
| MEF_CLIENT_CMD_DEV_CFG_SERVER_ERROR | MEF Client | DEV_CFG | 8.3.x.5.11 |
| MEF_CLIENT_CMD_DEV_CFG_SERVER_ERROR | MEF Client | DEV_CFG | 8.3.x.5.12 |
| MEF_CLIENT_CMD_MO_NODE_NOT_FOUND | MEF Client | MO_NODE | 8.3.x.5.13 |
| MEF_CLIENT_CMD_MO_NODE_TYPE_CONFLICT | MEF Client | MO_NODE | 8.3.x.5.14 |
| MEF_CLIENT_CMD_MO_NODE_UNACCEPTABLE_ARGS | MEF Client | MO_NODE | 8.3.x.5.15 |
| MEF_CLIENT_CMD_MO_NODE_EXECUTION_ERROR | MEF Client | MO_NODE | 8.3.x.5.16 |
| NOTE 1: In normal circumstances, an MEF Client should not provide this cmdStatus when the issued command has cmdClass indicating NO_MORE_COMMANDS. |

##### 8.3.x.5.2	cmdStatus MEF_CLIENT_CMD_ISSUED

The MEF is issuing the command, and the MEF expects that this is the first time that the MEF Client is receiving the command.

##### 8.3.x.5.3	cmdStatus MEF_CLIENT_CMD_REISSUED

The MEF previously issued the command, and did not receive a corresponding MEF Client Command Update from the MEF Client (in particular, providing the status of the executed command), and consequently the MEF is reissuing the command.

If the MEF Client already performed the command, then it reports the status, otherwise the MEF Client performs the command.

##### 8.3.x.5.4	cmdStatus  MEF_CLIENT_CMD_OK

The MEF Client successfully performed the command

##### 8.3.x.5.5	cmdStatus MEF_CLIENT_CMD_ REPEATED_CMD_ID

The cmdID in the MEF Client Command Response message matches the cmdID sent in the most recent MEF Client Command Update procedure. This would indicate some processing error on the MEF.

##### 8.3.x.5.6	cmdStatus MEF_CLIENT_CMD_CLASS_NOT_SUPPORTED

The MEF Client does not support the requested cmdClass.

##### 8.3.x.5.7	cmdStatus MEF_CLIENT_CMD_BAD_ARGUMENTS

The MEF Client supports the cmdClass, but the MEF Client could not parse cmdArgs.

##### 8.3.x.5.8	cmdStatus MEF_CLIENT_CMD_UNACCEPTABLE_ARGUMENTS

The MEF Client supports the cmdClass, and the MEF Client parsed cmdArgs element, but was unable to process any of the arguments.

##### 8.3.x.5.9	cmdStatus MEF_CLIENT_CMD_CERT_PROV_SERVER_ERROR

The MEF Client supports the CERT_PROV cmdClass, and the MEF Client parsed the cmdsArgs element, but was unable to perform the command due to some error regarding communicating with the Certificate Provisioning server or an error internal to the Certificate Provisioning server.

##### 8.3.x.5.10	cmdStatus MEF_CLIENT_CMD_CERT_PROV_CLIENT_ERROR

The MEF Client supports the CERT_PROV cmdClass, and the MEF Client parsed the cmdsArgs element, but was unable to perform the command due to a processing error on the MEF Client.

##### 8.3.x.5.11	cmdStatus MEF_CLIENT_CMD_DEV_CFG_SERVER_ERROR

The MEF Client supports the DEV_CFG cmdClass, and the MEF Client parsed the cmdsArg element s, but was unable to perform the command due to some error regarding communicating with the Device Configuration server or an error internal to the Device Configuration server.

##### 8.3.x.5.12	cmdStatus MEF_CLIENT_CMD_DEV_CFG_SERVER_ERROR

The MEF Client supports the DEV_CFG cmdClass, and the MEF Client parsed the cmdsArg element s, but was unable to perform the command due to some issue a processing error on the MEF Client.

##### 8.3.x.5.13	cmdStatus MEF_CLIENT_CMD_MO_NODE_NOT_FOUND

The MEF Client supports the MO_Node cmdClass, and parsed the cmdsArgs element, but could not find the MO node at the MONodePath element in the MEF Client Command arguments.

##### 8.3.x.5.14	cmdStatus MEF_CLIENT_CMD_MO_NODE_TYPE_CONFLICT

The MEF Client supports the MO_Node cmdClass, parsed the cmdsArgs element, and found the MO node at the MONodePath element, but the type of the MO Node does not match the MONodeType element in the MEF Client Command arguments.

##### 8.3.x.5.15	cmdStatus MEF_CLIENT_CMD_MO_NODE_UNACCEPTABLE_ARGS

The MEF Client supports the MO_Node cmdClass, parsed the cmdsArgs element, and found the MO node at the MONodePath element, and the type of the MO Node matches the MONodeType element, but the remaining MO-type-specific arguments in MEF Client Command arguments are unacceptable to the MEF Client.

##### 8.3.x.5.16	cmdStatus MEF_CLIENT_CMD_MO_NODE_EXECUTION_ERROR

The MEF Client supports the MO_Node cmdClass, parsed the cmdsArgs element, and found the MO node at the MONodePath element, and the type of the MO Node matches the MONodeType element, and the remaining MO-type-specific arguments in MEF Client Command arguments are acceptable, but there has been some other error in executing command on the MO Node.

#### 8.3.x.6. NO_MORE_COMMANDS MEF Client Command Class-specific Processes

Purpose: When cmdClassID indicates NO_MORE_COMMANDS, then the MEF is indicating that the MEF has no more MEF Client Commands for the MEF Client.

Elements of cmdArgs: For NO_MORE_COMMANDS MEF Client Command Class, then cmdArgs shall include the following elements

- retryDuration: indicating a time duration, after which the MEF Client is expected to attempt MEF Client Command Retrieve. The retryDuration is cancelled if the MEF Client successfully performs another MEF Client Command procedure, within the scope of the MEF Client Registration, before the retryDuration completes. See clause 8.3.4.6 for other mechanisms which can trigger MEF Client Command procedures.

Forming cmdDescription:

- The MEF shall form cmdArgs containing the elements described in “Elements of cmdArgs” above:

  - retryDuration: set to the time duration before the MEF wishes the MEF Client to attempt the next MEF Client Command Retrieve, with the understanding that the retryDuration is cancelled if the MEF Client successfully performs another MEF Client Command procedure.

- The MEF shall form cmdDescription with cmdClassID indicating NO_MORE_COMMANDS and cmdArgs formed in step 2.

Parsing and Executing cmdArgs:

- The MEF Client shall attempt to parse cmdArgs into the elements described in “Elements of cmdArgs”. If the parsing succeeds, then the MEF Client proceeds to step 4.  If parsing fails, then the then the MEF Client exits the procedure, triggering MEF Client Command Update procedure for this cmdID with cmdStatusCode set to the value for MEF_CLIENT_CMD_BAD_ARGUMENTS.

- The MEF Client MEF Client Command will not perform a MEF Client Command Retrieve procedure or MEF Client Command Update procedure unless triggered.

- The MEF Client shall set a timer based on retryDuration.

  - The timer shall be cancelled if, by some other mechanism as described in clause 8.3.4.6, the MEF Client is triggered to performs an MEF Client Command Retrieve procedure or MEF Client Command Update procedure before the timer expires.

  - If the time expires, then the MEF Client shall perform an MEF Client Command Retrieve procedure, (clause 8.3.x.2), at some time selected by the MEF Client.

#### 8.3.x.7 CERT_PROV MEF Client Command Class-specific Processes

#### 8.3.x.8 DEV_CFG MEF Client Command Class-specific Processes

#### 8.3.x.9	MO_NODE MEF Client Command Class-specific Processes

##### 8.3.x.9.1	[authenticationProfile]-specific Processes

##### 8.3.x.9.1	[trustAnchor]-specific Processes

##### 8.3.x.9.1	[MAFClientRegCfg]-specific Processes

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

## 12.2	Simple Security-Specific oneM2M Data Types

Table 12.2-1 describes simple data type definitions specific to security. The types in table 12.2-1 are either:

Atomic data types derived from XML Schema data types by restrictions other than enumeration

List data types constructed from other XML Schema or oneM2M-defined atomic data types.

Table 12.2-1: Security-specific oneM2M simple data types

| XSD type name | Used for | Examples | Description |
| --- | --- | --- | --- |
| sec:relKeyID | Relative part of symmetric key Identifiers | 1he83he, my-key_name, firstname.lastname | Any combination of the Roman alphabet, numerals, '.', '_' and '-' characters |
| sec:credentialID | Credential Identifier | 10-thiskey@mymef.com | A sec:credIDTypeID and a xs:anyURI separated by the ‘-‘ character. See clause 10.4. The xs:anyURI is the value part of the credential-lD |
| sec:deviceConfigURI | deviceConfigURI attribute of the <MEFBase> resource, see TS-0032 [58] | 1:http://server.dmprovider.com | A sec:devMgmtID value (see clause 12.3.2.2) separated with colon “:” from the URI of a device management server |

## 12.3	Enumerated Security-Specific oneM2M Data Types

### 12.3.1	Introduction

The enumerated security-specific oneM2M data types are treated identically to the enumerated oneM2M data types defined in clause 6.3.4 of oneM2M TS-0004 [4]. These data types are based on <xs:integer>, with the numeric values interpreted as specified in clause 12.3.2.

### 12.3.2	Enumeration type definitions

#### 12.3.2.1	sec:credIDTypeID

The sec:credIDTypeID enumeration type is used in sec:credentialID to identify the type of the identified credential.

Table 12.3.2.1-1: Interpretation of the sec:credIDTypeID enumeration type.

| Value | Interpretation | Note |
| --- | --- | --- |
| 10 | Symmetric key used to authenticate to a MEF (KpmID) | See clause 8.3.2.1 |
| 11 | Symmetric key used to authenticate to a MAF (KmID) | See clause 8.8.3.1 |
| 12 | Symmetric key used to authenticate in an SAEF (KpsaID or KcID) | See clauses 8.2.2.1, 8.2.2.3 |
| 13 | Symmetric key used to authenticate in ESPrim (pairwiseESPrimKeyID) | See clauses 8.4.2 |
| 14 | Symmetric key used for direct encryption in the ESData Encryption-only or Nested-Sign-then-encrypt security classes (generic symmetric key identifier format) | See clause 8.5.2 |
| 15 | Symmetric key used for symmetric key wrap in the ESData Encryption-only or Nested-Sign-then-encrypt security classes (generic symmetric key identifier format) | See clause 8.5.2 |
| 16 | Symmetric key used for HMAC in the ESData Signature-only security class (generic symmetric key identifier format) | See clause 8.5.2 |
| 30 | Raw Public Key Certificate used in TLS: (Public Key Identifier) | 10.1.2 |
| 31 | Device Certificate used in TLS (globally unique hardware instance identifier) | 10.1.1.4 |
| 32 | CSE-ID Certificate used in TLS (CSE-ID) | oneM2M TS-0001 [1] |
| 33 | AE-ID Certificate used in TLS (AE-ID) | oneM2M TS-0001 [1] |
| 41 | Raw Public Key Certificate used for RSA or ECDH Key management in the ESData Encryption-only or Nested-Sign-then-encrypt security classes: (Public Key Identifier) | 10.1.2 |
| 42 | Device Certificate used for RSA or ECDH Key management in the ESData Encryption-only or Nested-Sign-then-encrypt security classes (globally unique hardware instance identifier) | 10.1.1.4 |
| 43 | CSE-ID Certificate used for RSA or ECDH Key management in the ESData Encryption-only or Nested-Sign-then-encrypt security classes (CSE-ID) | oneM2M TS-0001 [1] |
| 44 | AE-ID Certificate used for RSA or ECDH Key management in the ESData Encryption-only or Nested-Sign-then-encrypt security classes (AE-ID) | oneM2M TS-0001 [1] |
| 51 | Raw Public Key Certificate used for RSA or ECDH Key management in the ESData Signature-only security class: (Public Key Identifier) | 10.1.2 |
| 52 | Device Certificate used for RSA or ECDSA signatures in the ESData Signature-only security class (globally unique hardware instance identifier) | 10.1.1.4 |
| 53 | CSE-ID Certificate used for RSA or ECDH Key management in the ESData Signature-only security class (CSE-ID) | oneM2M TS-0001 [1] |
| 54 | AE-ID Certificate used for RSA or ECDH Key management in the ESData Signature-only security class (AE-ID) | oneM2M TS-0001 [1] |
| NOTE: The form of the identifier for the credential type is described in brackets. |

#### 12.3.2.2	sec:devMgmtID

The sec:devMgmtID enumeration type is used in sec:deviceConfigURI as an identifier of  the device management technology used for field device configuration (cf. TS-0022 [57]).

Table 12.3.2.2-1: Interpretation of the sec:devMgmtID enumeration type.

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | OMA DMv1.3 | See TS-0005 |
| 2 | OMA DMv2.0 | See TS-0005 |
| 3 | OMA LwM2M | See TS-0005 |
| 4 | BBF TR-069 | See TS-0006 |

#### 12.3.2.3	sec:cmdClassID

The sec:cmdClassID enumeration type is used in the MEF Client Command cmdDescription element (see clause  8.3.x.5) to indicate the cmdClass of the cmdDescription. The cmdDescription is also an attribute of the <mefClientCmd> resource type in oneM2M TS-0032 [58]).

Table 12.3.23-1: Interpretation of the sec:cmdClassID enumeration type.

| Value | Interpretation | Note |
| --- | --- | --- |
| 0 | NO_MORE_COMMANDS | The command class is specified in clause 8.x.3.6.2. |
| 1 | CERT_PROV | The command class is specified in clause 8.x.3.6.3. Certificate Provisioning is specified in clause 8.3.6 |
| 2 | DEV_CFG | The command class is specified in clause 8.x.3.6.4. Device Configuration is specified in oneM2M TS-0022 [57] |
| 3 | MO_NODE | The command class is specified in clause 8.x.3.7. |

#### 12.3.2.4	sec:cmdStatusCode

The sec:cmdStatusCode enumeration type is used by the cmdStatusCode element to indicating the status of an MEF Client Command. The cmdStatus is also an attribute of the <mefClientCmd> resource type in oneM2M TS-0032 [58].

Table 12.3.23-1: Interpretation of the sec:cmdStatusCode enumeration type.

| Value | Interpretation | Note |
| --- | --- | --- |
| 10 | MEF_CLIENT_CMD_ISSUED | See 8.3.x.5.2 |
| 11 | MEF_CLIENT_CMD_REISSUED | See 8.3.x.5.3 |
| 20 | MEF_CLIENT_CMD_OK | See 8.3.x.5.4 |
| 40 | MEF_CLIENT_CMD_ REPEATED_CMD_ID | See 8.3.x.5.5 |
| 41 | MEF_CLIENT_CMD_CLASS_NOT_SUPPORTED | See 8.3.x.5.6 |
| 42 | MEF_CLIENT_CMD_BAD_ ARGUMENTS | See 8.3.x.5.7 |
| 43 | MEF_CLIENT_CMD_UNACCEPTABLE_ARGUMENTS | See 8.3.x.5.8 |
| 100 | MEF_CLIENT_CMD_CERT_PROV_SERVER_ERROR | See 8.3.x.5.9 |
| 101 | MEF_CLIENT_CMD_CERT_PROV_CLIENT_ERROR | See 8.3.x.5.10 |
| 201 | MEF_CLIENT_CMD_DEV_CFG_SERVER_ERROR | See 8.3.x.5.11 |
| 202 | MEF_CLIENT_CMD_DEV_CFG_SERVER_ERROR | See 8.3.x.5.12 |
| 300 | MEF_CLIENT_CMD_MO_NODE_NOT_FOUND | See 8.3.x.5.13 |
| 301 | MEF_CLIENT_CMD_MO_NODE_TYPE_CONFLICT | See 8.3.x.5.14 |
| 302 | MEF_CLIENT_CMD_MO_NODE_UNACCEPTABLE_ARGS | See 8.3.x.5.15 |
| 303 | MEF_CLIENT_CMD_MO_NODE_EXECUTION_ERROR | See 8.3.x.5.16 |

#### 12.3.2.5	sec:certProvProtocolID

The sec:certProvProtocolID enumeration type is used for the certProvProtocolID element of the cmdArgs element of the MEF Client Command cmdDescription element (see clause  8.3.x.7) to indicate the Certificate Provisioning protocol to be used. The cmdDescription is also an attribute of the <mefClientCmd> resource type in oneM2M TS-0032 [58])

Table 12.3.23-1: Interpretation of the sec:certProvProtocolID enumeration type.

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | EST | See clause 8.3.6.2 |
| 2 | SCEP | See clause 8.3.6.3 |

## 12.4	Complex Security-Specific oneM2M Data Types

### 12.4.1	MAF and MEF client configuration data

Table 12.4.1-1 defines the assignment of data types to the four data containers which are used in MAF and MEF client registration and key registration configuration procedures. Note that these data containers are not defined in the form of resource types since the information is not remotely accessible. The information elements of these containers are managed by means of Device Management procedures (cf. TS-0022 [57]) or by manual provisioning.

Table 12.4.1-1: Types used in MAF and MEF Registration Configuration procedures.

| data container name | Used in | Data Type | Notes |
| --- | --- | --- | --- |
| mefClientRegCfg | MEF Client Registration Configuration, see 8.3.7.2 | sec:clientRegCfg | See clause 12.4.2 |
| mafClientRegCfg | MAF Client Registration Configuration, see 8.8.3.2 |  |  |
| mefKeyRegCfg | MEF Key Registration Configuration, see 8.3.7.3 | sec:keyRegCfg | See clause 12.4.3 |
| mafKeyRegCfg | MAF Key Registration Configuration, see 8.8.3.3 |  |  |

### 12.4.2	sec:clientRegCfg

Data type sec:clientRegCfg applies to the mefClientRegCfg and mafClientRegCfg data containers used in MEF Client Registration Configuration and MAF Client Registration Configuration, see clause 8.3.7.2 and clause 8.8.3.2, respectively.

Table 12.4.2-1: Type definition of sec:clientRegCfg

| Element Path | Element Type | Multiplicity | Notes |
| --- | --- | --- | --- |
| expirationTime | m2m:timestamp | 0..1 | oneM2M TS-0004 [4] |
| labels | m2m:labels | 0..1 | oneM2M TS-0004 [4] |
| fqdn | xs:anyURI | 1 |  |
| adminFQDN | xs:anyURI | 1 |  |
| httpPort | xs:unsignedByte | 0..1 |  |
| coapPort | xs:unsignedByte | 0..1 |  |
| websocketPort | xs:unsignedByte | 0..1 |  |

### 12.4.3	sec:keyRegCfg

Data type sec:keyRegCfg applies to the mefKeyRegCfg and mafKeyRegCfg data containers used in MEF Key Registration Configuration and MAF Key Registration Configuration, see clause 8.3.7.3 and clause 8.8.3.3, respectively.

Table 12.4.3-1: Type definition of sec:keyRegCfg.

| Element Path | Element Type | Multiplicity | Notes |
| --- | --- | --- | --- |
| expirationTime | m2m:timestamp | 0..1 | oneM2M TS-0004 [4] |
| labels | m2m:labels | 0..1 | oneM2M TS-0004 [4] |
| adminFQDN | xs:anyURI | 1 |  |
| SUID | m2m:suid | 1 | oneM2M TS-0004 [4] |
| targetIDs | m2m:listOfM2MIDs | 0..1 | oneM2M TS-0004 [4] |

### 12.4.A	sec:cmdDescription

The sec:cmdDescription complex type is used by the cmdDescription element to describe an MEF Client Command, described in clause 8.3.x.5. The cmdDescription is also an attribute of the <mefClientCmd> resource type in oneM2M TS-0032 [58].

Table 12.4.2-1: Type definition of sec:cmdDescription

| Element Path | Element Type | Multiplicity | Notes |
| --- | --- | --- | --- |
| cmdClassID | sec:cmdClassID | 1 |  |
| cmdArgs | sec:noMoreCmdArgs sec:certProvCmdArgs or sec:devCfgCmdArgs or sec:MONodeCmdArgs | 1 | See clauses 12.4.B, 12.4.C, 12.4.D, 12.4.E |
| targetID | m2m:ID | 1 |  |

### 12.4.B	sec:noMoreCmdArgs

The sec:noMoreCmdArgs complex type is used in sec:cmdDescription.

Table 12.4.2-1: Type definition of sec:certProvCmdArgs

| Element Path | Element Type | Multiplicity | Notes |
| --- | --- | --- | --- |
| retryDuration | xs:duration | 1 |  |

### 12.4.C	sec:certProvCmdArgs

The sec:certProvCmdArgs complex type is used in sec:cmdDescription.

Table 12.4.2-1: Type definition of sec:certProvCmdArgs

| Element Path | Element Type | Multiplicity | Notes |
| --- | --- | --- | --- |
| certProvProtocolID | sec:certProvProtocolID | 1 |  |
| URI | xs:anyURI | 1 |  |

### 12.4.D	sec:devCfgCmdArgs

The sec:devCfgCmdArgs complex type is used in sec:cmdDescription.

Table 12.4.2-1: Type definition of sec:devCfgCmdArgs

| Element Path | Element Type | Multiplicity | Notes |
| --- | --- | --- | --- |
| deviceConfigURI | sec:deviceConfigURI | 1 | See clause 12.2 |

### 12.4.E	sec:MONodeCmdArgs

The sec:MONodeCmdArgs complex type is used in sec:cmdDescription.

Table 12.4.2-1: Type definition of sec:MONodeCmdArgs

| Element Path | Element Type | Multiplicity | Notes |
| --- | --- | --- | --- |
| objectPath | xs:AnyURI |  |  |
| objectType | Enum |  |  |
| objectTypeSpecifcArgs |  |  |  |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4---------------------------------------------