| CHANGE REQUEST |
| --- |
| Meeting ID:* | SEC 30 |
| Source:* | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com |
| Date:* | 2017-07-03 |
| Reason for Change/s:* | Adding new <mefClientCmd> resource type |
| CR against: Release* | 2A |
| CR against: WI* | Active <WI-0057> MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0032 v0.1.0 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | TS-0003 v2.9.0 |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution introduces a new resource type <mefClientCmd> appliocable to the Mmef interface. This resource type provides a means to the MEF to trigger Enrolment Exchange procedures to be executed by the MEF clients. This new <mefClientCmd> resource type represents a child of the <mefClientReg> resource of the associated MEF client.  The actual command is delivered by the MEF to the MEF client in the response to a  <mefClientCmd> retrieve request.

### -----------------------Start of change 1-------------------------------------------

## 7.5	Resource Type <mefClientReg>

The <mefClientReg> resource shall represent a MEF Client enrolled with an M2M SP or M2M Trust Enabler (MTE).

NOTE: 	A single MEF Client can be enrolled with at most one M2M SP and any number of MTEs (typically enabling end-to-end security to MEF Clients outside the MEF Client’s M2M SP’s domain). Consequently, a single MEF Client can be associated with multiple <mefClientReg> resources on multiple MEFs. It is also possible that a single MEF Client can be associated with multiple <mefClientReg> resources on a single MEF acting on behalf of multiple administrating stakeholders.

The <mefClientReg> resource shall contain the child resources specified in table 7.5-1.

Table 7.5-1: Child resources of <mefClientReg> resource

| Child Resources of <mefClientReg> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| “cmd” | <mefClientCmd> | 1 | See clause 7.7 |

The <mefClientReg> resource shall contain the attributes specified in table 7.5-2.

Table 7.5-2: Attributes of <mefClientReg> resource

| Attributes of <mefClientReg> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of [1] |
| resourceID | 1 | RO | See clause 9.6.1.3 of [1]. |
| resourceName | 1 | RO | See clause 9.6.1.3 of [1]. |
| parentID | 1 | RO | See clause 9.6.1.3 of [1]. |
| creationTime | 1 | RO | See clause 9.6.1.3 of [1]. |
| labels | 1 | RW | See clause 9.6.1.3 of [1]. |
| expirationTime | 1 | WO | See clause 9.6.1.3 of [1]. |
| creator | 1 | WO | This attribute shall include the identifier of the MEF client which has created this resource. |
| adminFQDN | 1 | WO | FQDN of the M2M SP or MTE who is the administrating stakeholder of this enrolment |
| assignedSymmKeylID | 0..1 | RO | When the MEF Client uses a symmetric key to authenticate to the MEF, then the MEF may use this attribute to provide a symmetry key identifier within the domain of the MEF. Assigned by the MEF. |
| sourceIDs | 0..1 | RW | List of AE-IDs and CSE-IDs associated with a MEF client acting on behalf of a Node. This attribute shall be supplied if the creator attribute inclides a Node-ID |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## 7.7	Resource Type <mefClientCmd>

A <mefClientCmd> resource includes instructions for the MEF client associated with the parent <mefClientReg> resource to be executed.

The <mefClientCmd> resource shall contain no child resources.

The <mefClientCmd> resource shall contain the attributes specified in table 7.7-1.

Table 7.7-1: Attributes of <mefClientCmd> resource

| Attributes of <mefClientCmd> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of.[1]. |
| resourceID | 1 | RO | See clause 9.6.1.3 of.[1]. |
| resourceName | 1 | RO | See clause 9.6.1.3 of.[1]. |
| parentID | 1 | RO | See clause 9.6.1.3 of.[1]. |
| creationTime | 1 | RO | See clause 9.6.1.3 of.[1]. |
| labels | 1 | RW | See clause 9.6.1.3 of.[1]. |
| expirationTime | 1 | WO | See clause 9.6.1.3 of.[1]. |
| cmdID | 1 | RW | This attribute shall include a MEF-assigned identifier of a command issued by the MEF. See clause 8.3.x.1 of [2] for further details. |
| cmdDescription | 1 | RO | This attribute provides the description of a command issued by the MEF to be executed by the MEF client. See clause 8.3.x.5 of [2] for further details. |
| cmdStatusCode | 1 | RW | This attribute shall be used forthe status of the command issued by the MEF. See clause 8.3.x.6 of [2] for further details. |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

## 8.4	Resource Type <mefClientReg>

### 8.4.1	Introduction

A <mefClientReg> resource shall represent a MEF Client enrolled with the MEF on behalf of an M2M Service Provider or M2M Trust Enabler. A <mefClientReg> resource shall be a child resource of the MEF’s <MEFBase> resource.

Table 8.4.1-1: Data Type Definition of <mefClientReg>

| Data Type ID | File Name | Note |
| --- | --- | --- |
| mefClientReg | SEC-mefClientReg-v2_x_0.xsd |  |

Table 8.4.1-2: Universal/Common Attributes of <mefClientReg> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | NP | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| creationTime | NP | NP |
| labels | O | O |
| expirationTime | M | M |
| creator | NP | NP |

Table 8.4.1-3: Resource Specific Attributes of <mefClientReg> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| fqdn | M | NP | xs:anyURI | No default |
| assignedSymmKeyID | NP | NP | sec:credentialID | No default |
| sourceIDs | O | NP | List of m2m:ID | No default |

Table 8.4.1-4: Child resources of <mefClientReg> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to Resource Type Definition |
| --- | --- | --- | --- |
| <mefClientCmd> | ”cmd” | 1 | Clause 7.7 |

### 8.4.2	<mefClientReg> resource specific procedures on CRUD operations

#### 8.4.2.1	Create

This procedure is denoted MEF Client Registration in clause 8.3.5.2.3 of TS-0003 [2]. The To parameter of the <mefClientReg> create request primitive includes the MEF-FQDN and the character “–“ (dash) as a shorthand notation for the name of the <MEFBase> resource:

//{MEF-FQDN}/–/

Example:   //mef123.mefprovider.org/–/

The MEF-FQDN represents a globally unique identifier of a MEF (aka. MEF ID)..

The From parameter of the <mefClientReg> create request primitive shall be left empty if the MEF client does not have a MEF Client ID assigned yet. If the MEF client interfaces with the MEF on behalf of the node (cf. clause 5.2.1), the Node-ID of the respective ADN, ASN, MN or IN shall serve as MEF Client ID.

Originator:

No change from the generic procedures in clause 7.2.2.1 of [3] with clarifications discussed in clauses 5.2.2 and 6.3, and with following differences:

In step Orig-6.0: “Process Response primitive”, if the Originator used a symmetric key to authenticate to the MEF, and the <mefClientReg> resource in the response contained an assignedSymmKeyID then the originator shall use the assignedSymmKeyID to identify this symmetric key when it is subsequently used in authenticating to the MEF.

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [3] with clarifications discussed in clauses 5.2.2 and 6.3, and with following differences:

The Receiver shall perform the following steps in order in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized to register with the administrating stakeholder (M2M SP or MTE) identified by fqdn attribute. The present document does not specify how the Receiver makes this determination.

  - If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

  - If the Originator is authorized, then the Receiver shall allow the request.

The Receiver shall perform the following steps in order as part of “Create the resource” (clause 7.3.3.5)” during Step Recv-6.5: “Create/Update/Retrieve/Delete/Notify operation is performed”:

- If the Originator authenticated using symmetric key with a key identifier which does not use the Receiver’s FQDN, then

  - The Receiver shall assign a symmetric key identifier with the Receiver’s FQDN and with relative part which is unique within the scope of symmetric key identifiers issued by the Receiver. The Receiver shall associate this symmetric key identifier with the symmetric key used for authenticating the Originator.

  - The Receiver shall set the assignedSymmKeyID attribute to be the Credential-ID formed from the assigned symmetric key identifier as specified in clause 10.4.

- If the Originator authenticated using a symmetric key with a key identifier which does not use the Receiver’s FQDN, or if the Originator authenticated using a certificate, then the Receiver shall not include an assignedSymmKeyID attribute in the created resource.

- The Receiver shall assign the creator attribute to an AE-ID or CSE-ID or Node-ID on instructions from the administrating stakeholder. The present document does not specify any details of how the AE-ID or CSE-ID or Node-ID is determined.

- The Receiver shall instantiate the child <mefClientCmd> Resource.

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

## 8.6	Resource Type <mefClientCmd>

### 8.6.1	Introduction

A <mefClientCmd> resource shall represent a command to be indicated to a MEF client by a MEF, and a status report on the attempted parsing and execution of that command to be indicated to the MEF by a MEF Client. The retrieve procedure and update procedure are used for this purpose.

Table 8.6.1-1: Data Type Definition of <mefClientCmd>

| Data Type ID | File Name | Note |
| --- | --- | --- |
| mefClientCmd | SEC-mefClientCmd-v2_0_0.xsd |  |

Table 8.6.1-2: Universal/Common Attributes of <mefClientCmd> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Update |
| @resourceName | NP |
| resourceType | NP |
| resourceID | NP |
| parentID | NP |
| creationTime | NP |
| labels | O |
| expirationTime | NP |

Table 8.6.1-3: Resource Specific Attributes of <mefClientCmd> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Update |  |  |
| cmdID | M | m2m:requestID | No default |
| cmdDescription | NP | sec:cmdDescription | No default |
| cmdStatusCode | M | sec:cmdStatusCode | No default |

The <mefClientCmd> resource shall contain no child resources.

### 8.6.2	<mefClientCmd> resource specific procedures on CRUD operations

#### 8.6.2.1	Create

Originator:

The <mefClientCmd> resource shall not be created via API. It is instantiated by a MEF when the parent <mefClientReg> resource is created as described in clause 8.4.2.1.

Receiver:

The primitive specific operation on Recv-1.0 "Check the syntax of received message" defined in TS-0004 [3] applies:

- If the request is received, the Receiver CSE shall execute the following steps in order.

- "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

- "Send the Response primitive".

#### 8.6.2.2	Retrieve

This procedure is denoted MEF Client Command Retrieval in clause 8.3.X.2 of TS-0003 [2]. This procedure is used to retrieve the <mefClientCmd> resource.

Originator:

No change from the generic procedures in clause 7.2.2.1 of [3] with clarifications discussed in clauses 5.2.2 and 6.3, and with following difference:

In step Orig-6.0: “Process Response primitive”, the Originator shall extract the cmdID, cmdDescription and cmdStatusCode from the response and pass these to the MEF Client Command processing as specified in clause 8.3.X.2 in oneM2M TS-0003 [2].

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [3] with clarifications discussed in clauses 5.2.2 and 6.3, and with following differences:

The Receiver shall perform the following steps in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized by checking if the Originator is the creator of the parent <mefClientReg> resource.

- If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

If the Originator is authorized, then the Receiver shall allow the request. The Receiver shall perform the following steps in order as part of “Create the resource” (clause 7.3.3.5)” during Step Recv-6.5: “Create/Update/Retrieve/Delete/Notify operation is performed”:

- If the Receiver has a pending MEF Client Command to be issued to the Originator, then the Receiver shall set the cmdID, cmdDescription and cmdStatusCode attributes as specified in clause 8.3.X.2 of oneM2M TS-0003 [2]. The values of these attributes should remain set to these values until the MEF Client performs an Update on the Resource (see clause 8.6.2.3). If the MEF Client takes too long to perform an Update (for example, if the Response is not received by the Originator) then the MEF may choose replace the attributes with a new MEF Client Command.

NOTE:	The cmdDescription includes cmdClass which can be set to “NO_MORE_COMMANDS” to indicate that there are no further commands to be issued.

#### 8.6.2.3	Update

This procedure is denoted MEF Client Command Update in clause 8.3.X.3 of TS-0003 [2]. This procedure is used by the MEF Client to report on the status of an issued MEF Client Command, and for an MEF to issue another MEF Client Command.

NOTE 1:	The cmdDescription includes cmdClass which can be set to “NO_MORE_COMMANDS” to indicate that there are no further commands to be issued.

Originator:

No change from the generic procedures in clause 7.2.2.1 of [3] with clarifications discussed in clauses 5.2.2 and 6.3, and with following differences:

In step Orig-1.0: “Compose of a Request primitive”, the Originator shall include the cmdID and cmdStatusCode attributes in the Content of the request, with attribute values assigned as described in clause 8.3.X.3 of oneM2M TS-0003 [2].

In step Orig-6.0: “Process Response primitive”, the Originator shall extract the cmdID, cmdDescription and cmdStatusCode attributes from the response and pass these to the MEF Client Command processing specified in clause 8.3.X.3 in oneM2M TS-0003 [2].

Receiver:

Same as the generic procedures in clause 7.2.2.2 of [3] with clarifications discussed in clauses 5.2.2 and 6.3, and with the following differences:

The Receiver shall perform the following step in the place of Recv-6.3: “Check authorization of the Originator”:

- The Receiver shall determine if the Originator is authorized by checking if the Originator is the creator of the parent <mefClientReg> resource.

- If the Originator is not authorized, then the Receiver shall execute the following steps in order.

    - "Create an unsuccessful Response primitive" with the Response Status Code indicating "ACCESS_DENIED" error.

    - "Send the Response primitive".

- If the Originator is authorized, then the Receiver shall allow the request.

The Receiver shall perform the following steps in order as part of “Update the resource” (clause 7.3.3.7)” during Step Recv-6.5: “Create/Update/Retrieve/Delete/Notify operation is performed”:

- The Receiver shall extract the cmdID and cmdStatusCode attributes and pass these to the MEF Client Command processing in the MEF described in clause 8.3.X.3 of oneM2M TS-0003 [x].

- If the Receiver has a pending MEF Client Command to be issued to the Originator, then the Receiver shall set the cmdID, cmdDescription and cmdStatusCode attributes as specified in clause 8.3.X.3 of oneM2M TS-0003 [2]. The values of these attributes should remain set to these values until the MEF Client performs a subsequent Update on the Resource. If the MEF Client takes too long to perform an Update (for example, if the Response is not received by the Originator) then the MEF may choose replace the attributes with a new MEF Client Command.

NOTE 2:	The cmdDescription includes cmdClass which can be set to “NO_MORE_COMMANDS” to indicate that there are no further commands to be issued.

#### 8.6.2.4	Delete

Originator:

The <mefClientCmd> resource shall not be deleted via API. It is deleted by a MEF when the parent <mefClientReg> resource is deleted.

Receiver:

The primitive specific operation on Recv-1.0 "Check the syntax of received message" defined in TS-0004 [3] applies:

- If the request is received, the Receiver CSE shall execute the following steps in order.

- "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

- "Send the Response primitive".

### -----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5-------------------------------------------

## 9.2	Security-specific oneM2M Resource attributes

In protocol bindings resource attributes names shall be translated into short names of Table 9.2-1 and in Table 8.2.3-1 of oneM2M TS-0004 [3].

Table 9.2-1: Security-specific oneM2M Attribute Short Names.

| Attribute Name | Occurs in | Short Name | Notes |
| --- | --- | --- | --- |
| resourceType | All | ty* | Defined in oneM2M TS-0004 [3]. |
| resourceID | All | ri* | Defined in oneM2M TS-0004 [3]. |
| resourceName | All | rn* | Defined in oneM2M TS-0004 [3]. |
| parentID | mafClientReg, mefClientReg, symmKeyReg | pi* | Defined in oneM2M TS-0004 [3]. |
| expirationTime | All | et* | Defined in oneM2M TS-0004 [3]. |
| creationTime | All | ct* | Defined in oneM2M TS-0004 [3]. |
| labels | mafClientReg, mefClientReg, symmKeyReg | lbl* | Defined in oneM2M TS-0004 [3]. |
| creator | mafClientReg, mefClientReg, symmKeyReg | cr* | Defined in oneM2M TS-0004 [3]. |
| fqdn | mafClientReg, mefClientReg, symmKeyReg | fq |  |
| SUID | symmKeyReg | suid |  |
| assignedSymmKeyID | mafClientReg, mefClientReg | aski |  |
| estBaseURI | MEFBase | estu |  |
| deviceConfigURIs | MEFBase | dcu |  |
| targetIDs | symmKeyReg | tgis |  |
| keyValue | symmKeyReg | kv |  |
| cmdID | mefClientCmd | mcci |  |
| cmdDescription | mefClientCmd | mccd |  |
| cmdStatusCode | mefClientCmd | mccs |  |
| NOTE: Marked short names have been already assigned for primitive parameters or resource attributes in oneM2M TS-0004 [3]. |

## 9.3	Security-specific oneM2M Resource types

In protocol bindings resource type names shall be translated into short names of Table 9.3-1.

Table 9.3-1: Security-specific Resource Type Short Names

| Attribute Name | Short Name |
| --- | --- |
| MAFBase | maf |
| MEFBase | mef |
| mafClientReg | macr |
| mefClientReg | mecr |
| symmKeyReg | mkr |
| mefClientCmd | mcc |

## 9.4	Security-specific oneM2M Complex data type members

In protocol bindings complex data types member names shall be translated into short names of Table 9.4-1.

NOTE:     The member names of the security configuration parameters mefClientRegCfg, mafClientRegCfg, mefKeyRegCfg and mafKeyRegCfg are defined in clause 12.4 of TS-0003 [2].

Table 9.4-1: Security-specific oneM2M Complex data type member short names

| Member Name | Occurs in | Short Name | Notes |
| --- | --- | --- | --- |
| expirationTime | mefClientRegCfg, mefKeyRegCfg, mafClientRegCfg, mafKeyRegCfg | et* | Defined in oneM2M TS-0004 [3] |
| labels | mefClientRegCfg, mefKeyRegCfg, mafClientRegCfg, mafKeyRegCfg | lbl* | Defined in oneM2M TS-0004 [3] |
| fqdn | mefClientRegCfg, mefKeyRegCfg mafClientRegCfg, mafKeyRegCfg | fq |  |
| adminFQDN | mefClientRegCfg, mafClientRegCfg | adfq* | Defined in oneM2M TS-0004 [3] |
| httpPort | mefClientRegCfg, mafClientRegCfg | hpt |  |
| coapPort | mefClientRegCfg, mafClientRegCfg | cpt |  |
| websocketPort | mefClientRegCfg, mafClientRegCfg | wpt |  |
| ppsk | mefClientRegCfg, mafClientRegCfg | pk |  |
| rpsk | mefClientRegCfg, mafClientRegCfg | rk |  |
| certAuth | mefClientRegCfg, mafClientRegCfg | cert |  |
| credID | mefClientRegCfg, mafClientRegCfg | crdi |  |
| caCerts | mefClientRegCfg, mafClientRegCfg | cact |  |
| SUID | mefKeyRegCfg, mafClientRegCfg | suid* |  |
| targetIDs | mefKeyRegCfg, mafClientRegCfg | tgis |  |
| targetID | cmdDescription | tgi |  |
| cmdClassID | cmdDescription | ccid |  |
| cmdArgs | cmdDescription | cma |  |
| certProvProtocolID | certProvCmdArgs | cppi |  |
| URI | certProvCmdArgs | uri* |  |
| deviceConfigURI | devCfgCmdArgs | dcu |  |
| objectPath | MONodeCmdArgs | ajop* |  |
| objectType | MONodeCmdArgs | otyp |  |
| objectTypeSpecificArgs | MONodeCmdArgs | otsa |  |
| retryDuration | noMoreCmdArgs | rdu |  |
| noMoreCmdArgs | cmdArgs | nmca |  |
| certProvCmdArgs | cmdArgs | cpca |  |
| devCfgCmdArgs | cmdArgs | dcca |  |
| MONodeCmdArgs | cmdArgs | nnca |  |
| NOTE: * marked short names have been already assigned to an attribute in Table 9.2-1. |

### -----------------------End of change 5---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M Drafting Rules (http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf))

## 2.2	Informative references

[i.1]	oneM2M Drafting Rules (http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf)

### -----------------------End of Changes to References  -------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

<defined term>: <definition>

<defined term>[N]: <definition>

## 3.2	Symbols

<symbol>	<Explanation>

## 3.3	Abbreviations and Acronyms

<ABBREVIATION/ACRONYM>	<Explanation>

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?