| CHANGE REQUEST |
| --- |
| Meeting ID:* | SEC31 |
| Source:* | Norihiro Okui, KDDI, no-okui@kddi.com Yutaka Miyake, KDDI, yu-miyake@kddi.com |
| Date:* | 2017-09-18 |
| Reason for Change/s:* | PPM supports both distributed authorization and dynamic authorization in Rel3 |
| CR against: Release* | 3 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003 v3.4.0 |
| Clauses * | 11 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

PPM is defined as distributed authorization in release 2 at first, but a specification of distributed authorization was postponed to release 3. So, PPM is defined as direct dynamic authorization in release 2. In release 3, specification of distributed authorization is defined.

PPM could support both dynamic authorization and distributed authorization. This contribution provides complete revision about PPM in order to comform to the specification of release 3.

### -----------------------Start of change 1-------------------------------------------

# 11	Privacy Protection Architecture using Privacy Policy Manager（PPM)

## 11.1	Introduction

This clause provides an architecture for the Privacy Policy Manager (PPM). PPM is a distributed authorization privacy protection architecture using user's privacy preference and service’s privacy policy.

The PPM is a personal data management framework based on the user's privacy preferences and creates access control information from policies agreed by a user. The PPM protects user's personal data from unauthorized parties and unauthorized collection. The PPM may be operated by an M2M Service Provider or another stakeholder acting as trusted third party. If a Service Provider provides user’s personal data to a third party, the Service Provider needs to get the user’s consent. In case that the user accepted a privacy policy which indicates provision to third party, the Service Provider could provide the personal data to third party. However, if the privacy policy did not include provision to third party, the Service Provider needs to update the privacy policy and get the user's consent to it.

## 11.2	Components of PPM

## 11.2.1	Privacy Preference and Privacy Policy

The PPM shall manage privacy preferences and privacy policies.

- Privacy preference

  - Privacy preference is user's preference regarding the provision of personal data.

  - User creates a user’s privacy preference and registers it to the PPM.

  - List of privacy attributes is described in Annex J.

- Privacy policy

  - Privacy policy describes a required personal data to provide a service to an end user by a Service Provider.

  - A Service Provider creates a privacy policy and registers it to the PPM.

  - List of privacy attributes is described in Annex J.

11.2.2	Functions of PPM

The PPM shall have the following functions.

- Sophisticated consent mechanism for privacy policy

- Privacy policy describes required personal data to provide a service to an end user by a Service Provider.

- When the user subscribes to a service which is provided by a Service Provider, the Service Provider needs to get the user’s consent to the service’s privacy policy. The PPM provides user friendly consent mechanism by comparing the privacy preference and the privacy policy.

- This function is described in clause 11.4.1.2.

- Functions of the Policy Decision Point (PDP), Policy Retrieval Point (PRP) and Dynamic Authorization Server (DAS).

- PDP

When an Originator requests personal data from an Hosting CSE which acts as PEP, the Hosting CSE requests access control decision from the PPM which acts as PDP. The PPM creates <authorizationDecision> from access control information that is created from policies agreed by user and respond <authorizationDecision> to the Hosting CSE.

Detail of PDP and <authorizationDecision> are described in TS-0003 clause 7.5.2 and TS-0001 clause 9.6.42, respectively.

- PRP

When an Originator requests personal data from an Hosting CSE which acts as PDP, the Hosting CSE requests access control policies from the PPM which acts as PRP. The PPM creates <authorizationPolicy> based on policies agreed by users and respond <authorizationPolicy> to the Hosting CSE.

Detail of PRP and <authorizationPolicy> are described in TS-0003 clause 7.5.3 and TS-0001 clause 9.6.43, respectively.

- Dynamic Authorization Server model

Direct Dynamic Authorization

    - When an Originator requests personal data from an Hosting CSE, the Hosting CSE requests <dynamicACPInfo> or <token> from the PPM. The PPM creates <dynamicACPInfo> or <token> based on policies agreed by users and respond <dynamicACPInfo> or <token> to the Hosting CSE.

    - Detail of Direct Dynamic Authorization is described in TS-0003 clause 7.3.2.2.

    - Detail of <dynamicACPInfo> and <token> are described in TS-0001 clause 9.6.40 and  clause 9.6.39, respectively.

Indirect Dynamic Authorization

    - Before an Originator requests personal data from an Hosting CSE, the Originator requests <token> or tokenID from the PPM. The PPM creates <token> based on policies agreed by users and respond  <token> or tokenID to the Originator. Then, the Originator requests personal data from Hosting CSE with <token> or tokenID.

    - Detail of Indirect Dynamic Authorization is described in TS-0003 clause 7.3.2.3

- Traceability of personal data usage

- PPM shall store the access log that records which Originator accessed which kind of collected data.

- This function is for further study of oneM2M, but this function can be implemented using components that are defined in oneM2M.

## 11.3	Privacy Policy Management Architecture

### 11.3.1	Introduction

- The PPM manage user’s preference and service’s privacy policy in a M2M Service Provider. Basically, one M2M Service Provider have one PPM in infrastructure domain and manage status of user consent in the PPM. There are four procedures in the use of the PPM. This clause explains relationships between steps in the PPM scenario and components of oneM2M.

- A data subject joins an IN-CSE such as an M2M Platform.

- The data subject subscribes to a service offered by an IN-AE. This may happen concurrently with step 1.

- The IN-AE requests personal data that are stored in a Hosting CSE.

- The data subject checks the access log of his/her own personal data and requests the deletion of the collected personal data from the Hosting CSE.

### 11.3.2	Involved Entities

Data subject:

  - An end user can make use of services on an IN-CSE by subscribing to a service of an IN-AE which provides functions that control access to information in the IN-CSE.

  - When an end user subscribes to a service by an IN-AE, the end user becomes a data subject.

Personal Data

  - Personal data is information that can be used on its own or with other information to identify an individual to form Personally Identifiable Information (PII).

  - A Hosting CSE collects and stores personal data.

  - Examples of personal data: Sensor data, Electrical power consumption, Operating state of air conditioner, etc.

ADN-AE, ASN-AE

  - An ADN-AE or ASN-AE collects various kinds of data, such as sensor inputs.

  - The ADN-AE or ASN-AE sends the data to a Hosting CSE such as ASN-CSE, MN-CSE or IN-CSE

Hosting CSE

  - If the Hosting CSE use the PPM as PDP, the Hosting CSE should act as Policy Enforcement Point (PEP).

  - If the Hosting CSE use the PPM as PRP, the Hosting CSE should act as PDP.

  - If the Hosting CSE use the PPM as DAS, the Hosting CSE should configure <dynamicAuthorizationConsultation> resources linked to the requested resource.

    - <dynamicAuthorizationConsultation> resource is described in TS-0001 clause 9.6.40.

IN-AE

  - An IN-AE provides services to an end user who joins the IN-CSE.

  - An IN-AE requests personal data from an IN-CSE in order to provide services.

IN-CSE

  - M2M Portal

    - An M2M portal is a kind of Web site or Web application managing services provided by an M2M Platform (IN-CSE and related IN-AEs).

    - An end user accesses a portal to join an IN-CSE. A data subject accesses the portal to subscribe to a service offered by an IN-AE.

PPM

  - The PPM shall create access control information based on policies agreed by a user. Access control information is <authorizationDecision>, <authorizationPolicy>, <dynamicACPInfo> or <Token>.

  - If the PPM act as PDP or PRP, the PPM shall have an IN-CSE. If the PPM act as DAS, the PPM shall have an IN-AE.

  - The PPM may have a PPM portal which is a kind of Web site or Web application. An end user accesses the PPM portal to configure the end user’s privacy preference. The PPM portal is outscope of oneM2M.

### 11.3.3	Management Flow in PPM Architecture

#### 11.3.3.0	Introduction

This clause describes the case where an IN-CSE stores personal data. In this case, the IN-CSE is a Hosting CSE.

#### 11.3.3.1	Joining an IN-CSE

When a data subject joins an IN-CSE, the data subject configures a privacy preferences using the PPM. A privacy preference explains what kind of data are allowed to be accessed by IN-AEs. Figure 11.3.3.1 illustrates the overview of this process.

Figure 11.3.3.1: A data subject joins an IN-CSE

1.	A data subject accesses the M2M portal of an IN-CSE.

- This process is typically uses Web access protocols such as HTTP, HTTPS and so on.

- This process is described in clause 11.4.1.2.

2.	A data subject configures a privacy preference and registers it on the PPM portal.

- A data subject accesses the PPM portal, or the M2M portal redirects the data subject to the PPM portal. This process uses Web access protocols.

- This process is described in clause 11.4.1.2.

3.	The IN-CSE collects and stores data from AEs.

#### 11.3.3.2	Subscription to a service by IN-AE

The data subject can subscribe to various kinds of services provided by IN-AEs through the IN-CSE. Service lists are registered on an M2M portal and the data subject can select services to subscribe to. When the data subject subscribes to a service, the data subject needs to accept a privacy policy. In order for the data subject to easily understand this policy, the PPM shall create the customized privacy policy based on the privacy policy provided by the IN-AE and the data subject's privacy preference. Therefore, the data subject can control personal data and agreement implies understanding of the privacy policy. Figure 11.3.3.2 shows the overview of this process.

Figure: 11.3.3.2: The data subject subscribes to an IN-AE's service

1.	The data subject accesses the M2M portal and select an IN-AE's service to subscribe. The M2M portal or the IN-AE redirects to the PPM portal to get the data subject’s consent.

- This process typically uses Web access protocols such as HTTP, HTTPS and so on.

- This process is described in clause 11.4.1.1.

2.	The data subject needs to accept a privacy policy to subscribe to the IN-AE's service. The PPM shall create the customized privacy policy for each data subject based on the data subject's privacy preference and service’s privacy policy. It is easy for the data subject to confirm differences between the privacy preference and the privacy policy and to understand what kind of personal data are collected by the IN-AE. After the data subject accepts the privacy policy, the data subject can subscribe to the IN-AE's service.

- The function of creating a customized privacy policy is described in clause 11.4.1.3.

3.	The PPM shall create or update access control policies using the privacy policy that the data subject accepted:

- The function of creating or updating access control policies in the PPM may rely on the authorization mechanisms specified in clauses 7.3 and 7.5. The details of the synchronization process are not specified in the present document.

#### 11.3.3.3	Request for personal data to the IN-CSE

#### 11.3.3.3.1	Introduction

If the IN-AE needs personal data to provide the service, the IN-AE requests the personal data from the IN-CSE. The PPM shall work as PDP, PRP or DAS.

If the PPM works as PDP, the IN-CSE acts as PEP and requests <authorizationDecision> from the PPM and controls the data access using them. Figure 11.3.3.3.2 illustrates the overview of this process.

If the PPM works as PRP, the IN-CSE acts as PDP and requests <authorizationPolicy> from the PPM and controls the data access using them. Figure 11.3.3.3.3 illustrates the overview of this process.

If the PPM works as DAS (Direct dynamic authorization), the IN-CSE checks <dynamicAuthorizationConsultation> and requests <dynamicACPInfo> or <token> from the PPM. Figure 11.3.3.3.4.1 illustrates the overview of this process.

If the PPM works as DAS (Indirect dynamic authorization), the IN-AE requests <token> or tokenID from the PPM. Figure 11.3.3.3.4.2 illustrates the overview of this process. (Detail of this request is not specified in oneM2M)

11.3.3.3.2	PPM works as PDP

The PPM shall be implemented as CSE and shall provide an interface that enables access control for personal data using the PPM as PDP.

Figure 11.3.3.3-1: Request for personal data to the IN-CSE (the PPM works as PDP)

- The IN-AE requests personal data from the IN-CSE.

- PEP in the IN-CSE requests <authorizationDecision> from the PPM. The PPM shall create <authorizationDecision> using access control information.

Detail of creating <authorizationDecision> from access control informain is not specified in oneM2M

- the PPM shall respond <authorizationDecision> to the IN-CSE.

- If accessing personal data is permitted, the IN-CSE accesses the personal data and sends the personal data to the IN-AE as a response.

##### 11.3.3.3.3	PPM works as PRP

- The PPM shall be implemented as CSE and shall provide an interface that enables access control for personal data using the PPM as PRP.

Figure 11.3.3.3-2: Request for personal data to the IN-CSE (the PPM works as PRP)

- The IN-AE requests personal data from the IN-CSE.

- PEP in the IN-CSE requests access control decision from PDP. Then, the PDP requests <authorizationPolicy> from the PPM. The PPM shall create <authorizationPolicy> using access control information.

- The PPM respond <authorizationPolicy> to PDP in the IN-CSE. Then, the PDP decides to permit or deny access to the personal data using the <authorizationPolicy> and sends a result as "Decision Response" to PEP.

- If accessing personal data is permitted, the IN-CSE accesses the personal data and sends the personal data to the IN-AE as a response.

##### 11.3.3.3.4	PPM works as DAS

###### 11.3.3.3.4.1	Direct Dynamic Authorization

The PPM shall be implemented as AE and shall provide an interface that enables access control for personal data using the PPM as DAS.

Figure 11.3.3.3.4.1: Request for personal data to the IN-CSE (the PPM works as DAS and case of direct dynamic authorization)

- The IN-AE requests personal data from the IN-CSE.

- The IN-CSE performs procedure of direct dynamic authorization. The IN-CSE checks <dynamicAuthorizationConsultation> and requests <dynamicACPInfo> or <token> from the PPM.

- The PPM creates <dynamicACPInfo> or <token> and respond <dynamicACPInfo> or <token> to the IN-CSE.

- The IN-CSE make access control decision. If accessing personal data is permitted, the IN-CSE accesses the personal data and sends the personal data to the IN-AE as a response.

###### 11.3.3.3.4.2	Indirect Dynamic Authorization

The PPM shall be implemented as AE and shall provide an interface that enables access control for personal data using the PPM as DAS. In this clause, some optional procedures of indirect dynamic authorization are omitted and focused on procedures related to the PPM.

Figure 11.3.3.3.4.2: Request for personal data to the IN-CSE (the PPM works as DAS and case of indirect dynamic authorization)

- The IN-AE requests <token> or tokenID from the PPM.

- The PPM creates <token> and respond <token> or tokenID to the IN-AE.

Details of above two procedures are not specified in oneM2M.

- The IN-AE requests personal data from the IN-CSE with <token> or tokenID.

- The IN-CSE make access control decision using <token>. If the IN-CSE receive tokenID, the IN-CSE requests <token> from the PPM with tokenID. If accessing personal data is permitted, the IN-CSE accesses the personal data and sends the personal data to the IN-AE as a response.

### -----------------------End of change 1---------------------------------------------