| Input Contribution |
| --- |
| Meeting ID* | SEC 32 |
| Title:* | App-ID Function interface and Metadata |
| Source:* | Ian Deakin, iconectiv, ideakin@iconectiv.com |
| Date:* | 2017-11-06 |
| Input related to* | WI-0073 - App-ID Registry Function |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | NA |
| Decision requested or recommendation:* | Approve these changes in text to the TR-0048-V0.0.2 |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 6	App-ID Registry Function Metadata

The following section provides an assessment for the proposed architecture options for integration of the App-ID Registry Function within the oneM2M architecture. Including the scope of the metadata to be registered with an App-ID.

## 6.1	App-ID Registry Function – Metadata related Requirements

The following is a list of basic requirements to be considered in design and analysis of the App-ID Registry Function :-

3, The App-ID Registry Function shall allow registration of App-ID together with metadata.

4, The App-ID Registry Function shall support a metadata profile to characterize the M2M application.

5, The App-ID Registry Function shall provide a M2M Service infrastructure with the metadata for a registered App-ID.

## 6.2	Candidate Architecture for App-ID Registry Function

The Candidate Architecture for the App-ID Registry Function to provide Metadata with the M2M Service infrastructure is as follows:

OPTION #1 – Standalone App-ID Registry function (ARF)

- The App-ID Registry function is defined as a new entity of the oneM2M architecture.

- Defining a new interface for the CSE to query the App-ID Metadata.

OPTION #2 –  App-ID Registry is part of existing oneM2M MEF interface specification

- App-ID Registry function that is part of an existing oneM2M architectural entity MEF.

- Update the current MEF interface to enable query of the App-ID Registry Function Metadata.

#### 6.2.1	OPTION #1 – Standalone App-ID Registry function (ARF)

For the architecture of a standalone App-ID Registry Function, a new entity (ARF) and interface is defined as ‘Marf’.

Figure X :  App-ID Registry Function new entity and interface

#### 6.2.2	OPTION #2 –  App-ID Registry Function within MEF

For the App-ID Registry Function to be part of the existing oneM2M architecture , it is proposed that the ARF is an extended function of the MEF. The existing MEF entity and interface Mmef is extended called Mmef’ ( Mmef prime) .

Figure X :  App-ID Registry Function as part of the MEF entity and interface

## 6.3 App-ID registry Function Metadata

The App-ID Registry Function provides meta data for each registered App-ID and its corresponding AE-ID’s.

#### 6.3.1	App-ID Metadata

The following table provides the candidate list of AppID metadata attributes defined into sub sections.

| Group | Attribute | Description | Mandatory/Conditional/Optional |
| --- | --- | --- | --- |
| Identity | App-ID | The Registered Application Identity | Mandatory |
| Identity | Management Authority of the App-ID | The App-ID management Authority :- ATIS | Mandatory |
| Idenity | The Registration Authority issuing the App-ID | The registration Authority issuing the App-ID to the application provider. :- Option for multiple registration authorities. | Mandatory |
| Type | Verticle application type | The Tyoe group of the application. For example :- Home Automation Healthcare Automotive Energy Industrial | Mandatory |
| Type | Unique Type | The specific tyope of application within the verticle, for example for Home Automation :- Light Switch Thermostat Camera | Mandatory |
| Capability | Data Resources | How resource intensive the application is for projecting data. Streamed through to periodic long interval notifications. | Optional |
| Security | Authentication Type | Authentication Type :- RPK, PSK, PKI | Mandatory |
| Security | Issuing CA | The URL of the issuing CA | Optional is providing certificate for the App-ID instances. |
| Security | Issuing CA Authrised by management authority | The Management Authority that has authorised the issuing CA to issue certificates for this App-ID. | Optional ( if authorised ) |
| Security | Issuing CA assurance level | The Management Authority assurance level for the issuing CA | Optional ( if authorised ) |
| Security | MAF Identity | Where MAF is used for the App-ID instance authentication, the Idenity. | Optional ( if MAF is used to authenticate the App-ID instances ) |
| Security | MEF Identity | Where MEF is used for the App-ID instance enrolement, the Idenity. | Optional ( if MEF is used to enrole the App-ID instances ) |
| Instance | AE-ID Range | The Range of AE-ID’s that are valid for theis App-ID | Optional if defined |
| Instance | AE-ID Range | Revoked AE-ID identities. List of the AE-ID’s that have been revoked including the specific reason codes. Used to prevent an AE-ID from being authenticated. | Optional if defined. |