| Work Item |
| --- |
| Work Item Title:* | Product Categorization |
| Document Number* | WI-00xx-Product_Categorization-V0_0_1 |
| Supporting Members or Partner type 2* | List the supporting members or Partners type 2 Huawei Technologies Co.,Ltd., KETI, DT, InterDigital, Qualcomm, Spirent, AT4Wireless, UL, R&S, Anritsu |
| Date:* | 2016-7-11 |
| Abstract:* | The proposed work item defines the categorization of products when used in different scenarios. The proposed work item figures out the minimum set of functions needed to be supported by the product if the product is intended for certain services. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Copyright statement

No part may be reproduced except as authorized by written permission.

The copyright and the foregoing restriction extend to reproduction in all media.

All rights reserved.

1	Title (Acronym)

Product categorization

2	Justification

There have been many discussions on the complexity of oneM2M specifications. Among many common functions and resource types defined by oneM2M, as an implementer, it’s hard to know which resource types and funtions are essential for the product that is intended to be used in certain services. Especially in some services where constraint device are widely used, it’s highly demanded that only really relevant functions be implemented to reduce the size of the footprint. However, in the current oneM2M specifications, no such guidance is provided.

When considering vertical services, some of the functions provided by oneM2M seem to be not useful as well. For example, dynamic location service is very important for connected vehicles, but in case of infrastructure management where devices weren’t move after deployment, dynamic location service is no longer very important.

In testing and certification, selection of test cases that are needed for certification is vital to the certify process. Certification of unuseful functions is a great waste for both product manufactures and test houses. The certification without the proper selection of test cases raises the barrier of IoT market as well which is not good for the ecosystem building of oneM2M.

The proposed WI is to investigate on how to categorize the products to satify the requirements from the market. For a certain type of product, it’s easy to get from the proposed WI the needed minimum feature sets for the implementation of the product as well as the test cases need to go through if the product is to be certified by oneM2M.

3	Intended Output

| Tick all the appropriate cases |  |
| --- | --- |
|  | Change request(s) to existing Technical Specification(s) |
|  | Change request(s) to existing Technical Reports(s) |
| √ | New Normative Technical Specifications(s) |
| √ | New Permanent Technical Reports(s) |
|  | New Temporary Technical Reports(s) |

4	Impact

4.1	oneM2M Work Items

WI-0032 may be impacted by the proposed WI. The deliverable of the proposed WI may need modifications to the TSS of the conformance testing WI.

5	Scope

The scope of the proposed WI includes:

- The methodology of how the product categorization work could be proceeded.

- The methodology of bridging the real market requirements to the definition of product categorization.

- The definition of categorization of products.

- The minimum function set needed for each categorization.

- The definition of extended function set if the product is needed to provide more value added services.

- The selection of test cases depends on the function set.

The proposed WI will be primarily responsible by TST working group, however, involvements of experts from other working groups are needed for the determinication of the selection of functions.

6	Schedule and impacted specifications

Provide the schedule of tasks to be performed;

| New Specifications (if any) |
| --- |
| Document Type | Document Number* | Title | Schedule (TP No.) | Lead WG | Impacted WGs | Comments |
|  |  |  | Start | Change Control | Freeze | Approval |  |  |  |
| TR | 00xx | Methodology of product categorization definition | TP 25 | TP 27 | TP 27 | TP 28 | TST |  |  |
| TS | 00yy | Definition of product categorization in oneM2M | TP25 | TP 32 | TP33 | TP34 | TST | ARC,PRO,SEC,MAS |  |

* Optional for first versions (i.e. before it will be assigned by the secretariat)

7	Work Item Rapporteur(s)

Provide the name and contact details of the Work Item Rapporteurs

Jiaxin Yin, Huawei Technologies Co., Ltd., yinjiaxin@huawei.com

8	History

| Document history |
| --- |
| V0.0.1 (Example) | 10 February 2015 (Example) | Initial proposal (Example) |

-------------------------------