| oneM2M Technical Specification |
| --- |
| Document Number | TS-0025-V-2.0.0 |
| Document Name: | Definition of product profiles |
| Date: | 2018-03-12 |
| Abstract: | The document provides definition to product profiles that comply with oneM2M standards. |
| Template Version: 08 September 2015 (Dot not modify) |

This Specification is provided for future development work within oneM2M only. The Partners accept no liability for any use of this Specification.

The present document has not been subject to any approval process by the oneM2M Partners Type 1.  Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices.

About oneM2M

The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide.

More information about oneM2M may be found at:  http//www.oneM2M.org

Copyright Notification

© 2018, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSDSI, TTA, TTC).

All rights reserved.

The copyright extends to reproduction in all media.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

Contents

1	Scope	4

2	References	4

2.1	Normative references	4

2.2	Informative references	4

3	Definitions, symbols and abbreviations	4

4	Conventions	4

5	Product service profiles	5

5.1	Introduction	5

5.2	Constrained sensor as ADN	5

5.2.1	Profile description	5

5.2.2	Profile usage examples	5

5.2.3	Fundamental feature sets	5

5.2.4	Extendable feature sets	7

5.3	Constrained actuator as ADN	7

5.3.1	Profile description	7

5.3.2	Profile usage examples	7

5.3.3	Fundamental feature sets	8

5.3.4	Extendable feature sets	8

5.4	ADN profile 3	8

5.4.1	Profile description	8

5.4.2	Profile usage examples	9

5.4.3	Fundamental feature sets	9

5.4.4	Extendable feature sets	9

5.5	ADN Profile 4	10

5.5.1	Profile description	10

5.5.2	Profile usage examples	10

5.5.3	Fundamental feature sets	10

5.5.4	Extendable feature sets	13

5.6	IN Profile	13

5.6.1	Profile description	13

5.6.2	Profile usage examples	13

5.6.3	Fundamental feature sets	14

5.6.4	Extendable feature sets	20

5.7	Constrained actuator as ASN	23

5.7.1	Profile description	23

5.7.2	Profile usage examples	23

5.7.3	Fundamental feature sets	23

5.7.4	Extendable feature sets	23

5.8	Gateway as MN	24

5.8.1	Profile description	24

5.8.2	Profile usage examples	24

5.8.3	Fundamental feature sets	25

5.8.4	Extendable feature sets	32

Annex A (normative):	Mapping of feature to test purposes	35

History	43

# 1	Scope

The document specifies the detailed defined product profiles that can be used by manufactures and service providers where for each dedicated product, one of the defined product profile can be selected. The product profile would provide guidance to what features shall be implemented, what features should be implemented and what features may be implemented. The present document also describes the test purposes that need to go through if the product need to be certified.

# 2	References

## 2.1	Normative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

The following referenced documents are necessary for the application of the present document.

Not applicable.

## 2.2	Informative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules.

NOTE:	Available at http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf.

[i.2]	oneM2M TS-0031: "oneM2M Features".

[i.3]	oneM2M TS-0001: "Functional Architecture".

# 3	Definitions, symbols and abbreviations

Void.

# 4	Conventions

The key words "Shall", "Shall not", "May", "Need not", "Should", "Should not" in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1].

# 5	Product service profiles

## 5.1	Introduction

The clause defines Product Profiles. Product may be Implementations of oneM2M specification. The Implementation is claimed to comply with one or multiple Product Profiles. Each profile is defined with fundamental feature set and extendable feature set. Fundamental feature set includes Features that shall be implemented if the Implementation under test needs to be certified against the profile. Extendable feature set includes features that are recommanded to be implemented for optimization purpose. The features in the extendable feature set may be tested based on the requirement. The features in the clause are defined in oneM2M TS-0031 [i.2]. Each profile is also composed of a profile description and a profile example. The profile description is the definition of profile and describes the suitable products that should comply to this profile. The profile example gives some real market product examples as well as the usage and scenarios of the product.

Each of the Profile contains the following Features as common Features.

Table 5.1-1: Fundamental feature sets for all Profiles

| Function | Feature Set | Feature | Remark |
| --- | --- | --- | --- |
| GEN | GE/GEN/00001 | At least one | Support one of the bindings. |
|  | GE/GEN/00002 | At least one | Support one of the serializations. |

## 5.2	Constrained sensor as ADN

### 5.2.1	Profile description

The profile defines constraint sensor that is powered by battery and intended to be used for years after deployment without any human interference for maintenance. Therefore, the function of  constraint sensor need to be very limited.

A sensor is intended to be reporting sensed data to the CSE periodically or according to some other period. Everytime the sensor reports data, it sends one message to the CSE. In order to save battery, the sensor can be sleeping before and after the reporting of sensed data.

For the successful report of data, there is needed some context resource architecture like the AE resource, the container resource etc. The resource architecture can be pre-configured in order to minimize the complexity of the constraint sensor.

### 5.2.2	Profile usage examples

The profile applies to constraint sensors that report periodically sensed data. Some example of this kind of product include:

Electricity, water, gas meters that report consumed amount of electricity, water or gas to the CSE. The meters are deployed inside houses and are powered by battery.

Temperature, humidity sensors that are deployed in the open air for environment monitoring. The sensors can be deployed in places that are hardly reachable for people that the sensor's need to be working without human inference for years powered with battery.

### 5.2.3	Fundamental feature sets

For constrained sensors, the features in the fundamental feature sets assume that the registration relationship between the ADN and the registrar CSE has been pre-configured before hand. The <container> resource has also been pre-configured and the resource id of the <container> resource was provisioned to the ADN as well. The ADN could utilize the resource id of the <container> resource to create <contentInstance> directly.

Table 5.2.3-1: Fundamental feature sets for constrained sensor as ADN

| Function | Feature Set | Feature | Remark |  |
| --- | --- | --- | --- | --- |
| GEN | AE/GEN/00001 | At least one | Support one of the format of resource identification | TP/oneM2M/AE/GEN/CRE/001_CSR TP/oneM2M/AE/GEN/CRE/001_SPR TP/oneM2M/AE/GEN/CRE/001_ABS TP/oneM2M/AE/GEN/CRE/002_CSR TP/oneM2M/AE/GEN/CRE/002_SPR TP/oneM2M/AE/GEN/CRE/002_ABS TP/oneM2M/AE/GEN/UPD/001_CSR TP/oneM2M/AE/GEN/UPD/001_SPR TP/oneM2M/AE/GEN/UPD/001_ABS TP/oneM2M/AE/GEN/UPD/002_CSR TP/oneM2M/AE/GEN/UPD/002_SPR TP/oneM2M/AE/GEN/UPD/002_ABS TP/oneM2M/AE/GEN/RET/001_CSR TP/oneM2M/AE/GEN/RET/001_SPR TP/oneM2M/AE/GEN/RET/001_ABS TP/oneM2M/AE/GEN/RET/002_CSR TP/oneM2M/AE/GEN/RET/002_SPR TP/oneM2M/AE/GEN/RET/002_ABS TP/oneM2M/AE/GEN/DEL/001_CSR TP/oneM2M/AE/GEN/DEL/001_SPR TP/oneM2M/AE/GEN/DEL/001_ABS TP/oneM2M/AE/GEN/DEL/002_CSR TP/oneM2M/AE/GEN/DEL/002_SPR TP/oneM2M/AE/GEN/DEL/002_ABS |
|  | AE/GEN/00002 | AE/GEN/00002/00001 | Support create request | TP/oneM2M/AE/DMR/CRE/001 |
| DMR | AE/DMR/00002 | AE/DMR/00002/00001 | Support create contentInstance | TP/oneM2M/AE/DMR/CRE/002 |

### 5.2.4	Extendable feature sets

Table 5.2.4-1: Extendable feature sets for constrained sensor as ADN

| Function | Feature Set | Feature | Remark |  |
| --- | --- | --- | --- | --- |
| REG | AE/REG/00002 | AE/REG/00002/00001 | Create <AE> | TP/oneM2M/AE/REG//CRE/001 TP/oneM2M/AE/REG/CRE/002_RR |
|  |  | AE/GEN/00003/00001 | Create <AE> with resourceName | TP/oneM2M/AE/REG/CRE/002_RN |
|  |  | AE/GEN/00003/00002 | Create <AE> with expirationTime | TP/oneM2M/AE/REG/CRE/002_ET |
|  |  | AE/DIS/00001/00017 | Create <AE> with labels | TP/oneM2M/AE/REG/CRE/002_LBL |
|  |  | AE/REG/00002/00002 | Create <AE> with applicationName | TP/oneM2M/AE/REG/CRE/002_APN |
| DMR | AE/DMR/00001 | AE/DMR/00001/00001 | Create <container> with no attribute set | TP/oneM2M/AE/DMR/CRE/001 |
|  |  | AE/GEN/00003/00001 | Create <container> with resourceName | TP/oneM2M/AE/DMR/CRE/004_RN |
|  |  | AE/GEN/00003/00002 | Create <container> with expirationTime | TP/oneM2M/AE/DMR/CRE/004_ET |
|  |  | AE/DIS/00001/00017 | Create <container> with labels | TP/oneM2M/AE/DMR/CRE/004_LBL |
|  |  | AE/DMR/00001/00002 | Create <container> with maxNrOfInstances | TP/oneM2M/AE/DMR/CRE/004_MNI |
|  |  | AE/DMR/00001/00003 | Create <container> with maxByteSize | TP/oneM2M/AE/DMR/CRE/004_MBS |
|  |  | AE/DMR/00001/00004 | Create <container> with maxInstanceAge | TP/oneM2M/AE/DMR/CRE/004_MIA |
|  | AE/DMR/00002 | AE/GEN/00003/00001 | Create <contentInstance> with resourceName | TP/oneM2M/AE/DMR/CRE/003_RN |
|  |  | AE/GEN/00003/00002 | Create <contentInstance> with expirationTime | TP/oneM2M/AE/DMR/CRE/003_ET |
|  |  | AE/DIS/00001/00017 | Create <contentInstance> with labels | TP/oneM2M/AE/DMR/CRE/003_LBL |
|  |  | AE/DMR/00002/00002 | Create <contentInstance> with contentInfo | TP/oneM2M/AE/DMR/CRE/003_CNF |

## 5.3	Constrained actuator as ADN

### 5.3.1	Profile description

The profile defines constraint actuator that is powered by battery and intended to be used fro years after deployment without any human interference for maintenance. Therefore, the function of constraint actuator need to be very limited.

An actuator is intended to be receiving control command from CSE via notification or other means. The actuator then actuates according to the control command.

The actuator need to receive control command. As a result, the actuator need to be request reachable to receive notification or be able to start a polling channel.

### 5.3.2	Profile usage examples

Swithes deployed along the street light to switch on or off the street light remotely.

### 5.3.3	Fundamental feature sets

Table 5.3.3-1: Fundamental feature sets for constrained sensor as ADN

| Function | Feature Set | Feature | Remark |  |
| --- | --- | --- | --- | --- |
| GEN | AE/GEN/00001 | At least one | Resource identifiers | TP/oneM2M/AE/GEN/CRE/001_CSR TP/oneM2M/AE/GEN/CRE/001_SPR TP/oneM2M/AE/GEN/CRE/001_ABS TP/oneM2M/AE/GEN/CRE/002_CSR TP/oneM2M/AE/GEN/CRE/002_SPR TP/oneM2M/AE/GEN/CRE/002_ABS TP/oneM2M/AE/GEN/UPD/001_CSR TP/oneM2M/AE/GEN/UPD/001_SPR TP/oneM2M/AE/GEN/UPD/001_ABS TP/oneM2M/AE/GEN/UPD/002_CSR TP/oneM2M/AE/GEN/UPD/002_SPR TP/oneM2M/AE/GEN/UPD/002_ABS TP/oneM2M/AE/GEN/RET/001_CSR TP/oneM2M/AE/GEN/RET/001_SPR TP/oneM2M/AE/GEN/RET/001_ABS TP/oneM2M/AE/GEN/RET/002_CSR TP/oneM2M/AE/GEN/RET/002_SPR TP/oneM2M/AE/GEN/RET/002_ABS TP/oneM2M/AE/GEN/DEL/001_CSR TP/oneM2M/AE/GEN/DEL/001_SPR TP/oneM2M/AE/GEN/DEL/001_ABS TP/oneM2M/AE/GEN/DEL/002_CSR TP/oneM2M/AE/GEN/DEL/002_SPR TP/oneM2M/AE/GEN/DEL/002_ABS |
| GEN | AE/GEN/00002 | AE/GEN/00002/00001 | Support Create request targeting one resource | TP/oneM2M/AE/DMR/CRE/001 |
| REG | AE/REG/00002 | AE/REG/00002/00001 | Create <AE> with mandatory attributes[2] | TP/oneM2M/AE/REG//CRE/001 TP/oneM2M/AE/REG/CRE/002_RR |
| REG | AE/REG/00002 | AE/REG/00002/00003 | Create <AE> with pointOfAccess | TP/oneM2M/AE/REG/CRE/002_POA |
| SUB | AE/SUB/00001 | AE/SUB/00001/00001 | Create <subscription> with mandatory attributes [2] | TP/oneM2M/AE/SUB/CRE/001 |

### 5.3.4	Extendable feature sets

Void.

## 5.4	ADN profile 3

### 5.4.1	Profile description

This profile defines features for normal sensor devices or software components that desire to implement oneM2M sensing services. The sensing services such as monitoring temperature, detecting illumination, collection of location information etc are characterized with collecting and uploading measurement data into a destination e.g. a repository. The scope of normal sensor devices cover those that are powered by electricity power or by battery that can be easily changed when the battery is off and have rich resources compared to resource-constraint sensor devices.

The sensing service profile defines a set of features required to implement sensing functionalities including creation and update of <container>, creation of <contentInstance>, etc.

### 5.4.2	Profile usage examples

This profile applies to normal sensors deployed in non critial environments have relative rich resources and are powered by electricity power or by battery that can be easily changed. This profile can also apply to software components that implements sensing services.

Taking smart socket as an example, when a manufacturer-A decides to design a smart socket with oneM2M sensing service, he can refer to the Sensing Service Profile to check the fundamental features that are required to implement. The fundamental features for Sensing Service Profile are defined in clause 5.4.3. When another manufacturer-B also designs a smart socket complying with the Sensing Service Profile, these two smart sockets produced from two different manufacturers are interoperable potentially to work together to implement complex tasks.

### 5.4.3	Fundamental feature sets

Container is used for storing the measurements of sensing device and whenever there is data measured from the sensing device, the data will be sent to the CSE for storage by sending a <contentInstance> create request from the originator where the encoded measurement is included within the payload of the <contentInstance> create request.

oneM2M sensing service profile consists of minimum features to implement Data Management for Container and ContentInstance functionality shown in table 5.4.3-1.

Table 5.4.3-1: Fundamental feature set for ADN profile 3

| Function | Feature Set | Feature | Remark |  |
| --- | --- | --- | --- | --- |
| GEN | AE/GEN/00001 | At least one | Support one of the format of resource identification | TP/oneM2M/AE/GEN/CRE/001_CSR TP/oneM2M/AE/GEN/CRE/001_SPR TP/oneM2M/AE/GEN/CRE/001_ABS TP/oneM2M/AE/GEN/CRE/002_CSR TP/oneM2M/AE/GEN/CRE/002_SPR TP/oneM2M/AE/GEN/CRE/002_ABS TP/oneM2M/AE/GEN/UPD/001_CSR TP/oneM2M/AE/GEN/UPD/001_SPR TP/oneM2M/AE/GEN/UPD/001_ABS TP/oneM2M/AE/GEN/UPD/002_CSR TP/oneM2M/AE/GEN/UPD/002_SPR TP/oneM2M/AE/GEN/UPD/002_ABS TP/oneM2M/AE/GEN/RET/001_CSR TP/oneM2M/AE/GEN/RET/001_SPR TP/oneM2M/AE/GEN/RET/001_ABS TP/oneM2M/AE/GEN/RET/002_CSR TP/oneM2M/AE/GEN/RET/002_SPR TP/oneM2M/AE/GEN/RET/002_ABS TP/oneM2M/AE/GEN/DEL/001_CSR TP/oneM2M/AE/GEN/DEL/001_SPR TP/oneM2M/AE/GEN/DEL/001_ABS TP/oneM2M/AE/GEN/DEL/002_CSR TP/oneM2M/AE/GEN/DEL/002_SPR TP/oneM2M/AE/GEN/DEL/002_ABS |
|  | AE/GEN/00002 | AE/GEN/00002/00001 | Support Create request targeting one resource | TP/oneM2M/AE/DMR/CRE/001 |
| REG | AE/REG/00002 | AE/REG/00002/00001 | Create <AE> with mandatory attributes | TP/oneM2M/AE/REG//CRE/001 TP/oneM2M/AE/REG/CRE/002_RR |
| DMR | AE/DMR/00001 | AE/DMR/00001/00001 | Create <container> with no attribute set | TP/oneM2M/AE/DMR/CRE/001 |
|  | AE/DMR/00002 | AE/DMR/00002/00001 | Create <contentInstance> with mandatory attributes | TP/oneM2M/AE/DMR/CRE/002 |

### 5.4.4	Extendable feature sets

Void.

## 5.5	ADN Profile 4

### 5.5.1	Profile description

oneM2M provides serveral logical entity concepts called 'Node' to explain oneM2M Architecture in oneM2M TS-0001 [i.3]. And from the descriptions about the node types indicates some examples that particular node could match with pyshical oneM2M devices (e.g. ADN -> constrainted oneM2M Device). But for the oneM2M device developers, may require more detail information to design and implement physical devices.

This ADN Profile 1 defines set of common features which could be used for small originator device types of oneM2M services.

### 5.5.2	Profile usage examples

ADN Profile 1 could be the basic profile of oneM2M devices like sensor, actuator etc. And also this profile could be used independently when developers want to implement oneM2M device with special functions.

### 5.5.3	Fundamental feature sets

Table 5.5.3-1: Feature set for ADN Profile 4

| Function | Feature Set | Feature | Remark |  |
| --- | --- | --- | --- | --- |
| GEN | AE/GEN/00001 | At least one | Support one of the format of resource identification | TP/oneM2M/AE/GEN/CRE/001_CSR TP/oneM2M/AE/GEN/CRE/001_SPR TP/oneM2M/AE/GEN/CRE/001_ABS TP/oneM2M/AE/GEN/CRE/002_CSR TP/oneM2M/AE/GEN/CRE/002_SPR TP/oneM2M/AE/GEN/CRE/002_ABS TP/oneM2M/AE/GEN/UPD/001_CSR TP/oneM2M/AE/GEN/UPD/001_SPR TP/oneM2M/AE/GEN/UPD/001_ABS TP/oneM2M/AE/GEN/UPD/002_CSR TP/oneM2M/AE/GEN/UPD/002_SPR TP/oneM2M/AE/GEN/UPD/002_ABS TP/oneM2M/AE/GEN/RET/001_CSR TP/oneM2M/AE/GEN/RET/001_SPR TP/oneM2M/AE/GEN/RET/001_ABS TP/oneM2M/AE/GEN/RET/002_CSR TP/oneM2M/AE/GEN/RET/002_SPR TP/oneM2M/AE/GEN/RET/002_ABS TP/oneM2M/AE/GEN/DEL/001_CSR TP/oneM2M/AE/GEN/DEL/001_SPR TP/oneM2M/AE/GEN/DEL/001_ABS TP/oneM2M/AE/GEN/DEL/002_CSR TP/oneM2M/AE/GEN/DEL/002_SPR TP/oneM2M/AE/GEN/DEL/002_ABS |
|  | AE/GEN/00002 | AE/GEN/00002/00001 | Support Create request targeting one resource | TP/oneM2M/AE/DMR/CRE/001 |
|  |  | AE/GEN/00002/00002 | Support Retrieve request targeting one resource | TP/oneM2M/AE/DMR/RET/001_CB TP/oneM2M/AE/DMR/RET/001_AE TP/oneM2M/AE/DMR/RET/001_CNT |
|  |  | AE/GEN/00002/00003 | Support Update request targeting one resource | TP/oneM2M/AE/DMR/UPD/002_LBL |
|  |  | AE/GEN/00002/00004 | Support Delete request targeting one resource | TP/oneM2M/AE/DMR/DEL/003 |
| REG | AE/REG/00001 | AE/REG/00001/00001 | The Retrieval of <CSEBase> resource | TP/oneM2M/AE/DMR/RET/001_CB |
|  | AE/REG/00002 | AE/REG/00002/00001 | Create <AE> with mandatory attributes | TP/oneM2M/AE/REG//CRE/001 TP/oneM2M/AE/REG/CRE/002_RR |
|  |  | AE/GEN/00003/00001 | Create <AE> with resourceName attribute | TP/oneM2M/AE/REG/CRE/002_RN |
|  |  | AE/GEN/00003/00002 | Create <AE> with expirationTime attribute | TP/oneM2M/AE/REG/CRE/002_ET |
|  |  | AE/DIS/00001/00017 | Create <AE> with labels | TP/oneM2M/AE/REG/CRE/002_LBL |
|  |  | AE/REG/00002/00002 | Create <AE> with applicationName | TP/oneM2M/AE/REG/CRE/002_APN |
|  |  | AE/REG/00002/00003 | Create <AE> with pointOfAccess | TP/oneM2M/AE/REG/CRE/002_POA |
|  |  | AE/REG/00002/00004 | Create <AE> with nodeLink | TP/oneM2M/AE/REG/CRE/002_NL |
|  |  | AE/REG/00002/00005 | Create <AE> with contentSerialization | TP/oneM2M/AE/REG/CRE/002_CSZ |
|  |  | AE/GEN/00003/00002 | Update <AE> with expirationTime | TP/oneM2M/AE/DMR/UPD/001_ET |
|  |  | AE/DIS/00001/00017 | Update <AE> with labels | TP/oneM2M/AE/DMR/UPD/001_LBL |
|  |  | AE/REG/00002/00007 | Update <AE> with applicationName | TP/oneM2M/AE/DMR/UPD/001_APN |
|  |  | AE/REG/00002/00008 | Update <AE> with pointOfAccess | TP/oneM2M/AE/DMR/UPD/001_POA |
|  |  | AE/REG/00002/00009 | Update <AE> with nodeLink | TP/oneM2M/AE/DMR/UPD/001_NL |
|  |  | AE/GEN/00002/00005 | Update <AE> with requestReachability | TP/oneM2M/AE/DMR/UPD/001_RR |
|  |  | AE/REG/00002/00010 | Update <AE> with contentSerialization | TP/oneM2M/AE/DMR/UPD/001_CSZ |
|  |  | AE/REG/00002/00013 | Delete <AE> | TP/oneM2M/AE/REG/DEL/001 |
|  |  | AE/REG/00002/00012 | Retrieve <AE> | TP/oneM2M/AE/DMR/RET/001_AE |
| DMR | AE/DMR/00001 | AE/DMR/00001/00001 | Create <container> with no attribute set | TP/oneM2M/AE/DMR/CRE/001 |
|  |  | AE/GEN/00003/00001 | Create <container> with resourceName | TP/oneM2M/AE/DMR/CRE/004_RN |
|  |  | AE/GEN/00003/00002 | Create <container> with expirationTime | TP/oneM2M/AE/DMR/CRE/004_ET |
|  |  | AE/DIS/00001/00017 | Create <container> with labels | TP/oneM2M/AE/DMR/CRE/004_LBL |
|  |  | AE/DMR/00001/00002 | Create <container> with maxNrOfInstances | TP/oneM2M/AE/DMR/CRE/004_MNI |
|  |  | AE/DMR/00001/00003 | Create <container> with maxByteSize | TP/oneM2M/AE/DMR/CRE/004_MBS |
|  |  | AE/DMR/00001/00004 | Create <container> with maxInstanceAge | TP/oneM2M/AE/DMR/CRE/004_MIA |
|  |  | AE/GEN/00003/00002 | Update <container> with expirationTime | TP/oneM2M/AE/DMR/UPD/002_ET |
|  |  | AE/DIS/00001/00017 | Update <container> with labels | TP/oneM2M/AE/DMR/UPD/002_LBL |
|  |  | AE/DMR/00001/00006 | Update <container> with maxNrOfInstances | TP/oneM2M/AE/DMR/UPD/002_MNI |
|  |  | AE/DMR/00001/00007 | Update <container> with maxByteSize | TP/oneM2M/AE/DMR/UPD/002_MBS |
|  |  | AE/DMR/00001/00008 | Update <container> with maxInstanceAge | TP/oneM2M/AE/DMR/UPD/002_MIA |
|  |  | AE/DMR/00001/00011 | Delete <container> | TP/oneM2M/AE/DMR/DEL/003 |
|  |  | AE/DMR/00001/00012 | Retrieve <container> | TP/oneM2M/AE/DMR/RET/004 |
|  | AE/DMR/00002 | AE/DMR/00002/00001 | Create <contentInstance> with mandatory attributes | TP/oneM2M/AE/DMR/CRE/002 |
|  |  | AE/GEN/00003/00001 | Create <contentInstance> with resourceName | TP/oneM2M/AE/DMR/CRE/003_RN |
|  |  | AE/GEN/00003/00002 | Create <contentInstance> with expirationTime | TP/oneM2M/AE/DMR/CRE/003_ET |
|  |  | AE/DIS/00001/00017 | Create <contentInstance> with labels | TP/oneM2M/AE/DMR/CRE/003_LBL |
|  |  | AE/DMR/00002/00002 | Create <contentInstance> with contentInfo | TP/oneM2M/AE/DMR/CRE/003_CNF |
|  |  | AE/DMR/00002/00003 | Create <contentInstance> with contentRef | TP/oneM2M/AE/DMR/CRE/003_CONR |
|  |  | AE/DMR/00002/00004 | Retrieve <contentInstance> resource targeting the <contentInstance> resource | TP/oneM2M/AE/DMR/RET/005 |
|  |  | AE/DMR/00002/00005 | Retrieve oldest <contentInstance> resource targeting the <oldest> resource | TP/oneM2M/AE/DMR/RET/002 |
|  |  | AE/DMR/00002/00006 | Retrieve latest <contentInstance> resource targeting the <latest> resource | TP/oneM2M/AE/DMR/RET/003 |
|  |  | AE/DMR/00002/00007 | Delete <contentInstance> | TP/oneM2M/AE/DMR/DEL/004 |
|  |  | AE/DMR/00002/00008 | Delete oldest <contentInstance> resource targeting the <oldest> resource | TP/oneM2M/AE/DMR/DEL/001 |
|  |  | AE/DMR/00002/00009 | Delete latest <contentInstance> resource targeting the <latest> resource | TP/oneM2M/AE/DMR/DEL/002 |

### 5.5.4	Extendable feature sets

Table 5.5.4-1

| Function | Feature Set | Feature | Remark |  |
| --- | --- | --- | --- | --- |
| REG | AE/REG/00002 | AE/REG/00002/00001 | Create <AE> with App-ID attribute | TP/oneM2M/AE/REG/CRE/002_API |
|  |  | VOID | Create <AE> with ontologyRef attribute | TP/oneM2M/AE/REG/CRE/002_OR |
|  |  | VOID | Update <AE> with ontologyRef attribute | TP/oneM2M/AE/DMR/UPD/001_OR |
| DMR | AE/DMR/00001 | AE/SEC/00001/00007 | Create <container> with acpi | TP/oneM2M/AE/DMR/CRE/004_ACPI |
|  |  | VOID | Create <container> with ontologyRef | TP/oneM2M/AE/DMR/CRE/004_OR |
|  |  | VOID | Create <container> with locationID | TP/oneM2M/AE/DMR/CRE/004_LI |
| SUB | AE/SUB/00001 | AE/SUB/00001/00002 | Create <subscription> with labels | TP/oneM2M/AE/SUB/CRE/002_LBL |
|  |  | AE/SUB/00001/00005 | Create <subscription> with subscriberURI | TP/oneM2M/AE/SUB/CRE/002_SU |
|  |  | AE/SEC/00001/00007 | Create <subscription> with acpi | TP/oneM2M/AE/SUB/CRE/002_ACPI |
|  |  | AE/SUB/00002/00001 | Create <subscription> with eventNotificationCriteria | TP/oneM2M/AE/SUB/CRE/002_ENC |
|  |  | AE/SUB/00002/00002 | Create <subscription> with expirationCounter | TP/oneM2M/AE/SUB/CRE/002_EXC |
|  |  | AE/SUB/00003/00001 | Create <subscription> with notificationForwardingURI | TP/oneM2M/AE/SUB/CRE/002_NFU |
|  |  | AE/SUB/00002/00009 | Create <subscription> with notificationContentType | TP/oneM2M/AE/SUB/CRE/002_NCT |
|  |  | AE/SUB/00002/00010 | Create <subscription> with notificationEventCat | TP/oneM2M/AE/SUB/CRE/002_NEC |
|  |  | VOID | Support NOTIFY Request | TP/oneM2M/AE/SUB/NTF/001 TP/oneM2M/AE/SUB/NTF/002 |

## 5.6	IN Profile

### 5.6.1	Profile description

oneM2M provides serveral logical entity concepts called 'Node' to explain oneM2M Architecture in oneM2M TS-0001 [i.3]. And from the descriptions about the node types indicates some examples that particular node could match with pyshical oneM2M devices (e.g. ADN -> constrainted oneM2M Device). But for the oneM2M device developers, may require more detail information to design and implement physical devices.

This IN Profile 1 defines set of common features which could be used for server device type of oneM2M services.

### 5.6.2	Profile usage examples

IN Profile 1 could be the common profile of oneM2M devices like service server etc. And also this profile could be used independently when developers want to implement oneM2M device with special functions.

### 5.6.3	Fundamental feature sets

Table 5.6.3-1: Fundamental feature set for IN Profile

| Function | Feature Set | Feature | Remark |  |
| --- | --- | --- | --- | --- |
| GEN | CE/GEN/00001 | CE/GEN/00001/00001 | Support Unstructured resource identifier | TP/oneM2M/CSE/GEN/CRE/001_CSR TP/oneM2M/CSE/GEN/CRE/001_SPR TP/oneM2M/CSE/GEN/CRE/001_ABS TP/oneM2M/CSE/GEN/UPD/001_CSR TP/oneM2M/CSE/GEN/UPD/001_SPR TP/oneM2M/CSE/GEN/UPD/001_ABS TP/oneM2M/CSE/GEN/RET/001_CSR TP/oneM2M/CSE/GEN/RET/001_SPR TP/oneM2M/CSE/GEN/RET/001_ABS TP/oneM2M/CSE/GEN/DEL/001_CSR TP/oneM2M/CSE/GEN/DEL/001_SPR TP/oneM2M/CSE/GEN/DEL/001_ABS |
|  |  | CE/GEN/00001/00002 | Support Structured resource identifier | TP/oneM2M/CSE/GEN/CRE/002_CSR TP/oneM2M/CSE/GEN/CRE/002_SPR TP/oneM2M/CSE/GEN/CRE/002_ABS TP/oneM2M/CSE/GEN/UPD/002_CSR TP/oneM2M/CSE/GEN/UPD/002_SPR TP/oneM2M/CSE/GEN/UPD/002_ABS TP/oneM2M/CSE/GEN/RET/002_CSR TP/oneM2M/CSE/GEN/RET/002_SPR TP/oneM2M/CSE/GEN/RET/002_ABS TP/oneM2M/CSE/GEN/DEL/002_CSR TP/oneM2M/CSE/GEN/DEL/002_SPR TP/oneM2M/CSE/GEN/DEL/002_ABS |
| GEN | CE/GEN/00002 | CE/GEN/00002/00001 | Support blocking request |  |
| REG | CE/REG/00001 | CE/REG/00001/00001 | Support <CSEBase> resource. | TP/oneM2M/CSE/REG/CRE/021 TP/oneM2M/CSE/REG/RET/001 TP/oneM2M/CSE/REG/RET/008 TP/oneM2M/CSE/REG/UPD/001 TP/oneM2M/CSE/REG/DEL/001 |
|  |  | CE/REG/00001/00002 | Support the cseType attribute of <CSEBase> | TP/oneM2M/CSE/REG/RET/002_CST TP/oneM2M/CSE/REG/RET/005 |
|  |  | CE/REG/00001/00003 | Support the nodeLink attribute of <CSEBase> | TP/oneM2M/CSE/REG/RET/002_NL |
|  | CE/REG/00002 | CE/REG/00002/00001 | Support <AE> resource | TP/oneM2M/CSE/REG/RET/003 TP/oneM2M/CSE/REG/DEL/003 TP/oneM2M/CSE/DMR/RET/013_AE TP/oneM2M/CSE/DMR/UPD/016_AE/ET TP/oneM2M/CSE/DMR/UPD/016_AE/RR |
|  |  | CE/REG/00002/00002 | AE registration/de-registration without a pre-assigned AE-ID in the registration request and where the AE-ID Stem is configured with 'C'. | TP/oneM2M/CSE/REG/CRE/004 TP/oneM2M/CSE/REG/CRE/009 TP/oneM2M/CSE/REG/CRE/011 TP/oneM2M/CSE/REG/CRE/016 TP/oneM2M/CSE/REG/CRE/017_API TP/oneM2M/CSE/REG/CRE/017_RR TP/oneM2M/CSE/REG/CRE/022 TP/oneM2M/CSE/REG/CRE/023 |
|  |  | CE/REG/00002/00003 | AE registration/de-registration without a pre-assigned AE-ID in the registration request and where the AE-ID Stem is configured with 'S'. |  |
|  |  | CE/REG/00002/00004 | AE registration/de-registration without a pre-assigned AE-ID in the registration request and where no AE-ID Stem is included. |  |
|  |  | CE/REG/00002/00005 | AE registration/de-registration without a pre-assigned AE-ID in the registration request and where the AE-ID Stem is configured with 'S' and where announcement to an IN-CSE is needed to get an AE-ID assigned |  |
|  |  | CE/DIS/00001/00006 | Support the labels attribute of <AE> resource | TP/oneM2M/CSE/REG/CRE/012_AE/LBL TP/oneM2M/CSE/REG/RET/004_LBL TP/oneM2M/CSE/DMR/UPD/015_AE/LBL |
|  |  | CE/REG/00002/00007 | Support the applicationName attribute of <AE> resource | TP/oneM2M/CSE/REG/CRE/012_AE/APN TP/oneM2M/CSE/REG/RET/004_APN TP/oneM2M/CSE/DMR/UPD/015_AE/APN |
|  |  | CE/REG/00002/00008 | Support the pointOfAccess attribute of <AE> resource | TP/oneM2M/CSE/REG/CRE/012_AE/POA TP/oneM2M/CSE/REG/RET/004_POA TP/oneM2M/CSE/DMR/UPD/015_AE/POA |
|  |  | CE/REG/00002/00009 | AE registration with pre-assigned AE-ID | TP/oneM2M/CSE/REG/CRE/001 TP/oneM2M/CSE/REG/CRE/002 |
|  | CE/REG/00004 | CE/REG/00004/00001 | Support <remoteCSE> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/REG/CRE/018 TP/oneM2M/CSE/REG/CRE/019 TP/oneM2M/CSE/REG/CRE/025 TP/oneM2M/CSE/REG/RET/006 TP/oneM2M/CSE/REG/RET/010 TP/oneM2M/CSE/REG/DEL/002 TP/oneM2M/CSE/DMR/UPD/016_CSR/ET TP/oneM2M/CSE/DMR/UPD/016_CSR/RR |
|  |  | CE/DIS/00001/00006 | Support the labels attribute of <remoteCSE> resource | TP/oneM2M/CSE/REG/CRE/013_LBL TP/oneM2M/CSE/REG/CRE/028_LBL TP/oneM2M/CSE/REG/RET/007_LBL TP/oneM2M/CSE/REG/UPD/002_LBL |
|  |  | CE/REG/00004/00002 | Support the cseType attribute of <remoteCSE> resource | TP/oneM2M/CSE/REG/CRE/013_CST TP/oneM2M/CSE/REG/RET/007_CST |
|  |  | CE/REG/00004/00003 | Support the pointOfAccess attribute of <remoteCSE> resource | TP/oneM2M/CSE/REG/CRE/013_POA TP/oneM2M/CSE/REG/CRE/028_POA TP/oneM2M/CSE/REG/RET/007_POA TP/oneM2M/CSE/REG/UPD/002_POA |
|  |  | CE/REG/00004/00004 | Support the nodeLink attribute of <remoteCSE> resource | TP/oneM2M/CSE/REG/CRE/013_NL TP/oneM2M/CSE/REG/CRE/028_NL TP/oneM2M/CSE/REG/RET/007_NL TP/oneM2M/CSE/REG/UPD/002_NL |
| DMR | CE/DMR/00001 | CE/DMR/00001/00001 | Support <container> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/DMR/CRE/001_CNT/CB TP/oneM2M/CSE/DMR/CRE/001_CNT/AE TP/oneM2M/CSE/DMR/CRE/001_CNT/CNT TP/oneM2M/CSE/DMR/CRE/002_CNT TP/oneM2M/CSE/DMR/CRE/003_CNT TP/oneM2M/CSE/DMR/CRE/007 TP/oneM2M/CSE/DMR/CRE/008 TP/oneM2M/CSE/DMR/CRE/009 TP/oneM2M/CSE/DMR/CRE/010 TP/oneM2M/CSE/DMR/CRE/011 TP/oneM2M/CSE/DMR/CRE/014_CNT_CIN TP/oneM2M/CSE/DMR/RET/001_CNT TP/oneM2M/CSE/DMR/RET/013_CNT TP/oneM2M/CSE/DMR/UPD/001_CNT/LBL TP/oneM2M/CSE/DMR/UPD/002_CNT/LBL TP/oneM2M/CSE/DMR/UPD/003_CNT/LBL TP/oneM2M/CSE/DMR/UPD/004_CNT/ET/MNI/LBL TP/oneM2M/CSE/DMR/UPD/005_CNT/EXC TP/oneM2M/CSE/DMR/UPD/007_CNT/CT TP/oneM2M/CSE/DMR/UPD/008_CNT/ET TP/oneM2M/CSE/DMR/UPD/009_CNT/LBL TP/oneM2M/CSE/DMR/UPD/010 TP/oneM2M/CSE/DMR/UPD/016_CNT/ET TP/oneM2M/CSE/DMR/DEL/001_CNT TP/oneM2M/CSE/DMR/DEL/005 TP/oneM2M/CSE/DMR/DEL/006 |
|  |  | CE/DIS/00001/00006 | Support the labels attribute of <container> resource | TP/oneM2M/CSE/DMR/CRE/012_CNT/LBL TP/oneM2M/CSE/DMR/UPD/014_CNT/LBL TP/oneM2M/CSE/DMR/UPD/015_CNT/LBL |
|  |  | CE/DMR/00002/00001 | Support the creator attribute of <container> resource | TP/oneM2M/CSE/DMR/CRE/012_CNT/CR |
|  |  | CE/DMR/00001/00002 | Support the maxNrOfInstances attribute of <container> resource | TP/oneM2M/CSE/DMR/CRE/005_MNI TP/oneM2M/CSE/DMR/CRE/006_MNI TP/oneM2M/CSE/DMR/CRE/012_CNT/MNI TP/oneM2M/CSE/DMR/UPD/014_CNT/MNI TP/oneM2M/CSE/DMR/UPD/015_CNT/MNI |
|  |  | CE/DMR/00001/00003 | Support the maxByteSize attribute of <container> resource | TP/oneM2M/CSE/DMR/CRE/005_MBS TP/oneM2M/CSE/DMR/CRE/006_MBS TP/oneM2M/CSE/DMR/CRE/012_CNT/MBS TP/oneM2M/CSE/DMR/CRE/013 TP/oneM2M/CSE/DMR/UPD/014_CNT/MBS TP/oneM2M/CSE/DMR/UPD/015_CNT/MBS |
|  |  | CE/DMR/00001/00004 | Support the maxInstanceAge attribute of <container> resource | TP/oneM2M/CSE/DMR/CRE/005_MIA TP/oneM2M/CSE/DMR/CRE/006_MIA TP/oneM2M/CSE/DMR/CRE/012_CNT/MIA TP/oneM2M/CSE/DMR/UPD/014_CNT/MIA TP/oneM2M/CSE/DMR/UPD/015_CNT/MIA |
|  | CE/DMR/00002 | CE/DMR/00002/00001 | Support <contentInstance> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/DMR/CRE/001_CIN/CNT TP/oneM2M/CSE/DMR/RET/001_CIN TP/oneM2M/CSE/DMR/UPD/011 TP/oneM2M/CSE/DMR/DEL/001_CIN |
|  |  | CE/DIS/00001/00006 | Support the labels attribute of <contentInstance> resource | TP/oneM2M/CSE/DMR/CRE/012_CIN/LBL |
|  |  | CE/DMR/00002/00001 | Support the creator attribute of <contentInstance> resource | TP/oneM2M/CSE/DMR/CRE/012_CIN/CR |
|  |  | CE/DMR/00002/00002 | Support the contentInfo attribute of <contentInstance> resource | TP/oneM2M/CSE/DMR/CRE/012_CIN/CNF |
|  |  | CE/DMR/00002/00004 | Retrieve and Delete of latest <contentInstance> resource by <latest> virtual resource | TP/oneM2M/CSE/DMR/RET/012 TP/oneM2M/CSE/DMR/UPD/012 TP/oneM2M/CSE/DMR/DEL/007 |
|  |  | CE/DMR/00002/00057 | Retrieve and Delete of oldest <contentInstance> resource by <oldest> virtual resource | TP/oneM2M/CSE/DMR/RET/010 TP/oneM2M/CSE/DMR/UPD/013 TP/oneM2M/CSE/DMR/DEL/009 |
| SUB | CE/SUB/00001 | CE/SUB/00001/00001 | The Support of <subscription> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/DMR/CRE/001_SUB/CB TP/oneM2M/CSE/DMR/CRE/001_SUB/AE TP/oneM2M/CSE/DMR/CRE/001_SUB/CNT TP/oneM2M/CSE/DMR/CRE/001_SUB/ACP TP/oneM2M/CSE/DMR/CRE/001_SUB/CSR TP/oneM2M/CSE/DMR/CRE/001_SUB/GRP TP/oneM2M/CSE/DMR/CRE/002_SUB TP/oneM2M/CSE/DMR/CRE/003_SUB TP/oneM2M/CSE/DMR/RET/001_SUB TP/oneM2M/CSE/DMR/RET/013_SUB TP/oneM2M/CSE/DMR/UPD/001_SUB/LBL TP/oneM2M/CSE/DMR/UPD/002_SUB/LBL TP/oneM2M/CSE/DMR/UPD/003_SUB/LBL TP/oneM2M/CSE/DMR/UPD/004_SUB/ET/LBL/EXC TP/oneM2M/CSE/DMR/UPD/005_SUB/MNI TP/oneM2M/CSE/DMR/UPD/007_SUB/CT TP/oneM2M/CSE/DMR/UPD/008_SUB/ET TP/oneM2M/CSE/DMR/UPD/009_SUB/LBL TP/oneM2M/CSE/DMR/UPD/016_SUB/ET TP/oneM2M/CSE/DMR/UPD/016_SUB/NU TP/oneM2M/CSE/DMR/UPD/016_SUB/NCT TP/oneM2M/CSE/DMR/DEL/001_SUB |
|  |  | CE/DIS/00001/00006 | Support the labels attribute of <subscription> resource. | TP/oneM2M/CSE/DMR/CRE/012_SUB/LBL TP/oneM2M/CSE/DMR/UPD/014_SUB/LBL TP/oneM2M/CSE/DMR/UPD/015_SUB/LBL |
|  |  | CE/SUB/00001/00001 | Support the creator attribute of <subscription> resource | TP/oneM2M/CSE/DMR/CRE/012_SUB/CR |
|  |  | CE/SUB/00001/00001 | Support the subscriberURI attribute of <subscription> resource | TP/oneM2M/CSE/DMR/CRE/012_SUB/SU |
|  | CE/SUB/00004 | CE/SUB/00004/00001 | Notify the address indicated in notificationURI with notification elements multiplicity equals 1[2] | TP/oneM2M/CSE/SUB/CRE/001_SUB TP/oneM2M/CSE/SUB/CRE/001_CIN TP/oneM2M/CSE/SUB/CRE/003 TP/oneM2M/CSE/SUB/CRE/005 |
|  |  | CE/SUB/00004/00002 | Notify with notificationEvent/representation set in the notification | TP/oneM2M/CSE/SUB/CRE/005 TP/oneM2M/CSE/SUB/UPD/001 TP/oneM2M/CSE/SUB/DEL/001 |
|  |  | CE/SUB/00004/00003 | Notify with creator set in the notification | TP/oneM2M/CSE/SUB/CRE/004 |
| SEC | CE/SEC/00001 | CE/SEC/00001/00001 | Support <accessControlPolicy> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/DMR/CRE/001_ACP/CB TP/oneM2M/CSE/DMR/CRE/001_ACP/AE TP/oneM2M/CSE/DMR/CRE/001_ACP/AEA TP/oneM2M/CSE/DMR/CRE/002_ACP TP/oneM2M/CSE/DMR/CRE/003_ACP TP/oneM2M/CSE/DMR/RET/001_ACP TP/oneM2M/CSE/DMR/RET/013_ACP TP/oneM2M/CSE/DMR/UPD/001_ACP/LBL TP/oneM2M/CSE/DMR/UPD/002_ACP/LBL TP/oneM2M/CSE/DMR/UPD/003_ACP/LBL TP/oneM2M/CSE/DMR/UPD/004_ACP/PV/AT/LBL TP/oneM2M/CSE/DMR/UPD/005_ACP/EXC TP/oneM2M/CSE/DMR/UPD/007_ACP/CT TP/oneM2M/CSE/DMR/UPD/008_ACP/ET TP/oneM2M/CSE/DMR/UPD/009_ACP/LBL TP/oneM2M/CSE/DMR/UPD/016_ACP/ET TP/oneM2M/CSE/DMR/UPD/016_ACP/PV TP/oneM2M/CSE/DMR/UPD/016_ACP/PVS TP/oneM2M/CSE/DMR/DEL/001_ACP TP/oneM2M/CSE/SEC/ACP/CRE/001 TP/oneM2M/CSE/SEC/ACP/CRE/002 TP/oneM2M/CSE/SEC/ACP/CRE/003 TP/oneM2M/CSE/SEC/ACP/CRE/004 |
|  |  | CE/DIS/00001/00006 | Support the labels attribute of <accessControlPolicy> resource | TP/oneM2M/CSE/DMR/CRE/012_ACP/LBL TP/oneM2M/CSE/DMR/UPD/014_ACP/LBL TP/oneM2M/CSE/DMR/UPD/015_ACP/LBL |
|  | CE/SEC/00002 | CE/SEC/00002/00001 | Support accessControlPolicyIDs attribute for <resource> that the Implementation supports. | TP/oneM2M/CSE/DMR/CRE/012_SUB/ACPI TP/oneM2M/CSE/DMR/CRE/012_CNT/ACPI TP/oneM2M/CSE/DMR/UPD/014_CNT/ACPI TP/oneM2M/CSE/DMR/UPD/015_AE/ACPI TP/oneM2M/CSE/DMR/UPD/015_CNT/ACPI TP/oneM2M/CSE/DMR/UPD/015_SUB/ACPI TP/oneM2M/CSE/DMR/UPD/015_GRP/ACPI TP/oneM2M/CSE/SEC/ACP/UPD/001 TP/oneM2M/CSE/SEC/ACP/UPD/002 |
|  |  | CE/SEC/00002/00002 | Support access control decision and enforcement making on the Hosting CSE | TP/oneM2M/CSE/DMR/CRE/004_CNT TP/oneM2M/CSE/DMR/CRE/004_ACP TP/oneM2M/CSE/DMR/CRE/004_SUB TP/oneM2M/CSE/DMR/CRE/004_GRP TP/oneM2M/CSE/DMR/RET/003_ACP TP/oneM2M/CSE/DMR/RET/003_CNT TP/oneM2M/CSE/DMR/RET/003_SUB TP/oneM2M/CSE/DMR/RET/014_ACP TP/oneM2M/CSE/DMR/RET/014_AE TP/oneM2M/CSE/DMR/RET/014_CNT TP/oneM2M/CSE/DMR/RET/014_CSR TP/oneM2M/CSE/DMR/RET/014_SUB TP/oneM2M/CSE/DMR/RET/014_GRP TP/oneM2M/CSE/DMR/UPD/006_CNT/LBL TP/oneM2M/CSE/DMR/UPD/006_ACP/LBL TP/oneM2M/CSE/DMR/UPD/006_SUB/LBL TP/oneM2M/CSE/DMR/DEL/002_CNT TP/oneM2M/CSE/DMR/DEL/002_ACP TP/oneM2M/CSE/DMR/DEL/002_SUB TP/oneM2M/CSE/DMR/DEL/002_GRP TP/oneM2M/CSE/SUB/CRE/002 TP/oneM2M/CSE/SEC/ACP/001_CRE TP/oneM2M/CSE/SEC/ACP/001_UPD TP/oneM2M/CSE/SEC/ACP/001_RET TP/oneM2M/CSE/SEC/ACP/001_DEL TP/oneM2M/CSE/SEC/ACP/002_CRE TP/oneM2M/CSE/SEC/ACP/002_UPD TP/oneM2M/CSE/SEC/ACP/002_RET TP/oneM2M/CSE/SEC/ACP/002_DEL TP/oneM2M/CSE/SEC/ACP/003_CRE TP/oneM2M/CSE/SEC/ACP/003_UPD TP/oneM2M/CSE/SEC/ACP/003_RET TP/oneM2M/CSE/SEC/ACP/003_DEL TP/oneM2M/CSE/SEC/ACP/004_CRE TP/oneM2M/CSE/SEC/ACP/004_UPD TP/oneM2M/CSE/SEC/ACP/004_RET TP/oneM2M/CSE/SEC/ACP/004_DEL TP/oneM2M/CSE/SEC/ACP/005_CRE TP/oneM2M/CSE/SEC/ACP/005_UPD TP/oneM2M/CSE/SEC/ACP/005_RET TP/oneM2M/CSE/SEC/ACP/005_DEL TP/oneM2M/CSE/SEC/ACP/006_CRE TP/oneM2M/CSE/SEC/ACP/006_UPD TP/oneM2M/CSE/SEC/ACP/006_RET TP/oneM2M/CSE/SEC/ACP/006_DEL TP/oneM2M/CSE/SEC/ACP/007_CRE TP/oneM2M/CSE/SEC/ACP/007_UPD TP/oneM2M/CSE/SEC/ACP/007_RET TP/oneM2M/CSE/SEC/ACP/007_DEL TP/oneM2M/CSE/SEC/ACP/008_CRE TP/oneM2M/CSE/SEC/ACP/008_UPD TP/oneM2M/CSE/SEC/ACP/008_RET TP/oneM2M/CSE/SEC/ACP/008_DEL TP/oneM2M/CSE/SEC/ACP/009_CRE TP/oneM2M/CSE/SEC/ACP/009_UPD TP/oneM2M/CSE/SEC/ACP/009_RET TP/oneM2M/CSE/SEC/ACP/009_DEL TP/oneM2M/CSE/SEC/ACP/010_CRE TP/oneM2M/CSE/SEC/ACP/010_UPD TP/oneM2M/CSE/SEC/ACP/010_RET TP/oneM2M/CSE/SEC/ACP/010_DEL TP/oneM2M/CSE/SEC/ACP/011_CRE TP/oneM2M/CSE/SEC/ACP/011_UPD TP/oneM2M/CSE/SEC/ACP/011_RET TP/oneM2M/CSE/SEC/ACP/011_DEL TP/oneM2M/CSE/SEC/ACP/012_CRE TP/oneM2M/CSE/SEC/ACP/012_UPD TP/oneM2M/CSE/SEC/ACP/012_RET TP/oneM2M/CSE/SEC/ACP/012_DEL |

### 5.6.4	Extendable feature sets

Table 5.6.4-1: Extendable feature set for IN Profile

| Function | Feature Set | Feature | Remark |  |
| --- | --- | --- | --- | --- |
| DIS | CE/DIS/00001 | CE/DIS/00001/00001 | Support the Discovery request with filterUsage equals to "Discovery" | TP/oneM2M/CSE/DIS/001 TP/oneM2M/CSE/DIS/002 TP/oneM2M/CSE/DIS/003 TP/oneM2M/CSE/DIS/004 TP/oneM2M/CSE/DIS/005 TP/oneM2M/CSE/DIS/006 |
|  |  | CE/DIS/00001/00002 | Support discovery with filterCriteria (createdBefore, createdAfter, modifiedSince, unmodifiedSince, stateTagSmaller, stateTagBigger, expireBefore, expireAfter, labels, resourceType, sizeAbove, sizeBelow, contentType, limit, attribute) | TP/oneM2M/CSE/DIS/007 TP/oneM2M/CSE/DIS/008 TP/oneM2M/CSE/DIS/009 |
|  |  | CE/DIS/00001/00003 | Support discovery with filterCriteria (level, offset) |  |
|  |  | CE/DIS/00001/00004 | Support discovery with content filter (contentFilterSyntax, contentFilterQuery of filterCriteria) |  |
|  |  | CE/DIS/00001/00005 | Support discovery with filterCriteria (filterOperation) |  |
| GMG | CE/GMG/00001 | CE/GMG/00001/00001 | Support the <group> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/DMR/CRE/001_GRP/CB TP/oneM2M/CSE/DMR/CRE/001_GRP/AE TP/oneM2M/CSE/DMR/CRE/002_GRP TP/oneM2M/CSE/DMR/CRE/003_GRP TP/oneM2M/CSE/DMR/RET/001_GRP TP/oneM2M/CSE/DMR/RET/013_GRP TP/oneM2M/CSE/DMR/UPD/001_GRP/LBL TP/oneM2M/CSE/DMR/UPD/002_GRP/LBL TP/oneM2M/CSE/DMR/UPD/003_GRP/LBL TP/oneM2M/CSE/DMR/UPD/004_GRP/ET/GN/LBL TP/oneM2M/CSE/DMR/UPD/005_GRP/EXC TP/oneM2M/CSE/DMR/UPD/006_GRP/LBL TP/oneM2M/CSE/DMR/UPD/007_GRP/CT TP/oneM2M/CSE/DMR/UPD/008_GRP/ET TP/oneM2M/CSE/DMR/UPD/009_GRP/LBL TP/oneM2M/CSE/DMR/UPD/016_GRP/ET TP/oneM2M/CSE/DMR/UPD/016_GRP/MNM TP/oneM2M/CSE/DMR/UPD/016_GRP/MID TP/oneM2M/CSE/DMR/DEL/001_GRP TP/oneM2M/CSE/DMR/DEL/002_GRP TP/oneM2M/CSE/GMG/CRE/001 TP/oneM2M/CSE/GMG/CRE/003 TP/oneM2M/CSE/GMG/UPD/002 TP/oneM2M/CSE/GMG/UPD/007 TP/oneM2M/CSE/GMG/UPD/008 |
|  |  | CE/DIS/00001/00006 | Support the labels attribute of <group> resource | TP/oneM2M/CSE/DMR/UPD/015_GRP/LBL |
|  |  | CE/GMG/00001/00001 | Support the creator attribute of <group> resource |  |
|  |  | CE/GMG/00001/00001 | Support the groupName attribute of <group> resource | TP/oneM2M/CSE/DMR/UPD/015_GRP/GN |
|  | CE/GMG/00002 | CE/GMG/00002/00001 | Support the memberTypeValidated attribute of <group> resource |  |
|  |  | CE/GMG/00002/00002 | Support the validation of member's resource type and set the memberTypeValidated as well as the procedure to update the group according to consistencyStrategy | TP/oneM2M/CSE/GMG/CRE/002 TP/oneM2M/CSE/GMG/CRE/004 TP/oneM2M/CSE/GMG/CRE/005 TP/oneM2M/CSE/GMG/CRE/006 TP/oneM2M/CSE/GMG/CRE/007 TP/oneM2M/CSE/GMG/UPD/001 TP/oneM2M/CSE/GMG/UPD/003 TP/oneM2M/CSE/GMG/UPD/004 TP/oneM2M/CSE/GMG/UPD/005 TP/oneM2M/CSE/GMG/UPD/006 TP/oneM2M/CSE/GMG/UPD/009 TP/oneM2M/CSE/GMG/UPD/010 |
|  |  | CE/GMG/00002/00003 | Support the consistencyStrategy attribute of <group> resource |  |
|  | CE/GMG/00003 | CE/GMG/00003/00001 | Fan out of request to all members and aggregate member responses | TP/oneM2M/CSE/GMG/RET/001 TP/oneM2M/CSE/GMG/001_CRE TP/oneM2M/CSE/GMG/001_RET TP/oneM2M/CSE/GMG/001_UPD TP/oneM2M/CSE/GMG/001_DEL TP/oneM2M/CSE/GMG/002_CRE TP/oneM2M/CSE/GMG/002_RET TP/oneM2M/CSE/GMG/002_UPD TP/oneM2M/CSE/GMG/002_DEL TP/oneM2M/CSE/GMG/003_CRE TP/oneM2M/CSE/GMG/003_RET TP/oneM2M/CSE/GMG/003_UPD TP/oneM2M/CSE/GMG/003_DEL TP/oneM2M/CSE/GMG/004_CRE TP/oneM2M/CSE/GMG/004_RET TP/oneM2M/CSE/GMG/004_UPD TP/oneM2M/CSE/GMG/004_DEL TP/oneM2M/CSE/GMG/005_CRE TP/oneM2M/CSE/GMG/005_RET TP/oneM2M/CSE/GMG/005_UPD TP/oneM2M/CSE/GMG/005_DEL TP/oneM2M/CSE/GMG/006_CRE TP/oneM2M/CSE/GMG/006_RET TP/oneM2M/CSE/GMG/006_UPD TP/oneM2M/CSE/GMG/006_DEL |
|  |  | CE/GMG/00003/00002 | Create sub group resource in case multiple members belong to same member CSE |  |
|  |  | CE/GMG/00003/00003 | Create <subscription> resource via group without aggregating notifications |  |
|  |  | CE/GMG/00003/00004 | Create <subscription> resource via group and aggregate notifications |  |
|  |  | CE/GMG/00003/00005 | Support the membersAccessControlPolicyIDs attribute of <group> resource | TP/oneM2M/CSE/DMR/UPD/015_GRP/MACP |
| DMG | CE/DMG/00001 | CE/DMG/00001/00001 | Support <node> resource with attributes multiplicity equals 1[1] |  |
|  |  | CE/DMG/00001/00002 | Support the labels attribute of <node> resource |  |
|  |  | CE/DMG/00001/00003 | Support the hostedCSELink attribute of <node> resource |  |
|  | CE/DMG/00002 | CE/DMG/00002/00001 | Support <mgmtObj> resource with attributes multiplicity equals 1[1] |  |
|  |  | CE/DMG/00002/00002 | Support the labels attribute of <mgmtObj> resource |  |
|  |  | CE/DMG/00002/00003 | Support the description attribute of <mgmtObj> resource |  |
|  |  | CE/DMG/00002/00004 | Support the mgmtLink attribute of <mgmtObj> resource |  |
|  | CE/DMG/00003 | CE/DMG/00003/00001 | Support the [software] specialization attributes multiplicity equals 1[1] |  |
|  |  | CE/DMG/00003/00002 | Support the activate attribute of [software] resource |  |
|  |  | CE/DMG/00003/00003 | Support the deactivate attribute of [software] resource |  |
|  |  | CE/DMG/00003/00004 | Support the activeStatus attribute of [software] resource |  |
|  | CE/DMG/00004 | CE/DMG/00004/00001 | Support the [firmware] specialization attributes multiplicity equals 1[1] |  |
|  | CE/DMG/00005 | CE/DMG/00005/00001 | Support the [deviceInfo] specialization attributes multiplicity equals 1[1] |  |
|  | CE/DMG/00006 | CE/DMG/00006/00001 | Support [deviceCapability] specialization attributes multiplicity equals 1[1] |  |
|  |  | CE/DMG/00006/00002 | Support the enable attribute of [deviceCapability] resource |  |
|  |  | CE/DMG/00006/00003 | Support the disable attribute of [deviceCapability] resource |  |
|  | CE/DMG/00007 | CE/DMG/00007/00001 | Support [reboot] specialization attributes multiplicity equals 1[1] |  |
|  | CE/DMG/00008 | CE/DMG/00008/00001 | Support [memory] specialization attributes multiplicity equals 1[1] |  |
|  | CE/DMG/00009 | CE/DMG/00009/00001 | Support the [battery] specialization attributes multiplicity equals 1[1] |  |
|  | CE/DMG/00010 | CE/DMG/00010/00001 | Support [eventLog] specialization attributes multiplicity equals 1[1] |  |
|  | CE/DMG/00011 | CE/DMG/00011/00001 | Support [areaNwkInfo] specialization attributes multiplicity equals 1[1] |  |
|  | CE/DMG/00012 | CE/DMG/00012/00001 | Support [areaNwkDeviceInfo] specialization attributes multiplicity equals 1[1] |  |
|  |  | CE/DMG/00012/00002 | Support the sleepInterval attribute of [areaNwkDeviceInfo] resource |  |
|  |  | CE/DMG/00012/00003 | Support the sleepDuration attribute of [areaNwkDeviceInfo] resource |  |
|  |  | CE/DMG/00012/00004 | Support the status attribute of [areaNwkDeviceInfo] resource |  |
|  | CE/DMG/00013 | CE/DMG/00013/00001 | Support the objectIDs attribute of <mgmtObj> resource |  |
|  |  | CE/DMG/00013/00002 | Support the objectPaths attribute of <mgmtObj> resource |  |
|  |  | CE/DMG/00013/00003 | Support the mgmtLink attribute of <mgmtObj> resource |  |

## 5.7	Constrained actuator as ASN

### 5.7.1	Profile description

The profile defines constraint actuator that is powered by battery and intended to be used for years after deployment without any human interference for maintenance. Therefore, the function of constraint actuator need to be very limited.

An actuator is intended to be receiving control command from CSE via notification or other means. The actuator then actuates according to the control command.

The actuator need to receive control command. As a result, the actuator need to be request reachable to receive notification or be able to start a polling channel.

The features described in this profile are features of CSE as the ASN exposes Mcc reference point outside. There are internal AEs of the ASN to synchronize the actual device state with the resource hosted by the ASN-CSE. However, in this profile, the ASN-AE is not sending information to the other CSE's, it's not necessary to include the oneM2M defined AE Features in this profile.

### 5.7.2	Profile usage examples

Swithes deployed along the street light to switch on or off the street light remotely.

### 5.7.3	Fundamental feature sets

The fundamental feature set assumes that the resource id of the <container> resource needed for create <contentInstance> is pre-configured at the ASN-CSE and provisioned to the AEs that tends to send request to the ASN-CSE.

Table 5.7.3-1: Fundamental feature sets for constrained sensor as ASN

| Function | Feature Set | Feature | Remark |  |
| --- | --- | --- | --- | --- |
| GEN | CE/GEN/00001 | CE/GEN/00001/00001 | Unstructured resource id |  |
|  |  | CE/GEN/00001/00002 | Structured resource id |  |
|  | CE/GEN/00002 | CE/GEN/00002/00001 | Support blocking request |  |
| REG | CE/REG/00005 | CE/REG/00005/00001 | The Creation with <remoteCSE> resource for CSE registration with mandatory attributes[2] | TP/oneM2M/CSE/REG/CRE/024 |
|  |  | CE/REG/00005/00006 | Create the <remoteCSE> with pointOfAccess | TP/oneM2M/CSE/REG/CRE/026_POA |
| DMR | CE/DMR/00002 | CE/DMR/00002/00001 | Support <contentInstance> resource with attributes multiplicity equals 1[1] |  |

### 5.7.4	Extendable feature sets

Void.

## 5.8	Gateway as MN

### 5.8.1	Profile description

The profile defines gateways that may support multiple different area network technologies and connect devices from the corresponding area networks. The devices may be oneM2M defined ADNs,  ASNs or NoDNs which are not defined by oneM2M. The gateway hosts resources to enforce common services that devices in the area network may utilize the enable local services without the dependency of the platform and the wide area network.

### 5.8.2	Profile usage examples

Home gateways deployed in the home for smart home:

Sensors, actuators and home appliances are connected with the home gateway. Applications can be connected through the platfrom to access the smart home service as well as applications can be directly connected with the gateway to do the same thing.

Head unit in connected vehicles:

Sensors and actuators in the car are connected with the head unit. The sensed data and control command are reported to delivered through the head unit. Applications may access the head unit and monitor the car state via the platform. Applications may also access the head unit once connected directly with the head unit via area network such as Wifi or Bluetooth.

### 5.8.3	Fundamental feature sets

Table 5.8.3-1: Fundamental feature sets for gateway as MN

| Function | Feature Set | Feature | Remark |  |
| --- | --- | --- | --- | --- |
| GEN | CE/GEN/00001 | CE/GEN/00001/00001 | Unstructured resource id | TP/oneM2M/CSE/GEN/CRE/001_CSR TP/oneM2M/CSE/GEN/CRE/001_SPR TP/oneM2M/CSE/GEN/CRE/001_ABS TP/oneM2M/CSE/GEN/UPD/001_CSR TP/oneM2M/CSE/GEN/UPD/001_SPR TP/oneM2M/CSE/GEN/UPD/001_ABS TP/oneM2M/CSE/GEN/RET/001_CSR TP/oneM2M/CSE/GEN/RET/001_SPR TP/oneM2M/CSE/GEN/RET/001_ABS TP/oneM2M/CSE/GEN/DEL/001_CSR TP/oneM2M/CSE/GEN/DEL/001_SPR TP/oneM2M/CSE/GEN/DEL/001_ABS |
|  |  | CE/GEN/00001/00002 | Structured resource id | TP/oneM2M/CSE/GEN/CRE/002_CSR TP/oneM2M/CSE/GEN/CRE/002_SPR TP/oneM2M/CSE/GEN/CRE/002_ABS TP/oneM2M/CSE/GEN/UPD/002_CSR TP/oneM2M/CSE/GEN/UPD/002_SPR TP/oneM2M/CSE/GEN/UPD/002_ABS TP/oneM2M/CSE/GEN/RET/002_CSR TP/oneM2M/CSE/GEN/RET/002_SPR TP/oneM2M/CSE/GEN/RET/002_ABS TP/oneM2M/CSE/GEN/DEL/002_CSR TP/oneM2M/CSE/GEN/DEL/002_SPR TP/oneM2M/CSE/GEN/DEL/002_ABS |
|  | CE/GEN/00002 | CE/GEN/00002/00001 | Support blocking request |  |
| REG | CE/REG/00001 | CE/REG/00001/00001 | Support <CSEBase> resource with attributes multiplicity equals 1[1]. | TP/oneM2M/CSE/REG/CRE/021 TP/oneM2M/CSE/REG/RET/001 TP/oneM2M/CSE/REG/RET/008 TP/oneM2M/CSE/REG/UPD/001 TP/oneM2M/CSE/REG/DEL/001 |
|  |  | CE/REG/00001/00002 | Support the cseType attribute of <CSEBase> resource | TP/oneM2M/CSE/REG/RET/002_CST TP/oneM2M/CSE/REG/RET/005 |
|  |  | CE/REG/00001/00003 | Support the nodeLink attribute of <CSEBase> resource. This is dependent on the feature set for <node> resource. | TP/oneM2M/CSE/REG/RET/002_NL |
|  | CE/REG/00002 | CE/REG/00002/00001 | Support <AE> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/REG/RET/003 TP/oneM2M/CSE/REG/DEL/003 TP/oneM2M/CSE/DMR/RET/013_AE TP/oneM2M/CSE/DMR/UPD/016_AE/ET TP/oneM2M/CSE/DMR/UPD/016_AE/RR |
|  |  | CE/REG/00002/00002 | AE registration/de-registration without a pre-assigned AE-ID in the registration request and where the AE-ID Stem is configured with 'C'. | TP/oneM2M/CSE/REG/CRE/004 TP/oneM2M/CSE/REG/CRE/005 TP/oneM2M/CSE/REG/CRE/006 TP/oneM2M/CSE/REG/CRE/007 TP/oneM2M/CSE/REG/CRE/008 TP/oneM2M/CSE/REG/CRE/010 TP/oneM2M/CSE/REG/CRE/011 TP/oneM2M/CSE/REG/CRE/016 TP/oneM2M/CSE/REG/CRE/017_API TP/oneM2M/CSE/REG/CRE/017_RR TP/oneM2M/CSE/REG/CRE/022 TP/oneM2M/CSE/REG/CRE/023 |
|  |  | CE/REG/00002/00003 | AE registration/de-registration without a pre-assigned AE-ID in the registration request and where the AE-ID Stem is configured with 'S'. |  |
|  |  | CE/REG/00002/00004 | AE registration/de-registration without a pre-assigned AE-ID in the registration request and where no AE-ID Stem is included. |  |
|  |  | CE/REG/00002/00005 | AE registration/de-registration without a pre-assigned AE-ID in the registration request and where the AE-ID Stem is configured with 'S' and where announcement to an IN-CSE is needed to get an AE-ID assigned |  |
|  |  | CE/DIS/00001/00006 | Support the labels attribute of <AE> resource | TP/oneM2M/CSE/REG/CRE/012_AE/LBL TP/oneM2M/CSE/REG/RET/004_LBL TP/oneM2M/CSE/DMR/UPD/015_AE/LBL |
|  |  | CE/REG/00002/00007 | Support the applicationName attribute of <AE> resource | TP/oneM2M/CSE/REG/CRE/012_AE/APN TP/oneM2M/CSE/REG/RET/004_APN TP/oneM2M/CSE/DMR/UPD/015_AE/APN |
|  |  | CE/REG/00002/00008 | Support the pointOfAccess attribute of <AE> resource | TP/oneM2M/CSE/REG/CRE/012_AE/POA TP/oneM2M/CSE/REG/RET/004_POA TP/oneM2M/CSE/DMR/UPD/015_AE/POA |
|  |  | CE/REG/00002/00009 | AE registration with pre-assigned AE-ID | TP/oneM2M/CSE/REG/CRE/002 TP/oneM2M/CSE/REG/CRE/003 TP/oneM2M/CSE/REG/CRE/020 |
|  | CE/REG/00004 | CE/REG/00004/00001 | Support <remoteCSE> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/REG/CRE/018 TP/oneM2M/CSE/REG/CRE/019 TP/oneM2M/CSE/REG/CRE/025 TP/oneM2M/CSE/REG/RET/006 TP/oneM2M/CSE/REG/RET/010 TP/oneM2M/CSE/REG/DEL/002 TP/oneM2M/CSE/DMR/UPD/016_CSR/ET TP/oneM2M/CSE/DMR/UPD/016_CSR/RR |
|  |  | CE/DIS/00001/00006 | Support the labels attribute of <remoteCSE> resource | TP/oneM2M/CSE/REG/CRE/013_LBL TP/oneM2M/CSE/REG/CRE/028_LBL TP/oneM2M/CSE/REG/RET/007_LBL TP/oneM2M/CSE/REG/UPD/002_LBL |
|  |  | CE/REG/00004/00002 | Support the cseType attribute of <remoteCSE> resource | TP/oneM2M/CSE/REG/CRE/013_CST TP/oneM2M/CSE/REG/CRE/027 TP/oneM2M/CSE/REG/RET/007_CST |
|  |  | CE/REG/00004/00003 | Support the pointOfAccess attribute of <remoteCSE> resource | TP/oneM2M/CSE/REG/CRE/013_POA TP/oneM2M/CSE/REG/CRE/028_POA TP/oneM2M/CSE/REG/RET/007_POA TP/oneM2M/CSE/REG/UPD/002_POA |
|  |  | CE/REG/00004/00004 | Support the nodeLink attribute of <remoteCSE> resource | TP/oneM2M/CSE/REG/CRE/013_NL TP/oneM2M/CSE/REG/CRE/028_NL TP/oneM2M/CSE/REG/RET/007_NL TP/oneM2M/CSE/REG/UPD/002_NL |
|  | CE/REG/00005 | CE/REG/00005/00001 | The Creation with <remoteCSE> resource for CSE registration with mandatory attributes[2] for Create and locally create <remoteCSE> that represents the Regstree CSE | TP/oneM2M/CSE/REG/CRE/024 TP/oneM2M/CSE/DMR/RET/013_CSR |
|  |  | CE/REG/00005/00001 | Create the <remoteCSE> with resourceName attribute | TP/oneM2M/CSE/REG/CRE/026_RN |
|  |  | CE/REG/00005/00001 | Create the <remoteCSE> with expirationTime attribute | TP/oneM2M/CSE/REG/CRE/026_ET |
|  |  | CE/REG/00005/00004 | Create the <remoteCSE> with labels attribute | TP/oneM2M/CSE/REG/CRE/026_LBL |
|  |  | CE/REG/00005/00002 | Create the <remoteCSE> with cseType attribute | TP/oneM2M/CSE/REG/CRE/026_CST |
|  |  | CE/REG/00005/00003 | Create the <remoteCSE> with pointOfAccess attribute | TP/oneM2M/CSE/REG/CRE/026_POA |
|  |  | CE/REG/00005/00005 | Create the <remoteCSE> with nodeLink attribute | TP/oneM2M/CSE/REG/CRE/026_NL |
|  |  | CE/DIS/00001/00006 | Update the <remoteCSE> with labels | TP/oneM2M/CSE/REG/UPD/003_LBL TP/oneM2M/CSE/DMR/UPD/015_CSR/LBL |
|  |  | CE/REG/00005/00001 | Update the <remoteCSE> with expirationTime | TP/oneM2M/CSE/REG/UPD/003_ET |
|  |  | CE/REG/00005/00006 | Update the <remoteCSE> with pointOfAccess attribute | TP/oneM2M/CSE/REG/UPD/003_POA TP/oneM2M/CSE/DMR/UPD/015_CSR/POA |
|  |  | CE/REG/00005/00007 | Update the <remoteCSE> with requestReachability | TP/oneM2M/CSE/REG/UPD/003_RR |
|  |  | CE/REG/00005/00008 | Update the <remoteCSE> with nodeLink attribute | TP/oneM2M/CSE/REG/UPD/003_NL TP/oneM2M/CSE/DMR/UPD/015_CSR/NL |
|  |  | CE/REG/00005/00001 | Delete the <remoteCSE> resource on the Registrar, also delete the <remoteCSE> resource on the Registree | TP/oneM2M/CSE/REG/DEL/004 |
|  |  | CE/REG/00005/00009 | Retrieve the <remoteCSE> resource | TP/oneM2M/CSE/REG/RET/009 |
| DMR | CE/DMR/00001 | CE/DMR/00001/00001 | Support <container> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/DMR/CRE/001_CNT/CB TP/oneM2M/CSE/DMR/CRE/001_CNT/AE TP/oneM2M/CSE/DMR/CRE/001_CNT/CNT TP/oneM2M/CSE/DMR/CRE/002_CNT TP/oneM2M/CSE/DMR/CRE/003_CNT TP/oneM2M/CSE/DMR/CRE/007 TP/oneM2M/CSE/DMR/CRE/008 TP/oneM2M/CSE/DMR/CRE/009 TP/oneM2M/CSE/DMR/CRE/010 TP/oneM2M/CSE/DMR/CRE/011 TP/oneM2M/CSE/DMR/CRE/014_CNT_CIN TP/oneM2M/CSE/DMR/RET/001_CNT TP/oneM2M/CSE/DMR/RET/013_CNT TP/oneM2M/CSE/DMR/UPD/001_CNT/LBL TP/oneM2M/CSE/DMR/UPD/002_CNT/LBL TP/oneM2M/CSE/DMR/UPD/003_CNT/LBL TP/oneM2M/CSE/DMR/UPD/004_CNT/ET/MNI/LBL TP/oneM2M/CSE/DMR/UPD/005_CNT/EXC TP/oneM2M/CSE/DMR/UPD/007_CNT/CT TP/oneM2M/CSE/DMR/UPD/008_CNT/ET TP/oneM2M/CSE/DMR/UPD/009_CNT/LBL TP/oneM2M/CSE/DMR/UPD/010 TP/oneM2M/CSE/DMR/UPD/016_CNT/ET TP/oneM2M/CSE/DMR/DEL/001_CNT TP/oneM2M/CSE/DMR/DEL/005 TP/oneM2M/CSE/DMR/DEL/006 |
|  |  | CE/DIS/00001/00006 | Support the labels attribute of <container> resource | TP/oneM2M/CSE/DMR/CRE/012_CNT/LBL TP/oneM2M/CSE/DMR/UPD/014_CNT/LBL TP/oneM2M/CSE/DMR/UPD/015_CNT/LBL |
|  |  | CE/DMR/00001/00001 | Support the creator attribute of <container> resource | TP/oneM2M/CSE/DMR/CRE/012_CNT/CR |
|  |  | CE/DMR/00001/00002 | Support the maxNrOfInstances attribute of <container> resource | TP/oneM2M/CSE/DMR/CRE/005_MNI TP/oneM2M/CSE/DMR/CRE/006_MNI TP/oneM2M/CSE/DMR/CRE/012_CNT/MNI TP/oneM2M/CSE/DMR/UPD/014_CNT/MNI TP/oneM2M/CSE/DMR/UPD/015_CNT/MNI |
|  |  | CE/DMR/00001/00003 | Support the maxByteSize attribute of <container> resource | TP/oneM2M/CSE/DMR/CRE/005_MBS TP/oneM2M/CSE/DMR/CRE/006_MBS TP/oneM2M/CSE/DMR/CRE/012_CNT/MBS TP/oneM2M/CSE/DMR/CRE/013 TP/oneM2M/CSE/DMR/UPD/014_CNT/MBS TP/oneM2M/CSE/DMR/UPD/015_CNT/MBS |
|  |  | CE/DMR/00001/00004 | Support the maxInstanceAge attribute of <container> resource | TP/oneM2M/CSE/DMR/CRE/005_MIA TP/oneM2M/CSE/DMR/CRE/006_MIA TP/oneM2M/CSE/DMR/CRE/012_CNT/MIA TP/oneM2M/CSE/DMR/UPD/014_CNT/MIA TP/oneM2M/CSE/DMR/UPD/015_CNT/MIA |
|  | CE/DMR/00002 | CE/DMR/00002/00001 | Support <contentInstance> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/DMR/CRE/001_CIN/CNT TP/oneM2M/CSE/DMR/RET/001_CIN TP/oneM2M/CSE/DMR/UPD/BV/011 TP/oneM2M/CSE/DMR/DEL/001_CIN |
|  |  | CE/DIS/00001/00006 | Support the labels attribute of <contentInstance> resource | TP/oneM2M/CSE/DMR/CRE/012_CIN/LBL |
|  |  | CE/DMR/00002/00001 | Support the creator attribute of <contentInstance> resource | TP/oneM2M/CSE/DMR/CRE/012_CIN/CR |
|  |  | CE/DMR/00002/00002 | Support the contentInfo attribute of <contentInstance> resource | TP/oneM2M/CSE/DMR/CRE/012_CIN/CNF |
|  |  | CE/DMR/00002/00004 | Retrieve and Delete of latest <contentInstance> resource by <latest> virtual resource | TP/oneM2M/CSE/DMR/RET/012 TP/oneM2M/CSE/DMR/UPD/012 TP/oneM2M/CSE/DMR/DEL/007 |
|  |  | CE/DMR/00002/00057 | Retrieve and Delete of oldest <contentInstance> resource by <oldest> virtual resource | TP/oneM2M/CSE/DMR/RET/010 TP/oneM2M/CSE/DMR/UPD/013 TP/oneM2M/CSE/DMR/DEL/009 |
| SUB | CE/SUB/00001 | CE/SUB/00001/00001 | The Support of <subscription> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/DMR/CRE/001_SUB/CB TP/oneM2M/CSE/DMR/CRE/001_SUB/AE TP/oneM2M/CSE/DMR/CRE/001_SUB/CNT TP/oneM2M/CSE/DMR/CRE/001_SUB/ACP TP/oneM2M/CSE/DMR/CRE/001_SUB/CSR TP/oneM2M/CSE/DMR/CRE/001_SUB/AEA TP/oneM2M/CSE/DMR/CRE/002_SUB TP/oneM2M/CSE/DMR/CRE/003_SUB TP/oneM2M/CSE/DMR/RET/001_SUB TP/oneM2M/CSE/DMR/RET/013_SUB TP/oneM2M/CSE/DMR/UPD/001_SUB/LBL TP/oneM2M/CSE/DMR/UPD/002_SUB/LBL TP/oneM2M/CSE/DMR/UPD/003_SUB/LBL TP/oneM2M/CSE/DMR/UPD/004_SUB/ET/LBL/EXC TP/oneM2M/CSE/DMR/UPD/005_SUB/MNI TP/oneM2M/CSE/DMR/UPD/007_SUB/CT TP/oneM2M/CSE/DMR/UPD/008_SUB/ET TP/oneM2M/CSE/DMR/UPD/009_SUB/LBL TP/oneM2M/CSE/DMR/UPD/016_SUB/ET TP/oneM2M/CSE/DMR/UPD/016_SUB/NU TP/oneM2M/CSE/DMR/UPD/016_SUB/NCT TP/oneM2M/CSE/DMR/DEL/001_SUB |
|  |  | CE/DIS/00001/00006 | Support the labels attribute of <subscription> resource. | TP/oneM2M/CSE/DMR/CRE/012_SUB/LBL TP/oneM2M/CSE/DMR/UPD/014_SUB/LBL TP/oneM2M/CSE/DMR/UPD/015_SUB/LBL |
|  |  | CE/SUB/00001/00001 | Support the creator attribute of <subscription> resource | TP/oneM2M/CSE/DMR/CRE/012_SUB/CR |
|  |  | CE/SUB/00001/00001 | Support the subscriberURI attribute of <subscription> resource | TP/oneM2M/CSE/DMR/CRE/012_SUB/SU |
|  | CE/SUB/00004 | CE/SUB/00004/00001 | Notify the address indicated in notificationURI with notification elements multiplicity equals 1[2] | TP/oneM2M/CSE/SUB/CRE/001_SUB TP/oneM2M/CSE/SUB/CRE/001_CIN TP/oneM2M/CSE/SUB/CRE/003 TP/oneM2M/CSE/SUB/CRE/005 |
|  |  | CE/SUB/00004/00002 | Notify with notificationEvent/representation set in the notification | TP/oneM2M/CSE/SUB/CRE/005 TP/oneM2M/CSE/SUB/UPD/001 TP/oneM2M/CSE/SUB/DEL/001 |
|  |  | CE/SUB/00004/00003 | Notify with creator set in the notification | TP/oneM2M/CSE/SUB/CRE/004 |
| SEC | CE/SEC/00001 | CE/SEC/00001/00001 | Support <accessControlPolicy> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/DMR/CRE/001_ACP/CB TP/oneM2M/CSE/DMR/CRE/001_ACP/AE TP/oneM2M/CSE/DMR/CRE/002_ACP TP/oneM2M/CSE/DMR/CRE/003_ACP TP/oneM2M/CSE/DMR/RET/001_ACP TP/oneM2M/CSE/DMR/RET/013_ACP TP/oneM2M/CSE/DMR/UPD/001_ACP/LBL TP/oneM2M/CSE/DMR/UPD/002_ACP/LBL TP/oneM2M/CSE/DMR/UPD/003_ACP/LBL TP/oneM2M/CSE/DMR/UPD/004_ACP/PV/AT/LBL TP/oneM2M/CSE/DMR/UPD/005_ACP/EXC TP/oneM2M/CSE/DMR/UPD/007_ACP/CT TP/oneM2M/CSE/DMR/UPD/008_ACP/ET TP/oneM2M/CSE/DMR/UPD/009_ACP/LBL TP/oneM2M/CSE/DMR/UPD/016_ACP/ET TP/oneM2M/CSE/DMR/UPD/016_ACP/PV TP/oneM2M/CSE/DMR/UPD/016_ACP/PVS TP/oneM2M/CSE/DMR/DEL/001_ACP TP/oneM2M/CSE/SEC/ACP/CRE/001 TP/oneM2M/CSE/SEC/ACP/CRE/002 TP/oneM2M/CSE/SEC/ACP/CRE/003 TP/oneM2M/CSE/SEC/ACP/CRE/004 |
|  |  | CE/DIS/00001/00006 | Support the labels attribute of <accessControlPolicy> resource | TP/oneM2M/CSE/DMR/CRE/012_ACP/LBL TP/oneM2M/CSE/DMR/UPD/014_ACP/LBL TP/oneM2M/CSE/DMR/UPD/015_ACP/LBL |
|  | CE/SEC/00002 | CE/SEC/00002/00001 | Support accessControlPolicyIDs attribute for <resource> that the Implementation supports. | TP/oneM2M/CSE/DMR/CRE/012_SUB/ACPI TP/oneM2M/CSE/DMR/CRE/012_CNT/ACPI TP/oneM2M/CSE/DMR/UPD/014_CNT/ACPI TP/oneM2M/CSE/DMR/UPD/015_AE/ACPI TP/oneM2M/CSE/DMR/UPD/015_CNT/ACPI TP/oneM2M/CSE/DMR/UPD/015_SUB/ACPI TP/oneM2M/CSE/SEC/ACP/UPD/001 TP/oneM2M/CSE/SEC/ACP/UPD/002 |
|  |  | CE/SEC/00002/00002 | Support access control decision and enforcement making on the Hosting CSE | TP/oneM2M/CSE/DMR/CRE/004_CNT TP/oneM2M/CSE/DMR/CRE/004_ACP TP/oneM2M/CSE/DMR/CRE/004_SUB TP/oneM2M/CSE/DMR/RET/003 TP/oneM2M/CSE/DMR/RET/014_ACP TP/oneM2M/CSE/DMR/RET/014_AE TP/oneM2M/CSE/DMR/RET/014_CNT TP/oneM2M/CSE/DMR/RET/014_CSR TP/oneM2M/CSE/DMR/RET/014_SUB TP/oneM2M/CSE/DMR/UPD/006_CNT/LBL TP/oneM2M/CSE/DMR/UPD/006_ACP/LBL TP/oneM2M/CSE/DMR/UPD/006_SUB/LBL TP/oneM2M/CSE/DMR/DEL/002_CNT TP/oneM2M/CSE/DMR/DEL/002_ACP TP/oneM2M/CSE/DMR/DEL/002_SUB TP/oneM2M/CSE/SUB/CRE/002 TP/oneM2M/CSE/SEC/ACP/001_CRE TP/oneM2M/CSE/SEC/ACP/001_UPD TP/oneM2M/CSE/SEC/ACP/001_RET TP/oneM2M/CSE/SEC/ACP/001_DEL TP/oneM2M/CSE/SEC/ACP/002_CRE TP/oneM2M/CSE/SEC/ACP/002_UPD TP/oneM2M/CSE/SEC/ACP/002_RET TP/oneM2M/CSE/SEC/ACP/002_DEL TP/oneM2M/CSE/SEC/ACP/003_CRE TP/oneM2M/CSE/SEC/ACP/003_UPD TP/oneM2M/CSE/SEC/ACP/003_RET TP/oneM2M/CSE/SEC/ACP/003_DEL TP/oneM2M/CSE/SEC/ACP/004_CRE TP/oneM2M/CSE/SEC/ACP/004_UPD TP/oneM2M/CSE/SEC/ACP/004_RET TP/oneM2M/CSE/SEC/ACP/004_DEL TP/oneM2M/CSE/SEC/ACP/005_CRE TP/oneM2M/CSE/SEC/ACP/005_UPD TP/oneM2M/CSE/SEC/ACP/005_RET TP/oneM2M/CSE/SEC/ACP/005_DEL TP/oneM2M/CSE/SEC/ACP/006_CRE TP/oneM2M/CSE/SEC/ACP/006_UPD TP/oneM2M/CSE/SEC/ACP/006_RET TP/oneM2M/CSE/SEC/ACP/006_DEL TP/oneM2M/CSE/SEC/ACP/007_CRE TP/oneM2M/CSE/SEC/ACP/007_UPD TP/oneM2M/CSE/SEC/ACP/007_RET TP/oneM2M/CSE/SEC/ACP/007_DEL TP/oneM2M/CSE/SEC/ACP/008_CRE TP/oneM2M/CSE/SEC/ACP/008_UPD TP/oneM2M/CSE/SEC/ACP/008_RET TP/oneM2M/CSE/SEC/ACP/008_DEL TP/oneM2M/CSE/SEC/ACP/009_CRE TP/oneM2M/CSE/SEC/ACP/009_UPD TP/oneM2M/CSE/SEC/ACP/009_RET TP/oneM2M/CSE/SEC/ACP/009_DEL TP/oneM2M/CSE/SEC/ACP/010_CRE TP/oneM2M/CSE/SEC/ACP/010_UPD TP/oneM2M/CSE/SEC/ACP/010_RET TP/oneM2M/CSE/SEC/ACP/010_DEL TP/oneM2M/CSE/SEC/ACP/011_CRE TP/oneM2M/CSE/SEC/ACP/011_UPD TP/oneM2M/CSE/SEC/ACP/011_RET TP/oneM2M/CSE/SEC/ACP/011_DEL TP/oneM2M/CSE/SEC/ACP/012_CRE TP/oneM2M/CSE/SEC/ACP/012_UPD TP/oneM2M/CSE/SEC/ACP/012_RET TP/oneM2M/CSE/SEC/ACP/012_DEL |

### 5.8.4	Extendable feature sets

Table 5.8.4-1: Extendable feature set for gateway as MN

| Function | Feature Set | Feature | Remark |  |
| --- | --- | --- | --- | --- |
| DIS | CE/DIS/00001 | CE/DIS/00001/00001 | Support the Discovery request with filterUsage equals to "Discovery" | TP/oneM2M/CSE/DIS/001 TP/oneM2M/CSE/DIS/002 TP/oneM2M/CSE/DIS/003 TP/oneM2M/CSE/DIS/004 TP/oneM2M/CSE/DIS/005 TP/oneM2M/CSE/DIS/006 |
|  |  | CE/DIS/00001/00002 | Support discovery with filterCriteria (createdBefore, createdAfter, modifiedSince, unmodifiedSince, stateTagSmaller, stateTagBigger, expireBefore, expireAfter, labels, resourceType, sizeAbove, sizeBelow, contentType, limit, attribute) | TP/oneM2M/CSE/DIS/007 TP/oneM2M/CSE/DIS/008 TP/oneM2M/CSE/DIS/009 |
|  |  | CE/DIS/00001/00003 | Support discovery with filterCriteria (level, offset) |  |
|  |  | CE/DIS/00001/00004 | Support discovery with content filter (contentFilterSyntax, contentFilterQuery of filterCriteria) |  |
|  |  | CE/DIS/00001/00005 | Support discovery with filterCriteria (filterOperation) |  |
| GMG | CE/GMG/00001 | CE/GMG/00001/00001 | Support the <group> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/DMR/CRE/001_GRP/CB TP/oneM2M/CSE/DMR/CRE/001_GRP/AE TP/oneM2M/CSE/DMR/CRE/002_GRP TP/oneM2M/CSE/DMR/CRE/003_GRP TP/oneM2M/CSE/DMR/RET/001_GRP TP/oneM2M/CSE/DMR/RET/013_GRP TP/oneM2M/CSE/DMR/UPD/001_GRP/LBL TP/oneM2M/CSE/DMR/UPD/002_GRP/LBL TP/oneM2M/CSE/DMR/UPD/003_GRP/LBL TP/oneM2M/CSE/DMR/UPD/004_GRP/ET/GN/LBL TP/oneM2M/CSE/DMR/UPD/005_GRP/EXC TP/oneM2M/CSE/DMR/UPD/006_GRP/LBL TP/oneM2M/CSE/DMR/UPD/007_GRP/CT TP/oneM2M/CSE/DMR/UPD/008_GRP/ET TP/oneM2M/CSE/DMR/UPD/009_GRP/LBL TP/oneM2M/CSE/DMR/UPD/016_GRP/ET TP/oneM2M/CSE/DMR/UPD/016_GRP/MNM TP/oneM2M/CSE/DMR/UPD/016_GRP/MID TP/oneM2M/CSE/DMR/DEL/001_GRP TP/oneM2M/CSE/DMR/DEL/002_GRP TP/oneM2M/CSE/GMG/CRE/001 TP/oneM2M/CSE/GMG/CRE/003 TP/oneM2M/CSE/GMG/UPD/002 TP/oneM2M/CSE/GMG/UPD/007 TP/oneM2M/CSE/GMG/UPD/008 |
|  |  | CE/DIS/00001/00006 | Support the labels attribute of <group> resource | TP/oneM2M/CSE/DMR/UPD/015_GRP/LBL |
|  |  | CE/GMG/00001/00001 | Support the creator attribute of <group> resource |  |
|  |  | CE/GMG/00001/00001 | Support the groupName attribute of <group> resource | TP/oneM2M/CSE/DMR/UPD/015_GRP/GN |
|  | CE/GMG/00002 | CE/GMG/00002/00001 | Support the memberTypeValidated attribute of <group> resource |  |
|  |  | CE/GMG/00002/00002 | Support the validation of member's resource type and set the memberTypeValidated as well as the procedure to update the group according to consistencyStrategy | TP/oneM2M/CSE/GMG/CRE/002 TP/oneM2M/CSE/GMG/CRE/004 TP/oneM2M/CSE/GMG/CRE/005 TP/oneM2M/CSE/GMG/CRE/006 TP/oneM2M/CSE/GMG/CRE/007 TP/oneM2M/CSE/GMG/UPD/001 TP/oneM2M/CSE/GMG/UPD/003 TP/oneM2M/CSE/GMG/UPD/004 TP/oneM2M/CSE/GMG/UPD/005 TP/oneM2M/CSE/GMG/UPD/006 TP/oneM2M/CSE/GMG/UPD/009 TP/oneM2M/CSE/GMG/UPD/010 |
|  |  | CE/GMG/00002/00003 | Support the consistencyStrategy attribute of <group> resource |  |
|  | CE/GMG/00003 | CE/GMG/00003/00001 | Fan out of request to all members and aggregate member responses | TP/oneM2M/CSE/GMG/RET/001 TP/oneM2M/CSE/GMG/001_CRE TP/oneM2M/CSE/GMG/001_RET TP/oneM2M/CSE/GMG/001_UPD TP/oneM2M/CSE/GMG/001_DEL TP/oneM2M/CSE/GMG/002_CRE TP/oneM2M/CSE/GMG/002_RET TP/oneM2M/CSE/GMG/002_UPD TP/oneM2M/CSE/GMG/002_DEL TP/oneM2M/CSE/GMG/003_CRE TP/oneM2M/CSE/GMG/003_RET TP/oneM2M/CSE/GMG/003_UPD TP/oneM2M/CSE/GMG/003_DEL TP/oneM2M/CSE/GMG/004_CRE TP/oneM2M/CSE/GMG/004_RET TP/oneM2M/CSE/GMG/004_UPD TP/oneM2M/CSE/GMG/004_DEL TP/oneM2M/CSE/GMG/005_CRE TP/oneM2M/CSE/GMG/005_RET TP/oneM2M/CSE/GMG/005_UPD TP/oneM2M/CSE/GMG/005_DEL TP/oneM2M/CSE/GMG/006_CRE TP/oneM2M/CSE/GMG/006_RET TP/oneM2M/CSE/GMG/006_UPD TP/oneM2M/CSE/GMG/006_DEL |
|  |  | CE/GMG/00003/00002 | Create sub group resource in case multiple members belong to same member CSE |  |
|  |  | CE/GMG/00003/00003 | Create <subscription> resource via group without aggregating notifications |  |
|  |  | CE/GMG/00003/00004 | Create <subscription> resource via group and aggregate notifications |  |
|  |  | CE/GMG/00003/00005 | Support the membersAccessControlPolicyIDs attribute of <group> resource | TP/oneM2M/CSE/DMR/UPD/015_GRP/MACP |

Annex A (normative):
Mapping of feature to test purposes

# Table A-1: Mapping of feature to Test Purposes

| Feature ID | Feature Catalogue | Description | Mapped Test Purposes |
| --- | --- | --- | --- |
| CE/GEN/00001/00001 |  | Support Unstructured resource identifier |  |
| CE/GEN/00001/00002 |  | Support Structured resource identifier |  |
| CE/GEN/00002/00001 |  | Support blocking request |  |
| CE/REG/00001/00001 |  | Support <CSEBase> resource. |  |
| CE/REG/00001/00002 |  | Support the cseType attribute of <CSEBase> |  |
| CE/REG/00001/00003 |  | Support the nodeLink attribute of <CSEBase> |  |
| CE/REG/00002/00001 |  | Support <AE> resource |  |
| CE/REG/00002/00002 |  | AE registration without pre-assigned AE-ID in the registration request. Possible cases are: The request includes AE-ID Stem as 'C' The request includes AE-ID Stem as 'S' The request does not include AE-ID Stem | TP/oneM2M/CSE/REG/BV/001 TP/oneM2M/CSE/REG/BV/002 TP/oneM2M/CSE/REG/BV/003 TP/oneM2M/CSE/REG/BV/004 TP/oneM2M/CSE/REG/BV/005 TP/oneM2M/CSE/REG/BV/007 TP/oneM2M/CSE/REG/BV/008 TP/oneM2M/CSE/REG/BV/009 TP/oneM2M/CSE/REG/BV/010 |
| CE/REG/00002/00003 |  | Support the labels attribute of <AE> resource |  |
| CE/REG/00002/00004 |  | Support the applicationName attribute of <AE> resource |  |
| CE/REG/00002/00005 |  | Support the pointOfAccess attribute of <AE> resource |  |
| CE/REG/00002/00006 |  | AE registration with pre-assigned AE-ID |  |
| CE/REG/00004/00001 |  | Support <remoteCSE> resource with attributes multiplicity equals 1[1] |  |
| CE/REG/00004/00002 |  | Support the labels attribute of <remoteCSE> resource |  |
| CE/REG/00004/00003 |  | Support the cseType attribute of <remoteCSE> resource |  |
| CE/REG/00004/00004 |  | Support the pointOfAccess attribute of <remoteCSE> resource |  |
| CE/REG/00004/00005 |  | Support the nodeLink attribute of <remoteCSE> resource |  |
| CE/DMR/00001/00001 |  | Support <container> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/DMR/CRE/BV/001_01 TP/oneM2M/CSE/DMR/CRE/BV/002_01 TP/oneM2M/CSE/DMR/CRE/BV/003_01 TP/oneM2M/CSE/DMR/CRE/BV/004_01 TP/oneM2M/CSE/DMR/CRE/BV/005_0X TP/oneM2M/CSE/DMR/CRE/BV/006_0X TP/oneM2M/CSE/DMR/CRE/BV/009 TP/oneM2M/CSE/DMR/CRE/BV/012_01 TP/oneM2M/CSE/DMR/CRE/BV/013_01 TP/oneM2M/CSE/DMR/CRE/BV/014_01 TP/oneM2M/CSE/DMR/CRE/BV/015_01-07 TP/oneM2M/CSE/DMR/CRE/BV/016_02 TP/oneM2M/CSE/DMR/CRE/BV/017_02 TP/oneM2M/CSE/DMR/RET/BV/001_01 TP/oneM2M/CSE/DMR/RET/BO/002 TP/oneM2M/CSE/DMR/RET/BO/003_01 TP/oneM2M/CSE/DMR/RET/BV/004_01 TP/oneM2M/CSE/DMR/RET/BV/005_01 TP/oneM2M/CSE/DMR/RET/BV/006_01 TP/oneM2M/CSE/DMR/RET/BO/007_01 TP/oneM2M/CSE/DMR/RET/BO/008_01 TP/oneM2M/CSE/DMR/RET/BV/013_03 TP/oneM2M/CSE/DMR/RET/BO/014_03 TP/oneM2M/CSE/DMR/RET/BV/015_03 TP/oneM2M/CSE/DMR/RET/BV/016_03 TP/oneM2M/CSE/DMR/RET/BV/017_03 TP/oneM2M/CSE/DMR/RET/BV/018_03 TP/oneM2M/CSE/DMR/RET/BO/019_03 TP/oneM2M/CSE/DMR/UPD/BI/005_01 TP/oneM2M/CSE/DMR/UPD/BO/006_01 TP/oneM2M/CSE/DMR/UPD/BO/007_01 TP/oneM2M/CSE/DMR/UPD/BO/008_01 TP/oneM2M/CSE/DMR/UPD/BO/009_01 TP/oneM2M/CSE/DMR/UPD/BV/010 TP/oneM2M/CSE/DMR/UPD/BV/014_01-07 TP/oneM2M/CSE/DMR/UPD/BV/015_02 TP/oneM2M/CSE/DMR/UPD/BV/016_01 TP/oneM2M/CSE/DMR/DEL/BV/001_01 TP/oneM2M/CSE/DMR/DEL/BV/002_01 TP/oneM2M/CSE/DMR/DEL/BV/003 TP/oneM2M/CSE/DMR/DEL/BV/004_01 TP/oneM2M/CSE/DMR/DEL/BV/005 TP/oneM2M/CSE/DMR/DEL/BV/006 TP/oneM2M/CSE/DMR/BV/001_01 TP/oneM2M/CSE/DMR/BV/001_02 TP/oneM2M/CSE/DMR/BV/001_03 TP/oneM2M/CSE/DMR/BV/002_01 TP/oneM2M/CSE/DMR/BV/003_01 TP/oneM2M/CSE/DMR/BV/004_01 TP/oneM2M/CSE/DMR/BV/005_01 |
| CE/DMR/00001/00002 |  | Support the labels attribute of <container> resource | TP/oneM2M/CSE/DMR/CRE/BV/015_03 TP/oneM2M/CSE/DMR/UPD/BV/014_03 TP/oneM2M/CSE/DMR/UPD/BV/001_01 TP/oneM2M/CSE/DMR/UPD/BV/002_01 TP/oneM2M/CSE/DMR/UPD/BV/003_01 TP/oneM2M/CSE/DMR/UPD/BV/004_01 TP/oneM2M/CSE/DMR/UPD/BO/009 |
| CE/DMR/00001/00003 |  | Support the creator attribute of <container> resource |  |
| CE/DMR/00001/00004 |  | Support the maxNrOfInstances attribute of <container> resource | TP/oneM2M/CSE/DMR/CRE/BV/015_04 TP/oneM2M/CSE/DMR/CRE/BV/014_04 |
| CE/DMR/00001/00005 |  | Support the maxByteSize attribute of <container> resource | TP/oneM2M/CSE/DMR/CRE/BV/015_05 TP/oneM2M/CSE/DMR/CRE/BV/014_05 |
| CE/DMR/00001/00006 |  | Support the maxInstanceAge attribute of <container> resource | TP/oneM2M/CSE/DMR/CRE/BV/015_06 TP/oneM2M/CSE/DMR/CRE/BV/014_06 |
| CE/DMR/00002/00001 |  | Support <contentInstance> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/DMR/UPD/BV/011 TP/oneM2M/CSE/DMR/CRE/BV/007 TP/oneM2M/CSE/DMR/CRE/BV/008 TP/oneM2M/CSE/DMR/CRE/BI/010 TP/oneM2M/CSE/DMR/CRE/BI/011 TP/oneM2M/CSE/DMR/CRE/BV/015_08-12 TP/oneM2M/CSE/DMR/CRE/BV/016_03 TP/oneM2M/CSE/DMR/CRE/BV/017_03 TP/oneM2M/CSE/DMR/UPD/BV/011 TP/oneM2M/CSE/DMR/UPD/BI/012 TP/oneM2M/CSE/DMR/UPD/BI/013 |
| CE/DMR/00002/00002 |  | Support the labels attribute of <contentInstance> resource | TP/oneM2M/CSE/DMR/CRE/BV/015_09 |
| CE/DMR/00002/00003 |  | Support the creator attribute of <contentInstance> resource | TP/oneM2M/CSE/DMR/CRE/BV/015_10 |
| CE/DMR/00002/00004 |  | Support the contentInfo attribute of <contentInstance> resource | TP/oneM2M/CSE/DMR/CRE/BV/015_11 |
| CE/DMR/00002/00005 |  | Support the contentRef attribute of <contentInstance> resource | TP/oneM2M/CSE/DMR/CRE/BV/015_12 |
| CE/DMR/00002/00006 |  | Retrieve and Delete of latest <contentInstance> resource by <latest> virtual resource | TP/oneM2M/CSE/DMR/RET/BV/012 TP/oneM2M/CSE/DMR/RET/BO/009 TP/oneM2M/CSE/DMR/UPD/BI/012 TP/oneM2M/CSE/DMR/DEL/BV/007 TP/oneM2M/CSE/DMR/DEL/BO/008 |
| CE/DMR/00002/00007 |  | Retrieve and Delete of oldest <contentInstance> resource by <oldest> virtual resource | TP/oneM2M/CSE/DMR/RET/BV/010 TP/oneM2M/CSE/DMR/RET/BO/011 TP/oneM2M/CSE/DMR/UPD/BI/013 TP/oneM2M/CSE/DMR/DEL/BV/009 TP/oneM2M/CSE/DMR/DEL/BO/010 |
| CE/SUB/00001/00001 |  | The Support of <subscription> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/DMR/CRE/BV/001_06 TP/oneM2M/CSE/DMR/CRE/BV/002_06 TP/oneM2M/CSE/DMR/CRE/BV/003_06 TP/oneM2M/CSE/DMR/CRE/BV/004_06 TP/oneM2M/CSE/DMR/CRE/BV/012_06 TP/oneM2M/CSE/DMR/CRE/BV/013_06 TP/oneM2M/CSE/DMR/CRE/BV/014_06 TP/oneM2M/CSE/DMR/CRE/BV/015_15-31 TP/oneM2M/CSE/DMR/RET/BV/001_06 TP/oneM2M/CSE/DMR/RET/BO/002 TP/oneM2M/CSE/DMR/RET/BO/003_06 TP/oneM2M/CSE/DMR/RET/BV/004_06 TP/oneM2M/CSE/DMR/RET/BV/005_06 TP/oneM2M/CSE/DMR/RET/BV/006_06 TP/oneM2M/CSE/DMR/RET/BO/007_06 TP/oneM2M/CSE/DMR/RET/BO/008_06 TP/oneM2M/CSE/DMR/RET/BV/013_14 TP/oneM2M/CSE/DMR/RET/BO/014_14 TP/oneM2M/CSE/DMR/RET/BV/015_14 TP/oneM2M/CSE/DMR/RET/BV/016_14 TP/oneM2M/CSE/DMR/RET/BV/017_14 TP/oneM2M/CSE/DMR/RET/BV/018_14 TP/oneM2M/CSE/DMR/RET/BO/019_14 TP/oneM2M/CSE/DMR/UPD/BI/005_06 TP/oneM2M/CSE/DMR/UPD/BO/006_06 TP/oneM2M/CSE/DMR/UPD/BO/007_06 TP/oneM2M/CSE/DMR/UPD/BO/008_06 TP/oneM2M/CSE/DMR/UPD/BO/009_06 TP/oneM2M/CSE/DMR/UPD/BV/014_12-25 TP/oneM2M/CSE/DMR/DEL/BV/001_06 TP/oneM2M/CSE/DMR/DEL/BV/002_06 TP/oneM2M/CSE/DMR/DEL/BV/003 TP/oneM2M/CSE/DMR/DEL/BV/004_06 TP/oneM2M/CSE/DMR/DEL/BV/005 TP/oneM2M/CSE/DMR/DEL/BV/006 TP/oneM2M/CSE/DMR/BV/001_01 TP/oneM2M/CSE/DMR/BV/001_02 TP/oneM2M/CSE/DMR/BV/001_03 TP/oneM2M/CSE/DMR/BV/002_06 TP/oneM2M/CSE/DMR/BV/003_06 TP/oneM2M/CSE/DMR/BV/004_06 TP/oneM2M/CSE/DMR/BV/005_06 TP/oneM2M/CSE/SUB/BV/001 TP/oneM2M/CSE/SUB/BV/002 TP/oneM2M/CSE/SUB/BV/003 TP/oneM2M/CSE/SUB/BV/004 TP/oneM2M/CSE/SUB/BV/005 |
| CE/SUB/00001/00002 |  | Support the labels attribute of <subscription> resource. | TP/oneM2M/CSE/DMR/CRE/BV/015_17 TP/oneM2M/CSE/DMR/UPD/BV/001_06 TP/oneM2M/CSE/DMR/UPD/BV/002_06 TP/oneM2M/CSE/DMR/UPD/BV/003_06 TP/oneM2M/CSE/DMR/UPD/BV/004_06 TP/oneM2M/CSE/DMR/UPD/BV/014_14 |
| CE/SUB/00001/00003 |  | Support the creator attribute of <subscription> resource | TP/oneM2M/CSE/DMR/CRE/BV/015_30 |
| CE/SUB/00001/00004 |  | Support the subscriberURI attribute of <subscription> resource | TP/oneM2M/CSE/DMR/CRE/BV/015_31 |
| CE/SUB/00004/00001 |  | Notify the address indicated in notificationURI with notification elements multiplicity equals 1[2] | TP/oneM2M/CSE/SUB/BV/006 TP/oneM2M/CSE/SUB/BV/007 TP/oneM2M/CSE/SUB/BV/008 TP/oneM2M/CSE/SUB/BV/009 TP/oneM2M/CSE/SUB/BV/011 TP/oneM2M/CSE/SUB/BV/012 TP/oneM2M/CSE/SUB/BV/013 TP/oneM2M/CSE/SUB/BV/014 TP/oneM2M/CSE/SUB/BV/015 TP/oneM2M/CSE/SUB/BV/016 TP/oneM2M/CSE/SUB/BV/017 TP/oneM2M/CSE/SUB/BV/018 TP/oneM2M/CSE/SUB/BV/019 TP/oneM2M/CSE/SUB/BV/020 TP/oneM2M/CSE/SUB/BV/021 |
| CE/SUB/00004/00002 |  | Notify with notificationEvent/representation set in the notification |  |
| CE/SUB/00004/00003 |  | Notify with creator set in the notification | TP/oneM2M/CSE/SUB/BV/010 |
| CE/SEC/00001/00001 |  | Support <accessControlPolicy> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/DMR/CRE/BV/001_03 TP/oneM2M/CSE/DMR/CRE/BV/002_03 TP/oneM2M/CSE/DMR/CRE/BV/003_03 TP/oneM2M/CSE/DMR/CRE/BV/004_03 TP/oneM2M/CSE/DMR/CRE/BV/015_13-14 TP/oneM2M/CSE/DMR/CRE/BV/016_01 TP/oneM2M/CSE/DMR/CRE/BV/017_01 TP/oneM2M/CSE/DMR/RET/BV/001_03 TP/oneM2M/CSE/DMR/RET/BO/002 TP/oneM2M/CSE/DMR/RET/BO/003_03 TP/oneM2M/CSE/DMR/RET/BV/004_03 TP/oneM2M/CSE/DMR/RET/BV/005_03 TP/oneM2M/CSE/DMR/RET/BV/006_03 TP/oneM2M/CSE/DMR/RET/BO/007_03 TP/oneM2M/CSE/DMR/RET/BO/008_03 TP/oneM2M/CSE/DMR/RET/BV/013_01 TP/oneM2M/CSE/DMR/RET/BO/014_01 TP/oneM2M/CSE/DMR/RET/BV/015_01 TP/oneM2M/CSE/DMR/RET/BV/016_01 TP/oneM2M/CSE/DMR/RET/BV/017_01 TP/oneM2M/CSE/DMR/RET/BV/018_01 TP/oneM2M/CSE/DMR/RET/BO/019_01 TP/oneM2M/CSE/DMR/UPD/BI/005_03 TP/oneM2M/CSE/DMR/UPD/BO/006_03 TP/oneM2M/CSE/DMR/UPD/BO/007_03 TP/oneM2M/CSE/DMR/UPD/BO/008_03 TP/oneM2M/CSE/DMR/UPD/BO/009_03 TP/oneM2M/CSE/DMR/UPD/BV/014_08-11 TP/oneM2M/CSE/DMR/UPD/BV/015_01 TP/oneM2M/CSE/DMR/DEL/BV/001_03 TP/oneM2M/CSE/DMR/DEL/BV/002_03 TP/oneM2M/CSE/DMR/DEL/BV/003 TP/oneM2M/CSE/DMR/DEL/BV/004_03 TP/oneM2M/CSE/DMR/DEL/BV/005 TP/oneM2M/CSE/DMR/DEL/BV/006 TP/oneM2M/CSE/DMR/BV/001_01 TP/oneM2M/CSE/DMR/BV/001_02 TP/oneM2M/CSE/DMR/BV/001_03 TP/oneM2M/CSE/DMR/BV/002_03 TP/oneM2M/CSE/DMR/BV/003_03 TP/oneM2M/CSE/DMR/BV/004_03 TP/oneM2M/CSE/DMR/BV/005_03 TP/oneM2M/CSE/SEC/ACP/BV/001 TP/oneM2M/CSE/SEC/ACP/BV/002 TP/oneM2M/CSE/SEC/ACP/BV/003 TP/oneM2M/CSE/SEC/ACP/BV/004 TP/oneM2M/CSE/SEC/ACP/BV/005 TP/oneM2M/CSE/SEC/ACP/BO/006 TP/oneM2M/CSE/SEC/ACP/BV/007 TP/oneM2M/CSE/SEC/ACP/BO/008 TP/oneM2M/CSE/SEC/ACP/BV/009 TP/oneM2M/CSE/SEC/ACP/BO/010 TP/oneM2M/CSE/SEC/ACP/BV/011 TP/oneM2M/CSE/SEC/ACP/BO/012 TP/oneM2M/CSE/SEC/ACP/BO/013 TP/oneM2M/CSE/SEC/ACP/BV/014 TP/oneM2M/CSE/SEC/ACP/BV/015 TP/oneM2M/CSE/SEC/ACP/BV/016 |
| CE/SEC/00001/00002 |  | Support the labels attribute of <accessControlPolicy> resource | TP/oneM2M/CSE/DMR/CRE/BV/015_14 TP/oneM2M/CSE/DMR/UPD/BV/014_09 |
| CE/SEC/00002/00001 |  | Support accessControlPolicyIDs attribute for <resource> that the Implementation supports. | TP/oneM2M/CSE/DMR/CRE/BV/015_01 TP/oneM2M/CSE/DMR/CRE/BV/014_01 TP/oneM2M/CSE/DMR/CRE/BV/015_15 TP/oneM2M/CSE/DMR/CRE/BV/014_15 |
| CE/SEC/00002/00002 |  | Support access control decision and enforcement making on the Hosting CSE |  |
| CE/DIS/00001/00001 |  | Support the Discovery request with filterUsage equals to "Discovery" | TP/oneM2M/CSE/DIS/BV/001 |
| CE/DIS/00001/00002 |  | Support discovery with filterCriteria (createdBefore, createdAfter, modifiedSince, unmodifiedSince, stateTagSmaller, stateTagBigger, expireBefore, expireAfter, labels, resourceType, sizeAbove, sizeBelow, contentType, limit, attribute) | TP/oneM2M/CSE/DIS/BV/002 TP/oneM2M/CSE/DIS/BV/003 TP/oneM2M/CSE/DIS/BV/004 TP/oneM2M/CSE/DIS/BO/005 TP/oneM2M/CSE/DIS/BO/006 TP/oneM2M/CSE/DIS/BI/007 TP/oneM2M/CSE/DIS/BI/008_01-04 |
| CE/DIS/00001/00003 |  | Support discovery with filterCriteria (level, offset) |  |
| CE/DIS/00001/00004 |  | Support discovery with content filter (contentFilterSyntax, contentFilterQuery of filterCriteria) |  |
| CE/DIS/00001/00005 |  | Support discovery with filterCriteria (filterOperation) |  |
| CE/GMG/00001/00001 |  | Support the <group> resource with attributes multiplicity equals 1[1] | TP/oneM2M/CSE/DMR/CRE/BV/001_02 TP/oneM2M/CSE/DMR/CRE/BV/002_02 TP/oneM2M/CSE/DMR/CRE/BV/003_02 TP/oneM2M/CSE/DMR/CRE/BV/004_02 TP/oneM2M/CSE/DMR/CRE/BV/012_02 TP/oneM2M/CSE/DMR/CRE/BV/013_02 TP/oneM2M/CSE/DMR/CRE/BV/014_02 TP/oneM2M/CSE/DMR/CRE/BV/016_04 TP/oneM2M/CSE/DMR/CRE/BV/017_04 TP/oneM2M/CSE/DMR/RET/BV/001_02 TP/oneM2M/CSE/DMR/RET/BO/002 TP/oneM2M/CSE/DMR/RET/BO/003_02 TP/oneM2M/CSE/DMR/RET/BV/004_02 TP/oneM2M/CSE/DMR/RET/BV/005_02 TP/oneM2M/CSE/DMR/RET/BV/006_02 TP/oneM2M/CSE/DMR/RET/BO/007_02 TP/oneM2M/CSE/DMR/RET/BO/008_02 TP/oneM2M/CSE/DMR/RET/BV/013_05 TP/oneM2M/CSE/DMR/RET/BO/014_05 TP/oneM2M/CSE/DMR/RET/BV/015_05 TP/oneM2M/CSE/DMR/RET/BV/016_05 TP/oneM2M/CSE/DMR/RET/BV/017_05 TP/oneM2M/CSE/DMR/RET/BV/018_05 TP/oneM2M/CSE/DMR/RET/BO/019_05 TP/oneM2M/CSE/DMR/UPD/BI/005_02 TP/oneM2M/CSE/DMR/UPD/BO/006_02 TP/oneM2M/CSE/DMR/UPD/BO/007_02 TP/oneM2M/CSE/DMR/UPD/BO/008_02 TP/oneM2M/CSE/DMR/UPD/BO/009_02 TP/oneM2M/CSE/DMR/UPD/BV/015_03 TP/oneM2M/CSE/DMR/UPD/BV/016_02 TP/oneM2M/CSE/DMR/DEL/BV/001_02 TP/oneM2M/CSE/DMR/DEL/BV/002_02 TP/oneM2M/CSE/DMR/DEL/BV/003 TP/oneM2M/CSE/DMR/DEL/BV/004_02 TP/oneM2M/CSE/DMR/DEL/BV/005 TP/oneM2M/CSE/DMR/DEL/BV/006 TP/oneM2M/CSE/DMR/BV/001_01 TP/oneM2M/CSE/DMR/BV/001_02 TP/oneM2M/CSE/DMR/BV/001_03 TP/oneM2M/CSE/DMR/BV/002_02 TP/oneM2M/CSE/DMR/BV/003_02 TP/oneM2M/CSE/DMR/BV/004_02 TP/oneM2M/CSE/DMR/BV/005_02 TP/oneM2M/CSE/GMG/BV/001 TP/oneM2M/CSE/GMG/BV/002 TP/oneM2M/CSE/GMG/BV/003 TP/oneM2M/CSE/GMG/BV/004 TP/oneM2M/CSE/GMG/BV/016 TP/oneM2M/CSE/GMG/BV/017 |
| CE/GMG/00001/00002 |  | Support the labels attribute of <group> resource |  |
| CE/GMG/00001/00003 |  | Support the creator attribute of <group> resource |  |
| CE/GMG/00001/00004 |  | Support the groupName attribute of <group> resource |  |
| CE/GMG/00002/00001 |  | Support the memberTypeValidated attribute of <group> resource |  |
| CE/GMG/00002/00002 |  | Support the validation of member's resource type and set the memberTypeValidated as well as the procedure to update the group according to consistencyStrategy | TP/oneM2M/CSE/GMG/BV/005 TP/oneM2M/CSE/GMG/BV/006 TP/oneM2M/CSE/GMG/BV/007 TP/oneM2M/CSE/GMG/BV/013 TP/oneM2M/CSE/GMG/BV/014 TP/oneM2M/CSE/GMG/BV/015 TP/oneM2M/CSE/GMG/BV/018 TP/oneM2M/CSE/GMG/BV/019 |
| CE/GMG/00002/00003 |  | Support the consistencyStrategy attribute of <group> resource |  |
| CE/GMG/00003/00001 |  | Fan out of request to all members and aggregate member responses | TP/oneM2M/CSE/GMG/BV/008 TP/oneM2M/CSE/GMG/BV/009 TP/oneM2M/CSE/GMG/BV/020_01-04 TP/oneM2M/CSE/GMG/BO/021_01-04 TP/oneM2M/CSE/GMG/BV/022_01-04 TP/oneM2M/CSE/GMG/BV/023_01-04 TP/oneM2M/CSE/GMG/BV/024 |
| CE/GMG/00003/00002 |  | Create sub group resource in case multiple members belong to same member CSE |  |
| CE/GMG/00003/00003 |  | Create <subscription> resource via group without aggregating notifications |  |
| CE/GMG/00003/00004 |  | Create <subscription> resource via group and aggregate notifications |  |
| CE/GMG/00003/00005 |  | Support the membersAccessControlPolicyIDs attribute of <group> resource |  |
| CE/DMG/00001/00001 |  | Support <node> resource with attributes multiplicity equals 1[1] |  |
| CE/DMG/00001/00002 |  | Support the labels attribute of <node> resource |  |
| CE/DMG/00001/00003 |  | Support the hostedCSELink attribute of <node> resource |  |
| CE/DMG/00002/00001 |  | Support <mgmtObj> resource with attributes multiplicity equals 1[1] |  |
| CE/DMG/00002/00002 |  | Support the labels attribute of <mgmtObj> resource |  |
| CE/DMG/00002/00003 |  | Support the description attribute of <mgmtObj> resource |  |
| CE/DMG/00002/00004 |  | Support the mgmtLink attribute of <mgmtObj> resource |  |
| CE/DMG/00003/00001 |  | Support the [software] specialization attributes multiplicity equals 1[1] |  |
| CE/DMG/00003/00002 |  | Support the activate attribute of [software] resource |  |
| CE/DMG/00003/00003 |  | Support the deactivate attribute of [software] resource |  |
| CE/DMG/00003/00004 |  | Support the activeStatus attribute of [software] resource |  |
| CE/DMG/00004/00001 |  | Support the [firmware] specialization attributes multiplicity equals 1[1] |  |
| CE/DMG/00005/00001 |  | Support the [deviceInfo] specialization attributes multiplicity equals 1[1] |  |
| CE/DMG/00006/00001 |  | Support [deviceCapability] specialization attributes multiplicity equals 1[1] |  |
| CE/DMG/00006/00002 |  | Support the enable attribute of [deviceCapability] resource |  |
| CE/DMG/00006/00003 |  | Support the disable attribute of [deviceCapability] resource |  |
| CE/DMG/00007/00001 |  | Support [reboot] specialization attributes multiplicity equals 1[1] |  |
| CE/DMG/00008/00001 |  | Support [memory] specialization attributes multiplicity equals 1[1] |  |
| CE/DMG/00009/00001 |  | Support the [battery] specialization attributes multiplicity equals 1[1] |  |
| CE/DMG/00010/00001 |  | Support [eventLog] specialization attributes multiplicity equals 1[1] |  |
| CE/DMG/00011/00001 |  | Support [areaNwkInfo] specialization attributes multiplicity equals 1[1] |  |
| CE/DMG/00012/00001 |  | Support [areaNwkDeviceInfo] specialization attributes multiplicity equals 1[1] |  |
| CE/DMG/00012/00002 |  | Support the sleepInterval attribute of [areaNwkDeviceInfo] resource |  |
| CE/DMG/00012/00003 |  | Support the sleepDuration attribute of [areaNwkDeviceInfo] resource |  |
| CE/DMG/00012/00004 |  | Support the status attribute of [areaNwkDeviceInfo] resource |  |
| CE/DMG/00013/00001 |  | Support the objectIDs attribute of <mgmtObj> resource |  |
| CE/DMG/00013/00002 |  | Support the objectPaths attribute of <mgmtObj> resource |  |
| CE/DMG/00013/00003 |  | Support the mgmtLink attribute of <mgmtObj> resource |  |

# History

| Publication history |
| --- |
| V2.0.0 | 12-Mar-2018 | Release 2A - Publication |