| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | No hop remoteCSE management |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr (LAAS-CNRS) monteil@laas.fr (LAAS-CNRS) drira@laas.fr (LAAS-CNRS) |
| Date:* | 2015-07-21 |
| Abstract:* | The contribution proposes reorganization and update of No hop remoteCSE test case to be added to TS-0013 |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

The contribution proposes reorganization and update of No hop remoteCSE test case to be added to TS-0013. The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

=========Start of  1st Part: Proposed Test Descriptions ==================

## No Hop configuration testing

## remoteCSE Management

## remoteCSE Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_01 |
| Objective: | Registree CSE registers to Registrar CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.1 [2] 7.3.3.2.1 |
| Pre-test conditions: | Void |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | Registree CSE is requested to send a remoteCSE Create request to registrar CSE |
| 2 | Mcc | PRO Check Primitive | Sent Create request contains Operation (op) = 1 (Create) To (to) = <CSEbase> of registrar CSE From (from) = empty Request Identifier (rqi) = Request-ID Resource Type (ty) = 16 (remoteCSE) Content (pc) = Serialized Representation of applicable <remoteCSE> resource attributes |
|  |  | PRO Check HTTP | Sent POST request contains Request method = POST Request URI: <CSEBase> of registrar CSE Host : Host address of Registrar CSE X-M2M-RI: Request-ID X-M2M-Origin: empty Content Type = application/vnd.onem2m-res+xml; ty=16 or application/vnd.onem2m-res+json; ty=16 Content-Length: size of payload in the message body in bytes Message-body: Serialized Representation of applicable <remoteCSE> resource attributes |
|  |  | PRO Check CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> of registrar CSE Content Type = application/vnd.onem2m-res+xml; ty=16 or application/vnd.onem2m-res+json; ty=16 oneM2M-FR: empty oneM2M-RQI: Request-ID Payload: Serialized Representation of applicable <remoteCSE> resource attributes |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<Registree CSE-ID>/<Registrar CSE-ID>” Payload: op = 1 to = <CSEBase> of registrar CSE fr = empty rqi = Request ID ty = 16 |
| 3 |  | IOP Check | Check if possible that the <remoteCSE> resource is created in registrar CSE. |
| 4 | Mcc | PRO Check Primitive | Response Status Code (rsc) = 2001 (CREATED) Request Identifier (rqi) = Request-ID Content (pc) = Serialized Representation of <remoteCSE> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 201 (Created) X-M2M-RSC: 2001 X-M2M-RI: Request-ID Content-Location : <Registrar CSEBase>/ <remoteCSE> Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+jsonContent-Length: size of payload in the message body in bytes Message-body: Serialized Representation of the created <remoteCSE> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.01 oneM2M-RSC: 2001 Location-Path: <Registrar CSEBase> Location-Path: <remoteCSE> oneM2M-RQI: Request-ID Payload: Serialized Representation of the created <remoteCSE> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<Registree CSE-ID>/<Registrar CSE-ID>” Payload: to = Registree CSE-ID fr = Registrar CSE-ID rqi = Request ID rsc = Response Status Code(2001) pc = Content(created <remoteCSE> resource representation) |
| 5 |  | IOP Check | Registree CSE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### remoteCSE Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_02 |
| Objective: | Registree CSE retrieves <remoteCSE> resource from Registrar CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.2 [2] 7.3.3.2.2 |
| Pre-test conditions: | Registree CSE has created a<remoteCSE> resource in registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | Registree CSE is requested to send a remoteCSE Retrieve request to Registrar CSE |
| 2 | Mcc | PRO Check Primitive | Sent Retrieve request contains Operation (op) = 2 (Retrieve) To (to) = <RegistrarCSE>/<remoteCSE> From (from) = CSE-ID of request originator Request Identifier (rqi) = Request-ID |
|  |  | PRO Check HTTP | Sent GET request contains Request method = GET Request-Target: <Registrar CSEBase>/<remoteCSE> Host : Host Address of Registrar CSE X-M2M-RI: value of rqi primitive parameter X-M2M-Origin: AE-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <Registrar CSEBase> Uri-Path: <remoteCSE> oneM2M-FR: AE-ID oneM2M-RQI: value of rqi primitive parameter Payload: empty |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<Registree CSE-ID>/<Registrar CSE-ID>” Payload: op = 2 to = <Registrar CSEBase>/<remoteCSE> fr = <CSE-ID> rqi = <Request ID> |
| 3 | Mcc | PRO Check Primitive | Response Status Code (rsc) = 2000 (OK) Request Identifier (rqi) = Request-ID Content (pc) = Serialized Representation of <remoteCSE> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) X-M2M-RSC: 2000 X-M2M-RI: value of rqi primitive parameter Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length = size of payload in the message body in bytes Message-body: Serialized Representation of <remoteCSE> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: value of rqi primitive parameter Payload: Serialized Representation of <remoteCSE> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<Registree CSE-ID>/<Registrar CSE-ID>” Payload: to = CSE-ID fr = Registrar CSE-ID rqi = Request ID rsc = Response Status Code(2000) pc = Content(retrieved <remoteCSE> resource representation |
| 4 |  | IOP Check | Registree CSE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### remoteCSE Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_03 |
| Objective: | Registree-CSE updates remoteCSE attributes in registrar-CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.3 [2] 7.3.3.2.3 |
| Pre-test conditions: | <remoteCSE> resource has been created in registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | Registree CSE is requested to send a remoteCSE Update request to the Registrar CSE |
| 2 | Mcc | PRO Check Primitive | Sent Update request contains Operation (op) = 3 (Update) To (to) = <Registrar CSEBase>/<remoteCSE> From (from) = Registree CSE-ID Request Identifier (rqi) = Request-ID Content (pc) = Serialized Representation of modified <remoteCSE> resource |
|  |  | PRO Check HTTP | Sent PUT request contains Request method = PUT Request-Target: <Registrar CSEBase>/<remoteCSE> Host : Host Address of Registrar CSE X-M2M-RI: Request-ID X-M2M-Origin: Registree CSE-ID Content Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Length: size of payload in the message body in bytes Message-body: Serialized Representation of modified <remoteCSE> resource |
|  |  | PRO Check CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <Registrar CSEBase> Uri-Path: <remoteCSE> oneM2M-FR: Registree CSE-ID oneM2M-RQI: Request-ID Payload: Serialized Representation of modified <AE> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<Registree CSE-ID>/<Registrar CSE-ID>” Payload: op = 3 to = <Registrar CSEBase>/<remoteCSE> fr = Registree CSE-ID rqi = Request-ID |
| 3 |  | IOP Check | Check if possible that the <remoteCSE> resource has been updated in registrar CSE. |
| 4 | Mcc | PRO Check Primitive | Response Status Code (rsc) = 2004 Request Identifier (rqi): Request-ID Content (pc) = Serialized Representation of updated <AE> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 X-M2M-RSC: 2004 X-M2M-RI: Request-ID Content-Type; application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Content-Location <RegistrarCSE>/<remoteCSE> Content-Length = size of payload in the message body in bytesMessage-body: Serialized Representation of modified attributes of the <remoteCSE> resource |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.04 oneM2M-RSC: 2004 oneM2M-RQI: Request-ID Payload: Serialized Representation of modified attributes of the <remoteCSE> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: to = Registree CSE-ID fr = Registrar CSE-ID rqi = Request ID rsc = Response Status Code(2004) pc = Content(modified attributes of <remoteCSE> resource representation) |
| 5 |  | IOP Check | Registree CSE and Registrar CSE indicate successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### remoteCSE Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_04 |
| Objective: | Registree-CSE deletes remoteCSE resource from registrar-CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.4 [2] 7.3.3.2.4 |
| Pre-test conditions: | <remoteCSE> resource has been created in registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | Registree CSE is requested to send a <remoteCSE> delete request to Registrar CSE |
| 2 | Mcc | PRO Check Primitive | Sent Delete request contains: Operation (op) = (Delete) To (to) = <Registrar CSEbase>/<RemoeCSE> From (from) = Registree CSE-ID Request Identifier (rqi) = Request-ID |
|  |  | PRO Check HTTP | Sent DELETE request contains Request method = DELETE Request-Target: <Registrar CSEbase>/<remoteCSE> Host : Registrar CSE X-M2M-RI: Request-ID X-M2M-Origin: registree CSE-ID Message-body: empty |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <Registrar CSEBase> Uri-Path: <remoteCSE> oneM2M-FR: Registree CSE-ID oneM2M-RQI: Request-ID Payload: empty |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the request topic “/oneM2M/req/<SP-Relative-AE-ID>/<Registrar CSE-ID>” Payload: op = 4 to = <Registrar CSEBase>/<remoteCSE> fr = Registree CSE-ID rqi = Request ID |
| 3 | Mcc | PRO Check Primitive | Response Status Code (rsc) = 2004 Request Identifier (rqi): Request-ID Content (pc) = empty |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 X-M2M-RSC: 2002 X-M2M-RI: Request-IDMessage-body: empty |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.02 oneM2M-RSC: 2002 oneM2M-RQI: Request-ID Payload: empty |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH protocol packet to the response topic “/oneM2M/resp/<Registree CSE-ID>/<Registrar CSE-ID>” Payload: to = Registree CSE-ID fr = Registrar CSE-ID rqi = Request-ID rsc = <Response Status Code(2004)> pc = empty |
| 4 |  | IOP Check | Check if possible that the <remoteCSE> resource has been removed from registrar CSE. |
| 5 |  | IOP Check | Check if possible that the <remoteCSE> resource is also removed from registree CSE. |
| 6 |  | IOP Check | Registree CSE and Registrar CSE indicate successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

====== == End of  1st Part: Proposed Test Descriptions ==================