| Input Contribution |
| --- |
| Meeting ID* | TST22.2 |
| Title:* | TS-0018-Test Purposes contribution |
| Source:* | Bob Flynn, Convida Wireless, Flynn.Bob@convidawireless.com |
| Uploaded Date:* | 2016-04-19 |
| Document(s) Impacted* | TS-0018 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution discusses the need for Group related test purposes to be added to TS-0018 (Test Suite Structure and Test Purposes) |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution addresses the Create <group> operation.

FROM TS-0001  (our ANNOTATED VERSION)

#### 10.2.7.3	Retrieve <group>

This procedure shall be used for retrieving <group> resource.

Table 10.2.7.3-1: <group> RETRIEVE

| <group> RETRIEVE |
| --- |
| Associated Reference Point | Mcc, Mca and Mcc' |
| Information in Request message | From: Identifier of the AE or the CSE that initiates the Request To: The address of the <group> resource |
| Processing at Originator before sending Request | The Originator shall request to obtain <group> resource information by using the RETRIEVE operation. The request shall address the specific <group> resource of a Hosting CSE. The Originator may be an AE or a CSE |
| Processing at Receiver | No change from the basic procedure in clause 10.1.2 |
| Information in Response message | No change from the basic procedure in clause 10.1.2 |
| Processing at Originator after receiving Response | None |
| Exceptions | No change from the basic procedure in clause 10.1.2 |

FROM TS-0004 ANNOTATED VERSION

##### Retrieve

No primitive specific operations.

Based on this text in TS-0001 and TS-0004

I think that there are no new test cases and that the group retrieve requirements listed below should be recorded as tested in the corresponding DMR test cases shown.

We should also confirm that those DMR tests capture the scenario to check that the operation allows the Originator to be an AE or CSE.

TP/oneM2M/CSE/DMR/RET/BV/001_?(group)		REQ-0001-10031, REQ-0004-07214

# Comments

REQ-0001-10031

Should we test this as GMG function or DMR function (valid child resource)?

I propose DMR function. BUT the specific test should be run with these for certification perposes.  How do we capture this?

REQ-0001-10031_X

Originator can be AE or CSE.  Does this need explicit call out?

REQ-0004-07124