| CHANGE REQUEST |
| --- |
| Meeting:* | TST 24 |
| Source:* | KETI |
| Date:* | 2016-07-18 |
| Contact:* | Ting Martin Miao, KETI, novamartin@keti.re.kr Il-Yeup Ahn, KETI, iyahn@keti.kr SeungMyeong Jeong, KETI, sm.jeong@keti.re.kr Sungchan Choi, KETI, csc@keti.re.kr Jaeho Kim, KETI, jhkim@keti.re.kr |
| Reason for Change/s:* | Update LOC testcase |
| CR against: Release* | Release-1 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 v0.1.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The LOC testcase identified with ID TP/oneM2M/CSE/LOC/BI/001 was defined with generic  RESOURCE_TYPE parameter and generic ATTRIBUTE_NAME parameter, which are supposed to be specified as <locationPolicy> specific attributes, i.e. <locationPolicy> type and <locationPolicy> specific attribute. We propose to change both the generic RESOURCE_TYPE and ATTRIBUTE_NAME parameter to <locationPolicy> type (value) and LocationUpdatePeriod parameter, respectively.

## -----------------------Start of change 1--------------------------------------------

# 7	Test Purposes (TP)

## 7.2.2.6 Location (LOC)

###### 7.2.2.6.3 Invalid Behavioural Test Case

| TP Id | TP/oneM2M/CSE/LOC/BI/001 |
| --- | --- |
| Test objective | Check that the IUT rejects AE to update the <locationPolicy> resource identified with LOCATION_ID when receiving an update request containing an invalid attribute |
| Reference | TS-0001 10.2.10.1.3, TS-0004 7.3.3.4 & 7.4.11.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type <locationPolicy> containing an optional RW attribute LocationUpdatePeriod and the AE having privileges to perform UPDATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a UPDATE request with from AE containing To set to TARGET_RESOURCE_ADDRESS and From set to AE_ID and Contents attribute containing LocationUpdatePeriod set to INVALID_LOCATION_UPDATE_PERIOD } | IUT ( AE |
|  | then { the IUT sends a Response message containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

## -----------------------End of change 1--------------------------------------------