| Input Contribution |
| --- |
| Meeting ID* | TST #25 |
| Title:* | TS-0025-Definition_of_product_profiles-V0_0_1_Generic Service Profile |
| Source:* | Keebum Kim, TTA, keebum.kim@tta.or.kr Sookhyun Jeon, TTA, shjeon@tta.or.kr Kanghae Lee, TTA, kanghae@tta.or.kr |
| Uploaded Date:* | 2016-10-12 |
| Document(s) Impacted* | TS-0025 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | This contribution proposes that the Generic Service Profile of oneM2M product intends to add in TS-0025. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Introduction

We propose a definition of generic device profiles based on node types for implementing oneM2M devices. These profiles will include minimum features required to implement devices for oneM2M services.

---------------Start of Change 1--------------------

# 7	Product service profiles

# 7.1	Introduction

## 7.2	Basic Device Profile

### 7.2.1	Profile description

oneM2M provides serveral logical entity concepts called ‘Node’ to explain oneM2M Architecture in TS-0001. And from the descriptions about the node types indicates some examples that particular node could match with pyshical oneM2M devices (e.g. ADN -> constrainted oneM2M Device). But for the oneM2M device developers, may require more detail information to design and implement physical devices.

This Basic Device Profile defines set of minimum features which should be used for many types of oneM2M devices.

### 7.2.2	Profile usage examples

### Basic Device Profile could be the basic profile of all oneM2M devices like sensor, actuator, gateway, service server etc. And also this profile could be used independently when developers want to implement oneM2M device with special functions.

### 7.2.3	Feature set

### 7.2.3.1 ADN Basic Device Profile

The features defined in this clause SHALL be implemented by the product.

Table 7.2.3.1 Feature set for ADN Basic Device Profile

| No. | Function | Sub-function | Feature | Operation | Test Purposes Mapping |
| --- | --- | --- | --- | --- | --- |
| 1 | Registration | AE registration | AE registration operation in originator role, only using mandatory attributes. | CREATE | Editor’s note: Mapping Test Purpose ids has to be updated here. |
|  |  | AE deregistration | AE deregistration operation in originator. | DELETE |  |
| 2 | Data Management | <container> resource management. | Create operation in originator role, only using mandatory attributes | CREATE |  |
|  |  | <contentInstance> resource management | Create operation in originator role, only using mandatory attributes | CREATE |  |

#### 7.2.3.2 ASN Basic Device Profile

The features defined in this clause SHALL be implemented by the product.

Editor's Note: add ASN Basic Device Profile feature set table.

#### 7.2.3.3 MN Basic Device Profile

The features defined in this clause SHALL be implemented by the product.

Editor's Note: add MN Basic Device Profile feature set table.

#### 7.2.3.4 IN Basic Device Profile

The features defined in this clause SHALL be implemented by the product.

Table 7.2.3.4 Feature set for IN Basic Device Profile

| No. | Function | Sub-function | Feature | Operation | Test Purposes Mapping |
| --- | --- | --- | --- | --- | --- |
| 1 | Registration | AE registration | AE registration operation in receiver role, only using mandatory attributes. | CREATE | Editor’s note: Mapping Test Purpose ids has to be updated here. |
|  |  |  | AE registration operation in receiver role, using optional attributes. | CREATE |  |
|  |  | AE deregistration | AE deregistration operation in receiver role. | DELETE |  |
|  |  | CSE registration | CSE registration operation in receiver role, only using mandatory attributes. | CREATE |  |
|  |  |  | CSE registration operation in receiver role, using optional attributes. | CREATE |  |
|  |  | CSE deregistration | CSE deregistration operation in receiver role. | DELETE |  |
| 2 | Data Management | <container> resource management. | Create operation in receiver role, only using mandatory attributes | CREATE |  |
|  |  |  | Create operation in receiver role, using optional attributes | CREATE |  |
|  |  |  | Update operation in receiver role, only using mandatory attributes | UPDATE |  |
|  |  |  | Update operation in receiver role, using optional attributes | UPDATE |  |
|  |  |  | Retrieve operation in receiver role. | RETRIEVE |  |
|  |  |  | Delete operation in receiver role. | DELETE |  |
|  |  | <contentInstance> resource management | Create operation in receiver role, only using mandatory attributes | CREATE |  |
|  |  |  | Create operation in receiver role, using optional attributes | CREATE |  |
|  |  |  | Update operation in receiver role, only using mandatory attributes | UPDATE |  |
|  |  |  | Update operation in receiver role, using optional attributes | UPDATE |  |
|  |  |  | Retrieve operation in receiver role. | RETRIEVE |  |
|  |  |  | Delete operation in receiver role. | DELETE |  |
|  |  | <latest>, <oldest> resource management | Retrieve operation in receiver role. | RETRIEVE |  |
|  |  |  | Delete operation in receiver role. | DELETE |  |
| 3 | Authorization | <accessControlPolicy> resource management | Create operation in receiver role, only using mandatory attributes | CREATE |  |
|  |  |  | Create operation in receiver role, using optional attributes | CREATE |  |
|  |  |  | Update operation in receiver role, only using mandatory attributes | UPDATE |  |
|  |  |  | Update operation in receiver role, using optional attributes | UPDATE |  |
|  |  |  | Retrieve operation in receiver role. | RETRIEVE |  |
|  |  |  | Delete operation in receiver role. | DELETE |  |
| 4 | Subscription and notification | <subscription> resource management | Create operation in receiver role, only using mandatory attributes | CREATE |  |
|  |  |  | Create operation in receiver role, using optional attributes | CREATE |  |
|  |  |  | Update operation in receiver role, only using mandatory attributes | UPDATE |  |
|  |  |  | Update operation in receiver role, using optional attributes | UPDATE |  |
|  |  |  | Retrieve operation in receiver role. | RETRIEVE |  |
|  |  |  | Delete operation in receiver role. | DELETE |  |

---------------End of Change 1----------------------