| Input Contribution |
| --- |
| Meeting ID* | TST#25 |
| Title:* | TS-0018 Test Purposes for Group AE |
| Source:* | Ting Martin Miao, KETI, novamartin@keti.re.kr Abdullah Aziz, KETI, G2016FFM082@sju.ac.kr |
| Uploaded Date:* | 2016-10-05 |
| Document(s) Impacted* | TS-0018 V0.1.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes two test purposes for AE REG group to address AE registration and AE re-registration case. Currently clasue 7.2.1 of Section 7.2 is empty and is not describing any test purpose for Group AE. This contribution will add Registration test purpose (7.2.1.1) with two cases, one for registration and second for re-registration.

## -----------------------Start of change 1--------------------------------------------

### 7.2.1	Group AE

Editor’s Note: We define a group of test purposes for AE in a manner that product profiles i.e. ADN can be mapped to at least one of the test purposes for AE. The hierarchical structure for the identitiy of test purposes defined for AE looks like: TP/oneM2M/{AE}/{CSF}/{testing_type}/{sequential_number}

## 7.2.1.1		Registration (REG)

Editor’s Note: We start defining test purposes for AE from REG capability.

Features defined in ADN1 sensing service profile are refered to propose a group of test purposes covering REG capability.

| TP Id | TP/oneM2M/AE/REG/BV/001 |
| --- | --- |
| Test objective | Check that the IUT sends an AE initial registration request including attribute App-ID set to APP-ID but no AE-ID-STEM provided when it is started |
| Reference | TS-0001 10.1.1.2.2 - case C, 9.6.19 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT never being registered and the IUT being switched off and the IUT having got a valid APP-ID } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is started } | NA |
|  | then { the IUT sends a valid CREATE request to CSE containing Resource-Type set to 2 (AE) and From set to empty and Content <AE> containing App-ID attribute set to APP-ID } | CSE ( IUT |

| TP Id | TP/oneM2M/AE/REG/BV/002 |
| --- | --- |
| Test objective | Check that the IUT sends an AE registration request including AE-ID-STEM when performing re-registration |
| Reference | TS-0001 10.1.1.2.2 - case d, 9.6.19 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT having been registered and the IUT being deregistered } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT intends to register again } | NA |
|  | then { the IUT sends a valid CREATE request to CSE containing Resource-Type set to 2 (AE) and From set to AE-ID-STEM and Content <AE> representation } | CSE ( IUT |

Editor’s Note: TP/oneM2M/AE/REG/BV/003 is expected to be updated in TST 26.

| TP Id | TP/oneM2M/AE/REG/BV/003 |
| --- | --- |
| Test objective | Check that the IUT receives an AE registration response including mandatory parameters after sending a valid AE registration request |
| Reference | TS-0001 10.1.1.2.2 & 10.1.1.1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being switched on } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT sends a valid CREATE request to CSE containing Resource-Type set to 2 (AE) and From set to AE-ID-STEM and Content <AE> representation } | CSE ( IUT |
|  | then { the IUT receives a AE CREATE response from CSE containing Content <AE> representation containing mandatory attributes representation (Resource-ID, parentID, creationTime, expirationTime, and lastModifiedTime) } | IUT ( CSE |

| TP Id | TP/oneM2M/AE/REG/BV/004 |
| --- | --- |
| Test objective | Check that the IUT sends an AE initial registration request including pointOfAccess attribute when it is started |
| Reference | TS-0001 10.1.1.2.2 - case C, 9.6.19 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT never being registered and the IUT being switched off and the IUT being accessible through POINT_OF_ACCESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is started } | NA |
|  | then { the IUT sends a valid CREATE request to CSE containing Resource-Type set to 2 (AE) and From set to empty and Content <AE> representation containing pointOfAccess set to POINT_OF_ACCESS } | CSE ( IUT |

Editor’s Note: TP/oneM2M/AE/REG/BV/005 is expected to be updated in TST26.

| TP Id | TP/oneM2M/AE/REG/BV/005 |
| --- | --- |
| Test objective | Check that the IUT receives an AE registration response including pointOfAccess attribute after sending a valid AE registration request |
| Reference | TS-0001 10.1.1.2.2 & 10.1.1.1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being switched on } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT sends a valid CREATE request to CSE containing Resource-Type set to 2 (AE) and From set to AE-ID-STEM and Content <AE> representation } | CSE ( IUT |
|  | then { the IUT receives a AE CREATE response from CSE containing Content <AE> representation containing pointOfAccess set to POINT_OF_ACCESS } | IUT ( CSE |

Editor’s Note: More test purposes for AE are call for contributors.

## -----------------------End of change 1--------------------------------------------

# Comments

The trigger event is supposed to be

When {

the IUT receives a AE create response

}

The trigger event is supposed to be

When {

the IUT receives a AE create response

}