| Input Contribution |
| --- |
| Meeting ID* | TST#25.2 |
| Title:* | TS-0018 Test Purposes for ADN DMR |
| Source:* | Ting Martin Miao, KETI, novamartin@keti.re.kr Abdullah Aziz, KETI, G2016FFM082@sju.ac.kr |
| Uploaded Date:* | 2016-11-22 |
| Document(s) Impacted* | TS-0018 V0.1.4 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes test purposes mapping with features defined in ADN profiles.  The scope of test purposes in this document covers data management of container and contentInstance.

## -----------------------Start of change 1--------------------------------------------

### 7.2.1	Group AE

Editor’s Note: We define a group of test purposes for AE in a manner that product profiles i.e. ADN can be mapped to at least one of the test purposes for AE. The hierarchical structure for the identitiy of test purposes defined for AE looks like: TP/oneM2M/{AE}/{CSF}/{testing_type}/{sequential_number}

## 7.2.1.2		Data Management and Repository (DMR)

Editor’s Note: We start defining test purposes for AE from DMR capability.

Features defined in ADN1 sensing service profile are refered to propose a group of test purposes covering DMR capability.

| TP Id | TP/oneM2M/AE/DMR/BV/001 |
| --- | --- |
| Test objective | Check that the IUT sends a Container creation request when it is triggered |
| Reference | TS-0001 10.1.1.1 & 10.2.4.1, TS-0004 7.2.2.1 & 7.4.7.1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE. |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT having privileges to perform CREATE operation on resource AE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a container create request } | IUT ( CSE |
|  | then { the IUT sends a valid Container CREATE request to CSE containing Resource-Type set to 3 (Container) and From set to AE_ID and Content <container> representation } | CSE ( IUT |

Editor’s Note: TP/oneM2M/AE/DMR/BV/002 is expected to be updated in TST26.

| TP Id | TP/oneM2M/AE/DMR/BV/002 |
| --- | --- |
| Test objective | Check that the IUT receives a container CREATE response including mandatory parameters after sending a valid container CREATE request without specifying ResultContent parameter |
| Reference | TS-0001 10.1.1.1, TS-0004 7.4.7.2.1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being switched on } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT sends a valid container CREATE request to CSE } | CSE ( IUT |
|  | then { the IUT receives a container CREATE response from CSE containing mandatory attributes representation (Resource-ID, parentID, creationTime, expirationTime, and lastModifiedTime) } | IUT ( CSE |

| TP Id | TP/oneM2M/AE/DMR/BV/003 |
| --- | --- |
| Test objective | Check that the IUT sends a ContentInstance creation request when it is triggered |
| Reference | TS-0001 10.1.1.1 & 10.2.4.1, TS-0004 7.2.2.1 & 7.4.8.2.1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE. |
| Initial conditions | with { the IUT being registered and the IUT having created a container resource CONTAINER_RESOURCE_ADDRESS and the IUT having privileges to perform CREATE operation on resource CONTAINER_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a contentInstance create request } | IUT ( CSE |
|  | then { the IUT sends a valid ContentInstance CREATE request to CSE containing Resource-Type set to 4 (ContentInstance) and From set to AE_ID and Content <contentInstance> representation } | CSE ( IUT |

Editor’s Note: TP/oneM2M/AE/DMR/BV/004 is expected to be updated in TST26.

| TP Id | TP/oneM2M/AE/DMR/BV/004 |
| --- | --- |
| Test objective | Check that the IUT receives a contentInstance CREATE response including mandatory parameters after sending a valid contentInstance CREATE request without specifying ResultContent parameter |
| Reference | TS-0001 10.1.1.1, TS-0004 7.4.8.2.1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being switched on } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT sends a valid contentInstance CREATE request to CSE } | CSE ( IUT |
|  | then { the IUT receives a contentInstance CREATE response from CSE containing mandatory attributes representation (Resource-ID, parentID, creationTime, expirationTime, and lastModifiedTime) } | IUT ( CSE |

## -----------------------End of change 1--------------------------------------------