| Input Contribution |
| --- |
| Meeting ID* | TST#25.2 |
| Title:* | TS-0018 Test Purposes for ADN SUB |
| Source:* | Ting Martin Miao, KETI, novamartin@keti.re.kr Abdullah Aziz, KETI, G2016FFM082@sju.ac.kr |
| Uploaded Date:* | 2016-11-22 |
| Document(s) Impacted* | TS-0018 V0.1.4 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes test purposes mapping with features defined in ADN2 profile.  The scope of test purposes in this document covers only fundamental feature of Subsription creation and Notification.

## -----------------------Start of change 1--------------------------------------------

### 7.2.1	Group AE

Editor’s Note: We define a group of test purposes for AE in a manner that product profiles i.e. ADN can be mapped to at least one of the test purposes for AE. The hierarchical structure for the identitiy of test purposes defined for AE looks like: TP/oneM2M/{AE}/{CSF}/{testing_type}/{sequential_number}

## 7.2.1.3	Subscription and Notification (SUB)

Editor’s Note: Fundamental features of ADN2 profile

| TP Id | TP/oneM2M/AE/SUB/BV/001 |
| --- | --- |
| Test objective | Check that the IUT sends a subscription creation request when it is started |
| Reference | TS-0001 10.1.1.1 & 10.2.4.1, TS-0004 7.2.2.1 & 7.4.9.2.1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE. |
| Initial conditions | with { the IUT being registered and the IUT being switched off and the IUT having privileges to perform CREATE operation on resource AE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is started } | NA |
|  | then { the IUT sends a valid subscription CREATE request to CSE containing Resource-Type set to 23 (Subscription) and From set to AE_ID and Content <subscription> representation } | CSE ( IUT |

| TP Id | TP/oneM2M/AE/SUB/BV/002 |
| --- | --- |
| Test objective | Check that the IUT receives a subscription CREATE response including mandatory parameters after sending a valid subscription CREATE request without specifying ResultContent parameter |
| Reference | TS-0001 10.1.1.1, TS-0004 7.4.9.2.1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being switched on } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT sends a valid subscription CREATE request to CSE } | CSE ( IUT |
|  | then { the IUT receives a subscription CREATE response from CSE containing mandatory attributes representation (Resource-ID, parentID, creationTime, expirationTime, and lastModifiedTime) } | IUT ( CSE |

| TP Id | TP/oneM2M/AE/SUB/BV/002 |
| --- | --- |
| Test objective | Check that the IUT receives a subscription CREATE response including mandatory parameters after sending a valid subscription CREATE request without specifying ResultContent parameter |
| Reference | TS-0001 10.1.1.1, TS-0004 7.4.9.2.1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being switched on } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT sends a valid subscription CREATE request to CSE } | CSE ( IUT |
|  | then { the IUT receives a subscription CREATE response from CSE containing mandatory attributes representation (Resource-ID, parentID, creationTime, expirationTime, and lastModifiedTime) } | IUT ( CSE |

| TP Id | TP/oneM2M/AE/SUB/BV/003 |
| --- | --- |
| Test objective | Check that the IUT is notified with single notification message with type of default notification content type when it is switched on |
| Reference | TS-0001 10.1.5, TS-0004 7.5.1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being switched off and the IUT being reachable through a URL ACCESSIBLE_URL } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is started } | NA |
|  | then { the IUT receives a notification message containing <notification> primitive representation containing mandatory attributes representation (notificationEvent/representation, and subscriptionReference) } | IUT ( CSE |

| TP Id | TP/oneM2M/AE/SUB/BV/004 |
| --- | --- |
| Test objective | Check that the IUT is notified with aggregated notifications with type of default notification content type when it is switched on |
| Reference | TS-0001 10.1.5, TS-0004 7.5.1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being switched off and the IUT being reachable through a URL ACCESSIBLE_URL } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is started } | NA |
|  | then { the IUT receives a notification message containing <aggregatedNotification> representation containing aggregated <notification> representation } | IUT ( CSE |

## -----------------------End of change 2--------------------------------------------