| Input Contribution |
| --- |
| Meeting ID* | TST#26 |
| Title:* | Clause_6_Functional_architecture_of_TR-0034 |
| Source:* | Shane He, shane.he@nokia.com |
| Uploaded Date:* | 2016-11-29 |
| Document(s) Impacted* | TR-0034 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | It is proposed to add context and figure of clause 6 of TR-0034 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 6	Functional architecture

This clause describes the architecture of this use case with components represented by the oneM2M entity roles.

In the oneM2M, two basic types of entities are defined. One is an AE (short for Application Entity) and the other is a CSE (short for Common Services Entity). Therefore, in this use case:

- The sensor, actuator, and the smartphone each host an AE. The AE which resides in the Application Dedicated Node is  called ADN-AE.

- An IN-CSE (short for Infrastructure Node CSE) is hosted in the cloud or server, and a MN-CSE (short for Middle Node CSE) is hosted on the gateway.

For instance, the architecture is show in figure 6.1.

Figure 6.1: oneM2M functional architecture of temperatue monitoring use case

The oneM2M defined Mca reference point is used to interface an AE and CSE, and the oneM2M defined Mcc reference point is used to interface CSEs. Therefore, in this use case:

- The reference point used between temperature sensor AE, actuator AE and gateway MN-CSE or Smartphone AE and IN-CSE is Mca.

- The reference point used between the gateway MN-CSE and IN-CSE is Mcc.

In summary, applications used in the current use case are classified as follows:

- ADN-AE-1: an application embedded in Sensor#1 with capabilities to monitor Sensor#1 and interact with the gateway MN-CSE through Mca reference point;

- ADN-AE-2: an application embedded in Sensor#2 with capabilities to monitor Sensor#2 and interact with the gateway MN-CSE through Mca reference point;

- ADN-AE-3: an application embedded in Actuator#1 with capabilities to control Actuator#1 and interact with the gateway MN-CSE through Mca reference point;

- ADN-AE-4: a smartphone application embedded in the smartphone device with capabilities to interact directly with the oneM2M service platform IN-CSE through Mca reference point and thereby remotely monitor and control Sensor#1, Sensor#2 and Actuator#1.

# End of the text