| Input Contribution |
| --- |
| Meeting ID* | TST 26 |
| Title:* | TS-0018 Test Purposes for ADN3 |
| Source:* | Ting Martin Miao, KETI, novamartin@keti.re.kr Abdullah Aziz, KETI, G2016FFM082@sju.ac.kr |
| Uploaded Date:* | 2016-12-05 |
| Document(s) Impacted* | TS-0018 V0.1.4 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution presents test purposes mapping to features defined in ADN3 profiles. New features for ADN3 profile is also proposed to cover optional attributes in oneM2M resource primitives.

A reference table for new features of ADN3 is shown as below.

| ADN3 constraint sensor profile | DMR (F)-contentInstance | Creation of <contentInstance> resource with mandatory attributes and optional attribute contentInfo as an originator | TP/oneM2M/AE/DMR/BV/005_01 | The action can be triggered by stimulus |
| --- | --- | --- | --- | --- |
|  | DMR (F)-contentInstance | Creation of <contentInstance> resource with mandatory attributes and optional attribute ontologyRef as an originator | TP/oneM2M/AE/DMR/BV/005_02 |  |
|  | REG (E)-AE | Creation of <AE> resource with mandatory attributes and optional attribute accessControlPolicyIDs | TP/oneM2M/AE/REG/BV/00x_01 | The action can be done in the preconfiguration phase |
|  |  | Creation of <AE> resource with mandatory attributes and optional attribute pointOfAccess | TP/oneM2M/AE/REG/BV/00x_02 |  |
|  |  | Creation of <AE> resource with mandatory attributes and optional attribute ontologyRef | TP/oneM2M/AE/REG/BV/00x_03 |  |
|  | DMR (E)-container | Creation of <container> resource with mandatory attributes and optional attribute accessControlPolicyIDs | TP/oneM2M/AE/DMR/BV/006_01 | The action either can be done in preconfiguration phase or through stimulus |
|  | DMR (E)-container | Creation of <container> resource with mandatory attributes and optional attribute maxNrOfInstances | TP/oneM2M/AE/DMR/BV/006_02 |  |
|  | DMR (E)-container | Creation of <container> resource with mandatory attributes and optional attribute maxByteSize | TP/oneM2M/AE/DMR/BV/006_03 |  |
|  | DMR (E)-container | Creation of <container> resource with mandatory attributes and optional attribute maxInstanceAge | TP/oneM2M/AE/DMR/BV/006_04 |  |
|  | DMR (E)-container | Creation of <container> resource with mandatory attributes and optional attribute ontologyRef | TP/oneM2M/AE/DMR/BV/006_05 |  |
|  | DMR (E)-container | Creation of <container> resource with mandatory attributes and optional attribute locationID | TP/oneM2M/AE/DMR/BV/006_06 |  |

## -----------------------Start of change 1--------------------------------------------

### 7.2.1	Group AE

Editor’s Note: We define a group of test purposes for AE in a manner that product profiles i.e. ADN can be mapped to at least one of the test purposes for AE. The hierarchical structure for the identitiy of test purposes defined for AE looks like: TP/oneM2M/{AE}/{CSF}/{testing_type}/{sequential_number}

## 7.2.1.2		Data Management and Repository (DMR)

7.2.1.2.1 Test Purposes mapping to ADN3 constraint sensor profile

Editor’s Note: New features  reflecting the usage of  optional attributes for ADN3 constraint sensor profile are proposed and corresponding test purposes mapped to those new features are present as following.

| TP Id | TP/oneM2M/AE/DMR/BV/005 |
| --- | --- |
| Test objective | Check that the IUT sends a ContentInstance creation request with optional attribute ATTRIBUTE_NAME when it sensed updated data |
| Reference | TS-0001 10.1.1.1 & 10.2.4.1, TS-0004 7.2.2.1 & 7.4.8.2.1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being registered through preconfiguration request and the IUT having created a container resource CONTAINER_RESOURCE_ADDRESS through preconfiguration request and the IUT having privileges to perform CREATE operation on resource CONTAINER_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is sensed updated data for contentInstance creation } | NA |
|  | then { the IUT sends a ContentInstance CREATE request to CSE containing Resource-Type set to 4 (ContentInstance) and From set to AE_ID and Content containing Content set to SENSED_DATA_QUANTITY_VALUE and ATTRIBUTE_NAME set to ATTRIBUTE_VALUE } | CSE ( IUT |

| TP ID | ATTRIBUTE_NAME | ATTRIBUTE_VALUE |
| --- | --- | --- |
| TP/oneM2M/AE/DMR/BV/005_01 | Content Info | METADATA_INFO |
| TP/oneM2M/AE/DMR/BV/005_02 | Ontology Ref | ONTOLOGY_REFERENCE |

Editor’s Note: In case the container resource is created by hosting CSE instead of constraint IUT, the constraint IUT is not expected to send Container creation request to the hosting CSE. While in case that container resource is created as a result of container creation request to the hosting CSE, the constraint IUT is triggered to send container creation request to the hosting CSE.

| TP Id | TP/oneM2M/AE/DMR/BV/006 |
| --- | --- |
| Test objective | Check that the IUT sends a Container creation request with optional attribute ATTRIBUTE_NAME when it is triggered |
| Reference | TS-0001 10.1.1.1 & 10.2.4.1, TS-0004 7.2.2.1 & 7.4.7.1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE. |
| Initial conditions | with { the IUT being registered and the IUT having privileges to perform CREATE operation on resource AE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a container request } | IUT ( CSE |
|  | then { the IUT sends a Container CREATE request to CSE containing Resource-Type set to 3 (Container) and From set to AE_ID and Content containing ATTRIBUTE_NAME set to ATTRIBUTE_VALUE } | CSE ( IUT |

| TP ID | ATTRIBUTE_NAME | ATTRIBUTE_VALUE |
| --- | --- | --- |
| TP/oneM2M/AE/DMR/BV/006_01 | Access ControlPolicy IDs | ACCESS_CONTRL_POLICY_IDS |
| TP/oneM2M/AE/DMR/BV/006_02 | Max Number Of Instances | MAX_NR_OF_INSTANCES |
| TP/oneM2M/AE/DMR/BV/006_03 | Max Byte Size | MAX_BYTE_SIZE |
| TP/oneM2M/AE/DMR/BV/006_04 | Max Instance Age | MAX_INSTANCE_AGE |
| TP/oneM2M/AE/DMR/BV/006_05 | Ontology Ref | ONTOLOGY_REFERENCE |
| TP/oneM2M/AE/DMR/BV/006_06 | Location ID | LOCATION_ID |

Editor’s Note: Combination of optional attributes that are included in the Content of container creation request can be extended to generate more test cases based on this test case.

## -----------------------End of change 1--------------------------------------------

# Comments

The AE registration and Container creation can be done during preconfiguration phase for constraint sensors.

The AE registration is done by preconfiguration during the installation phase for ADN3 constraint sensors