| Input Contribution |
| --- |
| Meeting ID* | TST 26 |
| Title:* | TS-0018 Test Purposes for ADN SUB |
| Source:* | Ting Martin Miao, KETI, novamartin@keti.re.kr Abdullah Aziz, KETI, G2016FFM082@sju.ac.kr |
| Uploaded Date:* | 2016-12-08 |
| Document(s) Impacted* | TS-0018 V0.1.4 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution presents test purposes mapping to features defined in ADN profiles. New features for ADN profile are also proposed to cover optional attributes in oneM2M resource primitives.

A reference table for new features of ADN4 is shown as below.

| ADN4 constraint actuator profile | SUB (F)-subscription | Creation of <subscription> resource with mandatory attribute notificationURI and optional attribute accessControlPolicyIDs | TP/oneM2M/AE/SUB/BV/004_01 |
| --- | --- | --- | --- |
|  |  | Creation of <subscription> resource with mandatory attribute notificationURI and optional attribute eventNotificationCriteria | TP/oneM2M/AE/SUB/BV/004_02 |
|  |  | Creation of <subscription> resource with mandatory attribute notificationURI and optional attribute expirationCounter | TP/oneM2M/AE/SUB/BV/004_03 |
|  |  | Creation of <subscription> resource with mandatory attribute notificationURI and optional attribute notificationForwardingURI | TP/oneM2M/AE/SUB/BV/004_04 |
|  |  | Creation of <subscription> resource with mandatory attribute notificationURI and optional attribute notificationContentType | TP/oneM2M/AE/SUB/BV/004_05 |
|  |  | Creation of <subscription> resource with mandatory attribute notificationURI and optional attribute notificationEventCat | TP/oneM2M/AE/SUB/BV/004_06 |
|  |  | Creation of <subscription> resource with mandatory attribute notificationURI and optional attribute subscriberURI | TP/oneM2M/AE/SUB/BV/004_07 |

## -----------------------Start of change 1--------------------------------------------

### 7.2.1	Group AE

7.2.1.3	Subscription and Notification (SUB)

| TP Id | TP/oneM2M/AE/SUB/BV/004 |
| --- | --- |
| Test objective | Check that the IUT sends a subscription creation request with optional attribute ATTRIBUTE_NAME when it is triggered |
| Reference | TS-0001 10.1.1.1 & 10.2.11.2, TS-0004 7.2.2.1 & 7.4.9.2.1 |
| Config Id | CF03 |
| PICS Selection | PICS_AE. |
| Initial conditions | with { the IUT being registered and the IUT having privileges to perform CREATE operation on resource AE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a subscription request } | IUT ( CSE |
|  | then { the IUT sends a subscription CREATE request to CSE containing To set to TARGET_RESOURCE_ADDRESS and Resource-Type set to 23 (Subscription) and From set to AE_ID and Primitive Content containing NotificationURI attribute and ATTRIBUTE_NAME with assigned field value by the IUT } | CSE ( IUT |

| TP ID | Reference | ATTRIBUTE_NAME |
| --- | --- | --- |
| TP/oneM2M/AE/SUB/BV/004_01 | TS-0001 9.6.8, TS-0004 7.4.9.1 | accessControlPolicyIDs |
| TP/oneM2M/AE/SUB/BV/004_02 | TS-0001 9.6.8, TS-0004 7.4.9.1 | eventNotificationCriteria |
| TP/oneM2M/AE/SUB/BV/004_03 | TS-0001 9.6.8, TS-0004 7.4.9.1 | expirationCounter |
| TP/oneM2M/AE/SUB/BV/004_04 | TS-0001 9.6.8, TS-0004 7.4.9.1 | notificationForwardingURI |
| TP/oneM2M/AE/SUB/BV/004_05 | TS-0001 9.6.8, TS-0004 7.4.9.1 | notificationContentType |
| TP/oneM2M/AE/SUB/BV/004_06 | TS-0001 9.6.8, TS-0004 7.4.9.1 | notificationEventCat |
| TP/oneM2M/AE/SUB/BV/004_07 | TS-0001 9.6.8, TS-0004 7.4.9.1 | subscriberURI |

Editor’s Note: Combination of optional attributes that are included in the Content of subscription creation request can be extended to generate more test cases based on this test case.

## -----------------------End of change 1------------------------------------------