| Input Contribution |
| --- |
| Meeting ID* | TST 26 |
| Title:* | TS-0018 Test Purposes for ADN3 Preconfiguration of AE and Container |
| Source:* | Ting Martin Miao, KETI, novamartin@keti.re.kr |
| Uploaded Date:* | 2016-12-05 |
| Document(s) Impacted* | TS-0018 V0.1.4 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

Preconfiguration might be required for constraint devices in terms of creation of AE and/or container for the constraint devices by a hosting CSE during installation phase. This contribution presents test purposes mapping to this feature.

A reference table for new features of ADN3 is shown as below.

| ADN3 constraint sensor profile | REG (E)-AE | Creation of <AE> resource with mandatory attributes and optional attribute accessControlPolicyIDs | TP/oneM2M/AE/REG/BV/00x_01 | The action can be done in the preconfiguration phase |
| --- | --- | --- | --- | --- |
|  | REG (E)-AE | Creation of <AE> resource with mandatory attributes and optional attribute pointOfAccess | TP/oneM2M/AE/REG/BV/00x_02 |  |
|  | REG (E)-AE | Creation of <AE> resource with mandatory attributes and optional attribute ontologyRef | TP/oneM2M/AE/REG/BV/00x_03 |  |
|  | DMR (E)-container | Creation of <container> resource with mandatory attributes and optional attribute accessControlPolicyIDs | TP/oneM2M/AE/DMR/BV/006_01 | The action either can be done in preconfiguration phase or through stimulus |
|  | DMR (E)-container | Creation of <container> resource with mandatory attributes and optional attribute maxNrOfInstances | TP/oneM2M/AE/DMR/BV/006_02 |  |
|  | DMR (E)-container | Creation of <container> resource with mandatory attributes and optional attribute maxByteSize | TP/oneM2M/AE/DMR/BV/006_03 |  |
|  | DMR (E)-container | Creation of <container> resource with mandatory attributes and optional attribute maxInstanceAge | TP/oneM2M/AE/DMR/BV/006_04 |  |
|  | DMR (E)-container | Creation of <container> resource with mandatory attributes and optional attribute ontologyRef | TP/oneM2M/AE/DMR/BV/006_05 |  |
|  | DMR (E)-container | Creation of <container> resource with mandatory attributes and optional attribute locationID | TP/oneM2M/AE/DMR/BV/006_06 |  |

## -----------------------Start of change 1--------------------------------------------

### 7.2.2	Group AE

## 7.2.2.0		Preconfiguration

Editor’s Note: Features for preconfiguration for ADN3 constraint sensors are proposed and corresponding test purposes mapped to those new features are present as following.

| TP Id | TP/oneM2M/AE/REG/BV/00X |
| --- | --- |
| Test objective | Check that the IUT receives configuration response when connecting to CSE for initial AE configuration |
| Reference |  |
| Config Id | CF0x |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being initial state and the IUT never being registered and the IUTbeing disconnected with CSE } |
| Expected behaviour | Test events | Direction |
|  | when { IUT connects to the CSE } | NA |
|  | then { the IUT sends a configuration request after connected with the CSE containing <AE> representation containg ATTRIBUTE_NAME set to ATTRIBUTE_VALUE } | CSE ( IUT |

| TP ID | ATTRIBUTE_NAME | ATTRIBUTE_VALUE |
| --- | --- | --- |
| TP/oneM2M/AE/REG/BV/00x_01 | Access Control Policy IDs | ACCESS_CONTRL_POLICY_IDS |
| TP/oneM2M/AE/REG/BV/00x_02 | Point Of Access | POINT_OF_ACCESS |
| TP/oneM2M/AE/REG/BV/00x_03 | Ontology Ref | ONTOLOGY_REFERENCE |

| TP Id | TP/oneM2M/AE/DMR/BV/00X |
| --- | --- |
| Test objective | Check that the IUT receives configuration response when connecting to CSE for container configuration |
| Reference |  |
| Config Id | CF0x |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being initial state and the IUT being registered through preconfiguration of AE resource and the IUTbeing disconnected with CSE } |
| Expected behaviour | Test events | Direction |
|  | when { IUT connects to the CSE } | NA |
|  | then { the IUT sends a configuration request after connected with the CSE containing <container> representation containg ATTRIBUTE_NAME set to ATTRIBUTE_VALUE } | CSE ( IUT |

| TP ID | ATTRIBUTE_NAME | ATTRIBUTE_VALUE |
| --- | --- | --- |
| TP/oneM2M/AE/DMR/BV/00x_01 | Access ControlPolicy IDs | ACCESS_CONTRL_POLICY_IDS |
| TP/oneM2M/AE/DMR/BV/00x_02 | Max Number Of Instances | MAX_NR_OF_INSTANCES |
| TP/oneM2M/AE/DMR/BV/00x_03 | Max Byte Size | MAX_BYTE_SIZE |
| TP/oneM2M/AE/DMR/BV/00x_04 | Max Instance Age | MAX_INSTANCE_AGE |
| TP/oneM2M/AE/DMR/BV/00x_05 | Ontology Ref | ONTOLOGY_REFERENCE |
| TP/oneM2M/AE/DMR/BV/00x_06 | Location ID | LOCATION_ID |

## -----------------------End of change 1--------------------------------------------

# Comments

The configuration request includes preference info for the configuration e.g. infor for AE REG preference and/or container CREATE preference

NOTE:

The configuration request primitive NEEDs TO BE SPECIFIED in TST standards.

The configuration request includes preference info for the configuration e.g. infor for AE REG preference and/or container CREATE preference

NOTE:

The configuration request primitive NEEDs TO BE SPECIFIED in TST standards.