| CHANGE REQUEST |
| --- |
| Meeting:* | TST 26 |
| Source:* | Ting Martin MIAO, KETI, novamartin@keti.re.kr |
| Date:* | 2016-12-05 |
| Contact:* | Ting Martin MIAO, KETI, novamartin@keti.re.kr |
| Reason for Change/s:* | Update uTPort and ASPs for AE automation testing |
| CR against: Release* | Release-1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0019 |
| Clauses/Sub Clauses* | 5.4.2.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Update utPort in terms of primitives used for Automation AE testing.

### -----------------------Start of change 1-------------------------------------------

### 5.4.2 utPort

#### 5.4.2.0 Introduction

The utPort has been included in the oneM2M ATS in order to be able to stimulate the IUT and receive extra information from IUT upper layers. The utPort can be applied to automated AE testing shown as section 5.4.2.1.

Editor’s Note: The utPort can also be provided for future extension.

#### 5.4.2.1 Usage for Automated AE Testing

The utPort can be used to implement the automated AE testing when SUT is an AE.

The utPort is in charges of the communication between TTCN-3 Test Component module in Test Sytem and the Upper Tester Application in SUT.

Functionalities that TTCN-3 Test Component module and the Upper Tester Application are required to implement are listed as following:

- The TTCN-3 Test Component module builds a transport link by opening a utPort with the Upper Tester Transport module to transport the triggering messages;

- TTCN-3 Test Component is able to configure the Test System and sends (standardized) triggering commands to the SUT (Upper Tester Application);

- Upper Tester Application can process the triggering command messages received from Test System (TTCN-3 Test Component) and stimulates IUT to act following the corresponding triggering command i.e. sending oneM2M service primitives to Test System through mca port.

Primitives defined for utPort are listed as following:

- UtTriggerPrimitive: trigger request primitive that is used to send triggering commands to the SUT.

- UtTriggerResultPrimitive: trigger response primitive that is used to receive the triggering result message from the SUT.

The triggering commands supported by UtTriggerPrimitive are summarized as following:

- The UtStart primitive is used to initialize IUT.

- The UtTrigger primitive is used to trigger upper layer events in IUT i.e. sending oneM2M service primitives to Test System through mca port.

- The triggering response primitive consists of  triggering result messages as following:

- The UtStartResult primitive is used to receive responses from upper layer as a result of initialization in IUT.

- The UtTriggerResult primitive is used to receive responses from upper layer as a result of triggering event stimulus.

Editor’s Note: The format of primitives defined for utPort is supposed to be defined here in the future.

The Upper Tester Application in SUT (AE) can be implemented as an embedded source code within an AE. An example for implementation of automated AE test for Registration is shown as Figure Y.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Text boxes

SUT

TEST SYSTEM

TTCN-3 Test Component

-

CSE

Upper Tester Application

IUT (AE)

Stimulate Registration

Stimulate Container Create

Registration

Container Create

Trigger Registration

Function call

utPort

utPort

mcaPort

mcaPort

Ut

Mca

Figure Y. An example for automated AE test for Registration