| CHANGE REQUEST |
| --- |
| Meeting:* | TST 26.1 |
| Source:* | TTA |
| Date:* | 2017-01-06 |
| Contact:* | Keebum Kim, TTA, keebum.kim@tta.or.kr Sookhyun Jeon, TTA, shjeon@tta.or.kr |
| Reason for Change/s:* | To add TDs for missing resources (mgmtCmd, execInstance) |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active <Work Item number> MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0013-V.2.0.1 |
| Clauses/Sub Clauses* | 8.1.15 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes to add Test Descriptions for resources which are related to device management operations. It includes <mgmtCmd> CRUD and <execInstance> RUD operations.

### -----------------------Start of change 1-------------------------------------------

### 8.1.15	External Management Operations Management

#### 8.1.15.1	mgmtCmd Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_58 |
| Objective: | AE creates a mgmtCmd resource |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.9.2 TS-0004 [2], clause 7.4.16.2.1 |
| Pre-test conditions: | AE has created an application resource <AE> on Registrar CSE AE has created a node resource <node> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a mgmtCmd Create Request |
| 2 | Mca | PRO Check Primitive | op = 1 (Create) to = {CSEBaseName} fr = AE-ID rqi = (token-string) ty = 12 (mgmtCmd) pc = Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check HTTP | Sent request contains Request method = POST Request-Target: {CSEBaseName} Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Content-Type: application/vnd.onem2m-res+xml; ty=12 or application/vnd.onem2m-res+json; ty=12 Message-body: Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check CoAP | Sent request contains Method: 0.02 (POST) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName} Content-type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json oneM2M-TY: 12 oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message: Topic: "/oneM2M/req/<AE-ID>/<Registrar CSE-ID>" Payload: op = 1 (Create) to = {CSEBaseName} fr = AE-ID rqi = (token-string) ty = 12 (mgmtCmd) pc = Serialized representation of <mgmtCmd> resource |
| 3 |  | IOP Check | Check if possible that the <mgmtCmd> resource is created in Registrar CSE. |
| 4 | Mca | PRO Check Primitive | rsc = 2001 (CREATED) rqi = (token-string) same as received in request message pc = Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 201 (OK) X-M2M-RSC: 2001 X-M2M-RI: (token-string) same as received in request message Content-Location : URI of the created <mgmtCmd> resource Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check CoAP | Registrar CSE sends response containing: Response Code = 2.01 oneM2M-RSC: 2001 oneM2M-RQI: (token-string) same as received in request message Location-Path: URI of the created <mgmtCmd> resource Payload: Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH message: Topic: "/oneM2M/resp/<AE-ID>/<Registrar CSE-ID>" Payload: to = AE-ID fr = Registrar CSE-ID rsc = 2001 (CREATED) rqi = (token-string) same as received in request message pc = Serialized representation of <mgmtCmd> resource |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict | Set verdict to pass if IOP check goal is achieved exactly, otherwise verdict fail is set with corresponding error message. |
| PRO Verdict |  |

#### 8.1.15.2	mgmtCmd Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_59 |
| Objective: | AE retrieves mgmtCmd resource |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.9.3 TS-0004 [2], clause 7.4.16.2.2 |
| Pre-test conditions: | AE has created an application resource <AE> on Registrar CSE AE has created a node resource <node> on Registrar CSE AE has created a mgmtCmd resource <mgmtCmd> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a mgmtCmd Retrieve Request |
| 2 | Mca | PRO Check Primitive | op = 2 (RETRIEVE) to = {CSEBaseName}/{mgmtCmd} fr = AE-ID rqi = (token-string) |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}/{mgmtCmd} Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Content-Type: application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/{mgmtCmd} Content-format: application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; oneM2M-FR: AE-ID oneM2M-RQI: (token-string) |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH message: Topic: "/oneM2M/req/<AE-ID>/<Registrar CSE-ID>" Payload: op = 2 (Retrieve) to = {CSEBaseName}/{mgmtCmd} fr = <AE-ID> rqi = (token-string) |
| 3 | Mca | PRO Check Primitive | rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code =200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message Message-body: Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check CoAP | Registrar CSE sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message Payload: Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH message: Topic: "/oneM2M/resp/<AE-ID>/<Registrar CSE-ID>" Payload: to = AE-ID fr = Registrar CSE-ID rsc = 2000 rqi = (token-string) same as received in request message pc = Serialized representation of <mgmtCmd> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.1.15.3	mgmtCmd Update (Normal)

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_60 |
| Objective: | AE updates attribute (not with ‘true’ in execEnable attribute) in mgmtCmd resource |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.9.4 TS-0004 [2], clause 7.4.16.2.3.1 |
| Pre-test conditions: | AE has created an application resource <AE> on Registrar CSE AE has created a node resource <node> on Registrar CSE AE has created a mgmtCmd resource <mgmtCmd> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a mgmtCmd Update Request |
| 2 | Mca | PRO Check Primitive | op = 3 (Update) to = {CSEBaseName}/{mgmtCmd} fr = AE-ID rqi = (token-string) pc = Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check HTTP | Sent request contains Request method = PUT Request-Target: {CSEBaseName}/{mgmtCmd} Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Content-Type: application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; Message-body: Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check CoAP | Sent request contains Method: 0.03 (PUT) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/{mgmtCmd} Content-format: application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message Topic: "/oneM2M/req/<AE-ID>/<Registrar CSE-ID>" Payload: op = 3 (Update) to = {CSEBaseName}/{mgmtCmd} fr = AE-ID rqi = (token-string) pc = Serialized representation of <mgmtCmd> resource |
| 3 |  | IOP Check | Check if possible that the <mgmtCmd> resource is updated in Registrar CSE. |
| 4 | Mca | PRO Check Primitive | rsc = 2004 (UPDATED) rqi = (token-string) same as received in request message pc = Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 X-M2M-RSC: 2004 X-M2M-RI: (token-string) same as received in request message Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check CoAP | Registrar CSE sends response containing: Response Code = 2.05 oneM2M-RSC: 2004 oneM2M-RQI: (token-string) same as received in request message Payload: Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH message Topic: "/oneM2M/resp/<AE-ID>/<Registrar CSE-ID>" Payload: to = AE-ID fr = Registrar CSE-ID rqi = (token-string) same as received in request message rsc = 2004 pc = Serialized representation of <mgmtCmd> resource |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.1.15.4	mgmtCmd Update (Execute)

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_61 |
| Objective: | AE updates attribute (with ‘true’ in execEnable attribute) in mgmtCmd resource |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.9.6 TS-0004 [2], clause 7.4.16.2.3.2 |
| Pre-test conditions: | AE has created an application resource <AE> on Registrar CSE AE has created a node resource <node> on Registrar CSE AE has created a mgmtCmd resource <mgmtCmd> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a mgmtCmd Update Request |
| 2 | Mca | PRO Check Primitive | op = 3 (Update) to = {CSEBaseName}/{mgmtCmd} fr = AE-ID rqi = (token-string) pc = Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check HTTP | Sent request contains Request method = PUT Request-Target: {CSEBaseName}/{mgmtCmd} Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Content-Type: application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; Message-body: Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check CoAP | Sent request contains Method: 0.03 (PUT) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/{mgmtCmd} Content-format: application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message Topic: "/oneM2M/req/<AE-ID>/<Registrar CSE-ID>" Payload: op = 3 (Update) to = {CSEBaseName}/{mgmtCmd} fr = AE-ID rqi = (token-string) pc = Serialized representation of <mgmtCmd> resource |
| 3 |  | IOP Check | Check if possible that the <mgmtCmd> resource is updated in Registrar CSE. |
| 4 | Mca | PRO Check Primitive | rsc = 2004 (UPDATED) rqi = (token-string) same as received in request message pc = Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 X-M2M-RSC: 2004 X-M2M-RI: (token-string) same as received in request message Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check CoAP | Registrar CSE sends response containing: Response Code = 2.05 oneM2M-RSC: 2004 oneM2M-RQI: (token-string) same as received in request message Payload: Serialized representation of <mgmtCmd> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH message Topic: "/oneM2M/resp/<AE-ID>/<Registrar CSE-ID>" Payload: to = AE-ID fr = Registrar CSE-ID rqi = (token-string) same as received in request message rsc = 2004 pc = Serialized representation of <mgmtCmd> resource |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.1.15.5	mgmtCmd Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_62 |
| Objective: | AE deletes mgmtCmd resource |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.9.5 TS-0004 [2], clause 7.4.16.2.4 |
| Pre-test conditions: | AE has created an application resource <AE> on Registrar CSE AE has created a node resource <node> on Registrar CSE AE has created a mgmtCmd resource <mgmtCmd> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a mgmtCmd Delete Request |
| 2 | Mca | PRO Check Primitive | op = 4 (DELETE) to = {CSEBaseName}/{mgmtCmd} fr = AE-ID rqi = (token-string) |
|  |  | PRO Check HTTP | Sent DELETE request contains Request method = DELETE Request-Target: {CSEBaseName}/{mgmtCmd} Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/{mgmtCmd} oneM2M-FR: AE-ID oneM2M-RQI: (token-string) |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH message Topic: "/oneM2M/req/< AE-ID>/<Registrar CSE-ID>" Payload: op = 4 to = {CSEBaseName}/{mgmtCmd} fr = AE-ID rqi = (token-string) |
| 3 | Mca | PRO Check Primitive | rsc = 2002 (DELETED) rqi = (token-string) same as received in request message |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 X-M2M-RSC: 2002 X-M2M-RI: (token-string) same as received in request message |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 oneM2M-RSC: 2002 oneM2M-RQI: (token-string) same as received in request message |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH message Topic: "/oneM2M/resp/<AE-ID>/<Registrar CSE-ID>" Payload: to = AE-ID fr = Registrar CSE-ID rqi = (token-string) same as received in request message rsc = 2002 |
| 4 |  | IOP Check | Check if possible that the <mgmtCmd> resource is deleted in Registrar CSE. |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.1.15.6	execInstance Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_63 |
| Objective: | AE retrieves execInstance resource |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.9.8 TS-0004 [2], clause 7.4.17.2.2 |
| Pre-test conditions: | AE has created an application resource <AE> on Registrar CSE AE has created a node resource <node> on Registrar CSE AE has created a mgmtCmd resource <mgmtCmd> on Registrar CSE AE has executed the mgmtCmd resource <mgmtCmd> on Registrar CSE (update execEnable attribute with ‘true’) |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a execInstance Retrieve Request |
| 2 | Mca | PRO Check Primitive | op = 2 (RETRIEVE) to = {CSEBaseName}/{mgmtCmd}/{execInstance} fr = AE-ID rqi = (token-string) |
|  |  | PRO Check HTTP | Sent request contains Request method = GET Request-Target: {CSEBaseName}/{mgmtCmd}/{execInstance} Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Content-Type: application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; |
|  |  | PRO Check CoAP | Sent request contains Method: 0.01 (GET) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/{mgmtCmd}/{execInstance} Content-format: application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; oneM2M-FR: AE-ID oneM2M-RQI: (token-string) |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH message: Topic: "/oneM2M/req/<AE-ID>/<Registrar CSE-ID>" Payload: op = 2 (Retrieve) to = {CSEBaseName}/{mgmtCmd}/{execInstance} fr = <AE-ID> rqi = (token-string) |
| 3 | Mca | PRO Check Primitive | rsc = 2000 (OK) rqi = (token-string) same as received in request message pc = Serialized representation of <execInstance> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code =200 (OK) X-M2M-RSC: 2000 X-M2M-RI: (token-string) same as received in request message Message-body: Serialized representation of <execInstance> resource |
|  |  | PRO Check CoAP | Registrar CSE sends response containing: Response Code = 2.05 oneM2M-RSC: 2000 oneM2M-RQI: (token-string) same as received in request message Payload: Serialized representation of <execInstance> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH message: Topic: "/oneM2M/resp/<AE-ID>/<Registrar CSE-ID>" Payload: to = AE-ID fr = Registrar CSE-ID rsc = 2000 rqi = (token-string) same as received in request message pc = Serialized representation of <execInstance> resource |
| 4 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.1.15.7	execInstance Update (Cancel)

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_64 |
| Objective: | AE upates attribute ‘execDisable’ to true in execInstance resource to cancel pending management command. |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.9.7 TS-0004 [2], clause 7.4.17.2.1 |
| Pre-test conditions: | AE has created an application resource <AE> on Registrar CSE AE has created a node resource <node> on Registrar CSE AE has created a mgmtCmd resource <mgmtCmd> on Registrar CSE AE has executed the mgmtCmd resource <mgmtCmd> on Registrar CSE (update execEnable attribute with ‘true’) |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a execInstance Update Request |
| 2 | Mca | PRO Check Primitive | op = 3 (Update) to = {CSEBaseName}/{mgmtCmd}/{execInstacne} fr = AE-ID rqi = (token-string) pc = Serialized representation of <execInstance> resource |
|  |  | PRO Check HTTP | Sent request contains Request method = PUT Request-Target: {CSEBaseName}/{mgmtCmd}/{execInstacne} Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID Content-Type: application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; Message-body: Serialized representation of <execInstance> resource |
|  |  | PRO Check CoAP | Sent request contains Method: 0.03 (PUT) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/{mgmtCmd}/{execInstacne} Content-format: application/vnd.onem2m-res+xml; or application/vnd.onem2m-res+json; oneM2M-FR: AE-ID oneM2M-RQI: (token-string) Payload: Serialized representation of <execInstance> resource |
|  |  | PRO Check MQTT | Sent MQTT PUBLISH message Topic: "/oneM2M/req/<AE-ID>/<Registrar CSE-ID>" Payload: op = 3 (Update) to = {CSEBaseName}/{mgmtCmd}/{execInstacne} fr = AE-ID rqi = (token-string) pc = Serialized representation of <execInstance> resource |
| 3 |  | IOP Check | Check if possible that the <execInstance> resource is updated in Registrar CSE. |
| 4 | Mca | PRO Check Primitive | rsc = 2004 (UPDATED) rqi = (token-string) same as received in request message pc = Serialized representation of <execInstance> resource |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Code = 200 X-M2M-RSC: 2004 X-M2M-RI: (token-string) same as received in request message Content-Type: application/vnd.onem2m-res+xml or application/vnd.onem2m-res+json Message-body: Serialized representation of <execInstance> resource |
|  |  | PRO Check CoAP | Registrar CSE sends response containing: Response Code = 2.05 oneM2M-RSC: 2004 oneM2M-RQI: (token-string) same as received in request message Payload: Serialized representation of <execInstance> resource |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH message Topic: "/oneM2M/resp/<AE-ID>/<Registrar CSE-ID>" Payload: to = AE-ID fr = Registrar CSE-ID rqi = (token-string) same as received in request message rsc = 2004 pc = Serialized representation of <execInstance> resource |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

#### 8.1.15.8	execInstance Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_65 |
| Objective: | AE deletes execInstance resource |
| Configuration: | M2M_CFG_01 |
| References: | TS-0001 [1], clause 10.2.9.9 TS-0004 [2], clause 7.4.17.2.3 |
| Pre-test conditions: | AE has created an application resource <AE> on Registrar CSE AE has created a node resource <node> on Registrar CSE AE has created a mgmtCmd resource <mgmtCmd> on Registrar CSE AE has executed the mgmtCmd resource <mgmtCmd> on Registrar CSE (update execEnable attribute with ‘true’) |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a execInstance Delete Request |
| 2 | Mca | PRO Check Primitive | op = 4 (DELETE) to = {CSEBaseName}/{mgmtCmd}/{execInstacne} fr = AE-ID rqi = (token-string) |
|  |  | PRO Check HTTP | Sent DELETE request contains Request method = DELETE Request-Target: {CSEBaseName}/{mgmtCmd}/{execInstacne} Host: IP address or the FQDN of Registrar CSE X-M2M-RI: (token-string) X-M2M-Origin: AE-ID |
|  |  | PRO Check CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: IP address or the FQDN of Registrar CSE Uri-Path: {CSEBaseName}/{mgmtCmd}/{execInstacne} oneM2M-FR: AE-ID oneM2M-RQI: (token-string) |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH message Topic: "/oneM2M/req/< AE-ID>/<Registrar CSE-ID>" Payload: op = 4 to = {CSEBaseName}/{mgmtCmd}/{execInstacne} fr = AE-ID rqi = (token-string) |
| 3 | Mca | PRO Check Primitive | rsc = 2002 (DELETED) rqi = (token-string) same as received in request message |
|  |  | PRO Check HTTP | Registrar CSE sends response containing: Status Code = 200 X-M2M-RSC: 2002 X-M2M-RI: (token-string) same as received in request message |
|  |  | PRO Check CoAP | Registrar sends response containing: Response Code = 2.05 oneM2M-RSC: 2002 oneM2M-RQI: (token-string) same as received in request message |
|  |  | PRO Check MQTT | Sent a MQTT PUBLISH message Topic: "/oneM2M/resp/<AE-ID>/<Registrar CSE-ID>" Payload: to = AE-ID fr = Registrar CSE-ID rqi = (token-string) same as received in request message rsc = 2002 |
| 4 |  | IOP Check | Check if possible that the <execInstance> resource is deleted in Registrar CSE. |
| 5 |  | IOP Check | AE indicates successful operation |
| IOP Verdict |  |
| PRO Verdict |  |

### -----------------------End of change 1---------------------------------------------