| Input Contribution |
| --- |
| Meeting ID* | TST 27.1 |
| Title:* | TS-0019-Abstract Test Method – Definition of Upper Tester Trigger Control Message |
| Source:* | Ting Martin Miao, KETI, martin.miao@keti.re.kr JaeYoung Hwang, Sejong University, forest62590@sju.ac.kr Abdullah Aziz, Sejong University, G2016FFM082@sju.ac.kr |
| Uploaded Date:* | 2017-03-26 |
| Document(s) Impacted* | TS-0019 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution defines abstract service primitives and formats for AE triggering control message. Protocol and serialization are also clarified for transportation of AE triggering control message.

## -----------------------Start of change 1--------------------------------------------

# 5	Abstract Test Method (ATM)

### 5.4.2 utPort

#### 5.4.2.2 Upper Tester Control Primitives

#### 5.4.2.2.1 Introduction

The upper tester triggering message is used by utPort to transport control commands between Test System and the Upper Tester Application over UDP/TCP connections. The upper tester triggering message type maps to particular message formats for exchanging data and those message formats are defined by TTCN-3 primitive as shown at table 5.4.2.2.1-1, UtTrigger and UtTriggerAck primitive.

Table 5.4.2.2.1-1 Mapping of TTCN-3 Primitives to oneM2M Service Primitives

| Upper TesterControl Message Type | TTCN-3 Primitives | Direction |
| --- | --- | --- |
|  |  | TS | UT |
| Trigger | UtTrigger Primitive | ( |
| Trigger Acknowledgement | UtTriggerAck Primitive | ( |

#### 5.4.2.2.2 UtTrigger and UtTriggerAck Primitives

UtTrigger primtive is used for triggering progress as depicted as Figure 5.4.2.2.2-1.

The UtTrigger primitive is initialized by the Test System to send triggering message to the target IUT. The IUT will send acknowledgement message back to the Test System using UtTriggerAck primitive if trigger message is successfully transported to the IUT. Then IUT starts interaction with Test System through oneM2M request and response primitives.

The payload of Trigger primitive consists of TestcaseID, Protocol Type and Serialization.

Figure 5.4.2.2.2-1 Trigger message flow

Table A.3-1 lists a mapping table that maps each field of UtTrigger primitive to oneM2M data types.

Table 5.4.2.2.2-1 Specific attribuite of UtTrigger primitive

| Field | Mapping to oneM2M data types | Reference | Example |
| --- | --- | --- | --- |
| Testcase ID | One single testcase identifier that maps to associated test purpose in TS-0018 | TS-0018 [] | TC_AE_DMR_BV_001 |
| Protocol | HTTP | TS-0009 [] | - |
| Serialization | JSON | TS-0004 [] | - |

Table 5.4.2.2.2-2 Specific attribuite of UtTriggerAck primitive

| Field | oneM2M data types | Reference | Example |
| --- | --- | --- | --- |
| Response Status Code | HTTP status code | 6.3.2-1 Status Code Mapping TS-0009 [] | 200 (OK) |

UtTrigger primitive is represented by oneM2M requestPrimitive serialized in JSON as following:

{

"requestPrimitive":{

"primitiveContent": {

"m2m:UtTrigger" :{

"testcaseID": "TC_AE_DMR_BV_001"

}

},

"protocol":"HTTP",

"serialization":"JSON"

}

}

Similarly, UtTriggerAck primitive is represented in oneM2M responsePrimitive:

{

"responsePrimitive":{

"responseStatusCode": {

"200"

}

}

}

When the UtTrigger primitive is transported using HTTP protocol, the payload of HTTP request is represented by the primitiveContent:

{

"m2m:UtTrigger" :{

"testcaseID": "TC_AE_DMR_BV_001"

}

}

Editor’s Note: Short name has to be mapped from corresponding long name when implemented using HTTP protocol with JSON serialization.

While when the UtTriggerAck primitive is transported using HTTP protocol, the response status code parameter is included within a HTTP header.

## -----------------------End of change 1--------------------------------------------

## -----------------------Start of change 2--------------------------------------------

#### 5.4.2.2.2 Control Communication Protocol

Protocol used for proceeding communications between TS and Upper Tester Application is designated to the Hypertext Transfer Protocol (HTTP) protocol owning it is an application protocol that is widely supported by most all IoT devices and various intrinsic features such as persistent connection, ease of programming, flexibility etc.

#### 5.4.2.2.3 Control Message Serialization

Control commands that are wrapped within a request body of HTTP message shall be serialized into JavaScript Object Notation (JSON) because it is very lightweight and easy to parse and generate for machines.

#### Appendix: ADN profiles

| Function | Feature Set | Feature | Remark |
| --- | --- | --- | --- |
| REG | AE/REG/00002 | AE/REG/00002/00001 | Create <AE> |
|  |  | AE/REG/00002/00002 | Create <AE> with resourceName |
|  |  | AE/REG/00002/00003 | Create <AE> with expiration Time |
|  |  | AE/REG/00002/00004 | Create <AE> with labels |
|  |  | AE/REG/00002/00005 | Create <AE> with applicationName |
| DMR | AE/DMR/00001 | AE/DMR/00001/00001 | Create <container> with no attribute set |
|  |  | AE/DMR/00001/00002 | Create <container> with resourceName |
|  |  | AE/DMR/00001/00003 | Create <container> with expirationTime |
|  |  | AE/DMR/00001/00004 | Create <container> with labels |
|  |  | AE/DMR/00001/00005 | Create <container> with creator |
|  |  | AE/DMR/00001/00006 | Create <container> with maxNrOfInstances |
|  |  | AE/DMR/00001/00007 | Create <container> with maxByteSize |
|  |  | AE/DMR/00001/00008 | Create <container> with maxInstanceAge |
|  | AE/DMR/00002 | AE/DMR/00002/00002 | Create <contentInstance> with resourceName |
|  |  | AE/DMR/00002/00003 | Create <contentInstance> with expirationTime |
|  |  | AE/DMR/00002/00004 | Create <contentInstance> with labels |
|  |  | AE/DMR/00002/00005 | Create <contentInstance> with creator |
|  |  | AE/DMR/00002/00006 | Create <contentInstance> with contentInfo |
|  |  | AE/DMR/00002/00007 | Create <contentInstance> with contentRef |

< AND Profile1 >

| Function | Feature Set | Feature | Remark |
| --- | --- | --- | --- |
| GEN | AE/GEN/00001 | At least one | Resource Identifiers |
| GEN | AE/GEN/00002 | AE/GEN/00002/00001 | Support Create request targeting one resource |
| REG | AE/REG/00002 | AE/REG/00002/00001 | Create <AE> with mandatory attributes |
| REG | AE/REG/00002 | AE/REG/00002/00006 | Create <AE> with pointOfAccess |
| SUB | AE/SUB/00001 | AE/SUB/00001/00001 | Create <subscription> with mandatory attributes |

< ADN Profile2 >

| Function | Feature Set | Feature | Remark |
| --- | --- | --- | --- |
| GEN | AE/GEN/00001 | At least one | Support one of the format of resource identification |
|  | AE/GEN/00002 | AE/GEN/00002/00001 | Support Create request targeting one resource |
| REG | AE/REG/00002 | AE/REG/00002/00001 | Create<AE> with mandatory attributes |
| DMR | AE/DMR/00001 | AE/DMR/00001/00001 | Create <container with no attribute set |
|  | AE/DMR/00002 | AE/DMR/00002/00001 | Create <contentInstance> with mandatory attributes |

< ADN Profile3 >

## -----------------------End of change 2--------------------------------------------